## Slide 1
MICROCONTROLERS
& OPEN SOURCE HARDWARE
Jérémie GRISOLIA
Département de Génie Physique – INSA TOULOUSE
05.61.55.96.58 – Bureau 138 (1er étage)
jeremie.grisolia@insa-toulouse.fr
PTP ISS: http://moodle.insa-toulouse.fr/course/view.php?id=494
I4GPMH11: https://moodle.insa-toulouse.fr/course/view.php?id=1663
Version 08/04/2024

## Slide 2
ANALOG ELECTRONIC CIRCUIT
PCB SHIELD ELABORATION (KICAD)
GRAPHITE STRAIN SENSOR
INTRODUCTION TO SENSOR AND MEASUREMENT CHAIN
SENSOR DATASHEET
MICROCONTROLERS & OPEN SOURCE HARDWARE
TEST BENCH
GITHUB
UF I4GPMH21: du capteur au banc de test en open source hardware !
Collaborative tool
https://moodle.insa-toulouse.fr/course/view.php?id=1663

## Slide 3: PRATICAL WORK I4GPMH21
TP n°1A: My first program : Blink
TP n°1C: Serial Monitor (Arduino => PC)
[ TP n°1F: Buzzer melody ]
TP n°1G: temperature sensor
TP n°2A: Touch Pad DS
[TP n°2B: LCD (autonomous)]
[ TP n°2D: LCD & Temperature (1/2 Group) ]
[ TP n°2C: Touch Pad & LCD (1/2 Group) ]
TP n°3A: Continous Current Motor
TP n°3B: Photorésistance
[ TP n°3C: Servo-motor ]
[ TP n°3D: Software debouncing ]
[ TP n°3E: Hardware debouncing ]
TP n°3F: Interruptions
TP n°4B: I2C (Nunchuk Wii)
[ TP n°4C: Nunchuk Wii & Servo-motor ]
[ TP n°5A: My first library ]
[ TP n°5B: Processing & Arduino ]
TP n°1
« basics »
TP n°2
« Analog/
Digital »
TP n°3
« actuators
/sensors»
TP n°4
« bus com »
TP n°1D: Serial Monitor (PC => Arduino)
TP PCB DESIGN
KiCAD + Design de shield Arduino®
TP5C: Android and Arduino application creation : bi-direction communication
TP n°5
« interacting »
Files for TP n°1 to 12 are avalaible on MOODLE: https://moodle.insa-toulouse.fr/course/view.php?id=1663
TP GiTHub
GitHub
[ TP6 - Connexion Arduino - C# ]
TP n°6
Piste Verte
Piste Bleue
Piste Rouge
TP n°8
  [TP8 - 1 - TP ANALOG READ ON ESP32]
  [TP8 - 2 - TP OLED ON ESP32]
  [TP8 - 3 - TP ANALOG + OLED ON ESP32]
  [TP8 - 4 - TP CAPACITIVE TOUCH]
  [TP8 - 5 - TP HALL EFFECT SENSOR]
TP n°11
[TP11 ARDUINO ET INTELLIGENCE ARTIFICIELLE]
TP INTRO
[MICROPYTHON PROGRAMMING BASICS]
[GETTING STARTED WITH uPiCraft]
TP n°1B: Blink without delay
TP n°1E: Module HC-05 Bluetooth
TP n°3G: Encodeur rotatoire
Facultatifs:
TP n°4F: SPI Digital Potentiometer
[TP n°3Bextended: Photorésistance + Machine à état]
TP n°3C: Flex Sensor + Servo Motor
TP n°3C: Flex Sensor
TP n°4E: OLED Screen
TP INTRO
[TP VISUAL STUDIO CODE + PLATFORM IO]
TP n°4A: SERIAL (Arduino => Python)
[ ]: FACULATIFS
TP n°4G: SPI Mystery device !

## Slide 4: INTRODUCTION
OBJECTIVES: what are microcontrollers, their internal and architecture, their possibilities
- Set-up of an Arduino® ecosystem around Open-Source Hardware Platform, ESP32…
This course provides all the necessary elements to the design and implementation of many applications with particularly:
elements to create its own electronic circuits (simulation and schematic to the routing to pull its PCB)
presentation of the language syntax of programming and development environment;
Dozens of pattern interfaces with the most various devices (displays, motors, sensors, bus I2C, Nunchuk, touch-screen DS...).
Several dozens of program examples for implementing these interfaces
elements to create your own libraries
elements to create your own human interface device
elements of interfacing Arduino/Processing (programming interfaces Java), C#, ANDROID and microPython
elements to create an IoT application
The Arduino® is a complete platform of electronic development to achieve lower cost high performance microcontroller-based applications.

## Slide 5: SIMPLIFIED SUMMARY OF THE LECTURE
I - MICROCONTROLLERS AND THEIR ARCHITECTURES:
II - THE OPEN - SOURCE ARDUINO® PLATFORM
II-1 What is an Arduino?
II-2 IDE development platform
II-3 the addressable components: actuators and sensors?
III - IMPLEMENTATION OF THE ARDUINO :
III-1 input/output digital
III-2 inputs/outputs analog
III-3 applications digital & analog
III-4 do the analog with digital debouncing
III-5 hardware and software debouncing
III-6 interrupts (hardware and software)
III-7 communication series: (RS232) asynchronous & synchronous (I2C, SPI, one wire)
III-8 create a library
III-9 the shields & their creation
IV - COMMUNICATION OF THE ARDUINO WITH OTHER PLATFORMS:
IV - 1 PROCESSING => JAVA,
IV - 2 ANDROID,
IV - x VISUAL STUDIO CODE + PLATFORM IO,
IV - 4 MICRO-PYTHON,
IV - 5 NODE-RED
IV - 6 MICRO-PYTHON,
IV - 7 IoT
V - IMPLEMENTATION OF THE ESP32 WITH MICRO-PYTHON:
V-1 ANALOG READ, OLED, LoRa, CAPACITIVE TOUCH, HALL EFFECT ON ESP32
V-2 MQTT ON ESP32/ESP8266
V-3 MQTT - Connect ESP32 to Node-RED
VI - IMPLEMENTATION OF ARTIFICIAL INTELLIGENCE
VI – 1 ARDUINO AND ARTIFICIAL INTELLIGENCE
VII - ESSENTIAL REFERENCES

## Slide 6: PLAN DETAILLE DU COURS (AVEC LIENS HYPERTEXTES)
1 - CONTEXT: OPEN SOURCE HARDWARE
2 - ARDUINO – PLATFORM
3 - GETTING STARTED WITH THE DEVELOPMENT ENVIRONMENT
4 – MICROCONTROLLERS
5 - WHAT FAMILY OF MICROCONTROLLERS
6 - AUTOPSY OF AN ARDUINO PLATFORM
7 DIGITALS INPUTS/OUTPUTS
  7 - 1 TP1A
  7 - 2 TP1B
  7 - 3 TP1C
8 - ANALOG INPUTS
  8 – 1 TP1E
  8 - 2 TP2A
9 - ADRESSABLE DEVICES ?
10 - DIGITAL & ANALOG APPLICATIONS
  10 - 1 TP2B
  10 – 2 TP2C
11 - DO "ANALOG" WITH DIGITAL
  11 – 1 TP3-A
  11 – 2 TP3-B
12 – DEBOUNCING
13 – INTERRUPTS
14 - HARDWARE INTERRUPTS
14 - 1 TP3-F
15 - SOFTWARE INTERRUPTS
16 – TIMERS
17 - SERIAL COMMUNICATION
  17-1 - ASYNCHRONOUS SERIAL COMMUNICATION
  17-2 - SYNCHRONOUS SERIAL COMMUNICATION
  17-3 - SYNCHRONOUS SERIAL COMMUNICATION: I2C
17 – 4 - TP4-A
18 - SYNCHRONOUS SERIAL COMMUNICATION: SPI
19 – LIBRAIRIES
20 - THE SHIELDS
21 - TO GO FURTHER: PROCESSING
21 - 1 - TP4-D
22 - PROCESSING FOR ANDROID
22 - 1 - TP5
23 - TO GO FURTHER: LIFA
24 - ARDUINO ET C#
25 - TO GO FURTHER: PYTHON
26 - OTHER INTERESTING TRACKS ?
27 - ARDUINO ET NODE-RED
28 - MICRO-PYTHON
29 - FLASHING MICRO-PYTHON TO ESP32
30 - GETTING STARTED WITH uPyCRAFT IDE
31 - MICROPYTHON PROGRAMMING BASICS
32 - MICROPYTHON MODULES
  32 - 1 - TP ANALOG READ ON ESP32
  32 - 2 - TP OLED ON ESP32
  32 - 3 - TP LoRa ON ESP32
  32 - 4 - TP CAPACITIVE TOUCH
  32 - 5 - TP HALL EFFECT SENSOR
34 - HOW MQTT WORKS
35 - TP - MQTT ON ESP32/ESP8266
36 - MQTT - Connect ESP32 to Node-RED
37 - ARDUINO ET INTELLIGENCE ARTIFICIELLE
38 – THINGS NETWORK + NODERED
39 - RAPPEL SUCCESSIVE APPROXIMATION ADC
40 - COMMANDES LINUX UTILES
41 – COMPARATIFS
42 - AND SECURITY ?
43 – REFERENCES
44 - QUIZZ

## Slide 7
I - CONTEXT:
OPEN SOURCE HARDWARE

## Slide 8: ARDUINO AND OPEN-SOURCE HARDWARE : A PHILOSOPHY
1 - 'hardware’ material is 'open source ':
2 - The 'software' is 'open source’:
we can use it, modify it and distribute it freely (under the same terms as the license of the original work).
The free hardware (OSHW - OpenSource Hardware) is a term that includes "tangible" products - machines, devices or all physical devices - whose plans have been made public in such a way that anyone can make them, edit, distribute and use (under the same terms as the license of the original work).
http://freedomdefined.org/OSHW/translations/fr
Most of the authors, regardless of their field of activity, and independently of their status of amateur or professional, have interest to foster an ecosystem where works can be distributed, re-used and derived in creative ways.
More easy is to reuse and derive works, the more our culture is enriched.
http://freedomdefined.org/Definition/Fr
Beware, in OSH, the hardware design (i.e. mechanical drawings, schematics, BOM, layout PCB, source code and layout of integrated circuits...), in addition to the software that drives the hardware are all required to approach free software (free and open-source software (FOSS))
http://en.wikipedia.org/wiki/Open_source_hardware
Major interest of open source work methods:
- principle of community development
- mutualisation of skills
- mutualization of problem solving.

## Slide 9: OPEN-SOURCE HARDWARE EXAMPLES
REPRAP

## Slide 10: AN OPEN LETTER TO HOBBYISTS by BILL GATES
http://fr.wikipedia.org/wiki/An_Open_Letter_to_Hobbyists

## Slide 11: LOIS ET PRINCIPES SOUS-TENDANT LES LICENCES LIBRES
-Copyleft is the authorization given by the author of a work subject to copyright (artwork, text, computer or other program) to use, study, modify and copy his work, insofar as this authorization remains preserved.
=> the author denies that his work can evolve with a restriction of the right to copy (copyright).
http://fr.wikipedia.org/wiki/Copyleft
The best-known free license using copyleft is the GNU General Public License, but there are also other licenses, created specifically for certain areas very various (art, role play, journal, etc.), which may be considered as of "copyleft licenses.
-As a result, the contributor making a change (correction, addition, re-use, etc.) is forced to redistribute its own contributions with the same conditions of use as the original.
In other words, the creations made from items under copyleft inherit de facto this copyleft.
http://des-trucs-pour-changer-de-vie.blogspot.fr/2013/02/des-trucs-pour-changer-de-vie-devient.html#.UUw2Pjc_4tI
http://artlibre.org/licence/lal
The free Copyleft license is the best way to encourage sharing and encourage creativity. Intellectual creation must free themselves from the shackles of copyright, because the copyright only serves the industry, not the culture.
Culture can flourish in the sharing!
If someone takes my work, improves it and makes something new, beautiful, great, useful, via Copyleft, then I'd be very happy and everyone will win.
In short, I think that the copy is not a brake, but a lever.

## Slide 12: EXEMPLE DE LICENCE LIBRE: LICENCE CREATIVE COMMONS
Creative Commons licenses were created on the premise that intellectual property was fundamentally different from physical property, and the observation that the current copyright laws were an obstacle to the dissemination of the culture.
http://fr.wikipedia.org/wiki/Licence_Creative_Commons
This License including although:
waiver - no matter which of the above conditions can be waived if you have the permission of the owner of rights.
GOAL: To provide a legal tool that guarantees the protection of the rights of the author of an artistic work and the free movement of the cultural content of this work, in order to allow authors to contribute to a legacy of works available in the 'public domain' (term taken in the broad sense).
http://creativecommons.org/licenses/by/3.0/deed.fr
-Paternity [BY] (grant): the work can be freely used provided that attribute it to the author by citing its name.
-No commercial use [NC] (Noncommercial): the owner of rights may authorize any use or instead restrict it to non-commercial use (commercial use remaining subject to approval).
-No change [ND] (NoDerivs): the owner of rights may continue to reserve the faculty to make derivative works of type or instead beforehand authorize modifications, translations.
-Sharing of initial conditions to the same [SA] (ShareAlike): the owner of the rights may authorize in advance changes; can overlap (SA) required for so-called derivative works to be offered to the public with the same freedoms (under the same Creative Commons options) as the original work.

## Slide 13: CLASSIFICATION OF LICENCES
Video explication licence CC
http://www.netpublic.fr/2015/04/comment-choisir-une-licence-creative-commons/
http://www.netpublic.fr/2012/12/creative-commons-video/ http://www.netpublic.fr/2012/03/creative-commons-dossier/

## Slide 14: CLASSIFICATION DES LICENCES
Désignation complète du contrat | Terme abrégé désignant la licence | Symboles désignant la licence |  |  |  | Type de licence
Paternité | CC-BY |  |  |  |  | Licence libre non copyleft
Paternité Partage des conditions initiales à l'identique | CC-BY-SA |  |  |  |  | Licence libre copyleft
Paternité Pas de modification | CC-BY-ND |  |  |  |  | Licence de libre diffusion
Paternité Pas d'utilisation commerciale | CC-BY-NC |  |  |  |  | Licence de libre diffusion
Paternité Pas d'utilisation commerciale Partage des conditions initiales à l'identique | CC-BY-NC-SA |  |  |  |  | Licence de libre diffusion
Paternité Pas d'utilisation commerciale Pas de modification | CC-BY-NC-ND |  |  |  |  | Licence de libre diffusion

## Slide 15: III - ARDUINO® PLATFORM
III - ARDUINO® PLATFORM

## Slide 16: WHAT IS AN ARDUINO ?
A software
A hardware
A communauty
http://arduino.cc
The microcontroller card is programmed using the Arduino programming language (based on WIRING) and the Arduino development environment (based on the PROCESSING).

## Slide 17: WHY AN ARDUINO ?
There are many microcontrollers and many platforms based on microcontrollers available for programmed Electronics: Parallax Basic Stamp, Netmedia's BX - 24, Phidgets, MIT's Handyboard, and many others that offer the comparable features.
So why Arduino?
A clear and simple programming environment: environmental programming Arduino (= the Arduino software) is easy to use for beginners, while being flexible enough so that advanced users can benefit also.
Cheap: Arduino cards are relatively expensive compared to other platforms. The less expensive versions of the Arduino module can be assembled by hand, and even the Arduino pre-assembled cost less than € 25 (microcontroller includes...)!
Cross-platform: the Arduino software, written in Java, runs on Windows, Macintosh and Linux operating systems. Most microcontrollers systems are limited to Windows.
Important communication platform:
  completely 'stand-alone', or
  he talks to other devices: ' it, Flash, Processing (Java), Pure data, MAX/MSP, Ruby, Python, .NET...
-On the internet, we find:
- A community of users.
- Use guides.
- Examples.
- Support forums...

## Slide 18: WHY AN ARDUINO ?
1 - Software Open Source and extensible: => can use it and modify it freely.
The Arduino software and the Arduino language are published under open source, available license to be supplemented by experienced programmers.
The language can also be extended using C++ libraries, and people who want to understand the technical details can reconstruct the passage of the Arduino language in c for AVR Microcontroller on which it is based.
Similarly, you can add code to the AVR - C language directly in your Arduino programs if you want to.
2 - Open source hardware and extensible: => you can copy it, manufacture it and modify it freely.
Arduino cards are based on the Atmel ATMEGA8 microcontrollers, 168, 328, etc...
Which patterns of the modules are published under a Creative Commons (CC) license. Circuits experienced or relatively inexperienced designers can make their own version of Arduino, complementing them and improving them.
But be careful: a software or a hardware OPEN SOURCE is before all a software or a hardware whose codes or plans are accessible and modifiable by all.
This sharing of knowledge does not preclude compensation!
The company Arduino is a commercial company, many companies work and thrive around the free (~ 100 M$ total in 2010) but allows especially exchanges and circulation of knowledge...
A period where the concerns about the sharing of knowledge are large, have a small ethical reflection on the merchandising of knowledge and his work seems beneficial...

## Slide 19: II – 2 L’ENVIRONNEMENT DE DEVELOPPEMENT
GETTING STARTED WITH THE DEVELOPMENT ENVIRONMENT

## Slide 20: AUTOPSY OF AN ARDUINO BOARD
I2C bus
PWM
INTERRUPTS
SERIAL PORT
Digital I/O
Power pins
Analog Inputs
Power supply
TX/RX LED
USB PORT: power supply and data
LED pin 13
LED power supply
RESET button
In Circuit Serial Programming
For donwloading other OS than bootloader
AVR Microcontoller

## Slide 21: IDE ARDUINO
Menu bar
Button bar
Open files tab
Editing window
Area current messages
Console display: messages from compilation
Verify (compilation)
Download
Serial Monitor
New
Open
Save
Send to arduino
Baudrate
Selection
Message display from Arduino
Editing area for sending to arduino

## Slide 22: PRINCIPLE OF OPERATION OF THE ARDUINO AND ITS IDE
Designing or opening an existing with the ARDUINO On software program
checks this program with the ARDUINO (compilation) software.
If errors are reported, you change / fix the program.
Load (upload) the program on the board,
the electronic Assembly wiring.
The program execution is automatic after a few seconds if the arduino is connected (possibly you did a reset)
powered the card either through the USB port, or by a stand-alone power source (battery 9 volts for example)
Check if the installation works (and possibly a debugging)
The Arduino to program in a high-level language (≠ machine language) mixing of C and C++ restricted and adapted to the possibilities of the board (language used by professionals).

## Slide 23: OPERATION OF THE IDE: STRUCTURE OF A PROGRAM

## Slide 24: OPERATION OF THE IDE: STRUCTURE OF A PROGRAM
TP to realize: download the program 'Blink' in the Arduino Uno

## Slide 25
III – 1 DIGITALS INPUTS/OUTPUTS

## Slide 26: DIGITAL INPUT/OUTPUT
The Arduino has 14 input/output digital D0 to D13.
In 'void setup', you must declare a PIN as an input or as an output by one of the following two statements:
pinMode (pin_name, INPUT); //input pin
pinMode (pin_name, OUTPUT); //output pin
Output: it sends either 5V on pin, or 0V.
This corresponds to a '1' or a '0', to a level "above" or at a "low" level
In the program this corresponds to the following instructions:
digitalWrite (pin_name, HIGH); //send 5V to pin is « 1 »
digitalWrite (pin_name, LOW); //send 0V on pin is “0”
Input: the board can read either a high level ('1' or HIGH) is a low level ('0' or LOW)
In the program this corresponds to the following instructions:
digitalRead (pin_name);

## Slide 27: VALUE LOW AND HIGH ON ARDUINO?
What gives for VCC = 5V:
logic low (LOW) in entry level: low = 0.3 x x 5V VCC = 0.3 = 1.5 Volts.
A voltage between-0.5 and less than 1.5V is considered to be a low level.
Logic (HIGH) high level input: HIV = 0.6 x VCC = 0.6 x 5V = 3.0 Volts.
A tension above 3V and lower than 5.5V is considered to be a high level.
-The intermediate zone 1, 5V - 3V is indeterminate and must be avoided.
=> LOW and HIGH level have pretty tolerant values.
For a remainder, we found here the voltage of the logical levels of entry for the Arduino (ATmega 328):

## Slide 28: DEFINITIONS OF DIGITAL PINS
3 possible definitions with pinMode () instruction:
INPUT,
INPUT_PULLUP and
OUTPUT
Pins configured as INPUTS:
INPUT: the Arduino (Atmega) pins are configured as input with
pinMode () in a State of high impedance (series resistance of 100 M)
Example the: pinMode (inPin, INPUT);
However, you probably want that spindle is referenced to the Earth, so 2 solutions:
either put a pull-down resistor (resistance to Earth) in the external circuit or
configure the pin entered as INPUT_PULLUP, which has a pull-up resistance
INPUT_PULLUP: the Atmega on the Arduino chip has an internal pull-up
resistance. Beware, since pull-up => this inverts the behavior of the pin,
since HIGH means that the sensor is "off", and LOW means that
the sensor is activated.
Example: pinMode (2, INPUT_PULLUP);
Pins configured as OUTPUTS:
-OUTPUT: pins configured as output with pinMode () are supposed to be in a State of low impedance. This means that they can provide a significant amount of current to other circuits. Example: pinMode (2, OUTPUT);

## Slide 29
TO GO FURTHER

## Slide 30: IF YOU NEED OTHER DIGITAL PINS
HOW DOES DO? Use the alias A0 (for the analog input 0), A1, etc...
For example, to use the pin A0 in digital output, the code looks like this:
pinMode (A0, OUTPUT);
digitalWrite (A0, HIGH); //put pullup on the analog pin 0
pull-up resistance is then enabled
Attention:
1 - the other analog pins also have a pull-up resistance, which works like the digital pins. They are activated by the command:
digitalWrite (A0, HIGH); //pullup put on the analog pin 0 even if the PIN is declared as input.
2. activation of a pullup will affect the values reported by the analogRead() function, used on the C PORT of analog pines (ATTENTION).
They have also all features of general use of the input/output (GPIO)
the same pins digital (0-13).
if a user needs more input/output digital pins: he can use the analog pins as GPIO.
The ATmega of the Arduino has 6 channels analog-digital (A/D) (8 in CMS version), for 10-bit resolution while the main function of the analog pins is to read sensors via analog INPUTS

## Slide 31
TP1A

## Slide 32: MY FIRST PROGRAM: BLINKING LED
http://www.oomlout.com/a/products/ardx/circ-01
LEDs (light emitting diodes) are widely used nowadays.
Let's start with something very simple:
turn on and turn off, several times
=> It is the 'HELLO WORLD’ of µ-controllers!
/* Blink *Turns on an LED on for one second, then off for one second, repeatedly. *The circuit: LED connected from digital pin 13 to ground. */ int ledPin = 13; // LED connected to digital pin 13 // The setup() method runs once, when the sketch starts
void setup() { pinMode(ledPin, OUTPUT); // initialize the digital pin as an output: } // the loop() method runs over and over again, as long as the Arduino has power void loop() { digitalWrite(ledPin, HIGH); // set the LED on delay(1000); // wait for a second digitalWrite(ledPin, LOW); // set the LED off delay(1000); // wait for a second }
<= BACK
QUESTION: Is it really reasonable to use a timer and the delay function (which is blocking!) ????

## Slide 33: PLAYING WITH OPENAI CHATGTP
https://chat.openai.com/chat

## Slide 34
Behind the scene
Behind the scene

## Slide 35: USEFUL INSTRUCTIONS: BLINK by ASM
2 — Ten (10) Asm Instructions used:
AVR Instruction Set — Manual
Instruction : Cycle : Descriptions
ldi : 1 : Load Immediate Into; Loads an 8-bit constant directly to regs.16 to 31.
cbi : 1 : Clear Bit In I/O Register — Clears a specified bit in an I/O register.
sbi : 1 : Set Bit in I/O Register — Sets a specified bit in an I/O Register.
out : 1 : Store Register to I/O Location — Stores data from register Rr in the Register File to I/O Space (Ports, Timers, Configuration Registers, etc.).
dec : 1 : Decrement — Subtracts one from the contents of register Rd and places the result in the destination register Rd.
adiw : 2 : Add Immediate to Word — Adds an immediate value (0–63) to a register pair and places the result in the register pair.
brne : 2 : Branch if Not Equal — Conditional relative branch. Tests the Zero Flag (Z) and branches relatively to PC if Z is cleared.
rcall : 1 : Relative Call to Subroutine — Relative call to an address within PC
ret : 1 : Return from Subroutine — Returns from subroutine.
rjmp : 1 : Relative Jump — Relative jump to an address.

## Slide 36: HELLO WORLD ASM
Init your code:
Let’s have look at probably the easiest program possible:
.ORG 0x000 ; the next instruction has to be written to add 0x0000
; infinite loop START: ; this is a label “START” rjmp START ; Relative JuMP to START
When the instruction is executed, the cpu (ALU — Arithmetic Logic Unit) will jump to START. The jump will be repeated over and over, resulting in an infinite loop. Alright, that not a big deal…
Do the Math !
Assuming that our Arduino AVR is running at 16 MHz (16 Million clock cycles per second),
How long does all this take?
T = 1/ F then T = 1 / 16x106 = 0,0000000625 seconds, not precisely 0,06 us
That’s pretty fast! We can not see at this frequency the blinking of the LED !!!
Remark:
We observed experimentally that human eye can’t make out a difference in the picture frame if it appears for less than 16ms to 13ms (0,016-0,013s).
Hence purely based on this, we can say sampling frequency is 60Hz to 80Hz (about 0,06 & 0,08 MHz).
Do the trick!
For example: let’s take a LED 0,5s ON and 0,5s OFF: at F=16 MHz, we need 8 000 0000 cycles cycles
(1 cycle = 0,0000000625 seconds at 16MHz => for 0,5s this makes 0,5 / 0,0000000625s)
How to achieve all this cycles if I can count only up to 255 (remember, we have an 8-bit chip)… magic?
BLINK by ASM

## Slide 37: HELLO WORLD ASM
For this we will have to implement two loops: inner and outloop.
First registers can be used in pairs, allowing to work with values from 0 to 65 535. That’s a word (16 bits).
The following piece of code clears registers 24 and 25 and increments them in a loop
until they overflow to zero again. When that condition occurs, the loop doesn’t go around again. Let’s go ahead!
clr r24 ; clr needs 1 cycle clr r25 ; clr needs 1 cycle
DELAY_05: ; we need .5s delay adiw r24, 1 ; adiw needs 2 cycles and brne DELAY_05 ; brne needs 2 cycles if the branch is done ; and 1 otherwise
The inner loop is treated like one BIG instruction needing 262145 clock cycles
Why ?
Every time the registers don’t overflow the loop takes adiw(2) + brne(2) = 4 cycles. The loop takes 0xFFFF (65 535) times before the overflow occurs.
The next time the loop only needs 3 cycles, because no branch is done. This adds up to 4 * 65 535(looping) + 3(overflow) + 2(clr) = 262 145 cycles.
This is still not enough: 8 000 000/262 145 ~ 30.51.
=> The “outer” loop will be down-counting from 31 to zero using r16.
BLINK by ASM

## Slide 38: HELLO WORLD ASM
This is where the fine-tuning comes in : we need to change the initial value of r24:r25. The outer loop is executed 31 times and includes the “big-inner-loop-instruction”. We have to subtract some cycles from the inner loop: 126 588 / 31 = 4 083 cycles per inner loop. This is what the inner loop has to be shorter.
Every iteration of the inner loop takes 4 cycles (the last one takes 3 but that’s not so important), so let’s divide those 4 083 by 4 = 1 020.8 or 1 021 less iterations.
This is our new initialisation value for r24:r25! =>
ldi r24, low(1021) ; load registers r24:r25 with 1021, our new ; init value
ldi r25, high(1021)
=> The result is 8 000 000 clock cycles!
ldi r16, 31
OUTER_LOOP: ; outer loop label ldi r24, 0 ; clear register 24 ldi r25, 0 ; clear register 25
DELAY_05: ; the loop label adiw r24, 1 ; “add immediate to word”: r24:r25 are ; incremented brne DELAY_05 dec r16 ; decrement r16 brne OUTER_LOOP ; load r16 with 8
The overall loop needs:
262 145 (inner loop) + 1 (dec) + 2 (brne) = 262 148 * 31 = 8 126 588 cycles.
this is more like what we want,
BUT 126 588 cycles too long.
BLINK by ASM

## Slide 39: HELLO WORLD ASM
.ORG 0x0000 ; the next instruction has to be written to
; address 0x0000
rjmp START ; the reset vector: jump to "main«
START:ldi r16, low(RAMEND) ; set up the stack
out SPL, r16
ldi r16, high(RAMEND)
out SPH, r16
ldi r16, 0xFF ; load register 16 with 0xFF (all bits 1)
out DDRB, r16 ; write the value in r16 (0xFF) to Data ; Direction Register B
LOOP:
sbi PortB, 5 ; switch off the LED
rcall delay_05 ; wait for half a second
cbi PortB, 5 ; switch it on
rcall delay_05 ; wait for half a secon
rjmp LOOP ; jump to loop
DELAY_05: ; the subroutine:
ldi r16, 31 ; load r16 with 31
OUTER_LOOP: ; outer loop label
ldi r24, low(1021) ; load registers r24:r25 with 1021, our new ; init value
ldi r25, high(1021) ; the loop label
DELAY_LOOP: ; "add immediate to word": r24:r25 are ; incremented
adiw r24, 1 ; if no overflow ("branch if not equal"), go ; back to "delay_loop"
brne DELAY_LOOP
dec r16 ; decrement r16
brne OUTER_LOOP ; and loop if outer loop not finished
ret ; return from subroutine
BLINK by ASM

## Slide 40: FIBONNACCI FILE
1 - Exemple : Fichier Fibonnacci
//FIBONACCI
//La suite des nombres de Fibonacci est la seule suite ayant les deux propriétés:
//Un+1 = Un + Un-1 et lim Un+1/Un = constante
//Le rapport entre deux nombres de Fibonacci consécutifs tend vers le nombre d’or. //lim Un+1/Un = Phi = (1+sqt(5)/2) = 1.618034
int x, y , z;
void setup() {
// put your setup code here, to run once:
x=0;
y=1;
Serial.begin(9600);//Affiche la suite des nombres
}
void loop() {
while (x<255) {
Serial.println(x);//Affiche la suite des nombres
z=y+x;
x=y;
y=z;
}
x=0; //Réinitilisation
}
2 – Version assemblée :
Récupérer le fichier .hex dans le répertoire de travail Arduino: C:\Users\Admin\AppData\Local\Temp\arduino_build_669485/Fibonacci.ino.hex"
Pour s’afficher ce lien, il faut activer les options de compilations dans les préférences : Afficher les résultats détaillés pendant la compilation
FIBONACCI by ASM

## Slide 41: HEX FILE
Fibonacci.ino.hex :
Offset(h) 00 01 02 03 04 05 06 07 08 09 0A 0B 0C 0D 0E 0F
00000000 3A 31 30 30 30 30 30 30 30 30 43 39 34 33 35 30 :100000000C94350
00000010 30 30 43 39 34 35 44 30 30 30 43 39 34 35 44 30 00C945D000C945D0
00000020 30 30 43 39 34 35 44 30 30 32 34 0D 0A 3A 31 30 00C945D0024..:10
00000030 30 30 31 30 30 30 30 43 39 34 35 44 30 30 30 43 0010000C945D000C
00000040 39 34 35 44 30 30 30 43 39 34 35 44 30 30 30 43 945D000C945D000C
00000050 39 34 35 44 30 30 45 43 0D 0A 3A 31 30 30 30 32 945D00EC..:10002
00000060 30 30 30 30 43 39 34 35 44 30 30 30 43 39 34 35 0000C945D000C945
00000070 44 30 30 30 43 39 34 35 44 30 30 30 43 39 34 35 D000C945D000C945
…

## Slide 42: DISASSEMBLED FILE
Résultat :
0000: 0C-94-35-00 jmp 0x6a ; Jump
0004: 0C-94-5D-00 jmp 0xba ; Jump
0008: 0C-94-5D-00 jmp 0xba ; Jump
000C: 0C-94-5D-00 jmp 0xba ; Jump
0010: 0C-94-5D-00 jmp 0xba ; Jump
0014: 0C-94-5D-00 jmp 0xba ; Jump
0018: 0C-94-5D-00 jmp 0xba ; Jump
001C: 0C-94-5D-00 jmp 0xba ; Jump
0020: 0C-94-5D-00 jmp 0xba ; Jump
0024: 0C-94-5D-00 jmp 0xba ; Jump
0028: 0C-94-5D-00 jmp 0xba ; Jump
002C: 0C-94-5D-00 jmp 0xba ; Jump
0030: 0C-94-5D-00 jmp 0xba ; Jump
0034: 0C-94-5D-00 jmp 0xba ; Jump
0038: 0C-94-5D-00 jmp 0xba ; Jump
003C: 0C-94-5D-00 jmp 0xba ; Jump
0040: 0C-94-BC-01 jmp 0x378 ; Jump
0044: 0C-94-5D-00 jmp 0xba ; Jump
0048: 0C-94-2C-02 jmp 0x458 ; Jump
004C: 0C-94-06-02 jmp 0x40c ; Jump
0050: 0C-94-5D-00 jmp 0xba ; Jump
0054: 0C-94-5D-00 jmp 0xba ; Jump
0058: 0C-94-5D-00 jmp 0xba ; Jump
005C: 0C-94-5D-00 jmp 0xba ; Jump
0060: 0C-94-5D-00 jmp 0xba ; Jump
0064: 0C-94-5D-00 jmp 0xba ; Jump
0068: 2E-03 fmul r18, r22 ; Fractional Multiply Unsigned
006A: 11-24 clr r17 ; Clear Register
006C: 1F-BE out 0x3f, r1 ; Store Register to I/O Location
006E: CF-EF ldi r28, 0xff ; Load Immediate
0070: D8-E0 ldi r29, 0x08 ; Load Immediate
0072: DE-BF out 0x3e, r29 ; Store Register to I/O Location
0074: CD-BF out 0x3d, r28 ; Store Register to I/O Location
0076: 11-E0 ldi r17, 0x01 ; Load Immediate
0078: A0-E0 ldi r26, 0x00 ; Load Immediate
007A: B1-E0 ldi r27, 0x01 ; Load Immediate
007C: E4-E1 ldi r30, 0x14 ; Load Immediate
007E: F7-E0 ldi r31, 0x07 ; Load Immediate
0080: 02-C0 rjmp .+4 ; Relative Jump
0082: 05-90 lpm r0, Z+ ; Load Program Memory
0084: 0D-92 st X+, r0 ; Store Indirect From Register to Data Space
0086: A6-31 cpi r26, 0x16 ; Compare with Immediate
0088: B1-07 cpc r27, r17 ; Compare with Carry
008A: D9-F7 brbc 1, .-10 ; Branch if Bit in SREG is Cleared
008C: 21-E0 ldi r18, 0x01 ; Load Immediate
008E: A6-E1 ldi r26, 0x16 ; Load Immediate
…
2 - Utilisation AVRDissassembler : https://github.com/christophediericx/AVRDisassembler
Télécharger la version x64 Windows
Dans l’invité de commande CMD de windows :
Exemple : AVRDisassembler.exe -i Fibonacci.ino.hex
D:\Mes_Documents\Mes_Fichiers\Logiciels_Microsoft\Word\INSA\MOSH\Ajouts_2018\AVRDisassembler-0.2.0-Windows-x64\AVRDisassembler-0.2.0-Windows-x64>AVRDisassembler.exe -i Fibonacci.ino.hex

## Slide 43: REFERENCES
https://gist.github.com/mhitza/8a4608f4dfdec20d3879
https://onlinedisassembler.com/static/home/
https://www.instructables.com/id/Command-Line-Assembly-Language-Programming-for-Ard-1/
https://www.instructables.com/id/Command-Line-Assembly-Language-Programming-for-Ard/
https://www.instructables.com/id/Command-Line-Assembly-Language-Programming-for-Ard-2/
https://www.instructables.com/id/Command-Line-Assembly-Language-Programming-for-Ard-3/
https://www.instructables.com/id/Command-Line-Assembly-Language-Programming-for-Ard-4/
https://medium.com/jungletronics/meeting-assembly-hello-world-arduino-blinking-code-330386652309

## Slide 44: DEBUGGING WITH THE HELP OF THE SERIAL PORT (VIA USB)
Once your program has been downloaded in Arduino, the program operates independently.
Everyone is happy if it works as expected... However, if this is not the case, start to understand what is happening.
Must be creative and develop assumptions... and I must admit that it is a tedious task because the board has no debugger or debugging message display!
Yet there is the serial port... so it is possible to send messages (message from debugging) since Arduino and reading them on the PC.
Arduino serial port and USB Port :
it is possible to communicate via the serial port of Arduino (what the microcontroller believes) but actually, all messages are returned via the USB (cf. FTDI) device to the PC (and its USB port).
Just listen to the USB port.
Caution: pins 0 and 1 for communication book series:
during a serial, the Pin0 connection and 1 are automatically re-configured (pin0) RX & TX (pin1).
=> it becomes impossible to use pins 0 & 1 for other purposes.
Note: it is also this same connection USB is also used to power the board.

## Slide 45: DISPLAYS TEXT ON THE SERIAL PORT => DEBUGGING
Caution: turn the monitor send a Reset signal to the microcontroller, which has the effect of restarting your program.
#define DEBUG
#ifdef DEBUG
unsigned int mavar =255;
#endif
void setup() {
#ifdef DEBUG
Serial.begin(9600); //Serial port init
#endif
}
void loop() {
#ifdef DEBUG
int droite=digitalRead(CNY_D);
Serial.print(« G:"); Serial.print(gauche);
Serial.print(", BP:");
Serial.println(digitalRead(BP));
#endif
} // fin de loop
COMMENT OR UNCOMMENT
THE PRE-PROCESSOR DIRECTIVES 

## Slide 46
TP1B

## Slide 47: MY SECOND PROGRAM: BLINKING LED WITHOUT DELAY
<= BACK
Beaucoup plus efficace que la fonction DELAY, non ?

## Slide 48
TP1C

## Slide 49: AFFICHE DU TEXTE SUR LE PORT SERIE => DEBUGGAGE
/* Blink
*Turns on an LED on for one second, then off for one second, repeatedly.
*The circuit: LED connected from digital pin 13 to ground.
* Note: On most Arduino boards, there is already an LED on the board
* connected to pin 13, so you don’t need any extra components for this example.
+ Displays the status of the LEDs in Serial monitor
*Created 1 June 2005, By David Cuartielles
*http://arduino.cc/en/Tutorial/Blink
*/
int ledPin = 13; // LED connected to digital pin 13
// The setup() method runs once, when the sketch starts
void setup() {
// opens serial port, sets data rate to 9600 bps
Serial.begin(9600);
// initialize the digital pin as an output:
pinMode(ledPin, OUTPUT);
}
// the loop() method runs over and over again, as long as the Arduino has power
void loop()
{
digitalWrite(ledPin, HIGH); // set the LED on
Serial.print("LED Status: ON\n");
delay(1000); // wait for a second
digitalWrite(ledPin, LOW); // set the LED off
Serial.print("LED Status: OFF\n");
delay(1000); // wait for a second
}
<= BACK

## Slide 50: COMMANDER L’ARDUINO PAR LE PORT SERIE: EXEMPLE
/* * Script montrant l'usage de la communication série
* pour débugger du code */
int pinBouton = 2;
int etatBouton;
int lecture1, lecture2;
void setup(){
pinMode( pinBouton, INPUT ); // Bouton d'entrée
etatBouton = digitalRead( pinBouton );
Serial.begin(9600); // Démarrage de la communication série
Serial.print("Démarrage du programme,\n");
Serial.print("Presser le bouton.\n");
}
void loop(){
// --- Lecture du bouton avec déparasitage logiciel ---
// Si pas de parasite, lecture1 égal lecture2
lecture1 = digitalRead( pinBouton ); // première lecture du bouton
delay( 10 ); // attendre 10 milli-secondes
lecture2 = digitalRead( pinBouton ); // deuxième lecture du bouton
// changement d'état ?
if( (lecture1==lecture2) && (lecture1 != etatBouton) )
changeEtatBouton( lecture1 ); }
void changeEtatBouton( int nouvelEtat ){
if( nouvelEtat == LOW ) {
Serial.print( "Bouton relache!\n" ); }
else {
Serial.print( "Bouton enfonce\n" ); }
etatBouton = nouvelEtat;
}
Exercice:
Faite un montage rudimentaire où on essaye de détecter la pression sur le bouton (Pin 2).
Un message de Debug est envoyé via le port série lorsque l'utilisateur enfonce ou relâche le bouton.
Matériel du kit:
Bouton poussoir
Résistances
=> Pont diviseur
http://arduino103.blogspot.com/2011/05/debugger-laide-du-port-serie-via-usb.html
<= BACK

## Slide 51: SEND CHARACTERS TO THE SERIAL PORT => DEBUGGING
int incomingByte = 0; // for incoming serial data
void setup() {
Serial.begin(9600);// opens serial port, sets data rate to 9600 bps
}
void loop() {
// send data only when you receive data:
if (Serial.available() > 0) {
// read the incoming byte:
incomingByte = Serial.read();
// say what you got:
Serial.print("I received: ");
Serial.println(incomingByte, DEC);
}
}
http://www.arduino.cc/en/Serial/Available
Get the number of bytes (characters) available to be read from the serial port. This is data that are already arrived and stored in the buffer of reception series (which holds 128 bytes).

## Slide 52: SERIAL TRACER – (IDE version > 1.6.6)
The series plotter displays a fixed number of data. It is important to set your delay() in the loop.

## Slide 53: I - LES MICROCONTROLEURS
TP1D

## Slide 54: MANAGING THE ARDUINO FROM THE SERIAL PORT: EXAMPLE
/* Blink
*Turns on an LED on for one second, then off for one second, repeatedly.
*The circuit: LED connected from digital pin 13 to ground.
*Created 1 June 2005, By David Cuartielles
*http://arduino.cc/en/Tutorial/Blink
*/
int ledPin = 13; // LED connected to digital pin 13
int incomingByte = 0; //serial char
// The setup() method runs once, when the sketch starts
void setup() {
// opens serial port, sets data rate to 9600 bps
Serial.begin(9600);
// initialize the digital pin as an output:
pinMode(ledPin, OUTPUT);
digitalWrite(ledPin, LOW);
}
// the loop() method runs over and over again, as long as the Arduino has power
void loop()
{
if (Serial.available() > 0) {
// read the incoming byte:
incomingByte = Serial.read();
if (incomingByte == 'y‘) {
digitalWrite(ledPin, HIGH); // set the LED ON
}
else if (incomingByte == 'n') {
digitalWrite(ledPin, LOW); // set the LED off
}
}
delay(250); // wait for a second
}
Exercise: Pick up the Assembly of the first program and provoke the ignition or the extinction of the LED by sending the character ‘y’ and ‘n’ respectively.
<= BACK

## Slide 55: AND IF THE SERIAL PORT IS OCCUPIED BY A DEVICE ?
How to debug? => "Software" series library : SoftwareSerial
For example: GPS module
Pin 0 module & Pin1 occupied for serial communication
the Pin 2 & Pin3 (for example) is defined to display the data
from the GPS on the Serial Monitor module
Of course, the display on the Serial monitor must go slower than the acquisition of data from the module!

## Slide 56
BLUETOOH MODULE

## Slide 57: MODULE Bluetooth HC-05
Qu’est ce que le bluetooth ? => Le bluetooth est un protocole de communication sans fil.
Né fin des années 1990, il n’a vraiment percé que dans les années 2000, et nous en sommes à la version 4.1 depuis la fin 2013.
À l’origine, la société Ericsson cherchait à développer un moyen d’utiliser une voie série sans passer par un fil. Petit à petit, ses utilisations se sont étendues pour atteindre ce que l’on connait aujourd’hui, un moyen de connecter sans fil de nombreux appareils, allant :
- d’une Arduino et sa voie série
- à un ordinateur, ou
- un casque audio ou
- encore une manette de jeu sur une console de salon.
Ce protocole est un cousin du Wi-Fi, qui respectent tous deux une même spécification IEEE et utilisent la même gamme de fréquences : 2.4 GHz (tout comme les téléphones portables et le zigbee par exemple).
C’est une communication bidirectionnelle: 2 modules peuvent communiquer ensemble en même temps.
Le comportement utilisé est "maître/esclave".
Un esclave pourra parler avec un seul maître, MAIS un maître pourra dialoguer avec plusieurs esclaves.
Pour son utilisation, elle se passe en plusieurs étapes :
Le maître se met en mode "reconnaissable"
L’esclave trouve le maître et demande à s’y connecter
Le maître accepte la connexion
Les périphériques sont alors appairés (ou associés)
=> La communication peut commencer
Ensuite, selon le type de composant que vous utilisez (une oreillette bluetooth, une manette de jeu-vidéo etc) la communication pourra se faire selon un protocole ou un autre.
Dans notre cas cela consistera simplement en une liaison série.
Au final, une liaison série habituelle mais toute la partie "filaire" de la communication sera englobée dans des trames bluetooth gérées par le module.

## Slide 58: MODULE Bluetooth HC-05
Il ne reste alors plus que les broches Key et Led. Led sert à connecter une LED de statut, vous pouvez la laisser déconnectée cela n’influencera pas le comportement du module.
Key sert à utiliser le mode "commande" du module.
Avec cette dernière vous pourrez reconfigurer la voie série (vitesse, parité etc…) et d’autres options liées au bluetooth (nom du module, mot de passe d’appairage, mode esclave/maître…).
Ce module communique via une liaison série avec une carte Arduino.
Cette liaison s’établit sur deux broches RX et TX définies dans notre programme en tant que broches 11 et 10.
La broche RX de la carte Arduino doit être raccordée à la broche TX du module Bluetooth HC-05.
La broche TX de la carte Arduino doit être raccordée à la broche RX du module HC-05.

## Slide 59: I - LES MICROCONTROLEURS
TP1E

## Slide 60: MODULE Bluetooth HC-05
Ce programme (à copier dans l’IDE Arduino) permet la réception et l’émission de données via le
moniteur série de l’IDE avec un autre périphérique Bluetooth (second Arduino, un PC ou comme dans
notre exemple avec un smartphone).
<= RETOUR

## Slide 61: Communication entre le Smartphone et le module HC-05 sur l’Arduino Uno
Il faudra ensuite installer sur le smartphone un programme comme Bluetooth Terminal HC-05 pour Android
et appairer le module HC-05.
Le code pin par défaut est : 1234 ou 0000 selon les constructeurs.
Il est maintenant possible de dialoguer entre le moniteur série du PC et le smartphone.
Testez:
1 – « test émission PC » depuis le moniteur série + Envoyer
2 – « test réception PC » depuis le smartphone + Send
La vitesse de transfert série doit être paramétrée sur 38400 bauds sinon une série de caractères illisibles apparaitra dans le moniteur.
<= RETOUR

## Slide 62: I - LES MICROCONTROLEURS
TP1F

## Slide 63: WIRE A BUZZER (PIEZO SPEAKER)
The buzzer cable on a digital output.
We then send it a periodic signal which is varying the frequency according to the note you wish to play:
example: A note is a signal of frequency f 440Hz

## Slide 64: WIRE A BUZZER (PIEZO SPEAKER) - PROGRAM
/* Melody (copyleft) 2005 D. Cuartielles for K3 * This example uses a piezo speaker to play melodies. It sends a square wave of the appropriate frequency to the piezo, generating * the corresponding tone. The calculation of the tones is made following the mathematical operation: timeHigh = period / 2 = 1 / (2 * toneFrequency) * where the different tones are described as in the table: * note frequency period timeHigh * c 261 Hz 3830 1915 * d 294 Hz 3400 1700 * e 329 Hz 3038 1519 * f 349 Hz 2864 1432 * g 392 Hz 2550 1275 * a 440 Hz 2272 1136 * b 493 Hz 2028 1014 * C 523 Hz 1912 956 * http://www.arduino.cc/en/Tutorial/Melody */ int speakerPin = 9;
int length = 15; // the number of notes char notes[] = “ccggaagffeeddc “; // a space represents a rest int beats[] = { 1, 1, 1, 1, 1, 1, 2, 1, 1, 1, 1, 1, 1, 2, 4 }; int tempo = 300;
void setup() { pinMode(speakerPin, OUTPUT); }
void loop() { for (int i = 0; i < length; i++) { if (notes[i] == ' ') { delay(beats[i] * tempo); // rest } else { playNote(notes[i], beats[i] * tempo); } delay(tempo / 2); // pause between notes } }
void playTone(int tone, int duration) { for (long i = 0; i < duration * 1000L; i += tone * 2) { digitalWrite(speakerPin, HIGH); delayMicroseconds(tone); digitalWrite(speakerPin, LOW); delayMicroseconds(tone); } }
void playNote(char note, int duration) { char names[] = { 'c', 'd', 'e', 'f', 'g', 'a', 'b', 'C' }; int tones[] = { 1915, 1700, 1519, 1432, 1275, 1136, 1014, 956 }; // play the tone corresponding to the note name for (int i = 0; i < 8; i++) { if (names[i] == note) { playTone(tones[i], duration); } } }
http://www.oomlout.com/a/products/ardx/circ-06
<= RETOUR

## Slide 65: III – 2 ANALOG INPUTS
III – 2 ANALOG INPUTS

## Slide 66: ANALOG INPUTS
Unlike the digital signal that can take only two different States, an analog signal can take an infinite number of values, such as a voltage that is vary progressively from 0V to 5V.
The Arduino works in digital, microcontroller includes only the '0' and '1 '.
Analog inputs A0 to A5 are therefore equipped with analog-to-digital converters that convert a tension in a suite of '0' and '1' card did match a number of 0 to 1023 (encoding 10-bit)
You can retrieve the information from a sensor.
AnalogRead(pin) => 10 bits => 1024 values
Conversion lasts 110µs (AT328), a flag says when it is completed
The accuracy depends on the wiring, which is difficult to guarantee the last 2 bits!
Valeur_lue = analogRead(AN0);

## Slide 67: RAPPEL SUCCESSIVE APPROXIMATION ADC

## Slide 68: SUCCESSIVE APPROXIMATION ADC - CIRCUIT
Example with a 4bit ADC:
B3 B2 B1 B0
VDAC =
We put the MSB to 0 (B3=1) (in the middle of VREF-VGND)
and the performs successive approximation by using a comparator.

## Slide 69: SUCCESSIVE APPROXIMATION ADC – USE CASE
8V
12V
10V
11V
11V
We put the first 1 => 1000
and Vin=11.2 > VDAC= 8V
=> we keep the first 1 and then put the 2nd one !
=> 1000 => 1100 = 12V
2. Vin=11.2 < VDAC= 12V
we remove the 2nd one !
and put the third one !
=> 1100 => 1010 = 10V
3. Vin=11.2 > VDAC= 10V => we keep the third 1 and put the 4th
=> 1010 => 1011 = 11V
4. Vin=11.2 > VDAC= 11V
1011 holds at 1011
Cause resolution = 16V/24 = 1V
And Vin is in between 12V and 11V
https://www.youtube.com/watch?v=h0CGtr4SC9s

## Slide 70: R-2R LADDER DAC

## Slide 71: I - LES MICROCONTROLEURS
TP1G

## Slide 72: TEMPERATURE SENSOR
The TMP36 is a sensor that is in the form of a small transistor.
Once powered (between 3 and 5V), he released an analog voltage directly proportional to the T.
The main advantages of the TMP36 are:
1 - broad range of temperatures (from-40 to + 150 ° C).
2 - The output voltage is completely independent of the power of the TMP36.
The TMP36 feature:
Size: box TO-92 3-pin (similar to a transistor)
Output voltage: 0.1V (-40 ° C) to 2.0V (150 ° C) but accuracy decreases after 125 ° C
Scale factor: 10mV/° C
Supply voltage: 2.7V to 5.5V
Load current: 0.05 mA
Convert the analog voltage level:
Attention, the TMP36 allows to measure negative temperatures!
0°C is placed at an offset of 500 mV.
If Vout < 500 mV => negative temperature.
T (°C) = (Vout (mV) - 500) / scale factor =>
T (° C) = (Vout (mV) - 500) / 10
Example: If Vout = 1 Volts, T (° C) = (1000 - 500) / 10 = 50 ° C
Equivalent to the TMP36: LM35/TMP35 (measure in °C) or LM34/TMP34 (measure in ° F). Attention to the conversion formulae: the LM35 doesn't have the 500mV to offset

## Slide 73: CAPTURE OF THE TEMPERATURE: PROGRAM
http://www.oomlout.com/a/products/ardx/circ-10
/* ——————————————————— * | Arduino Experimentation Kit Example Code | * | CIRC-10 .: Temperature :. (TMP36 Temperature Sensor) | * A simple program to output the current temperature to the IDE’s
debug window
* For more details on this circuit: http://tinyurl.com/c89tvd */
int temperaturePin = 0; //the analog pin the TMP36′s Vout (sense) pin is
connected to
void setup() { Serial.begin(9600); //Start the serial connection with the computer to view
the result open the serial monitor }
void loop() { float temperature = getVoltage(temperaturePin); //getting the voltage reading from the temperature sensor temperature = (temperature – 0.5) * 100; //converting from 10mV/°C with 500 mV //offset to degrees ((voltage – 500mV)*100) Serial.println(temperature); //printing the result delay(1000); //waiting a second }
/* getVoltage() – returns the voltage on the analog input defined by pin */ float getVoltage(int pin){ return (analogRead(pin) * .004882814);
//converting from a 0 to 1023 digital range // to 0 to 5 volts (each 1 reading equals ~ 5 mV) }
<= RETOUR
QUESTION: avec ce programme, le moniteur série affiche les valeurs de températures avec 2 digit après la virgule, EST-CE PERTINENT ?

## Slide 74: CONSIDERATION OF ACCURACY: TEMPERATURE SENSOR
The analog input takes a value between 0 and 1023 for a voltage between 0 and 5V.
Measurement accuracy: 5/210=5/1024=0.0048V (~4.8 mV). => precision of the analog input: about +/-0.5 ° C (e.g. for the TMP36: 4.8(mV)/10(mV/°C)).
How to increase the precision of the analog input?
By the analogReference (type) function that configures the voltage used for analog input:
DEFAULT: default reference = 5V or 3.3V
INTERNAL analog: an internal reference 1.1V for ATmega168, ATmega328
EXTERNAL: the voltage used by the AREF pin (0 to 5V).
EXTERNAL reference :
Supply 3.3V (from the Arduino) and using this voltage as reference (AREF pin) for analog readings, it improves the accuracy of reading: indeed, the analog input will evolve from 0 to 1023 for a voltage between 0 and ARef (3.3V).
=> measurement accuracy: 3.3/210=3/1024~3.2mV) => error is here reduced to +/-0.33 ° C.
INTERNAL reference :
By feeding into 1.1V, it improves the accuracy of reading:
indeed, the analog input will evolve from 0 to 1023 for a voltage between 0 and ARef (1.1V).
measurement accuracy: 1.1/210=1.1/1024~1.1mV)
error is here reduced to +/-0.1 ° C.
In practice: either analogReference (EXTERNAL) or analogReference (INTERNAL) in setup().
Attention, do not forget to change the line of code calculating the conversion of analogRead in tension. The line of code goes from float voltage = V * 5.0; to float voltage = V * 3.3; or float voltage = V * 1.1

## Slide 75: VOLTAGE DIVIDER
The voltage divider is a simple electronic circuit that allows to divide an input voltage. For example, the circuit consists of two resistances in series:
A U voltage input on these two resistances and the U2 output voltage is measured at the terminals of R2.
Application: reading higher voltages if you want to read V > 5 volts (e.g. 0 to 24 volts), then you must use this voltage divider.
<= BACK
Example with a divider for Umax = 24V :
U2max is fixed at 5V because of the Arduino, arbitrarily set R2 = 1kΩ, the necessary value for R1: => R1 = ((U/U2) * R2)-R2 = ((24/5) * 1000)-1000 = 3.8 kΩ thus, when the voltage U is 24 V (maximum), the maximum voltage on the analog input (U2) is 5V.
DECODING of analog playback (reminder: 10bits resolution):
What is the voltage at the entrance of the bridge, if analogRead() returns 436?
Method 1: the rule of three: analogRead() gives a value between 0 and 1023 (or 1024 values as possible) for a voltage between 0 and 24V => (24V/210) * 436 = 10.22 V
Méthod 2: use the above formula : each analogRead() interval gives 5/210=4.88mV =>
U2 = 436 * 4.88x10-3 = 2.12V => U = U2 * (R1 + R2) / R2 = 2.12 * (3800 + 1000) / 1000 = 10.22 V
Note: using a voltage divider, lost also precision in measurement since each interval represents a variation of voltage 24V U / 210 = 23.4 mV instead of 4.88mV.

## Slide 76: III – 2 ANALOG INPUTS
III – 2 ANALOG INPUTS:
APPLICATIONS

## Slide 77: TOUCH PAD DS
Small screens touch resistive 4-wire are now very cheap (< €10), because products in huge quantities for mobile phones, PDAs and video games (Nintendo DS)
Use bigger screens is also possible for less than € 150, because the popularity of netbooks with screens of 7 "and 10" did decrease their price. "
Although they are supplied with an electronic control unit and a USB interface, these screens are mainly in 4-wire resistive-online one Arduino can drive a tactile screen of 10 "(and more)
Note, however, that this "touch screen“ is actually the glass transparent that fits on the front of an LCD display for example.
They are very good at creating control panels customized with the "buttons" printed on a sheet behind the touch screen. The Arduino capturing the coordinates (X, Y) and comparing them with the coordinates of the button pressed. Of course, your control panel might represent something, not only the buttons.
You could have a top slider to select the volume or temperature level by touching somewhere along a scale, or it could be a plan of a House so that you can control the lights in different rooms by touching the correct part of the ground plane...
In what follows, we will implement a touch screen of the Nintendo DS on a sheet of paper to trigger actions.

## Slide 78: TOUCH PAD DS: HOW DOES IT WORKS
How a touch screen works (courtesy of Mercury from Wikimedia Commons).
1: Rigid layer.
2: Metal oxide layer.
3: Insulating dots.
4: Flexible layer with metal oxide film.

## Slide 79: TOUCH PAD DS: HOW DOES IT WORKS

## Slide 80: I - LES MICROCONTROLEURS
TP2A

## Slide 81: TOUCH PAD DS TEST
// Project 33 – TOUCH SCREEN
// Power connections
#define Left 8 // Left (X1) to digital pin 8
#define Bottom 9 // Bottom (Y2) to digital pin 9
#define Right 10 // Right (X2) to digital pin 10
#define Top 11 // Top (Y1) to digital pin 11
// Analog connections
#define topInput 0 // Top (Y1) to analog pin 0
#define rightInput 1 // Right (X2) to analog pin 1
int coordX = 0, coordY = 0;
void setup() {
Serial.begin(38400);
}
void loop() {
if (touch()) // If screen touched, print co-ordinates
{
Serial.print(coordX);
Serial.print(" ");
Serial.println(coordY);
delay(250);
}
}//fin du void
boolean touch() // return TRUE if touched, and set coordinates to touchX and touchY
{
boolean touch = false;
// get horizontal co-ordinates
pinMode(Left, OUTPUT);
digitalWrite(Left, LOW); // Set Left to Gnd
pinMode(Right, OUTPUT); // Set right to +5v
digitalWrite(Right, HIGH);
pinMode(Top, INPUT); // Top and Bottom to high impedance
pinMode(Bottom, INPUT);
delay(3);
coordX = analogRead(topInput);
// get vertical co-ordinates
pinMode(Bottom, OUTPUT); // set Bottom to Gnd
digitalWrite(Bottom, LOW);
pinMode(Top, OUTPUT); // set Top to +5v
digitalWrite(Top, HIGH);
pinMode(Right, INPUT); // left and right to high impedance
pinMode(Left, INPUT);
delay(3);
coordY = analogRead(rightInput);
// if co-ordinates read are less than 1000 and greater than 0 then the screen has been touched
if(coordX < 1000 && coordX > 0 && coordY < 1000 && coordY > 0) {touch = true;}
return touch;
}
Beginning Arduino Michael McRoberts APRESS
<= BACK

## Slide 82: ANOTHER EXAMPLE OF CODE FOR TOUCH PAD DS
/**
* Touch Control Panel
* Copyright 2009 Jonathan Oxer <jon@oxer.com.au>
* Copyright 2009 Hugh Blemings <hugh@blemings.org>
Reads touch coordinates on a Nintendo DS touch screen attached to an
Arduino and compares them to defined hot zones representing buttons and sliders.
If a touch occurs within a hot zone a matching event message is sent to the host via the serial port.
Based on the ReadTouchscreen example included in the TouchScreen library.
* www.practicalarduino.com/projects/touch-control-panel
*/
#include <TouchScreen.h>
TouchScreen ts(3, 1, 0, 2);
void setup()
{
Serial.begin(38400);
}
void loop()
{
int coords[2];
ts.read(coords);
Serial.print(coords[0]);
Serial.print(",");
Serial.print(coords[1]);
if((coords[0] > 696) && (coords[0] < 866) && (coords[1] > 546) && (coords[1] < 831)) { Serial.print(", Fan ON"); }
if((coords[0] > 696) && (coords[0] < 866) && (coords[1] > 208) && (coords[1] < 476)) { Serial.print(", Fan OFF"); }
if((coords[0] > 420) && (coords[0] < 577) && (coords[1] > 540) && (coords[1] < 866)) { Serial.print(", Drapes OPEN"); }
if((coords[0] > 420) && (coords[0] < 577) && (coords[1] > 208) && (coords[1] < 476)) { Serial.print(", Drapes CLOSE"); }
if((coords[0] > 139) && (coords[0] < 327) && (coords[1] > 208) && (coords[1] < 866)) { Serial.print(", Illumination:");
Serial.print(constrain(map(coords[1], 318, 756, 0, 100), 0, 100));
Serial.print("%");
}
Serial.println();
delay (100);
}
https://github.com/practicalarduino/TouchControlPanel/blob/master/TouchControlPanel.pde
Librairie TouchScreen: https://github.com/practicalarduino/TouchScreen
http://www.sparkfun.com/tutorials/139

## Slide 83: TO GO FURTHER: ACCELERATING THE ANALOG READ()
Tiré de la datasheet ATMEGA328P: doc8271 d’ATMEL
Prescaler from ARDUINO library (wiring.c, line 276.) to have 10 resolution bits because 50kHz <(16MHz/128=125kHz) <200kHz
Extracted from the doc2559 d’ATMEL datasheet :
“The ADC accuracy also depends on the ADC clock.
The recommended maximum ADC clock frequency is limited by the internal DAC in the conversion circuitry.
By default, the successive approximation circuitry requires an input clock frequency between 50kHz and 200kHz to get maximum resolution (10bits) (a normal conversion takes 13 ADC clock cycles. The first conversion after the ADC is switched on (ADEN in ADCSRA is set) takes 25 ADC clock cycles in order to initialize the analog circuitry)
However, frequencies up to 1 MHz do not reduce the ADC resolution significantly.
Operating the ADC with frequencies greater than 1 MHz is not characterized.
For Arduino and f=16Mhz Clock: since the ADC clock needs to be between 50 kHz & 200 kHz for 10 bit accuracy, we can only use the 128 prescaler and can achieve a 125 kHz ADC clock.
If a lower resolution than 10 bits is possible, the input clock frequency to the ADC can be higher than 200kHz to get a higher sample rate.
f(MHz)/Horloge à 16MHz
8
4
2
1
0,5
0,25
0,125

## Slide 84: TO GO FURTHER: ACCELERATING THE ANALOG READ()
cbi : clear bit in I/O register
Put 0 to the designed bit
sbi : set bit in I/O register
Put 1 to the designed bit

## Slide 85: TO GO FURTHER: ACCELERATING THE ANALOG READ()
Conclusions: From 128 to 4 prescaler, we go from 121µs to 18µs by reading the analog function ANALOG READ(), either about 10 x faster, without losing "too" precision (it remains in the bars of the TMP36 errors), even if there is a slight offset! We can quietly go up at least until f = 1 MHz (16 prescaler)
Attention: avoid the prescaler 0 and 2 who give completely erroneous values and more who don't win in reading speed!
http://www.marulaberry.co.za/index.php/tutorials/code/arduino-adc/
Prescaler | Fréquence (MHz) - Horloge 16MHz | temps lecture (1000 appels ANALOGREAD) (ms) | temps lecture/appel (µs) | Température avec TMP36 sur analog read() | Echantillons par seconde (théorie: f/13 cycles) | Echantillons par seconde (experience: 1/temps lecture) | Rapport fréquence (théorique) | Rapport fréquence (expérimental)
0 |  | 19 | 19 | 449,22 | 0 | 52632 |  | 
2 | 8 | 18 | 18 | 449,22 | 615385 | 55556 |  | 0,95
4 | 4 | 18 | 18 | 24,12 | 307692 | 55556 | 2 | 1,00
8 | 2 | 20 | 20 | 23,42 | 153846 | 50000 | 2 | 1,11
16 | 1 | 28 | 28 | 23,2 | 76923 | 35714 | 2 | 1,40
32 | 0,5 | 41 | 41 | 23,05 | 38462 | 24390 | 2 | 1,46
64 | 0,25 | 69 | 69 | 22,97 | 19231 | 14493 | 2 | 1,68
128 | 0,125 | 121 | 121 | 22,88 | 9615 | 8264 | 2 | 1,75
Chart: PRESCALER
| 0 | 2 | 4 | 8 | 16 | 32 | 64 | 128
 | 12 | 13 | 13 | 12 | 18 | 29 | 56 | 112
We double the frequency, and we get substantially the double samples/s between two successive measurement
http://arduino.cc/forum/index.php/topic,6549.0.html
http://www.arduino.cc/en/Reference/PortManipulation
http://playground.arduino.cc/Code/BitMath
http://www.fiz-ix.com/2012/01/how-to-configure-arduino-timer-2-registers-to-drive-an-ultrasonic-transducer-with-a-square-wave/

## Slide 86: III - 3 DIGITAL & ANALOG APPLICATIONS
III - 3 DIGITAL & ANALOG APPLICATIONS

## Slide 87: LCD GENERALITIES
This standardization => a lot of µ-controller platform has a ready-made library for development.
It is also the case with Arduino with the LiquidCrystal library.
This makes it possible to control the display with a few lines of command.
An LCD display is a cheap display device.
It is easy to interface with Arduino, because they contain their own microcontroller (black pad on the back) which manages the display logic.
This µcontroller is the Hitachi 44780 HD standard on the majority of viewers.
The majority of the current displays (e.g., LCD 2 x 16) have two benefits:
1 - the display is able to use 4-bit or 8-bit data bus: the 4-bit version is advantageous because it allows to send data to the display in using only 4 pins instead of 8. It's as much pine recovered to control other devices
2 - order logic (and library) can just use only 2 pins instead of 3 (with R/W the mass order, if you do not wish to read the memory of the display (do NC make only display))
So the display is fully controllable with only 6 pins!

## Slide 88: HITACHI HD44780 (LCD-II) Block Diagram

## Slide 89: LCD GENERALITIES
Also data lines DB0-DB7 that one driver using 4 or 8 pins to digital, and that convey both the displayed information and commands sent to the display,
Three control lines are also necessary for its functioning :
1 - E or Enable valid display when the pin is high. It can then receive orders or characters to display via its rows of data, it is insensitive to their condition otherwise.
2 - R/W for Read/Write indicates if you want to write a data display (R/W to 0) or read its information (R/W to 1). When you want to save input/output, this line is frequently grounded blocking the display mode (main mode of use) writing
=> cannot read its State registers and his memory of characters.
3 - RS to Register Select indicates if the data lines carry information to display (RS at 1) or orders of management display (RS to 0). Various commands, like moving the slider from right to left or vice versa, with or without deletion of character, erasing the display... are sent on the lines of data to DB7 DB0 putting RS at 0

## Slide 90: LCD COMMAND
DIALOGUE with the display in the case of a writing:
1 - set to 0 for line R/W
2 - RS at the level desired depending on whether you want to send a character or an order
3 - positioning of the code of the character or command on DB0 to DB7 (8 bit mode) or DB4 to DB7 (mode 4 bits) :
4 - setting to 1 line E to send these information
5 - set to 0 on line E making it insensitive to the State of DB0 display to DB7
►Sending data/command in 4 bits mode
It separates the strong 4 bits and the low 4 bits.
The common steps are:
Hide 4 LSB bits
Send to LCD
Send ENABLE signal
Hide 4 MSB bits
Send to LCD
Send ENABLE signal
REM: 4-bit mode saves pins but is slower than the 8-bit because we need to send the data in 2 times

## Slide 91: LCD PINOUTS AND COMMAND
The pinout and specifications of the display are available in the respective datasheets, but in general, they are as follows (pins 1 and 16 are shown on the display).

## Slide 92: I - LES MICROCONTROLEURS
TP2B

## Slide 93: LCD: CODE EXAMPLE
// Inclusion de la librairie
#include <LiquidCrystal.h> // Dimension de l'afficheur
const int numRows = 2;
const int numCols = 16; // Initialisation de la librarie
// avec le nbre de pins d'interface
// 4 bit de données dans notre cas.
/* Le montage: Afficheur LCD
* LCD RS - pin 2
* LCD Enable - pin 3
* LCD D4 - pin 4
* LCD D5 - pin 5
* LCD D6 - pin 6
* LCD D7 - pin 7
* LCD R/W - GND
* LCD Vo contrast- potentiomètre 10K (entre GND et +5V)
*/
LiquidCrystal lcd(2,3,4,5,6,7);
void setup()
{
Serial.begin(9600); // Bouton changer thème
lcd.begin(numCols,numRows); //--- Message de bienvenue -
lcd.print( "demo LCD" ); // placer curseur sur ligne 2
lcd.setCursor(0,1); // col, row
lcd.print( "Hello!" ); // clignotement curseur plein
lcd.blink();
}
void loop()
{
}
<= BACK
potentiometer

## Slide 94: LCD: ANOTHER EXAMPLE OF CODE
// --- Programme Arduino --- par X. HINAULT - 01/2010
// --- Que fait ce programme ? ---
/* Affiche des messages texte sur l'afficheur LCD*/
// --- Fonctionnalités utilisées ---
// Utilise un afficheur LCD 4x20 en mode 4 bits
// --- Circuit à réaliser ---
// Connexion du LCD sur les broches de la carte Arduino
// Connecter broche RS du LCD sur la broche 2
// Connecter broche E du LCD sur la broche 3
// Connecter broche D4 du LCD sur la broche 4
// Connecter broche D5 du LCD sur la broche 5
// Connecter broche D6 du LCD sur la broche 6
// Connecter broche D7 du LCD sur la broche 7
//**************** Entête déclarative *******
// A ce niveau sont déclarées les librairies, les constantes, les variables...
// --- Inclusion des librairies utilisées ---
#include <LiquidCrystal.h> // Inclusion de la librairie pour afficheur LCD
// --- Déclaration des constantes ---
// --- constantes des broches ---
const int RS=2; //declaration constante de broche
const int E=3; //declaration constante de broche
const int D4=4; //declaration constante de broche
const int D5=5; //declaration constante de broche
const int D6=6; //declaration constante de broche
const int D7=7; //declaration constante de broche
// --- Déclaration des variables globales ---
// --- Initialisation des fonctionnalités utilisées ---
LiquidCrystal lcd(RS, E, D4, D5, D6, D7);// initialisation LCD en mode 4 bits
//**************** FONCTION SETUP = Code d'initialisation *****
// La fonction setup() est exécutée en premier et 1 seule fois, au démarrage du programme
void setup() { // debut de la fonction setup()
// --- ici instructions à exécuter au démarrage ---
lcd.begin(20,4); // Initialise le LCD avec 20 colonnes x 4 lignes
delay(10); // pause rapide pour laisser temps initialisation
// Test du LCD
lcd.print("LCD OK") ; // affiche la chaîne texte - message de test
delay(2000); // pause de 2 secondes
lcd.clear(); // // efface écran et met le curseur en haut à gauche
delay(10); // pour laisser temps effacer écran
} // fin de la fonction setup()
// ********************************************************************
//*************** FONCTION LOOP = Boucle sans fin = coeur du programme *************
// la fonction loop() s'exécute sans fin en boucle aussi longtemps que l'Arduino est sous tension
void loop(){ // debut de la fonction loop()
lcd.print("Arduino...") ; // affiche la chaîne texte - message de test
delay(2000); // pause de 2 secondes
lcd.setCursor(9, 1) ; // 10ème col - 2ème ligne - positionne le curseur à l'endroit voulu (colonne, ligne) (1ère=0 !)
lcd.print("...pour te") ; // affiche la chaîne texte - message de test
delay(2000); // pause de 2 secondes
lcd.setCursor(4, 2) ; // 5ème col - 3ème ligne - positionne le curseur à l'endroit voulu (colonne, ligne) (1ère=0 !)
lcd.print("...servir") ; // affiche la chaîne texte - message de test
delay(2000); // pause de 2 secondes
lcd.setCursor(12, 3) ; // 13ème col - 4ème ligne - positionne le curseur à l'endroit voulu (colonne, ligne) (1ère=0 !)
lcd.print("...amigo") ; // affiche la chaîne texte - message de test
delay(2000); // pause de 2 secondes
lcd.clear(); // // efface écran et met le curseur en haut à gauche
delay(10); // pour laisser temps effacer écran
// --- ici instructions à exécuter par le programme principal ---
} // fin de la fonction loop() - le programme recommence au début de la fonction loop sans fin
// ********************************************************************************
// --- Fin programme ---
// ----- memo LCD ---
// LiquidCrystal(rs, enable, d4, d5, d6, d7) ; // initialisation 4 bits
// lcd.begin(cols, rows); // initialisation nombre colonne/ligne
//
// lcd.clear(); // efface écran et met le curseur en haut à gauche
// lcd.home(); // repositionne le curseur en haut et à gauche SANS effacer écran
//
// lcd.setCursor(col, row) ; // positionne le curseur à l'endroit voulu (colonne, ligne) (1ère=0 !)
// lcd.print("texte") ; // affiche la chaîne texte
//
// lcd.cursor() ; // affiche la ligne de base du curseur
// lcd.noCursor() ; // cache le curseur
// lcd.blink() ; // fait clignoter le curseur
// lcd.noBlink() ;// stoppe le clignotement du curseur
// lcd.noDisplay() ; // éteint le LCD sans modifier affichage
// lcd.display() ; // rallume le LCD sans modif affichage
//
// lcd.scrollDisplayLeft(); // décale l'affichage d'une colonne vers la gauche
// lcd.scrollDisplayRight(); // décale l'affichage d'une colonne vers la droite
// lcd.autoscroll() ; // les nouveaux caractères poussent les caractères déjà affichés
// noAutoscroll(); // stoppe le mode autoscroll

## Slide 95: LCD + TEMPERATURE SENSOR TMP36
/* Mesure de la température à l'aide d'un TMP36 et Affichage sur LCD: MOP-AL162A-BBTW: LCD 2x16
Le montage: Afficheur LCD
* LCD RS - pin 2
* LCD Enable - pin 3
* LCD D4 - pin 4
* LCD D5 - pin 5
* LCD D6 - pin 6
* LCD D7 - pin 7
* LCD R/W - GND
* LCD Vo contrast- potentiomètre 10K (entre Gnd et +5V)
Senseur de température:
* TMP36 Analog Output - Pin A0 (analogique)
// include the library code:
#include <LiquidCrystal.h>
int tempSensorPin = 0; // Pin analogique pour lecture de la tension de sortie du TMP36 (Vout).
// Resolution: 10 mV / degree celsius avec une offset de 500 mv. // Definition du caractere °
// initialize the library with the numbers of the interface pins
byte degrees[8] = { B00000, B01000, B10100, B01000, B00000, B00000, B00000, B00000, };
LiquidCrystal lcd(2, 3, 4, 5, 6, 7);
void setup(){
lcd.begin(16, 2); // set up the LCD's number of columns and rows:
lcd.clear(); //efface l’écran
lcd.createChar( 0, degrees ); } // initialiser le caractère ° dans le LCD
int lastTemp = -100; // mémorise la dernière température affichée
void loop(){
float temp = lectureTemp(); // rafraichit le LCD que si la // température a varié sensiblement
if( abs(temp-lastTemp)<0.20 ) return; lastTemp = temp; // Afficher la valeur en évitant le // lcd.clear(), pour éviter l'effet de // scintillement.
lcd.setCursor(0,0);
lcd.print( temp );
lcd.write( 0 ); // affiche le signe degré
lcd.print( "c" ); // Efface les derniers caractères si // la température chute subitement
lcd.print( " " ); // ne pas rafraichir trop souvent
delay(800); }
//Description: // Lecture de la température sur la pin A0 // //Returns: // La température en degré Celcius. //
float lectureTemp(){ // Lecture de la valeur sur l'entrée analogique // Retourne une valeur entre 0->1024 pour 0->5v
int valeur = analogRead(tempSensorPin); // Converti la lecture en tension
float tension = valeur * 5.0; tension /= 1024.0; // Convertir la tension (mv) en temperature
float temperature = ((tension * 1000) - 500) / 10;
return temperature; }
Source: http://arduino103.blogspot.com/search/label/sensor
LCD character editor: http://icontexto.com/charactercreator/
<= BACK

## Slide 96: I - LES MICROCONTROLEURS
TP2C

## Slide 97: TOUCH SCREEN & LCD
// Project 34
#include <LiquidCrystal.h>
LiquidCrystal lcd(2, 3, 4, 5, 6, 7); // create an lcd object
//and assign the pins
// Power connections
#define Left 8 // Left (X1) to digital pin 8
#define Bottom 9 // Bottom (Y2) to digital pin 9
#define Right 10 // Right (X2) to digital pin 10
#define Top 11 // Top (Y1) to digital pin 11
// Analog connections
#define topInput 0 // Top (Y1) to analog pin 0
#define rightInput 1 // Right (X2) to analog pin 1
int coordX = 0, coordY = 0;
char buffer[16];
void setup()
{
lcd.begin(16, 2); // Set the display to 16 columns and 2 rows
lcd.clear();
}
void loop()
{
if (touch())
{
if ((coordX>110 && coordX<300) && (coordY>170 && coordY<360)) {lcd.print("3");}
if ((coordX>110 && coordX<300) && (coordY>410 && coordY<610)) {lcd.print("2");}
if ((coordX>110 && coordX<300) && (coordY>640 && coordY<860)) {lcd.print("1");}
if ((coordX>330 && coordX<470) && (coordY>170 && coordY<360)) {lcd.print("6");}
if ((coordX>330 && coordX<470) && (coordY>410 && coordY<610)) {lcd.print("5");}
if ((coordX>330 && coordX<470) && (coordY>640 && coordY<860)) {lcd.print("4");}
if ((coordX>490 && coordX<710) && (coordY>170 && coordY<360)) {lcd.print("9");}
if ((coordX>490 && coordX<710) && (coordY>410 && coordY<610)) {lcd.print("8");}
if ((coordX>490 && coordX<710) && (coordY>640 && coordY<860)) {lcd.print("7");}
if ((coordX>760 && coordX<940) && (coordY>170 && coordY<360)) {scrollLCD();}
if ((coordX>760 && coordX<940) && (coordY>410 && coordY<610)) {lcd.print("0");}
if ((coordX>760 && coordX<940) && (coordY>640 && coordY<860)) {lcd.clear();}
delay(250);
}
}
// return TRUE if touched, and set coordinates to touchX and touchY
boolean touch()
{
boolean touch = false;
// get horizontal co-ordinates
pinMode(Left, OUTPUT);
digitalWrite(Left, LOW); // Set Left to Gnd
pinMode(Right, OUTPUT); // Set right to +5v
digitalWrite(Right, HIGH);
pinMode(Top, INPUT); // Top and Bottom to high impedance
pinMode(Bottom, INPUT);
delay(3); // short delay
coordX = analogRead(topInput);
// get vertical co-ordinates
pinMode(Bottom, OUTPUT); // set Bottom to Gnd
digitalWrite(Bottom, LOW);
pinMode(Top, OUTPUT); // set Top to +5v
digitalWrite(Top, HIGH);
pinMode(Right, INPUT); // left and right to high impedance
pinMode(Left, INPUT);
delay(3); // short delay
coordY = analogRead(rightInput);
// if co-ordinates read are less than 1000 and greater than 0 then the screen has been touched
if(coordX < 1000 && coordX > 0 && coordY < 1000 && coordY > 0) {touch = true;}
return touch;
}
void scrollLCD() {
for (int scrollNum=0; scrollNum<16; scrollNum++) {
lcd.scrollDisplayLeft();
delay(100);
}
lcd.clear();
}
<= BACK

## Slide 98: III - 4 DO "ANALOG" WITH DIGITAL
III - 4 DO "ANALOG" WITH DIGITAL

## Slide 99: PULSE WIDTH MODULATION (PWM)
The Arduino lack of a DIGITAL/ANALOG converter in the strict sense of the term.
=> Impossible to have a DC voltage which is the image of a digital data on one of the connectors.
On the other hand, they are capable of generating signals with pulse width modulation (PWM in English: pulse width modulation) that fill the failings of the analog control.
But elegant solution because we're working transistors in commutation (blocked and saturated regime; cf course features A semiconductor 3 A IMACS) => its dissipation is theoretically zero, since either the I or the U are 0 alternately.
The limitations of the analog control: if we are to control the brightness of an LED or the speed of a DC motor, apply a voltage higher or lower (analog control) does imply a getting the desired results-online brightness low for a led is absolutely not guaranteed (because it is a diode (rectifier)). Similarly, the slower starting the engine not provided (because of the inertia).
Duty cycle:
duty cycle = the ratio between the duration of the phenomenon over a period and this same period ( = tone/T)
The frequency of the PWM signal is of about ~ 490 Hertz (be a duty cycle of +/-2 ms) and ~ 1 kHz according to PWM pins.
Even if the signal is not an analog voltage, it can become so if we apply a filter low pass (which keeps only the average of the signal; VMOY = VA * RCYC)
Duty cycle 100% => signal high. Duty cycle 0% => signal down
all intermediate values are of course permitted

## Slide 100: PULSE WIDTH MODULATION (PWM)
Activation mode PWM:
Attention, there is no special instruction to activate the PWM mode and do not initialize the pin as Output before using the analogWrite() statement.
Then we select a pin PWM (3, 5, 6, 9, 10, 11) instead of an analog pin.
BEWARE: Limit of 5 & 6 in PWM pins:
Attention: following a technical constraint (sharing the function millis and delays), PWM control on pins 5 and 6 is inconsistent for the values 0 to 10 analogWrite.
As a result, a value of 0 on pins 5 and 6 does not necessarily a LOW output!
Calculation Note:
the value passed to analogWrite() indicates what proportion of the "duty cycle" in which the output is activated (see chart).
As AnalogWrite value can vary from 0 to 255:
A duty cycle of 50% of the time will give: 50% of 255 or 255 * 0.5 = 127.5 (so the statement analogWrite 127).
Or more generally: a duty cycle x % will give a ((255) n 100/x)).
OR vice versa:
If one has a value analogWrite() = n,
the duty cycle will be (n/255)*100% of the period.
Refinement: low pass filter=> http://arduino-info.wikispaces.com/Analog-Output

## Slide 101: « TRUE » ANALOG OUTPUT!
With "the trick" PWM signals, we can get a quasi analog, but how if I want a completely analog signal from a digital signal?
Solution: put a RC filter at the output of the PWM
1 - if the PWM signal is 1, the capacitor takes over.
2 - If the PWM signal goes to 0, the capacitor discharges.
and so on... involving a variation of voltage at the terminals of the capacitor that is similar to this:
What's new compared to the square wave?
Nothing more, the average value of the blue signal is the same as the red signal.
It should be noted that in this case, the time of charge/discharge of the capacitor is chosen equal to a half of the signal
What will happen if we choose a smaller or larger load/discharge time? For example a largest RC:
The voltage at the terminals of the capacitor does not reach the + 5V and 0V as in the previous timeline. The couple RC being larger that previously, the capacitor takes longer to load and as the signal "go faster" capacitor, it cannot be load/unload completely.
What will happen if we continue to increase the constant RC?
This signal approaches in addition to the average value of the PWM signal.
Have we won the game?
80%

## Slide 102: « TRUE » ANALOG OUTPUT !
The more you increase the load with RC, more the capacitor will take some time to stabilize at the desired level:
If we want to create an analogue signal which varies fairly quickly-online problem.
Which can sometimes save you it is persistence of vision of the eye for an LED application or that an engine that has inertia!
What to do if you want to have a beautiful right?
Further increase the time constant RC?
And then, we can conversely reduce the RC because changing tier will be faster, but the CPU voltage will tend to follow the signal: is the first timeline that we saw earlier.
How to properly calibrate the constant RC? Find the right balance!
-If a signal that is the closest possible value average: constant great RC.
-If instead we want a signal that is the fastest and the average value is an approximation, then as the low time constant.
-If you want a fast signal and the closest possible value average, you can also change the frequency of the PWM
Yes but be careful, take precautions, because problems can occur:
=> issue of time of stabilization between two levels (different cyclical reports)

## Slide 103
TO GO FURTHER
Example of 'real' DIGITAL-to-ANALOG converter:

## Slide 104: CHANGE THE FREQUENCY PWM - 1
The PWM value is set to 8/16 bit when calling analogWrite(): analogWrite(myPWMpin, 128);
This value is then compared to the value of one of the registers, counters OCRnX (8 - bit or 16 - bit):
1 - when the meter is less than the value of PWM: the PIN output high.
2 - When the count is greater than the PWM value, the output pin low.
With the 8-bit timer, the example above generates a square signal because the pin is the same amount of time at the top (of 0 to 127) and then at the bottom (from 128 to 255) level.
With the timer 16 bit => it count of 216 = 65536
On the ATMega: There are three types of registers timer/counter: TCCR0B, TCCR1B and TCCR2B.
1 - Each timer has two Output Compare Register OCRnA & OCRnB-online 3timers*2 OCR = 6-channel PWM
2 - each timer has a prescaler used to generate a frequency = frequency of clock/prescaler
This prescaler is defined by 3bits stored in the 3 low bits of the register of timer/counter: CS02, CS01, CS00
With only three registers (defining the 3 different prescalers), six PWM pins can only be grouped into three pairs, each pair having its own prescaler and thus its own frequency:
Pin 5 and 6: TCCR0B (timer0/8bits), Pin 9 and 10: TCCR1B (timer1 /) 16 bit), Pin 3 and 11: TCCR2B (timer2 / 8bits)
By default on the Arduino Diecimila: Pins 5 and 6: 1 kHz and Pins 9, 10, 11 and 3: 500 Hz (prescaler 64)
=> the frequency of the PWM signal is determined by the value of the prescaler, clock speed, and the resolution of the timer (255 or 65536 for the timer 8-bit or 16-bit respectively).

## Slide 105: CHANGE THE PWM FREQUENCY– 2 – FAST VS PHASE CORRECT PWM
The following code fragment sets up fast PWM on pins 3 and 11 (Timer 2), using OCR2A as the top value for the timer.
The waveform generation mode bits WGM are set to to 111 for fast PWM with OCRA controlling the top limit.
The OCR2A top limit is arbitrarily set to 180, and the OCR2B compare register is arbitrarily set to 50. OCR2A's mode is set to "Toggle on Compare Match" by setting the COM2A bits to 01.
pinMode(3, OUTPUT);
pinMode(11, OUTPUT);
TCCR2A = _BV(COM2A0) | _BV(COM2B1) | _BV(WGM21) | _BV(WGM20);
TCCR2B = _BV(WGM22) | _BV(CS22); OCR2A = 180; OCR2B = 50;
On the Arduino Duemilanove, these values yield:
Output A frequency: 16 MHz / 64 / (180+1) / 2 = 690.6Hz
Output A duty cycle: 50%
Output B frequency: 16 MHz / 64 / (180+1) = 1381.2Hz
Output B duty cycle: (50+1) / (180+1) = 28.2%
The following code fragment sets up phase-correct PWM on pins 3 and 11 (Timer 2), using OCR2A as the top value for the timer.
The waveform generation mode bits WGM are set to to 101 for phase-correct PWM with OCRA controlling the top limit.
The OCR2A top limit is arbitrarily set to 180, and the OCR2B compare register is arbitrarily set to 50. OCR2A's mode is set to "Toggle on Compare Match" by setting the COM2A bits to 01.
pinMode(3, OUTPUT);
pinMode(11, OUTPUT);
TCCR2A = _BV(COM2A0) | _BV(COM2B1) | _BV(WGM20); TCCR2B = _BV(WGM22) | _BV(CS22);
OCR2A = 180; OCR2B = 50;
On the Arduino Duemilanove, these values yield:
Output A frequency: 16 MHz / 64 / 180 / 2 / 2 = 347.2Hz
Output A duty cycle: 50%
Output B frequency: 16 MHz / 64 / 180 / 2 = 694.4Hz
Output B duty cycle: 50 / 180 = 27.8%
FAST PWM :
PHASE CORRECT PWM :
http://www.righto.com/2009/07/secrets-of-arduino-pwm.html
There are two modes of operation for the PWM timers:
1 - Fast PWM and
2 - Phase-correct PWM.
These modes work almost in the same way, except that once arrived at the TOP, down to the BOTTOM for the correct Phase PWM, is applying the same method of comparison. Advantage: increase the resolution, at the expense of the maximum frequency, which is divided by two.

## Slide 106: CHANGE THE PWM FREQUENCY - 2
In the part setup () to your Arduino code:
1 - Select the mode (Fast PWM...) in the relevant TCCRnA registers
TCCRnA and B registers have different bits:
- Waveform Generation Mode bits – WGM
- Clock Select bits – CS
- Compare Match Output bits – COMnA & COMnB
http://www.marulaberry.co.za/index.php/tutorials/code/pulse-width-modulation/
The frequencies can be then defined as follows according to the Timer that is used:
8-bit
16-bit
2 - set or clear the bit CS22 CS21, CS20 TCCRnB records relevant to set the prescaler.

## Slide 107: CHANGE THE PWM FREQUENCY- 3
EXAMPLE: if you want to configure the pins 5 and 6 to generate a PWM signal to the highest frequency possible, i.e. 64kHz-online TCCR0B = xxxxx001 (0-8-bit timer)
CS02 | CS01 | CS00 | DESCRIPTION | Fréquence (pins 5 et 6 (OC0A and OC0B): TIMER0 (8BIT PWM) | Fréquence [(pins 9, 10, (OC1A, OC1B) TIMER1 (16BIT PWM)] ET [pins 3, 11 (OC2A, OC2B): TIMER2 (8BIT PWM)]
0 | 0 | 0 | Timer/Counter Disabled |  | 
0 | 0 | 1 | No Prescaling | 64kHz | 32kHz
0 | 1 | 0 | Clock / 8 | 8kHz | 4kHz
0 | 1 | 1 | Clock / 64 | 1kHz (défaut) | 500Hz (défaut)
1 | 0 | 0 | Clock / 256 | 250Hz | 125Hz
1 | 0 | 1 | Clock / 1024 | 62.5Hz | 31.25Hz
Example:
Clock frequency f=16MHz
Prescaler à 64
fOCnxPWM=16/(64*256)~1kHz
http://www.righto.com/2009/07/secrets-of-arduino-pwm.html
Beware, by default in wiring.c: Timer 0 is initialized to Fast PWM,
While Timer 1 and Timer 2 is initialized to Phase Correct PWM.

## Slide 108: CHANGE THE PWM FREQUENCY - 4
SECOND METHOD:
//First, clear prescaler bits
// do 1<<2 => « 00000001 » => « 00000100 »
// ~ « 00000100 » = « 11111011 »
// TCCR0B ET « 11111011 »
TCCR0B &= ~(1<<CS02);
//idem for CS01, // do 1<<1 => « 00000001 » => « 00000010 »
TCCR0B &= ~(1<<CS01); //put CS00 to good value
TCCR0B |= (1<<CS00); //OR with TCCR0B.
https://sites.google.com/site/qeewiki/books/avr-guide/timers-on-the-atmega328
FIRST METHOD:
//First, clear prescaler bits
int prescalerVal = 0x07; // => prescalerVal = binaire "00000111" TCCR0B &= ~prescalerVal; //registre TCCR0B = ET logique entre TCCR0B et reverse (tilde) de prescalerVal “1111000“ //Then, put good bits values to prescaler
int prescalerVal = 1; //put prescalerVal to binary "00000001" TCCR0B |= prescalerVal; // OR logic between previous value of TCCR0B "11111000“ and binary "00000001“
Result "11111001” => CS02, CS01 has been cleared and CS00 activated !
No prescaling => max frequency
http://www.atmel.com/Images/doc2505.pdf
http://www.avrfreaks.net/
http://www.marulaberry.co.za/index.php/tutorials/code/pulse-width-modulation/

## Slide 109: APPLICATION OF PWM: WIRE A DC MOTOR
The so-called led "free wheel" allows to evacuate the current create when the engine slowed down so that it is no longer powered.
The supply voltage of the motor can be different (of course)
A transistor is used to drive the motor.
It sends a signal that the duty cycle varies according to the desired speed.

## Slide 110: I - LES MICROCONTROLEURS
TP3-A

## Slide 111: APPLICATION DU PWM: CABLER UN MOTEUR A COURANT CONTINU
Control DC motor via transistor (PWM):
as we have seen, the analog speed control is not really appropriate because we indeed have to overcome the inertia at startup.
With the same mounting, it is possible to fine-tune the speed with the PWM control:
CIRCUIT :
/* Contrôle d'un moteur DC - en utilisant une sortie PWM.
* Attention, les pin PWM 5 et 6 ont une limitation. */
int pinMoteur = 9; // pin contrôlant le moteur (PWM pin)
void setup(){
//En PWM il ne faut pas assigner la pin en output
}
void loop(){
MoteurVitessePWM();
MoteurAccelerationPWM();
}
// Contrôle de la vitesse du moteur en contrôlant le % du cycle de service PWM
// sur la pin 9 (de 0 à 255 pour le % du cycle de service ).
//
void MoteurVitessePWM(){
int vitesse1 = int(255) / 3; // High 33% du cycle
int vitesse2 = int(255) / 2; // High 50% du cycle
int vitesse3 = 2 * 255 / 3;
int vitesse4 = (int)255; // High 100% du cycle
analogWrite( pinMoteur, vitesse1 ); delay( 1000 );
analogWrite( pinMoteur, vitesse2 ); delay( 1000 );
analogWrite( pinMoteur, vitesse3 ); delay( 1000 );
analogWrite( pinMoteur, vitesse4 ); delay( 1000 );
analogWrite( pinMoteur, vitesse3 ); delay( 1000 );
analogWrite( pinMoteur, vitesse2 ); delay( 1000 );
analogWrite( pinMoteur, vitesse1 ); delay( 1000 );
analogWrite( pinMoteur, LOW );
}
// Contrôle plus fin de l'accélération du moteur via PWM.
// NB: Selon la qualité du moteur, celui-ci peut avoir du mal à décoller
// lorsque le % du cycle de service est assez bas.
// Un option est d'envoyer une impulsion pour démarrer/décoller le moteur.
void MoteurAccelerationPWM(){
// Impulsion de démarrage (75%)
//analogWrite( pinMoteur, 191 );
//delay(50); // Acceleration
for( int i = 30; i<= 255; i++ ){
analogWrite( pinMoteur, i );
delay(50); // delay pour avoir un progression
}
// pause de 2 secondes a plein régime
delay( 2000 );
// Deceleration
for( int i = 255; i>=0; i-- ){
analogWrite( pinMoteur, i );
delay(50); // delay pour avoir un progression }
}
http://arduino103.blogspot.com/2011/05/controle-moteur-dc-via-transistor-pwm.html
<= BACK
10kOhms
to be adjusted !
Beware of transistor different pinout from manufacturer
=> Always check the datasheet
QUESTION: pourquoi doit-on mettre une diode de roue libre en parallèle du moteur ?

## Slide 112: I - LES MICROCONTROLEURS
TP3-B
PHOTO-RESISTANCE

## Slide 113: PHOTO-RESISTANCE e.g. KLS6-3537
Sensibilité en fonction du matériau utilisé
http://www.cnkls.com/admin/product_upload/20190322144057KLS6-3537..pdf
http://www.klsele.com/products/Resistors/404/3248.html

## Slide 114: PHOTO-RESISTANCE e.g. KLS6-3537

## Slide 115: PHOTO-RESISTANCE KLS6-3537

## Slide 116: APPLICATION OF PWM PINS: EXAMPLE WITH PHOTO-RESISTANCE
/* A simple program that will change the intensity of a LED based on the
* amount of light incident on the photo resistor. */
//PhotoResistor Pin int lightPin = 0; //the analog pin the photoresistor is connected to the //photoresistor is not calibrated to any units so this is simply a raw sensor value (relative light) int ledPin = 9; //the pin the LED is connected to
//we are controlling brightness so, we use one of the PWM (pulse
//width modulation pins) void setup() {
Serial.begin(9600); pinMode(ledPin, OUTPUT); //sets the led pin to output } void loop() { int lightLevel = analogRead(lightPin); //Read the lightlevel
Serial.print(lightLevel); //Affiche le lightlevel sur le moniteur série
//ajuster les valeurs en fonction du lightlevel: adjust 180 to 610 to span 0 to 255
lightLevel = map(lightLevel, 250, 700, 0, 255);
Serial.print(","); Serial.println(lightLevel);
delay(50);
lightLevel = constrain(lightLevel, 0, 255);//make sure the value is between 0 et 255
analogWrite(ledPin, lightLevel); //write the value }
http://www.oomlout.com/a/products/ardx/circ-09
If the man can control a potentiometer, how to make the environment that controls (e.g. light).
We will take a photo-resistance (its resistance is dependent on the light received). However the Arduino cannot directly measure resistance (it does detect a voltage) we have implemented a voltage divider.
The measurement is done on an analog input.
The strength of the photoresistor decreases when the light increases
<= RETOUR
pin 9

## Slide 117: I - LES MICROCONTROLEURS
TP3-B – EXTENDED
MACHINE A ETATS
<= RETOUR

## Slide 118: MACHINE A ETATS ET PHOTORESISTANCE
R

## Slide 119
MACHINE A ETATS ET PHOTORESISTANCE

## Slide 120
MACHINE A ETATS ET PHOTORESISTANCE
luminosité =< SEUIL_NUIT
Millis() – heureNuit >= DELAI_NUIT
heureNuit <- millis()
luminosité > SEUIL_NUIT
Allumer la lumière
luminosité >= SEUIL_JOUR
luminosité < SEUIL_JOUR
heureJour <- millis()
Millis() – heureJour >= DELAI_JOUR
Eteindre la lumière
Transition pour passer d’un état à l’autre
Action à réaliser au changement d’état

## Slide 121
MACHINE A ETATS ET PHOTORESISTANCE

## Slide 122
MACHINE A ETATS ET PHOTORESISTANCE
=> Il faut hiérarchiser les différents tests
(millis() – heureNuit >= DELAI_NUIT) & (luminosite =< SEUIL_NUIT)
heureNuit <- millis()
luminosité > SEUIL_NUIT
Allumer la lumière
Attention, il faut que les 2 transitions ne soient pas vrais en même temps !
a
b.

## Slide 123
MACHINE A ETATS ET PHOTORESISTANCE

## Slide 124: I - LES MICROCONTROLEURS
SERVO-MOTOR

## Slide 125: SERVO-MOTOR
A servo motor is a type of electric motor. It is a device used to control the direction of a remote controlled car model. On a servo-motor, the angle can vary from a fixed angle between 0 and 180 ° depending on the signal being sent.
A servo-motor includes:
A (continuous) electric motor, usually small enough.
Gear reducer output of the engine (for less speed and more torque or force).
A sensor type "potentiometer" connected to the output (resistance which varies depending on the angle, which allows to measure the angle of rotation on the output shaft).
A servo electronic control the position/rotation of the output shaft to hold it in the correct position.
To manage a servo-motor?
Just send a pulse whose duration will determine the angle of the servo-motor.
This pulse time is some ms should be repeated at regular intervals (every 10 ms to 20ms) to maintain the position. Standard values:
1ms = - 90 ° | 1.5 ms = 0 ° (centered position): 2 ms = + 90 °
The animated below graph shows the correspondence between the pulse length and angle of the servo-motor.

## Slide 126: SERVOMOTOR WIRING
A servo motor is connected with only 3 wires:
the mass, the + 5V and the command pulse.
The black wire is connected to the 0V or GND.
The Red wire is connected to the 5V.
The yellow wire or white is connected to an output Digital PWM
One sends a signal that we do vary according to the direction and the desired position.
Wiring the actuator on an output Digital PWM: D11, D3, D10, D9, D6, D5.
Rotation
Translation
Program or even impulse drive is still possible but it would be tedious,
Arduino owns the Servo.h library, which allows you to easily take control.
This sub-program "servo.h" must be included in the program, it is easy to order.

## Slide 127: I - LES MICROCONTROLEURS
TP3-C

## Slide 128: SERVO MOTOR
//File > Examples > Library-Servo > Sweep (example from the great arduino.cc site
//check it out for other ideas)
#include <Servo.h>
Servo myservo; // create servo object to control a servo // a maximum of eight servo objects can be created
int pos = 0; // variable to store the servo position
void setup() { myservo.attach(9); // attaches the servo on pin 9 to the servo object }
void loop() {
for(pos = 0; pos < 180; pos += 1) // goes from 0 degrees to 180 degrees { // in steps of 1 degree myservo.write(pos); // tell servo to go to position in variable 'pos' delay(15); // waits 15ms for the servo to reach the position }
for(pos = 180; pos>=1; pos-=1) // goes from 180 degrees to 0 degrees { myservo.write(pos); // tell servo to go to position in variable ‘pos’ delay(15); // waits 15ms for the servo to reach the position } }
http://www.oomlout.com/a/products/ardx/circ-04
Attach(): allows to define and attach a
Detach() servo connection: obviously the opposite
Write(): main function of the servo control, it allows to generate the pulse train, the setting is the angular position of 0 to 180 ° (not the width 90 ° pulse) is the resting position or median
Read(): allows to know the position of the servo by returning the value of the last call to the Write()
<= BACK

## Slide 129: I - LES MICROCONTROLEURS
FLEX SENSOR
TP3-D

## Slide 130: FLEX SENSOR
A flex sensor is basically a variable resistor that varies in resistance upon bending.
Since the resistance is directly proportional to the amount of bending,
it is often called a Flexible Potentiometer.
A flex sensor consists of a phenolic resin substrate with conductive ink deposited. A segmented conductor is placed on top to form a flexible potentiometer in which resistance changes upon deflection.
Directions to Use :
Flex sensors are designed to flex in only one direction – away from ink (as shown in the figure). Bending the sensor in another direction may damage it.
Cette photo par Auteur inconnu est soumise à la licence CC BY-SA

## Slide 131: FLEX SENSOR

## Slide 132: FLEX SENSOR
How Flex Sensor Works?
The conductive ink printed on the sensor acts as a resistor.
When the sensor is bent, conductive layer is stretched, resulting in reduced cross section (imagine stretching a rubber band). This reduced cross section results in an increased resistance.
Reading a Flex Sensor
The easiest way to read the flex sensor is to connect it with a fixed value resistor (usually 47kΩ) to create a voltage divider.
For example, with 5V supply and 47K pull-down resistor:
when the sensor is flat (0°):
When flexed all the way (90°):
At 90° angle, this resistance is about 100KΩ.
When the sensor is straight, this resistance is about 25k.

## Slide 133: FLEX SENSOR
Ressources:
https://www.instructables.com/How-to-use-a-Flex-Sensor-Arduino-Tutorial/
https://www.electronicshub.org/interfacing-flex-sensor-with-arduino/
https://lastminuteengineers.com/flex-sensor-arduino-tutorial/
https://www.redohm.fr/2019/12/capteur-de-flexion/#bidirectionnel
https://learn.sparkfun.com/tutorials/flex-sensor-hookup-guide/all
<= RETOUR

## Slide 134: I - LES MICROCONTROLEURS
FLEX SENSOR & SERVO MOTOR
TP3-E

## Slide 135: TEST BENCH: FLEX SENSOR + SERVO MOTOR
<= RETOUR

## Slide 136: III-5 DEBOUNCING
III-5 DEBOUNCING

## Slide 137: BUTTON DEBOUNCING
When you press/release button, there is often the appearance of parasites for a few ms.
This parasites appear only during the times where is pushed / release the push button.
If you count the number of pressures (to make a counter), these parasites just disrupt the proper functioning of the software.
The problem is hardware... and parasites are added pressures "ghosts" .
There are several ways to correct the problem:
-software (Software debouncing) => introduce a software delay in the program
- hardware (Hardware debouncing) => use an ability of deworming (Hardware deboucing) (and possibly a trigger) Inverter Schmidt (Jeremy Blum Tutorial)
See the article of IkaLogic.com explaining how to debounce circuits (way software and hardware) or article from LadyADA http://www.ladyada.net/learn/arduino/lesson5.html

## Slide 138: SOFTWARE DEBOUNCING
// constants won't change. They're used here to set pin numbers:
const int buttonPin = 2; // the number of the pushbutton pin
const int ledPin = 13; // the number of the LED pin
// Variables will change:
int ledState = HIGH; // the current state of the output pin
int buttonState; // the current reading from the input pin
int lastButtonState = LOW; // the previous reading from the input pin
int compteur_filtre; //compteur filtré
int compteur_non_filtre; //compteur non filtré
// the following variables are long's because the time, measured in miliseconds, will quickly become a bigger number than can be stored in an int.
long lastDebounceTime = 0; // the last time the output pin was toggled
long debounceDelay = 50; // the debounce time; increase if the output flickers
void setup() {
Serial.begin (9600);
pinMode(buttonPin, INPUT);
pinMode(ledPin, OUTPUT);
}
void loop() {
// read the state of the switch into a local variable:
int reading = digitalRead(buttonPin);
// check to see if you just pressed the button (i.e. the input went from LOW to HIGH),
//and you've waited long enough since the last press to ignore any noise: If the switch changed, due to noise or pressing:
if (reading != lastButtonState) {
lastDebounceTime = millis(); // reset the debouncing timer
if (reading == 1) { compteur_non_filtre = compteur_non_filtre + 1; }
}
if ((millis() - lastDebounceTime) > debounceDelay)
{ // whatever the reading is at, it's been there for longer than the debounce delay, so take it as the actual current state:
if ((reading == 1) && (reading != buttonState)) { compteur_filtre = compteur_filtre + 1; }
buttonState = reading;
}
digitalWrite(ledPin, buttonState); // set the LED using the state of the button
lastButtonState = reading; // save the reading. Next time through the loop, it'll be the lastButtonState
Serial.print("Compteurs:");
Serial.print(compteur_non_filtre);
Serial.print(", ");
Serial.println(compteur_filtre);
}
http://www.arduino.cc/en/Tutorial/Debounce
/* Debounce: each time the input pin goes from LOW to HIGH (e.g. because of a push-button press), the output pin is toggled from LOW to HIGH or HIGH to LOW. There's a minimum delay between toggles to debounce the circuit (i.e. to ignore noise). The circuit: * LED attached from pin 13 to ground | * pushbutton attached from pin 2 to +5V | * 10K resistor attached from pin 2 to ground Created 21 November 2006, by David A. Mellis, modified 3 Jul 2009, by Limor Fried and J. Grisolia et B. Detroussel Oct 2011 */
The transitory phenomenon is only during a few ms, would suffice to two successive readings of the entry (after a delay of a few ms) and make sure that it is not a transitional phase. Reading the State of 10ms later entry would be the same as 10 ms earlier:
anyone arriving to press and release a button in less than 10 milliseconds!
<= RETOUR

## Slide 139: HARDWARE DEBOUNCING
Deboucing is done using a capacitor that can absorb the noise pulses. But alone it is not sufficient. In the case of a pull-up montage, there is a capacity of 100nF (in series with a resistor of 10kΩ) that is a time constant  = RC = 1ms
When you press the button:
the capacitor is instantly discharged (bypassed by the button) and the input goes LOW. If there are parasites (peaks to + 5 volts) at the button, they will be absorbed by the capacitor.
When you release the button:
the voltage is applied on the capacitor and it will load fast enough. However, the load is not instantaneous but gradual (depends on ) => the 5 volts are applied gradually to the entry =>
To avoid this new type of interference, you must insert a Schmitt trigger on the entry.
Thus, as long as the voltage is above the minimum logic 1, the trigger does not change from State to 1... and vice versa as long as the voltage will not be passed under the minimum threshold of the trigger (0 logic), the trigger don’t pass again to 0 (cf slide VIL and VIH).
The load curve spends some time in the zone of uncertainty where the microcontroller don't know if it's still a 0 or a 1 logic. The noise is always at the point where the button is released (but in a different form).

## Slide 140: HARDWARE DEBOUNCING
//Program by Jeremy Blum www.jeremyblum.com
//Debounced Switch Input via hardware
int switchPin = 2;
int ledPin = 13;
boolean lastButton = LOW;
boolean ledOn = false;
void setup()
{
pinMode(switchPin, INPUT);
pinMode(ledPin, OUTPUT);
Serial.begin(9600);
}
void loop()
{
Serial.println(digitalRead(switchPin));
if (digitalRead(switchPin) == HIGH && lastButton == LOW)
{
ledOn = !ledOn;
lastButton = HIGH;
}
else
{
//lastButton = LOW;
lastButton = digitalRead(switchPin);
}
digitalWrite(ledPin, ledOn);
}
http://jeremyblum.com/2011/03/07/arduino-tutorial-10-interrupts-and-hardware-debouncing/
PART LIST:
Inverting Schmitt Trigger: http://us.element-14.com/stmicroelectronics/m74hc14b1r/ic-hex-inverter-schmitt-trigger/dp/89K0862
10k ohm Resistor: http://us.element-14.com/multicomp/mccfr0w4j0103a50/resistor-carbon-film-10kohm-250mw/dp/58K5002
10uF Capacitor: http://us.element-14.com/multicomp/mcgpr100v106m6-3x11/capacitor-alum-elect-10uf-100v/dp/70K9661
<= RETOUR

## Slide 141: III – 6 INTERRUPTS
III – 6 - 1 INTERRUPTS

## Slide 142: INTERRUPTS
DEFINITION: an interruption, as its name implies, interrupts a running program (main program) to run a subroutine in the µcontroller through the interrupt service routine (ISR).
It ends with a return from interrupt instruction that allows the microcontroller to return to the main program where he had left it.
Why do? Interruptions are a very powerful way to monitor an external event. The use of interrupts releases including the microcontroller to do other things until an expected event does not occur.
For example, Suppose a program in which a push button must cause a change:
Classical programming: we put a test button in the program, without being sure that it will not support for example very brief.
Programming interruption: there is more need to test, because support of the button will generate the call to subprogram
Another example :
other sensors have a dynamic interface similar role, such as a sensor of sounds trying to detect a noise or a sensor infra-red (phototransistor) trying to detect an obstacle
An interruption can occur in two ways:
1 - material Interruption: she is asked by the hardware to perform a processing (read a key on the keyboard for example). In this case, it triggers an IRQ (Interrupt ReQuest) with a number unique to the port to which the equipment is connected.
2 - Software interrupt: she is requested by the software running.
To go further: http://www.iutc3.unicaen.fr/~fougep/assembleur/les_chapitres_du_cours/interruptions.html
http://www.technologuepro.com/microprocesseur/chap5_microprocesseur.htm

## Slide 143: III – 6 INTERRUPTS
III – 6 - 1 HARDWARE INTERRUPTS

## Slide 144: INTERRUPTS WITH ARDUINO
Most of the Arduino have 2 external interruptions: n ° 0 on digital Pin 2 and no. 1 on digital Pin 3 except, the Arduino Mega, who has four more: n ° 2, 3, 4, 5 on Pin 21, 20, 19, 18
Parameters:
- interruption: the interrupt (int type)
- function : the function to call when the interrupt occurs; the function should receive no parameters and returns nothing. This function is also called an interrupt service routine (or ISR).
mode: defines the way the external interruption must be taken into account. Four constants have valid predefined values:
  LOW: for triggering the interruption when the PIN is at the bottom
  CHANGE level: for triggering the interruption when the PIN changes state low/high
  RISING: for release of the interruption when the PIN changes from bottom to top (rising edge)
  FALLING: for release of the interruption when the PIN goes from the top state to the down state (falling edge)
attachInterrupt (interrupt, fonction, mode):
Example: attachInterrupt(0, blink, CHANGE); //attach external interrupt n°0 (Pin2) to fonction blink
Specifies the function to call when an external interruption occurs.
Attention:
- the inside of the function attached to the interruption, the delay function does not work and does not increment the value returned by millis. Why?
Data series received during execution of the function is lost.
You must declare all variables used in the function attached to the interruption "volatile": allows to make the variable accessible from all contexts, including in interruptions.

## Slide 145
BEHIND THE SCENE…
ISC11 à 1 et ISC10 à 0
Vecteurs appelés par l’interruption:
registers initialisation
Tell the microprocessor in the correct address (vector)
Arduino version more simple, but of course more slowly because they are so procedures that test...
http://www.atmel.com/webdoc/avrassembler/avrassembler.wb_SEI.html
Set global interrupt flag (I) in SREG (status register)

## Slide 146
TO GO FURTHER…
1
1
1
1
1
1
0
0
1
With pull-up: logic state 1 without pushing
Pushing : 1 => 0
1
0
0
0
1
0
1
1
1

## Slide 147: INTERRUPTS PROGRAM
An opto-coupler (or optocoupler) in fork combines in a single plastic case:
1 - a LED which emits infra-red and
2 - a phototransistor that detects the light emitted by the LED light.
Example: optocoupler in fork: Liton LTH 307-01
This component has 4 pins:
- 2 first rated pins A and K correspond to the pins of the LED
- 2 other rated pins C and E for the collector and the transmitter of the phototransistor. The base of the transistor is here a "photobase" receiving photons from the LED instead to receive a current
The two components are head to head and separated by a slot in which it is possible to pass an encoder wheel or rotating object any.
The whole forms a miniature photoelectric barrier.

## Slide 148: HOW DOES IT WORKS ?
For resistance RL to photo-transistor, goal is :
1 - 0V on RL (i.e. Output to 5V) When the phototransistor is not lit and
2 - ~5V on RL (i.e. Output to 0V, more precisely ~1V) when lit.
  - If ILED = 0mA:
  RL has no significance when the phototransistor is not lit because
  IC= 0mA and then UL= RL x IC = RL x 0 = 0 V
  - If ILED = 15mA: => IC = 1mA et UCE~1V (typical of a PN junction).
  For 5V on RL with IR=1mA equals : RL = (5V-1V)/0.001= 4 kΩ => 4,7 kΩ standardized value
How to choose RD et RL ?
For resistance RD to the LED :
LED Forward voltage ~1,1 V (cf datasheet)
=> for a ILED= 15mA (under VCC=5V): RD=U/I = (5-1,1)/0.015 = 260 Ω
=> 270Ω standardized value
  We can take : RD= 270 Ω and RL=4.7 kΩ
By setting the value of the resistors used cleverly, you get with VCC = 5V:
0V (or low) in out of the phototransistor when it will be lighted
5V (or high) the phototransistor output when it will not be lit.
=> It will be possible to detect the passage of an object in the slot.

## Slide 149: INTERRUPTS PROGRAM
Realize the following program:
the program counts the pulses from an opto-Coupler in fork using the external interruption n ° 0 on pin 2 of the Arduino board.
The result is displayed in the Terminal series of the Arduino software.
This program uses the following features:
using the connection set to the PC (pins 0 and 1 (via USB cable))
uses the external interrupt 0 (pin 2)
The interrupt handler should be called whenever a rising edge is detected on the PIN:
the count variable is incremented
- the result is displayed in the Terminal of the Arduino software window.

## Slide 150: I - LES MICROCONTROLEURS
TP3-F

## Slide 151: INTERRUPTS PROGRAM
/* Ce programme compte les impulsions en provenance d'un opto-coupleur en fourche en utilisant l'interruption externe n°0 sur la broche 2 de la carte Arduino. Le résultat est affiché dans le Terminal Série du logiciel Arduino. */ // --- Fonctionnalités utilisées --- // Utilise la connexion série vers le PC // Utilise l'interruption externe 0 (broche 2) // Utilise optocoupleur infra-rouge en fourche, type LTH301-7, // --- Déclaration des variables globales --- volatile int comptageImpulsion=0; // variable accessible dans la routine interruption externe 0 void setup() {
Serial.begin(115200); // initialise connexion série à 115200 bauds attachInterrupt(0, gestionINT0, RISING); // attache l'interruption externe n°0 à la fonction gestionINT0() // mode déclenchement possibles = LOW, CHANGE, RISING, FALLING }
void loop(){ // debut de la fonction loop() // tout se passe dans la fonction de gestion de l'interruption externe } // fin de la fonction loop()
// ------------------- fonction de gestion l'interruption externe n°0 (broche 2) ---------------- // cette fonction est appelée à chaque fois que l'interruption a lieu selon le mode configuré (LOW, //CHANGE, RISING, FALLING) void gestionINT0() {// la fonction appelée par l'interruption externe n°0 comptageImpulsion=comptageImpulsion+1; // Incrémente la variable de comptage // ATTENTION : delay() et millis() non dispo ici - données série perdues Serial.print("Nombre impulsions = "); //---- affiche le nombre d'impulsions sur le port série Serial.println(comptageImpulsion); }
http://www.mon-club-elec.fr/pmwiki_mon_club_elec/pmwiki.php?n=MAIN.ArduinoInitiationEntreesOnOffOptoFourcheComptageInterruption
Pour aller plus loin, interfaçage avec Processing: http://www.mon-club-elec.fr/pmwiki_mon_club_elec/pmwiki.php?n=MAIN.OutilsProcessingProgGraphOscilloSimple
<= BACK
CAUTION: REPLACE THE OPTOCOUPLER BY A PUSH BUTTON TO HIGHLIGHT THE REBOUNDS!
TRY WITH AN OSCILLOSCOP !

## Slide 152: I - LES MICROCONTROLEURS
TP3-G

## Slide 153: ENCODEUR ROTATOIRE
Un encodeur rotatoire à un nombre définit de positions pour une révolution complète (un tour de 360°)
On peut sentir un clic à chaque pas lorsqu’on tourne le curseur du potentiomètre.
Le KY-040 possède 30 pas, soit une résolution de 12 degrés.
Keyes KY-040
Ici on ne mesure pas la valeur d’une résistance variable, on mesure des signaux logiques sur deux broches digitales, eg de l’Arduino.
On one side of the switch there are three pins.
normally referred to as A, B and C.
In the case of the KY-040, they are oriented as shown.
Inside the encoder there are two switches.
- one switch connects pin A to pin C and
- the other switch connects pin B to C.
In each encoder position, both switches are either OPENED or CLOSED.
Le KY040 est également équipé d’un bouton que l’on actionne en appuyant sur l’axe.
Le signal est récupéré sur la broche repérée SW => s’en servir pour faire un Reset de la position (au démarrage), allumer un afficheur….
R2 and R3 in the schematic are pull up
resistors.

## Slide 154: Encodeur rotatoire – Cas du KY-040
The angular position of the A terminal and the B terminal is such that:
* Rotating the switch clockwise will cause the switch connecting A and C to change states first.
* Rotating the switch counterclockwise will cause the switch connecting B and C to change states first.
If we were to represent the opening an closing of the switches as wave forms, it would look something like this.
Essentially, determining which switch changed states RST is how the direction of rotation is determined.
If A changed states first, the switch is rotating in a clockwise direction.
If B changed states first, the switch is rotating in a counter clockwise direction.
Each click causes these switches to change states as follows:
* If both switches are closed, turning the encoder either clockwise or counterclockwise one position will cause both switches to open
* If both switches are open, turning the encoder either clockwise or counterclockwise one position will cause both switches to close.

## Slide 155: Exemple de programme pour encodeur rotatoire KY-040
<= RETOUR
C

## Slide 156: III – 6 INTERRUPTS
III – 6 - 1 SOFTWARE
INTERRUPTS

## Slide 157: SOFTWARE INTERRUPT WITH TIMER 2
http://www.mon-club-elec.fr/pmwiki_mon_club_elec/pmwiki.php?n=MAIN.ArduinoInitiationInterruptionsTemporisationTimer2UneSeconde
Exemple: http://blog.blinkenlight.net/experiments/removing-flicker/heartbeat/
This program generates:
- an interruption all the seconds using the Timer 2 (8 - bit)
- and briefly turns a LED
// --- Programme Arduino --- par X. HINAULT - Le 24/02/2010 www.mon-club-elec.fr
#include <MsTimer2.h> // inclusion de la librairie Timer2
const int LED=2; //declaration constante de broche
void setup() { // debut de la fonction setup()
pinMode(LED, OUTPUT); //met la broche en sortie
// initialisation interruption Timer 2
MsTimer2::set(1000, InterruptTimer2); // période 1000ms
MsTimer2::start(); // active Timer 2
} // fin de la fonction setup()
void loop(){ // debut de la fonction loop()
}
//*************** Autres Fonctions du programme *************
void InterruptTimer2() { // beginning of the function interruption Timer2
digitalWrite(LED, HIGH);
delayMicroseconds(10000); // delayMicroseconds doesn’t block the interrupts
digitalWrite(LED, LOW);
}
How to make 'software’ interrupts at regular intervals: library MSTimer2

## Slide 158: III – 6 INTERRUPTS
III – 6 - 2 TIMERS

## Slide 159: TIMERS
As a programmer Arduino, you used for timers and disruptions without knowing, because all the hardware low-level is hidden by the Arduino IDE.
Many functions use the timers: delay(), millis() analogWrite() for PWM, tone().
Even the Servo library uses timers and interrupts.
WHAT DOES A TIMER? A timer, or to be more precise a timer/counter, is a piece of hardware of the ATMega that behaves like a clock in order to:
-measure temporal events, to count, to repeat, to compare.
The ATMega 328 of the Arduino UNO has three timers, called timer0, timer1 and timer2 while the ATmega1280 and ATMEGA2560 of the Arduino Mega series has 6 (2 * 8bits and 4 * 16 bit):
-Timer0: (8-bit timer) used by delay(), millis() and micros(). If you change this timer() records that might influence these functions => ATTENTION
-Timer1: (16-bit timer) used by the bookstore Servo on the Arduino Uno (timer5 on the Arduino Mega).
-Timer2: (8-bit timer) as the timer0. Used by tone() in the Arduino Uno.
-Timer3, Timer4 Timer5: (16 bit timers) only available on the Arduino Mega.
Example: The tone() function uses the timer2-online you can not use the PWM on pins 3 and 11
All timers are dependent on the system clock of your Arduino (e.g. 16 MHz for the UNO) but some can operate at different frequencies: example the Arduino Pro at only 8 MHz
=> so be careful when you write your own functions of Timers.
The big difference between 8 and 16-bit timers is of course the clock resolution: 256 and 65536 values respectively for the 8 and 16-bit

## Slide 160: TIMERS
Timers are programmed by special registers, use the prescalers and has several modes of operation that we see now:
Activation of the pin stores the State of the TCNTn counter in the ICRn registry => we'll know when we had a transition on the pin
When the transfer is done => activate TIC flag
=> hardware interrupt flag
1 - Frequency of the timer-counter set by prescaler
2 - initialize registers,
3 - wait for the activation of TOV (Timer Overflow interrupt flag) (when the counter gets to the supplied value)
4 - a decision: e.g. you can't start from 0, but another value => less time to reach 255.
5 - Return to zero TOV
6 - reset TCNT to the desired time
=> measure times
Intermediate comparison with one or two values gives a lot of flexibility
PWM
In the logical block: we start at the activation of TOC (Timer Overflow Interrupt) and go to the activation of TOV

## Slide 161: TIMERS REGISTERS
TCNTx - Timer/Counter Register.
The value of the real clock is stored here.
OCRx - Output Compare Register
ICRx - Input Capture Register (only 16bit timers).
TIMSKx - Timer/Counter Interrupt Mask Register.
To toggle the clock interrupts.
TIFRx - Timer/Counter Interrupt Flag Register.
Indicates an interruption of clock on hold.
TIMERS registers: you can change the behavior of timers via timers registers. Timers the most important registers are the following:
TCCRxy - Counter/Timer Control Register.
where you can set the prescalers and other things...
Remarks:
-the x suffix represents the timer number (0... 2)
-the y suffix represents the letter of the output (A, B, C):
e.g. TIMSK1 (mask of the timer1 interrupt) or OCR2A (A register of OCR from timer 2).
Ref: Atmel 8-bit Microcontroller with 4/8/16/32KBytes In-System Programmable Flash: pages 132, 134, 160…

## Slide 162: FREQUENCIES AND MODES OF TIMERS
Modes of timers:
timers can be configured according to different modes:
1 - Mode PWM: output OCxy are used to generate PWM signals:
- Fast PWM
Phase Correct PWM
2 Mode CTC: Clear Timer on Compare match. When the timer counter reaches the value of the book for comparison, the timer is cleared.
Selection of the frequency of the timer and the clock cycle:
Different clock sources can be selected independently for each timer
Example : trigger value if you want to change the State of a pin at a frequency of f = 2 Hz with the timer1 (16-bits), a prescaler of 256 and 16 MHz system clock frequency:
Counter value = (16MHz/(256*65536))/2Hz=31250
If the result of the timer/counter compared to its maximum is OK (Yes 31250 <65536 =="">) => can use the timer1 with 8bits timer: 31250 > 256
could not
If failure in one of the two cases, solution: choose a larger prescaler (=> slow down the clock).

## Slide 163: INTERUPTS
Examples of interrupts:
1 - Timer Overflow: fires when that timer reaches its value limited. When this happens, the 'Timer Overflow bit' TOVx is put into registry "timer interrupt flag register" TIFRx. When the "timer overflow interrupt enable bit" TOIEx is set in the register "interrupt mask register" TIMSKx, the "timer overflow interrupt service routine" ISR (TIMERx_OVF_vect) is called.
2 - Output Compare Match: when an event Output Compare Match occurs, an OCFxy flag is set in the 'interrupt flag register' register TIFRx. When the "output compare interrupt enable bit" OCIExy is put into registry "interrupt mask register TIMSKx", the "output compare match interrupt service" ISR (TIMERx_COMPy_vect) is called.
3 - PWM: using records OCRxA, OCRxB......
To an interrupt pending is able to call ISR, be that:
-the interrupts are enabled. They are enabled/disabled by the Interrupt () /noInterrupts () functions. By default, they are enabled in the Arduino firmware.
Attention, the attachInterrupt() and detachInterrupt() functions are used for external interruptions on the pins (i.e. hardware INTERRUPTS).
-The mask of interrupts to be activated. It is enabled/disabled in defining/clear the bits of the register of the interrupt mask (TIMSKx).
In practice: when an interruption occurs, a 'flag' is set in the interrupt register (TIFRx). This interruption is then automatically cleared when entering the ISR or even clearing manually the bit in the registry that contains the flag.

## Slide 164: EXAMPLE OF SOFTWARE INTERRUPT
BLINKING A LED WITH TIMER/COUNTER COMPARE MATCH INTERRUPT:
This example uses the timer1 (16 - bit) in CTC mode and "compare match interrupt" to cause a LED to blink. The timer is set to a frequency of 2 Hz. The LED is now activated in the interrupt service routine.
Data: clock frequency system = 16MHz, Prescaler at 256
=> Counter = (16MHz/(256*65536))/2Hz=31250
http://letsmakerobots.com/node/28278
Same example but with TIMER OVERFLOW:
=> Counter = 65536 - (16MHz/(256*65536))/2Hz=34286

## Slide 165: TOWARDS REAL-TIME OS: DUIN-OS
With the craze for the Arduino, it was normal that a version of a RTOS appears: DuinOS
http://www.freertos.org/
https://github.com/carlosdelfino/DuinOS
http://code.google.com/p/duinos/
I suggest you to install DuinOS and write your first program multi-tasking under this RTOS.
FreeRTOS is real time for embedded systems (on more than 30 microcontrollers) very popular operating system. It is distributed under the GPL with an optional exception.
The exception permits the code for users to remain owner of the closed source, while maintaining the kernel itself as open source, which facilitates the use of FreeRTOS in proprietary applications. [2]
DuinOS is a system real time operating with a preemptive multitasking system for Arduino and Atmel AVR. It is developed by RobotGroup (from Argentina) and is based on FreeRTOS
http://www.pobot.org/Premiers-pas-avec-DuinOS.html
After the installation of the OS:
once you start the Arduino environment (with the arduino.exe file located at the root), you see no major change: but go to the "tools" menu and then the submenu "boards" and you will see the maps in version DuinOS:

## Slide 166: FIRST EXAMPLE WITH DUIN-OS
Code to do simply flashing the two leds in parallel:
If you compile using a card that does not mention "DuinOS", you will see an error from the statement "taskLoop" since the compiler expects a function declaration, but there is no type before.
error: expected constructor, destructor, or type conversion before '('...)
Schema of connection for quick test:
connect two leds directly on the Arduino between:
1 - the 3.3 volts (the lowest voltage available, and it's already too) and
2 - a controllable leg by a "digital" output
Reminder: "analog 0" and "analog 1" can be used simply everything or nothing, under the name of "digital 14" and "digital 15".
Can put one pull-up?

## Slide 167: FIRST EXAMPLE WITH DUIN-OS
At least you know that you have an environment that works with DuinOS, and you can calmly begin to discover the multi-task real-time programming.
Of course, the CPU can process only one order at a time, so the real time is obtained by putting an algorithm that distributes the time CPU turn (intelligently).

## Slide 168: IV-1 POUR ALLER PLUS LOIN:
LES PONTS-H

## Slide 169: COMMANDE DE MOTEURS DC
COMMENT COMMANDER UN MOTEUR À COURANT CONTINU SACHANT QUE :
Problème 1: que l’on veut faire varier sa vitesse. Or, pour démarrer, un moteur à besoin d’une tension minimale et sa fréquence de rotation n’est pas réellement proportionnelle à la tension d'alimentation.
Problème 2: le moteur doit pouvoir tourner dans les deux sens et fonctionner dans les 4 quadrants, c'est-à-dire, soit en moteur (M), soit en génératrice (G) (freinage du moteur),
Problème 3: le courant absorbé est beaucoup plus important que ce que peut fournir un microcontrôleur.
Les solutions suivantes peuvent être envisagées (ce ne sont surement pas les seules)
1°) Résolution du problème 1 :
Il suffit de fournir au moteur une tension qui reste constante : la tension maximale et en même temps, cette tension ne sera appliquée que par très courtes périodes de temps => utilisation de la PWM
En ajustant la durée de ces périodes, on arrive à faire varier la vitesse du moteur qui devient proportionnelle à la longueur des périodes de temps passées à la tension maximale par rapport au temps passé sans application de tension (tension nulle).
Problème, avec une PWM on ne peut contrôler un moteur DC que dans un seul sens . Il serait possible d'utiliser un relai pour inverser la connexion (polarisation) du moteur mais cette option serait extrêmement gourmande en énergie.
2°) Résolution du problème 2: => le pont H.
http://wiki.mdl29.net/doku.php?id=elec:moteur_a_courant_continu

## Slide 170: COMMANDE DE MOTEURS DC
2°) Résolution du problème 2 et 3 : PONT H
1 - Pour inverser le sens de rotation du moteur il suffit d’inverser la polarité de la tension à ses bornes. Le montage a utiliser est très simple : c’est un montage à 4 interrupteurs piloter 2 par 2 en alternance, d’où le nom pont en H.
Montés de telle façon, le courant peut passer soit dans un sens, soit dans l'autre dans la charge
Fonctionnement :
K1 et K4 fermés, K2 et K3 ouverts : UM = U
K1 et K4 ouverts, K2 et K3 fermés : UM = - U
H1, H2, H3 et H4 sont des interrupteurs pilotés à l’ouverture et à la fermeture (ce peut être des transistors ou des thyristors). L’inductance permet de lisser le courant.
2 - Les interrupteurs doivent pouvoir être commandés à l’ouverture et à la fermeture, et amplifier le courant fournit par le micro-contrôleur : on utilise des transistors en commutation , généralement des MOSFET.
Montage :

## Slide 171: COMMANDE DE MOTEURS DC
Fonctionnement dans les 4 quadrants :
1) H1 et H4 fermés, H2 et H3 ouverts ⇒ VS = U (le moteur tourne dans un sens)
Si IS < 0 alors le courant passe par D1 et D4 : (quadrant Q2)
2) H1 et H4 sont ouverts, H2 et H3 sont fermés ⇒ VS = -U (le moteur tourne dans l’autre sens)
Si IS > 0 alors le courant passe par D2 et D3 (quadrant Q4)
Les diodes sont appelées diodes de récupération, elles permettent la circulation du courant lorsque l’interrupteur est commandé et que le courant est dans le sens opposé à celui de l’interrupteur. Cette phase est appelée phase de récupération, elle correspond au freinage du moteur (qui fonctionne à ce moment précis en génératrice) appelé « freinage par récupération ».
Si IS > 0 alors le courant passe par H1 et H4 (quadrant Q1)
Si IS < 0 alors le courant passe par H2 et H3 (quadrant Q3)

## Slide 172: COMMANDE DE MOTEURS DC
Les L293NE et SN754410 sont des exemples basiques de pont-H:
1 - Ils disposent de deux ponts:
  - l'un sur le côté gauche de la puce et
  l’autre sur la droite,
2 - Ils peuvent commander 2 moteurs.
3 - Ils peuvent piloter jusqu'à 1A de courant
4 - et fonctionnent entre 4.5V et 36V.

## Slide 173: COMMANDE DE MOTEURS DC – QUELQUES RECOMMENDATIONS
1 - Nécessite absolument 4 diodes en roue libre pour protéger les sorties (Output) du pont-H.
Utiliser des diodes de type "fast" (BYV27-100-TAP: Diode Ultrafast, 2A, 100V. Farnell #1469371).
2 - MOSFET Vs Bipolaires => Anticiper la chute de tension
Exemple L298N:
Chute de tension VCE_SAT totale (total drop) de 1.8V (typique), 3.2V à IL=1A, 4.9V à IL=2A. Si cela semble beaucoup, c'est aussi un avantage car cela permet d'utiliser un accu de 7.2V directement avec un moteur 5V.
Les transistors bipolaires commutés en saturation présentent une légère chute de tension (VCE_SAT).
Et comme le courant qui actionne le moteur passe par deux transistors, la chute de tension intervient donc deux fois!

## Slide 174: COMMANDE DE MOTEURS DC
http://luckylarry.co.uk/arduino-projects/control-a-dc-motor-with-arduino-and-l293d-chip/
http://itp.nyu.edu/physcomp/Labs/DCMotorControl
http://arduino103.blogspot.com/2011/06/pont-h-transistor-pour-controler-un.html
http://wiki.mdl29.net/doku.php?id=elec:moteur_a_courant_continu

## Slide 175: III-7 SERIAL COMMUNICATION: ASYNCHRONOUS & SYNCHRONOUS
III-7 SERIAL COMMUNICATION:
ASYNCHRONOUS & SYNCHRONOUS

## Slide 176: SERIAL COMMUNICATIONS
Asynchronous communication
Synchronous Communication
Asynchronous, because no clock.
The data is represented with HIGH/LOW at certain times
Wires separated for
the transmission and reception
Synchronous, because clock.
The data is represented with HIGH/LOW when the clock changes
A single wire of clock and data for each of the directions
=> both devices need to communicate at the same rate
=> no need to have two devices communicating at the same rate, but one of the two is the MASTER
What is the best?
It depends on your application:
- the asynchronous are good when there are only two devices and they are pre-configured to talk at the same speed.
- Synchronous are usually better in speed

## Slide 177: ASYNCHRONOUS SERIAL COMMUNICATION : UART…
ASYNCHRONOUS SERIAL COMMUNICATION : UART…

## Slide 178: SERIAL INTERFACE – UART
Main principle :
It transmits on line 8 bits:
1 - preceded by a start bit (set to 0 over a period) and
2 - followed by a bit of stop 'silence' (set to 1 on a period)
Typical values: 8 bits, 1 stop bit, no parity, 9600 bps
Possible values: 300,... 9600, 19200,...115200 bits/s
The RS-232 is a bus of devices designed in 1962.
A RS-232 connection works:
-peer-to-peer; There is neither slave nor master defined at the level of the Protocol
- full duplex; the two peers can communicate at the same time.
Unlike SPI and I2C links, it is possible to use it on several tens of meters, at the expense of the flow (2400 to 115200 b/s and even more under certain conditions).

## Slide 179: I - LES MICROCONTROLEURS
TP4-A

## Slide 180: TP4-A MONTAGE ULTRASON : radar de recul avec alertes LED couleurs différentes selon distance
Faire clignoter des LED de couleurs différentes (rouge, orange, verte) selon la position de l’obstacle par rapport au capteur US. On utilise des résistances de protection de 220 Ω.
<= RETOUR

## Slide 181: DATA TRANSFER ARDUINO => PYTHON
<= RETOUR
Pour la communication avec la liaison série de la carte Arduino (via le câble USB), il faut importer la bibliothèque serial en écrivant ces deux lignes :
On initialise la liste pour les mesures de distances :
On définit une fonction qui permet à la fois :
- de détecter automatiquement le port série utilisé par la carte Arduino
- de se connecter à la carte
- de récupérer les données série venant de la carte

## Slide 182: DATA TRANSFER ARDUINO => PYTHON
Pour lire une ligne de données, utilisons la méthode .readline() pour récupérer chaque ligne sous forme de chaîne de caractères.
La méthode .strip() permettra de supprimer les caractères d’espacement et de tabulation en début et fin de chaîne.
On utilisera aussi la méthode .split() pour séparer les différentes informations de la ligne pour les stocker dans une liste.
Ensuite on afficher une seule ligne (en utilisant .readline()) et la liste correspondante (avec les méthode .strip() et .split()) :
Le résultat se présente de la façon suivante :
La première ligne est la chaîne de caractères récupérée, et la deuxième ligne est la liste que nous avons créée avec les différents éléments de cette chaîne. L’information qui nous intéresse (valeur de distance) est donc le 5ème élément de la liste … donc d’indice 4 … et oui rappelez-vous : l’indice du premier élément d’une liste est 0 !
Ces données ne sont pas vraiment des chaînes de caractères mais des données de type bytes (séquences d’octet). il faudra donc les décoder (avec la méthode .decode()) et éventuellement les convertir en float si on a besoin de faire des calculs.
Ensuite on fait appel à cette fonction pour récupérer les données :

## Slide 183
Nous demandons d’afficher une série de 20 valeurs (et de les stocker dans la liste liste_distance) de la façon suivante :
Quelques lignes de code supplémentaires pour enregistrer ces informations dans un fichier texte de format .txt. Cela peut être utile pour l’importation de ces données dans des logiciels ou tableurs (Latis pro, Regressi, Excel, Libre Office ,…). Le chemin est défini par défaut dans le dossier où se trouve le fichier python mais il est possible de définir d’autres chemins:

## Slide 184: DATA TRANSFER ARDUINO => PYTHON
<= RETOUR

## Slide 185: DATA TRANSFER ARDUINO => PYTHON + REAL TIME GRAPH
<= RETOUR

## Slide 186: LIAISON SERIE SYNCHRONE: I2C, SPI, ONE WIRE, …
SYNCHRONOUS SERIAL
COMMUNICATION : I2C, SPI, ONE WIRE, …

## Slide 187: SYNCHRONOUS SERIAL COMMUNICATION : I2C, SPI, ONE WIRE, …
SYNCHRONOUS SERIAL
COMMUNICATION : I2C

## Slide 188: I2C BUS
The I2C bus is characterized by a link in series produced using 2-wire mode. It's the Philips company which created the concept in the early 1980s. Its success is linked to its simplicity.
Here is the type of an I2C-bus architecture, we notice that several components (128 Max (because address coding 7bits)) are "grafted" on the same bus, the data passes through the lines:
-SDA: data signal, generated by the master or the slave.
-SCL: clock signal generated by the master.
Communication on the bus is orchestrated in the following way:
the master sends on the bus address of the component with which it wishes to communicate,
each of the slaves having a fixed address, the slave who recognizes responds in turn by a signal of confirmation,
then the master continues the communication... procedure: (read/write)
in all cases, transactions will be confirmed by an ACK (acknowledge)
Electrical characteristics:
Bus voltage: 5V DC
Maximum operating frequency: 400kHz (variable according to the components connected to the bus, see datasheet) Logical States: -HIGH: 3 to 5 Volts, -LOW: 0 to 1.5 Volts
Maximum eligible on the bus: 400 pf
Rise of signals time: less than 1 µs
Stability time for consideration of a signal: greater than 5 µs (general rule)
Pull-up Resistance : to calculate the impedance of the Bus (practical values observed from 1.5 K to 3.5 K)
Distance from community communication: some tens of centimeters, and several meters with a buffer.
Schéma d’interface matérielle des circuits compatibles I2C

## Slide 189: MANY I2C COMPONENTS
Examples of components using the I2C: memories, converters, analog/digital and digital / analog clocks real-time, integrated radio or TV receivers frequency synthesizers...
Boussole digitale indiquant le nord

## Slide 190: THE BASICS OF THE PROTOCOL
1 - The REST CONDITION :
Condition in which no components communicate, bus lines are in the HIGH state:
2 - The starting CONDITION:
the master force line SDA low to "wake up" the slaves when SCL is high:
4 - The stop CONDITION:
SDA and SCL lines are low, and then when SCL goes at the upper level, the master releases the SDA line at the high level. Now the bus is regarded as available:
3 – ACKNOWLEDGMENT :
once the data is transmitted, an acquittal is operated by the person who receives the data.
This procedure is performed in the end frame transmission, namely the ninth impulse.
Keeping receiver SDA line low during the rising of clock:

## Slide 191: ARCHITECTURE OF A FRAME
THE FRAME:
1 - must wake up the bus with a start condition,
2 - then come to interpolate data frames. The significant bit being sent first. The slave who received information perform the master to let her know that it successfully received the frame of data, otherwise, is the master to start the transactions since the start.
3 - to finish the Stop signal will end any communication.
THE ADDRESSING: to communicate with the ≠ components connected to the bus:
1 - after you give a start condition, the master shows with what slave it wishes to connect, for this he will send on the address of the slave composed of 7-bit,
2 – then a last bit showing the transfer direction: reading (1: slave-> master) or writing (0: master-> slave).
Wire function library : http://www.arduino.cc/en/Reference/Wire
The slave recognize his address will validate with an acknowledgment...

## Slide 192: COMMUNICATION BY BYTE
2 - Sequence of reading data in a memory EEPROM I2C:
1 - Start Condition
- Emission of the slave address, i.e. the EEPROM, with a write request. What for? just to point the internal memory register on the chosen address, otherwise, reading would be the value contained in this pointer, which can give you in return a no good values.
- Acknowledgment of the slave and stop condition (Restart is possible)
2 - Start condition
1 - Sequence of writing data to a memory EEPROM I2C:
Condition departure
Emission of the slave address, i.e. the EEPROM here
Acknowledgment of the slave
Emission by the master of the memory address in which he wishes to enter the future data, subsequent acknowledgment of the slave
Transmission of the data to write, acknowledgment on each receipt package
Stop condition
COMMUNICATION by byte: a complete Exchange on the bus between master and slave
We notice that the master, after emission of the address of data storage, didn't need to interrupt the communication at each byte and write again to the pointing address. I2C components are generally to 'auto-loading', that is to say that their address pointer automatically increments and this for the 8-byte value.
Show the slave address, ie. the EEPROM, with a read request this time. The component confirms the order and the data is sent. Playback can be done by block, in this case, confirm each data read by an ACK,
then before the stop condition, sent a NACK.
Stop condition

## Slide 193: REMARKS: SLAVE ADDRESSES
Type | Description | Constant adress
PCD 3311 | Générateur / Décodeur DTMF | 010010x
PCF 8570 | RAM Statique 2 Ko (256 x 8) | 1010xxx
PCF 8573 | Horloge/Calendrier temps réel | 11010xx
PCF 8574 | Extension de port parallèle 8 Bits | 0100xxx
PCF 8552 | EEprom 2 Ko (256 x 8) | 1010xxx
PCF 8583 | Horloge/Calendrier temps réel + 240 Octets de RAM | 101000x
PCF 8591 | Convertisseur A/N N/A 8 Bits | 1001xxx
SAA 1064 | Drivers d'affichage à leds 4 Digits | 01110xx
M24C256 | EEprom 128 Ko (32k x 8) | 1010xxx
On the I2C bus, an address is assigned at each component, but what do if there had several times the same TYPES of components present on the BUS?
To generalize, every family circuit consists of an "Silicon“ address, permanent and unchangeable, then other part entirely configurable totally accessible by external way, via the terminals of the integrated circuit:
In the example below, the PCF8583 (clock-calendar + RAM) address consists of 6 fixed bits and 1 editable, ie. the ability to connect 2 same circuits on the bus.
I2C popular component and the composition of their fixed addresses:
We notice that some circuits have the same address, but this is only of components of similar functions as the memories...

## Slide 194: PROGRAM EXAMPLE
Join the bus I2C
(as master)
Request the data
from the device
Retrieve the data

## Slide 195: EXEMPLE D’UTILISATION DU BUS I2C
#include <Wire.h>
byte position = 0;
void setup ()
{
Wire.begin (); // join i2c bus, Arduino en Maître
}
void loop ()
{
Wire.beginTransmission (0x2C); // L’AD5171 est à l’adresse 0x2C
Wire.send (0x40); // Envoi de l’instruction
Wire.send (position); // Envoi de la position
Wire.endTransmission (); // Fin de l’échange
Position++;
if (position == 64) //si le maximum (64 positions pour AD5171) est atteint
{
Position=0;
}
Delays (500);
}
I2C Device Address Bit. Allows a maximum of two AD5171s to be addressed.
interface Control of I2C digital potentiometer (AD5171) :
26 25 24 23 22 21 20
0 1 0 1 1 0 0
Reminder: I2C Pin on the Arduino : SDA: Analog In 4, SCK: Analog In 5
Decimal adress 44 (25 + 23 + 21 = 44) => 0x2C (Hexadecimal)

## Slide 196: I2C APPLICATION EXAMPLE : Real Time Clock: DS1307
The DS1307 which is a I2C controlled real-time clock.
I2C adress (7bits) of the DS1307 : 1101000
The addresses of registers:
register RTC 00h to 07h
registry RAM 08h to 3Fh

## Slide 197: I2C APPLICATION EXAMPLE : Real Time Clock: DS1307
Each bit in the different registers can only be 0 or 1.
How to represent the contents of the registry in hexadecimal?
Answer: You must first determine the binary representation and then convert it to hexadecimal.
Take 3th register 02H (HOURS) and an hour example to represent 12:34 pm :
Reading from left to right :
- Bit 7 is unused => 0.
- Bit 6 determine the hour display format (12- ou 24-hour): let’s choose 0 for example for the 12-hour
- Bit 5 (when bit 6 is 0) represent indicator AM/PM: let’s choose 1 for example for PM.
- Bit 4 represents the most left bit of the hour, i.e. the 1 in 12:34 pm: let’s choose 1 for example
- Bits 3 to 0 represent binary conversion of 2 from 12 i.e. is 0010.
Hence, the 3rd register allows to represent 12 pm by writing the binary 00110010
Converterd into hexadecimal i.e. 0×32, sent to register 02H.
To code minutes, we must proceed the same way with 2rd register 01H!!!

## Slide 198: I2C APPLICATION EXAMPLE : Real Time Clock: DS1307
In this chronogram, it is 9 hours 56 minutes 6 seconds, on Tuesday 20 May 2008.
Example of use: plug the SQW/OUT output signal (PIN 7) at 1 Hz frequency to one of the interrupt pins of the Arduino:
- that causes an interruption every 1000,000 ms.
- the Arduino reads the time and date in the DS1307, communication is via the I2C bus:
http://www.glacialwanderer.com/hobbyrobotics/?p=12
http://combustory.com/wiki/index.php/RTC1307_-_Real_Time_Clock
http://tronixstuff.wordpress.com/2010/05/20/getting-started-with-arduino-%E2%80%93-chapter-seven/
http://tronixstuff.wordpress.com/2010/10/07/add-a-real-time-clock-to-the-freetronics-twentyten/

## Slide 199: Nintendo Wii Nunchuck
The Wii Nunchuk has:
1 - standard interface I2C
2 - a 3 accelerometer axis resolution 10bits.
3 - a 2 axis analog joystick with a 8 bit A/D converter
4- 2 buttons
Nunchuk PinOUT
PinOUT adapter
Program: Nunchuk Print
read data every 100ms, and display:
- the joystick Position (x, y)
accelerometer (x, y, z)
buttons Z, C
Chip listing:
U1: Unknown manufacturer - "FNURVL" "A 405" "633KM" (custom processing chip? - TQFP48)
U2: ST Microelectronics LIS3L02AL 3-axis accelerometer - "1806" "3L02AE" "615" "MLT" (accelerometer - LGA-8)
GND
SDA
SCK
+V

## Slide 200: POUR ALLER PLUS LOIN
The Arduino must send a HandShake to communicate with the Nunchuck.
So, send first 2 bytes "0x40, 0x00".
Then send only 1 byte "0x00" whenever you request data from the Nunchuck.
These data will be returned to you by packs of 6 bytes.
Octet 1 : Joystick - Axis X : a byte from 0 to 255
Octet 2 : Joystick - Axis Y : a byte from 0 to 255
Octet 3 : Accelerometer - Axe X : a byte for 8 MSB over the possible 10 bits, if we only use this byte we’ll only have values from 0 to 255
Octet 4 : Accelerometer - Axe Y : a byte for 8 MSB over the possible 10 bits, if we only use this byte we’ll only have values from 0 to 255
Octet 5 : Accelerometer - Axe Z : a byte for 8 MSB over the possible 10 bits, if we only use this byte we’ll only have values from 0 to 255
Octet 6 : from MSB to LSB : 2 bits for Z axis accelerometer, concatened with previous 8 bits => obtaining 10 bits résolution, ie. Values from 0 to 1023.
2 bits for Y axis accelerometer, 2 bits for X axis accelerometer. 1 bit for C button: 0:pushed, 1:release. 1 bit for Z button: 0:pushed, 1:release.
Z
C
LSB Xacc (21)
LSB Xacc (20)
LSB Yacc (21)
LSB Yacc (20)
LSB Zacc (21)
LSB Zacc (20)
Bit 3
de Xacc (22)
Bit 10
de Xacc (210)
…
Beware:
X acceleration values are on 10 bits !
8 bits from n°3 + 2 bits from n°6

## Slide 201: bitshift left (<<), bitshift right (>>) OPERATORS
There are two C/C++ bit shift operators:
bitshift right (>>)
Syntax: variable << number_of_bits ou variable >> number_of_bits
Examples:
int a = 5; // binary: 0000000000000101 (over 16 bits)
int b = a << 3; // binary: 0000000000101000 => 40 (decimal) (5x23=5x8=40)
int c = b >> 3; // binary: 0000000000000101 => we return to 5
Remark 1 : When you offset a number to the left, left bit is literally lost!
Example:
int a = 5; // binary: 0000000000000101
int b = a << 14; // binary: 0100000000000000 – the first 1 from 101 is lost!
Remark 2 : bitshift left of a n number is multiplication by 2n
1 << 0 == 1 = 20
1 << 1 == 2 = 21
1 << 2 == 4 = 22
...
1 << 8 == 256 = 28
1 << 10 == 1024 = 210
...
In contrary, bitshift right of a n number is division by 2n
1 - the left shift operator << (bitshift left) who causes the shift to the left of the bits.
2 - right shift operator >> (bitshift right) that causes the right bit shift.
bitshift left (<<)

## Slide 202: Bitwise AND (&), Bitwise OR (|), Bitwise XOR (^)
Bitwise operator (AND, OR, XOR) perform their calculations on each bit position.
Bitwise AND (&):
If the two input bits are 1, the output is 1, otherwise 0.
The most common uses of the AND is to select bits by "masking."
0 0 1 1 operand1
0 1 0 1 operand2
----------
0 0 0 1 (operand1 & operand2) - returned result
Bitwise OR (|):
The OR binary of two bits is 1 if one OR the other input bits is 1, or 0.
0 0 1 1 operand1
0 1 0 1 operand2
----------
0 1 1 1 (operand1 | operand2) - returned result
0 0 1 1 operand1
0 1 0 1 operand2
----------
0 1 1 0 (operand1 ^ operand2) - returned result
Bitwise XOR (^): This operator is very similar to the OR operator (|), only it puts a bit to 0 when the two input bits are 1:
APPLICATIONS: decoding of the information of the Nunchuk
// byte outbuf[5] contains bits for z and c buttons and it also contains the least significant bits for the accelerometer data
// so we have to check each bit of byte outbuf[5]
if ((outbuf[5] >> 0) & 1) { z_button = 1; }
if ((outbuf[5] >> 1) & 1) { c_button = 1; }
if ((outbuf[5] >> 2) & 1) { accel_x_axis += 2; }

## Slide 203: I - LES MICROCONTROLEURS
TP4-B

## Slide 204: THE WII NUNCHUK CONTROL
#include <Wire.h>
#include <string.h>
#undef int
#include <stdio.h>
uint8_t outbuf[6]; // array to store arduino output
int cnt = 0;
int ledPin = 13;
void
setup ()
{
beginSerial (19200);
Serial.print ("Finished setup\n");
Wire.begin (); // join i2c bus as master
nunchuck_init (); // send the initilization handshake
}
void
nunchuck_init ()
{
Wire.beginTransmission (0x52); // transmit to device 0x52
Wire.send (0x40); // sends memory address
Wire.send (0x00); // sends sent a zero.
Wire.endTransmission (); // stop transmitting
}
void
send_zero ()
{
Wire.beginTransmission (0x52); // transmit to device 0x52
Wire.send (0x00); // sends one byte
Wire.endTransmission (); // stop transmitting
}
Void loop ()
{
Wire.requestFrom (0x52, 6); // request data from nunchuck
while (Wire.available ())
{
outbuf[cnt] = nunchuk_decode_byte (Wire.receive ()); // receive byte as an integer
digitalWrite (ledPin, HIGH); // sets the LED on
cnt++;
}
// If we received the 6 bytes, then go print them
if (cnt >= 5)
{
print ();
}
cnt = 0;
send_zero (); // send the request for next bytes
delay (100);
}
// Print the input data we have recieved
// accel data is 10 bits long
// so we read 8 bits, then we have to add
// on the last 2 bits. That is why I
// multiply them by 2 * 2
void
print ()
{
int joy_x_axis = outbuf[0];
int joy_y_axis = outbuf[1];
int accel_x_axis = outbuf[2] * 2 * 2;
int accel_y_axis = outbuf[3] * 2 * 2;
int accel_z_axis = outbuf[4] * 2 * 2;
int z_button = 0;
int c_button = 0;
// byte outbuf[5] contains bits for z and c buttons
// it also contains the least significant bits for the accelerometer data
// so we have to check each bit of byte outbuf[5]
if ((outbuf[5] >> 0) & 1)
{
z_button = 1;
}
if ((outbuf[5] >> 1) & 1)
{
c_button = 1;
}
if ((outbuf[5] >> 2) & 1)
{
accel_x_axis += 2;
}
if ((outbuf[5] >> 3) & 1)
{
accel_x_axis += 1;
}
if ((outbuf[5] >> 4) & 1)
{
accel_y_axis += 2;
}
if ((outbuf[5] >> 5) & 1)
{
accel_y_axis += 1;
}
if ((outbuf[5] >> 6) & 1)
{
accel_z_axis += 2;
}
if ((outbuf[5] >> 7) & 1)
{
accel_z_axis += 1;
}
Serial.print (joy_x_axis, DEC);
Serial.print ("\t");
Serial.print (joy_y_axis, DEC);
Serial.print ("\t");
Serial.print (accel_x_axis, DEC);
Serial.print ("\t");
Serial.print (accel_y_axis, DEC);
Serial.print ("\t");
Serial.print (accel_z_axis, DEC);
Serial.print ("\t");
Serial.print (z_button, DEC);
Serial.print ("\t");
Serial.print (c_button, DEC);
Serial.print ("\t");
Serial.print ("\r\n");
}
// Encode data to format that most wiimote drivers except
// only needed if you use one of the regular wiimote drivers
char
nunchuk_decode_byte (char x)
{
x = (x ^ 0x17) + 0x17;
return x;
}
http://www.windmeadow.com/node/42
http://todbot.com/blog/bionicarduino/
<= RETOUR

## Slide 205: Nintendo Wii Nunchuck & SERVO (Library version)
/* PROGRAMME PRINCIPAL
*/
#include <math.h>
#include <Servo.h>
#include "Wire.h"
#include "WiiChuck.h«
#define MAXANGLE 90
#define MINANGLE -90
Servo myservo; // create servo object to control a servo
int potpin = 0; // analog pin used to connect the potentiometer
WiiChuck chuck = WiiChuck();
int angleStart, currentAngle;
int tillerStart = 0;
double angle;
void setup()
{
//nunchuck_init();
Serial.begin(115200);
chuck.begin();
chuck.update();
//chuck.calibrateJoy();
// attaches the servo on pin 9 to the servo object
myservo.attach(9);
}
void loop()
{
delay(20);
chuck.update();
// sets the servo position according to the scaled value
myservo.write(chuck.readPitch());
Serial.print(chuck.readRoll());
Serial.print(", ");
Serial.print(chuck.readPitch());
Serial.print(", ");
Serial.print((int)chuck.readAccelX());
Serial.print(", ");
Serial.print((int)chuck.readAccelY());
Serial.print(", ");
Serial.print((int)chuck.readAccelZ());
Serial.println();
}
<= RETOUR
Insertion of the librairy: WiiChuck.h
(cf next slide)

## Slide 206: Nintendo Wii Nunchuck & SERVO (Library version)
/*
* Nunchuck -- Use a Wii Nunchuck
* Tim Hirzel http://www.growdown.com
*
notes on Wii Nunchuck Behavior.
This library provides an improved derivation of rotation angles from the nunchuck accelerometer data. The biggest different over existing libraries (that I know of ) is the full 360 degrees of Roll data
from teh combination of the x and z axis accelerometer data using the math library atan2. It is accurate with 360 degrees of roll (rotation around axis coming out of the c button, the front of the wii), and about 180 degrees of pitch (rotation about the axis coming out of the side of the wii). (read more below)
In terms of mapping the wii position to angles, its important to note that while the Nunchuck
sense Pitch, and Roll, it does not sense Yaw, or the compass direction. This creates an important
disparity where the nunchuck only works within one hemisphere. At a result, when the pitch values are less than about 10, and greater than about 170, the Roll data gets very unstable. essentially, the roll data flips over 180 degrees very quickly. To understand this property better, rotate the wii around the axis of the joystick. You see the sensor data stays constant (with noise). Because of this, it cant know the difference between arriving upside via 180 degree Roll, or 180 degree pitch. It just assumes its always 180 roll.
/*
* This file is an adaptation of the code by these authors:
* Tod E. Kurt, http://todbot.com/blog/
* The Wii Nunchuck reading code is taken from Windmeadow Labs
* http://www.windmeadow.com/node/42
*/
#ifndef WiiChuck_h
#define WiiChuck_h
#include "WProgram.h"
#include <Wire.h>
#include <math.h>
// these may need to be adjusted for each nunchuck for calibration
#define ZEROX 510
#define ZEROY 490
#define ZEROZ 460
#define RADIUS 210 // probably pretty universal
#define DEFAULT_ZERO_JOY_X 124
#define DEFAULT_ZERO_JOY_Y 132
class WiiChuck {
private:
byte cnt;
uint8_t status[6];// array to store wiichuck output
byte averageCounter;
//int accelArray[3][AVERAGE_N]; // X,Y,Z
int i;
int total;
uint8_t zeroJoyX; // these are about where mine are
uint8_t zeroJoyY; // use calibrateJoy when the stick is at zero to correct
int lastJoyX;
int lastJoyY;
int angles[3];
boolean lastZ, lastC;
public:
byte joyX;
byte joyY;
boolean buttonZ;
boolean buttonC;
void begin()
{
Wire.begin();
cnt = 0;
averageCounter = 0;
// instead of the common 0x40 -> 0x00 initialization, we use 0xF0 -> 0x55 followed
//by 0xFB -> 0x00, this lets us use 3rd party nunchucks (like cheap $4 ebay ones)
// while still letting us use official oness. Only side effect is that we no longer need
//to decode bytes in _nunchuk_decode_byte
// see http://www.arduino.cc/cgi-bin/yabb2/YaBB.pl?num=1264805255
Wire.beginTransmission(0x52);// device address
Wire.send(0xF0);
Wire.send(0x55);
Wire.endTransmission();
delay(1);
Wire.beginTransmission(0x52);
Wire.send(0xFB);
Wire.send(0x00);
Wire.endTransmission();
update();
for (i = 0; i<3;i++) {
angles[i] = 0;
}
zeroJoyX = DEFAULT_ZERO_JOY_X;
zeroJoyY = DEFAULT_ZERO_JOY_Y;
}
void calibrateJoy() {
zeroJoyX = joyX;
zeroJoyY = joyY;
}
void update() {
Wire.requestFrom (0x52, 6);// request data from nunchuck
while (Wire.available ()) { // receive byte as an integer
status[cnt] = _nunchuk_decode_byte (Wire.receive()); //
cnt++;
}
if (cnt > 5) {
lastZ = buttonZ;
lastC = buttonC;
lastJoyX = readJoyX();
lastJoyY = readJoyY();
//averageCounter ++;
//if (averageCounter >= AVERAGE_N)
// averageCounter = 0;
cnt = 0;
joyX = (status[0]);
joyY = (status[1]);
for (i = 0; i < 3; i++)
//accelArray[i][averageCounter] = ((int)status[i+2] << 2) + ((status[5] & (B00000011 << ((i+1)*2) ) >> ((i+1)*2)));
angles[i] = (status[i+2] << 2) + ((status[5] & (B00000011 << ((i+1)*2) ) >> ((i+1)*2)));
//accelYArray[averageCounter] = ((int)status[3] << 2) + ((status[5] & B00110000) >> 4);
//accelZArray[averageCounter] = ((int)status[4] << 2) + ((status[5] & B11000000) >> 6);
buttonZ = !( status[5] & B00000001);
buttonC = !((status[5] & B00000010) >> 1);
_send_zero(); // send the request for next bytes
}
}
// UNCOMMENT FOR DEBUGGING
//byte * getStatus() {
// return status;
//}
float readAccelX() {
// total = 0; // accelArray[xyz][averageCounter] * FAST_WEIGHT;
return (float)angles[0] - ZEROX;
}
float readAccelY() {
// total = 0; // accelArray[xyz][averageCounter] * FAST_WEIGHT;
return (float)angles[1] - ZEROY;
}
float readAccelZ() {
// total = 0; // accelArray[xyz][averageCounter] * FAST_WEIGHT;
return (float)angles[2] - ZEROZ;
}
boolean zPressed() {
return (buttonZ && ! lastZ);
}
boolean cPressed() {
return (buttonC && ! lastC);
}
// for using the joystick like a directional button
boolean rightJoy(int thresh=60) {
return (readJoyX() > thresh and lastJoyX <= thresh);
}
// for using the joystick like a directional button
boolean leftJoy(int thresh=60) {
return (readJoyX() < -thresh and lastJoyX >= -thresh);
}
int readJoyX() {
return (int) joyX - zeroJoyX;
}
int readJoyY() {
return (int)joyY - zeroJoyY;
}
// R, the radius, generally hovers around 210 (at least it does with mine)
// int R() {
// return sqrt(readAccelX() * readAccelX() +readAccelY() * readAccelY() + readAccelZ() * readAccelZ());
// }
// returns roll degrees
int readRoll() {
return (int)(atan2(readAccelX(),readAccelZ())/ M_PI * 180.0);
}
// returns pitch in degrees
int readPitch() {
return (int) (acos(readAccelY()/RADIUS)/ M_PI * 180.0); // optionally swap 'RADIUS' for 'R()'
}
private:
byte _nunchuk_decode_byte (byte x)
{
//decode is only necessary with certain initializations
//x = (x ^ 0x17) + 0x17;
return x;
}
void _send_zero()
{
Wire.beginTransmission (0x52);// transmit to device 0x52
Wire.send (0x00);// sends one byte
Wire.endTransmission ();// stop transmitting
}
};
#endif

## Slide 207
OLED SCREEN

## Slide 208: OLED SCREEN - 1
Caractéristiques d’un écran OLED i2C (monochrome, chipset SSD1306)
Les écrans OLED sont des écrans graphiques, monochromes ou multi-couleurs, permettant d’afficher du texte, des images, et des figures graphiques.
Ils intègrent généralement un contrôleur qui fait l’interface avec la partie « commande » (e.g. Arduino).
L’afficheur OLED est doté d’un contrôleur SSD1306
(OLED 0,96 pouces monochrome, faisant 128×64 pixels).
On les trouve principalement dans 2 protocoles de communication courants :
Le bus I2C (utilisant que 2 fils : SDA et SCL)
Le bus SPI (utilisant 4 fils : SCK, MOSI, MISO, et SS, aussi noté D0, D1, DC, et CS)
Ils s’alimentent généralement de 3,3 à 5V.

## Slide 209: OLED SCREEN - 3
3 - Quelle adresse i2c a mon écran OLED ? 0x3C, 0x3D, 0x78, ou 0x7A ?
On note 2 adresses i2c possibles : 0x78 ou 0x7A (c’est écrit en petit, sur la photo ci-dessus, là où j’ai entouré en rouge).
Pourtant : il faut utiliser 0x3C ou 0X3D dans le software
Pourquoi ?
En I2C, on ne travaille pour les adresses que sur 7 bits et non 8 bits
(cf DATASHEET).
Soit des nombres entiers de 0 à 127
0x00 à 0x7F en hexadécimal, ou de 000 0000 à 111 1111 en binaire)

## Slide 210: OLED SCREEN - 2
https://passionelectronique.fr/ecran-oled-i2c-arduino/
1 - Comment raccorder un écran OLED à l’Arduino ? (via le bus I2C)
2 - Comment trouver l’adresse: Scanner I2C !
Ce bout de code permet également de vérifier si le périphérique I2C en question (ici un écran OLED) n’est pas « mort ».
Téléverser le programme Scanner I2C:
https://moodle.insa-toulouse.fr/mod/resource/view.php?id=64321

## Slide 211: OLED SCREEN – 4
. la librairie « SSD1306 » de Adafruit (https://github.com/adafruit/Adafruit_SSD1306), spécialisée pour les écrans OLED dotés du contrôleur SSD1306, cette bibliothèque est clairement la plus facile à manipuler lorsqu’on fait ses premiers pas !
4 - Quelle librairie pour adresser l’écran ?
. la librairie « U8G2 » de Olikraus (https://www.arduino.cc/reference/en/libraries/u8g2/), très complète, mais pas forcément la plus facile à manipuler, lorsqu’on débute
Attention, la librairie SSD1306 d’Adafruit impose l’installation d’une dépendance, appelée « librairie GFX ».
Pour installer les librairies « Adafruit_SSD1306.h » et « Adafruit_GFX.h » de chez Adafruit,
il suffit simplement :
1 - Ouvrir son IDE Arduino, et de
2 - cliquer sur : Outils > Gérer les Bibliothèques ;
3 - puis renseigner le mot « ssd1306 » dans le champ de recherche,

## Slide 212: I - LES MICROCONTROLEURS
TP4-E

## Slide 213: OLED SCREEN – 5 – TP4E
EXEMPLE 3 : code arduino permettant d’afficher du texte à l’écran (de différentes tailles)
<= RETOUR

## Slide 214: SYNCHRONOUS SERIAL COMMUNICATION : I2C, SPI, ONE WIRE, …
SYNCHRONOUS SERIAL
COMMUNICATION : SPI

## Slide 215: THE BUS SPI - GENERAL INFORMATION
1 - SPI "Serial Peripheral Interface": (or Microwire (for National Semiconductor) or bus serial 3-wire)
The I2C bus is not alone, he is followed by other series synchronous circuits type SPI or One Wire.
These last two names, however, are less well standardized than the I2C bus.
  Synchronous serial data bus, using 4-wire (3fils + 1Masse)
  Connection of type master-slave, allowing the connection of several circuits => dedicated for inter-devices communication, see inter-boards, within the same system
  Full Duplex (the data can travel in both directions at the same time) - as opposed to (for example), the bus I2C (2 son + mass) which cannot do.
  Master-slave - a master only possible on the bus several slaves can coexist on a bus
  The selection of the recipient is made by a dedicated line chip select (CS).
The SPI bus contains 4 logical signals:
SCLK — Horloge (because SERIAL SYNCHRONOUS BUS)) (generated by MASTER)
MOSI — Master Output, Slave Input (generated by MASTER)
MISO — Master Input, Slave Output (généré par l'esclave)
SS — Slave Select, Slave active at LOW state (generated by MASTER)
  If high level, the component ignores what is happening on the bus
  => several peripheral components that share the 3 lines !
  Standard established by Motorola and taken up by different brands
Beware, you can encounter other names: SDI, DI, SI — Serial Data IN  MISO
            SDO, DO, SO — Serial Data OUT  MOSI
            nCS, CS, nSS, STE  SS

## Slide 216: THE SPI - CHRONOGRAM GENERAL BUS
Données Maître -> esclave
Horloge Maître -> esclave
Registre à décalage
Données Esclave -> maître
Registre
EMISSION / RECEPTION
Three settings:
- Clock speed (set by the master).
- The polarity of the clock (CPOL (Clock polarity) parameter): determines the logical level of the SCK line at rest.
- The phase of the clock (setting CPHA (Clock phase)): determines the front on which the data is changed and the front on which the data will be read.
(MASTER AND SLAVE MUST HAVE THE SAME PARAMETERS)
SPI-mode | CPOL (CKP) | CPHA (CKE)
0 | 0 | 0
1 | 0 | 1
2 | 1 | 0
3 | 1 | 1
the transmitter copy SSPBUF of the master in SSPSR
the output data are sent in SSPSR from the receiver to the clock pulses
receiver copy SSPSR in its SSPBUF
CPOL and CPHA have 2 possibles states : 4 possible configurations

## Slide 217
Example: in an EEPROM write permission
Sélection
-CS = 0
Horloge
-Sur front 
µC -> 00000110
-Le MSB en premier
Sortie EEPROM
-En haute impédance
Sélection
-CS = 0
Horloge
-Sur front 
µC -> 00000101
-Le MSB en premier
Sortie EEPROM
-En haute impédance
EEPROM-> 00000010
-Le MSB en premier
Example: the registry of an EEPROM reading
THE SPI - CHRONOGRAM GENERAL BUS

## Slide 218: THE BUS SPI - FEATURES
In master mode, the transmission speed is selected by 3 bits of the register SPCON (Serial Peripheral CONtrol register): SPR1, SPR2 and SPR0.
The clock frequency is chosen among 7 frequencies obtained by division of the operating frequency of the microcontroller.
SPR2 : SPR1 : SPR2 | SPI frequency | Example Ftransmission (quartz at Fµc=20MHz)
000 | Fμc/2 | 10
001 | Fμc/4 | 5
010 | Fμc/8 | 2.5
011 | Fμc/16 | 1.25
100 | Fμc/32 | 0.625
101 | Fμc/64 | 0.3125
110 | Fμc/128 | 0.156
BUS SPEED :
Several slaves (daisy chain): simultaneous selection
Some SPI components are designed to be chained together, simplifying the connections between components, reducing the number of lines SS.
Several slaves but only one active slave at the same time:

## Slide 219: CONTRÔLE D’UN POTENTIOMETRE DIGITAL AVEC LE BUS SPI
AD5206 Digital Potentiometer
http://arduino.cc/en/Tutorial/SPIDigitalPot
http://www.arduino.cc/en/Reference/SPI
The management of the SPI bus is easy because the Arduino contains a library named SPI.h
http://tronixstuff.wordpress.com/2011/05/13/tutorial-arduino-and-the-spi-bus/
Functions
begin()
end()
setBitOrder()
setClockDivider()
setDataMode()
transfer()

## Slide 220: A SPI BUS CONTROL FOR THE DIGITAL POTENTIOMETER
http://arduino.cc/en/Tutorial/SPIDigitalPot
/* Digital Pot Control
This example controls an Analog Devices AD5206 digital potentiometer.
The AD5206 has 6 potentiometer channels. Each channel's pins are labeled
A - connect this to voltage
W - this is the pot's wiper, which changes when you set it
B - connect this to ground.
The AD5206 is SPI-compatible, and to command it, you send two bytes,
one with the channel number (0 - 5) and one with the resistance value
for the channel (0 - 255).
The circuit:
* All A pins of AD5206 connected to +5V
* All B pins of AD5206 connected to ground
* An LED and a 220-ohm resisor in series connected from each W pin to ground
* CS - to digital pin 10 (SS pin)
* SDI - to digital pin 11 (MOSI pin)
* CLK - to digital pin 13 (SCK pin)
created 10 Aug 2010 by Tom Igoe
Thanks to Heather Dewey-Hagborg for the original tutorial, 2005
*/

## Slide 221: I - LES MICROCONTROLEURS
TP4-F

## Slide 222: WHAT ARE DIGITAL POTENTIOMETERS?
A mechanical potentiometer is a three-terminal resistor with a sliding or rotating contact.
It generally has three pins (A, Wiper, B) which comes in many forms ranging from large panel mount devices to small trimpots designed for PCB adjustments.
All pots are mechanically similar and consist of :
1 - a resistive element,
2 - a sliding contact (wiper) that moves along the element making electrical contact along its length,
3 - electrical terminals at each end of the element (pins A and B),
4 - a mechanism that moves the wiper from one end to the other, and
5 - a housing to contain and protect the element and wiper.
The device can form :
1 - a variable resistor or rheostat, if only two terminals are used (one end and the wiper) OR
2 - an adjustable voltage divider if all three terminals are used
Remarks:
1 - Pots are generally referenced by form factor and overall resistance (the resistance between terminals A and
2 - Connection between W and A avoids having an infinite resistance if mechanical potentiometer contact is lost!
What is a Digital Potentiometer?
Simply put, a digital potentiometer (a.k.a digipot) is electronic hardware that performs the same functions as analog potentiometers, but they have no moving parts.

## Slide 223: MCP 41xxx – DIGITAL POTENTIOMETER
https://arduinoplusplus.files.wordpress.com/2018/01/mcp41xxx-42xxx-digital-pot-with-spi-interface.pdf
MCP41xx Digital Potentiometer |  | 
Pin # | Pin Name | Description
1 | CS | The CS, or Chip Select, pin is the SS (slave select) pin for the SPI interface. It is active low. 0V means the chip is selected and 5V means it is not selected.
2 | SCLK | SCLK is the Shared/Serial Clock. It is the SPI clock line.
3 | SDI/SDO | These pins are the serial data in and out, also known as the MOSI and MISO.
4 | VSS | This is where ground is connected to.
5 | P0A | This is one terminal of the potentiometer.
6 | P0W | This is the wiper terminal of the potentiometer.
7 | P0B | This is one terminal of the potentiometer.
8 | VDD | This is where the positive voltage source connects to.
The MCP41100 is a simple SPI 100k digital potentiometer, although there are also 10k and 50k potentiometers, we will have to choose the one we need for our project.
There is also the MCP42XXX series which will be two potentiometers in the same package.
Controlling the Digipot: Pot control is through the SPI interface writing to the 8-bit pot control register => 256 values.
these pots can only be set in increments of 1/255th of the full scale resistance of the pot.
For example, a 10kΩ pot can be set in increments of 10,000/255 per step (or 39.2Ω/step) or 392 Ω/step for the 100k
In practice this is not a major limitation when using a digipot.

## Slide 224: MCP 41xxx – DIGITAL POTENTIOMETER - WIRING DIAGRAM
Multimeter
In the hardware setup, MCP41xxx is connected to the Arduino via the Arduino’s SPI Interface:
1 - Potentiometer terminals A (pin 5) and B (pin 7) are connected to the Arduino 5-volt supply (5 V) and Ground (Gnd).
2 - The wiper terminal W (pin 6) is either connected to a multimeter or through an Analog Pin of the Arduino.
The voltage at the analog pin is then read and displayed on the serial monitor.

## Slide 225: MCP 41xxx – DIGITAL POTENTIOMETER - CODE
https://www.arduino.cc/en/Reference/SPISettings
The SPISettings object is used to configure the SPI port for your SPI device.
All 3 parameters are combined to a single SPISettings object, which is given to SPI.beginTransaction().
Parameters
1 - speedMaximum: The maximum speed of communication. For a SPI chip rated up to 20 MHz, use 20000000.
2 - dataOrder: MSBFIRST or LSBFIRST
3 - dataMode : SPI_MODE0, SPI_MODE1, SPI_MODE2, or SPI_MODE3
Note: the integrated has in its interior an EEPROM memory that will serve to store the last position of the potentiometer, that is to say if we turn off our device and we turn it on again, it will have to maintain the last level of set resistance.

## Slide 226: MCP 41xxx – DIGITAL POTENTIOMETER - CODE

## Slide 227: MCP 41xxx – DIGITAL POTENTIOMETER - CODE
Multimeter
The code below is an example of how this is done. In this simple example the pot setting register is ramped through the 255 steps with a pause in between each so that the multimeter readings could be observed.

## Slide 228: MCP 41xxx – DIGITAL POTENTIOMETER – CODE RHEOSTAT MODE
Multimeter

<= RETOUR

## Slide 229: I - LES MICROCONTROLEURS
TP4-G

## Slide 230: TP4-G DECOUVRIR LES INFORMATIONS DU DISPOSITIF MYSTERE
Dans ce TP, nous vous donnons un composant mystère (U6A) qui contient des informations très importantes.
Votre mission, si vous l’acceptez:
découvrir les informations contenues dans ce composant (fourni en version DIP 8 broches)
Vous n’aurez pour cela besoin que :
- de mobiliser vos compétences en électronique et informatique,
- d’un peu de matériel (voltmètre, oscilloscope, et …
- pourquoi pas d’une source d’information : internet
A vous de jouer les détectives et de découvrir les informations cachées !!!
<= RETOUR

## Slide 231: BLIND DEVICE
Attention sur la carte PCB : PE et ORG sont sur la masse !

## Slide 232
1 – Vérifier l’alimentation:
page 3: recommended operating ranges shown below unless otherwise noted:
VCC = +2.5V to +6.0V
2 – Vérifier le pin Out :
CS, CLK, DI, DO => SPI interface
ORG : page 1:
Attention sur la carte PCB : ORG est sur la masse
CONCLUSION: 8K
CONCLUSION: SPI INTERFACE

## Slide 233
CONCLUSION:
PROGRAMMING INHIBITED
=> READ ONLY
Attention sur la carte PCB : PE est sur la masse

## Slide 234
On veut la READ command:
1 - qui sortira D0 à D7,
digitalWrite(CS, HIGH); // sélectionne le chip
word instruction = 0b1100000000000;
Protocole:
DI goes High puis CS goes high:
Un bit de Start SB
Un opcode : READ => 10
11 bits d’adresses : A0 à A10
D0 passe à low => 8 bits de données
Deux bits 1 et un 0 puis les 11 bits d’adresses
=> Word 0b1100000000000;

## Slide 235
Instructions, addresses
and write data are clocked into the DI pin on the rising
edge of the clock (CLK).
SB

## Slide 236
3.1 READ
The READ instruction outputs the serial data of the
addressed memory location on the DO pin. A dummy
zero bit precedes the 16-bit (x16 organization) or 8-bit
(x8 organization) output string. The output data bits will
toggle on the rising edge of the CLK and are stable
after the specified time delay (TPD). Sequential read is
possible when CS is held high and clock transitions
continue. The memory Address Pointer will
automatically increment and output data sequentially.

## Slide 237: Instruction READ sur ADRESSE 0

## Slide 238: Instruction READ sur les 2048 ADRESSES

## Slide 239: Instructions READ sur les 2048 ADRESSES façon fichier .bin

## Slide 240: THE SPI APPLICATION: TOWARDS THE FPGA
Gameduino is an Arduino with a controller graphics and sound shield type FPGA Xilinx.
His control is done by the SPI bus.
The code is used to send orders to the card to manage records toggle, memory and graphics functions.
The data is then managed by the Xilinx FPGA that allows:
video output is 400x300 pixels in 512 colors
all color processed internally at 15-bit precision
compatible with any standard VGA monitor (800x600 @ 72Hz)
background graphics
  512x512 pixel character background
  256 characters, each with independent 4 color palette
  pixel-smooth X-Y wraparound scroll
foreground graphics
  each sprite is 16x16 pixels with per-pixel transparency
  each sprite can use 256, 16 or 4 colors
  four-way rotate and flip
  pixel-perfect sprite collision detection
audio output is a stereo 12-bit frequency synthesizer
64 independent voices 10-8000 Hz
per-voice sine wave or white noise
sample playback channel
http://excamera.com/sphinx/gameduino/

## Slide 241: THE SPI APPLICATION: TOWARDS THE FPGA
http://www.xilinx.com/support/documentation/application_notes/xapp974.pdf

## Slide 242: THE SPI APPLICATION: TOWARDS THE FPGA
http://www.xilinx.com/support/documentation/data_sheets/ds529.pdf

## Slide 243: GAMEDUINO REFERENCE

## Slide 244: GAMEDUINO REFERENCE

## Slide 245: SPRITES
http://en.wikipedia.org/wiki/Sprite_%28computer_graphics%29#Hardware_sprites
In early video games, 'hardware' sprites were a method for managing bitmaps pretending to be part of a single image on a screen.

## Slide 246: BUS SPI PROS & CONS
PROS:
Full duplex Communication
enough throughput compared to I²C
flexibility of the number of bits to transmit
simplicity of the hardware interface
no need referee because no possible collision
slaves use the clock of the master and therefore did not need precision oscillator
sharing a common bus for the clock, MISO and MOSI between slave devices
have no need a unique ID unlike the I²C, the GPIB and SCSI
CONS:
Needs more legs of a case than the I2C or a UART which use only two.
no address Possible, but a line of selection by slave mode not chained. -
The Protocol has no acknowledgement. The master can talk in a vacuum without knowing.
There may be only one master on the bus.
Use on short distances unlike protocols RS-232, RS-485 or CAN bus

## Slide 247: SYNCHRONOUS SERIAL COMMUNICATION : I2C, SPI, ONE WIRE, …
SYNCHRONOUS SERIAL
COMMUNICATION : ONE-WIRE

## Slide 248: OTHER PROTOCOLS: ONE WIRE...
2. ONE WIRE created by Dallas (now called company MAXIM)
"One Wire" technology is a serial communication bus allowing the addressing and the use of several sensors in communication series on a single digital PIN.
Data bus synchronous series using only a single thread (+ 1 mass of potential reference).
Allows you to transmit data in both directions, each component can be transmitter and receiver at all moment.
But it also allows to feed (parasite power mode) for the less greedy!
The management of the bus ONE WIRE is easy because the Arduino contains a third-party library named: OneWire.h (author: Jim Studt)
http://www.milesburton.com/?title=Dallas_Temperature_Control_Library
http://www.arduino.cc/playground/Learning/OneWire

## Slide 249: SYNCHRONOUS SERIAL COMMUNICATION : I2C, SPI, ONE WIRE, …
SYNCHRONOUS SERIAL
COMMUNICATION :
A COMPARISON

## Slide 250
Bus One Wire :
The One Wire technology is comparable to the I2C technology (and better?).
COMPARISON OF PROTOCOLS: I2C/SPI/ONE WIRE

## Slide 251: COMPARISON OF PROTOCOLS: I2C/SPI/ONE WIRE
Whether to interconnect several boxes and speed is not a problem, prefer the I2C because it is a Protocol (which is not the case of the SPI)
If you want to speed the SPI is far ahead...
Software implementation on I/O : it is much easier (and it takes less resources) to the SPI by software on I/O pins of the I2C due to the state machine.
Implementation: the I2C is more complicated to implement (just see the number of questions on the I2C in forums...).
The interconnection of several boxes is also more delicate with the I2C because it takes into account the impedances of each of the boxes to calculate resistances of reminders.
Although there are variations of the I2C rising above 1 MHz, the vast majority of implementations use generally 100 or 400 kHz
For the SPI it is possible to find some components beyond 20 Mbits
I2C Transmission Speed SPI
I2C Topology SPI
It's a real protocol that allows the interconnection of multiple boxes in different configurations: slave /master, master/Multiple slaves, Multiple masters/multiple slaves
Generally point-to-point, you can connect several slave but must then have additional lines. A single master which generates the clock.
I2C Consomption SPI
the collector configuration / drain opened on the 2 lines of transmission (SDA + SCL), relatively high consumption
TTL/CMOS signal => low consomption
Pros / Cons
Bus One Wire :
The One Wire technology is comparable to the I2C technology (and better?).

## Slide 252: COMPARISON OF PROTOCOLS: I2C/SPI/ONE WIRE
Bus I2C - Inter Integrated Circuit:
Mainly developed for home automation and home electronics, this Protocol is very popular and used by many components.
The I2C Protocol requires only a 3-wire to operate and can be implemented on any microcontroller. Supports several masters (so collision)
Bus SPI - Serial Peripheral Interface:
The SPI bus is Full Duplex and based on master-slave communication.
The SPI bus supports multiple slaves but one can communicate both with the master (so selection logic!)
Bus One Wire :
La technologie One Wire est une technologie comparable à la technologie I2C (en mieux ?).

## Slide 253: EXAMPLE OF APPLICATION OF THE SERIAL COMMUNICATION
“Hacking Roomba”, out in a few weeks, http://hackingroomba.com/
Lantronix Wi-Port and Lantronix Xport http://lantronix.com/
Seetron Serial Graphic display and Mini SSC http://www.seetron.com/slcds.htm http://www.seetron.com/ssc.htm

## Slide 254
III – 8 LIBRAIRIES

## Slide 255
III – 8-1 LIBRAIRIE EXAMPLES

## Slide 256: EEPROM LIBRARY
The ATMEGA of Arduino has an EEPROM: memory whose values are retained when the map is off:
- 512 bytes on ATmega168,
- 1024 bytes (1 Ko) on ATmega328,
4096 bytes (4 Ko) on ATmega8,
The EEPROM library allows you to read and write these bytes:
#include <EEPROM.h>
int a = 0;
int value;
void setup()
{
Serial.begin(9600);
}
void loop()
{
value = EEPROM.read(a);
Serial.print(a);Serial.print("\t");
Serial.print(value);
Serial.println();
a = a + 1;
if (a == 512)
a = 0;
delay(500);
}
#include <EEPROM.h>
void setup()
{
for (int i = 0; i < 512; i++)
EEPROM.write(i, i);
}
void loop() {
}
Writing example
Reading example
Syntax
EEPROM.write(address, value)
Note: a writing EEPROM takes 3.3 ms. EEPROM memory has a specified life of 100,000 write/erase cycles. Be careful in the way we use it.
Syntax
EEPROM.read(address)
/* EEPROM Clear: Sets all of the bytes of the EEPROM to 0.*/
#include <EEPROM.h>
void setup()
{
// write a 0 to all 512 bytes of the EEPROM
for (int i = 0; i < 512; i++) EEPROM.write(i, 0);
}
void loop() {
}

## Slide 257
III – 8 - 2 CREATE A LIBRAIRY

## Slide 258: TO GO FURTHER – GOOD PRACTICES - 1
When you start to make big projects, it becomes useful or even essential to (very) well organize his code:
separate your code into different files in order to have separate logical entities from each other.
Generally, we do files by logic units.
In practice: to create a new file in the Arduino IDE, simply click on the small arrow at the top of the editing of the code space and then click on "New tab" as highlighted in the screenshot below:
Attention, whenever you want to create a new code file we will not create one but two!
1 - The file. h: the first file will have the extension .h meaning header. This file will regroup the prototypes of the functions as well as the definitions of structures or classes but we'll cover that later.
Prototype of a function: sets the name of the function, what goes inside (parameters) and what comes out (the return variable). So your main program will have an idea of how your function works outside.
char getHeure(); char getMinute(); char getSeconde();
char getJour(); char getMois();
char getAnnee(); void setHeure(char val);
void setMinute(char val); void setSeconde(char val);
void setJour(char val); void setMois(char val);
void setAnnee(char val); void afficherDate();
void afficherHeure(); void afficherDateHeure();
Example: Let’s imagine a file for RTC clock managing : horloge.h
As you can see, with these definitions we can know what is supposed to do the service through its name and the type of variable it handles input and output.

## Slide 259: TO GO FURTHER – GOOD PRACTICES - 2
3 - Link our files to the main program:
1 - Please make sure that your .h and .cpp files are in the same folder as your .ino
2 - include the at the top of your file's .h file: #include "horloge.h"
4 - Use:
you can now make simple calls to your custom functions in the program (setup(), loop() functions...!).
Now, when you compile, the compiler will fetch the file pointed by the include, compile it, then link it in your main program.
Remark1: it can happen that the connection with the symbols/library Arduino does not correctly. In this case, add the following at the beginning of your .h or .cpp include: #include "Arduino.h"
Remark2: with this technique: you can code in C++ to create classes and thus push the Organization even further!
2 - The second file .cpp:
it is used to implement the functions defined in the .h, i.e. write the content of your functions,
First step: include file prototypes via the #include preprocessor command:
For example:
#include "horloge.h" / / horloge.h for our example
Attention: this line should be the first of your .cpp file and it does not; at the end.
/* fichier horloge.cpp */
#include "horloge.h"
char getHeure() { Serial.println("getHeure"); return 0; }
char getMinute() { Serial.println("getHeure"); return 0; }
char getSeconde() { Serial.println("getHeure"); return 0; }
char getJour() { Serial.println("getHeure"); return 0; }
char getMois() { Serial.println("getHeure"); return 0; }
char getAnnee() { Serial.println("getHeure"); return 0; }
void setHeure(char val) { Serial.print("setHeure : "); Serial.println(val, DEC); }
void setMinute(char val) { Serial.print("setMinute : "); Serial.println(val, DEC); } void setSeconde(char val) { Serial.print("setSeconde : "); Serial.println(val, DEC); } void setJour(char val) { Serial.print("setJour : "); Serial.println(val, DEC); }
void setMois(char val) { Serial.print("setMois : "); Serial.println(val, DEC); }
void setAnnee(char val) { Serial.print("setAnnee : "); Serial.println(val, DEC); }
void afficherDate() { Serial.println("afficherDate"); }
void afficherHeure() { Serial.println("afficherHeure"); }
void afficherDateHeure() { Serial.println("afficherDateHeure"); }
Functions code:

## Slide 260: I - LES MICROCONTROLEURS
TP5-A
<= RETOUR

## Slide 261: CREATE AN ARDUINO LIBRARY - 1
- Creation of custom libraries to simplify the reuse of code.
- Many libraries are already present and integrated to the Arduino software.
- They allow you to program faster and more simply your systems.
We will see how to create a library through a concrete example: the Morse library.
Example from the official tutorial of creation of library: http://arduino.cc/en/Hacking/LibraryTutorial
Caution: Library is a false friend. The French translation is Bibliothèque not library.
Let's look at the code: the parts of the code that we will put in our new library are clearly
pinMode (pin, OUTPUT)
and dot() and dash() functions.
Now let's see how to create a library, e.g. Morse.

## Slide 262: CREATE AN ARDUINO LIBRARY - 2
STRUCTURE of a library: Arduino libraries are composed of at least 2 files:
a header file ending by .h (which contains the definitions of the functions available)
a source file ending with .cpp (which contains the implementation of the code, i.e. the code inside the functions that have been defined in the header file).
Header file (.h): in our case Morse.h
Contains all of the declarations of the methods of the Morse class that will represent the library.
Before the declaration of the class, you must ensure that the file of head will not be victim of infinite inclusion.
So as usual in C, we add a protection with preprocessor directives (e.g. #ifndef...).
To use the constants or functions as a part of the Arduino core, add an include before the declaration of the class =>
We also add a private property (private): _pin which will contain the number of LEDs to use pin.
In this way, during initialization of the Morse object, we can both put pin in OUTPUT mode and store it for not having to give it back when it will make a call to another method.
So now we can tackle the class declaration. What gives the final =>

## Slide 263: CREATE AN ARDUINO LIBRARY - 3
The source (.cpp) file: in our case Morse.cpp.
The source file contains the implementation of the methods described in the header file.
So there was this code =>
Use the library in the IDE: from now on you can see the library in the IDE in the Sketch menu > Import Library if you restart it:
Install the library:
Arduino in the software folder is a subfolder named "libraries" where each subfolder represents a library.
To add ours, we create a folder on the behalf of our library: e.g. "Morse" folder
and put the two files Morse.h and Morse.cpp.

## Slide 264: CREATE AN ARDUINO LIBRARY - 4
Click on the ‘MORSE' menu item, which will add the necessary code to use your library in Arduino:
#include <Morse.h>
FINAL RESULT:
Thanks to the library, you can now simplify our initial code. This allows us to have this code =>
-this code, of course, has the same effect as the code of the start.
The creation of the library is now ended.
Abuse of this feature to simplify your code.
Creating libraries ensures the logic of your code and decreases the time of future development.
In addition, you can share libraries to benefit the community !
<= BACK

## Slide 265: REFERENCE ARDUINO – GUIDE LINE LIBRARIES
Arduino Style Guide for Writing Libraries
This is a style guide to writing library APIs in an Arduino style. Some of these run counter to professional programming practice. We’re aware of that, but it’s what’s made it possible for so many beginners to get started with Arduino easily. So please code with these principles in mind. If you have suggestions on how to make Arduino libraries clearer for that core audience, please jump in the discussion. This is a work in progress.
Be kind to the end user. Assume you are writing an API for an intelligent person who has not programmed before. Come up with a clear mental model of the concept you’re working with, and the terms and functions you will use.
Match your API to the underlying capabilities. You don’t want to expose implementation details to the user but you also don’t want an API that suggests an inaccurate mental model of the possibilities. For example, if there are only a few possible options for a particular setting, don’t use a function that takes an int, as it implies you can use any value you want.
Organize your public functions around the data and functionality that the user wants. Quite often, the command set for a particular electronic module is overly complicated for the most common uses, or can be re-organized around higher level functionality. Think about what the average person thinks the thing does, and try to organise your API functions around that. Adafruit's BMP085 library is a good example. The readPressure() command performs all the necessary steps to get the final pressure. The library wraps this commonly executed series of functions into a high-level single command which returns the value the user's looking for in a format she expects. It abstracts away not only the low-level I2C commands, but also the mid-level temperature and pressure calculations, while still offering those mid-level functions as public functions for those who want them.
Don’t assume knowledge of pointers. Beginning users of C find this the biggest roadblock, and get very confused by & and *, so whenever you can avoid having them hanging out in the API, do so. One way is to pass by reference using array notation rather than * notation, for example.
void printArray( char* array);
can be replaced by
void printArray(char[] array);
Though there are some libraries where we pass pointers by using structures like const chars, avoid anything that requires the user to pass them. For example,rather than:
foo.readAccel(&x, &y, &z);
use something like this:
xAxis = adxl.readX();
yAxis = adxl.readY();
zAxis = adxl.readZ();
https://www.arduino.cc/en/Reference/APIStyleGuide

## Slide 266: III-9 THE SHIELDS & THEIR CREATION
III-9 THE SHIELDS & THEIR CREATION

## Slide 267: INTERFACE BOARD or SHIELDS
One of the major interests of the Arduino is there today on the market, a variety of interface cards (~ 300), called Shields, able to cover most of the needs of an application.
These shields neighboring dimensions of the Arduino to plug directly on the peripheral connectors of this last. They follow the same philosophy as Arduino: easy to set up and inexpensive to produce.
There are many shields between 15 and 30€ that add interesting features:
Ethernet
GPS
Wireless transmissions (Xbee, LoRa…),
interfaces graphic LCD color, monochrome, or text,
keyboard
Game shield
arrays of leds...
http://shieldlist.org/

## Slide 268: EXAMPLE
http://fritzing.org/projects/arduino-lcd-4-push-buttons/
Example: 4 buttons LCD
Fritzing can draw its way graphic, schematic, or electronic circuit
OPEN-SOURCE SOFTWARE:
ExpressPCB: http://www.expresspcb.com/
Fritzing: http://fritzing.org/
KiCAd: http://www.lis.inpg.fr/realise_au_lis/kicad/
TCI:http://b.urbani.free.fr/pagetci/tci.htm

## Slide 269: KiCad EDA
<= RETOUR

## Slide 270: KiCad EDA
NGSPICE simulation with KiCAD

## Slide 271: PRECAUTIONS: SHIELD STANDARDISATION
Design a shield requires a standardization that will make the whole system more modular and open up new fields of opportunity for the Arduino.
The idea is simple: when designing a shield, some logic must be respected
The following are guidelines for the assignment of pins in the design of a shield.
Pin | Reserved For
Analog 0 | User Selectable Input
Analog 1 | User Selectable Input
Analog 2 | User Selectable Input
Analog 3 | User Selectable Input
Analog 4 | I2C
Analog 5 | I2C
Digital 0 | RX
Digital 1 | TX
Digital 2 | Onewire
Digital 3 | PWM / Digital I/O / I2C Interrupt
Digital 4 | CS Select
Digital 5 | PWM / Digital I/O
Digital 6 | PWM / Digital I/O
Digital 7 | CS Select
Digital 8 | CS Select
Digital 9 | PWM / Digital I/O
Digital 10 | PWM / Digital I/O
Digital 11 | SPI
Digital 12 | SPI
Digital 13 | SPI
CREATE YOUR SHIELDS :
http://aaroneiche.com/2010/06/24/a-beginners-guide-to-making-an-arduino-shield-pcb/
http://www.krisbarrett.com/2008/09/03/make-a-custom-arduino-shield/
SHIELDS STANDARDISATION :
http://www.practicalarduino.com/news/id/661
http://www.practicalmaker.com/blog/arduino-shield-design-standards

## Slide 272: INTERACTING !!!
IV-1 INTERACTING WITH OTHER APPLICATIONS

## Slide 273
IV-1 PROCESSING

## Slide 274: PROCESSING
"PROCESSING" makes the JAVA programming as fun and easy as the AVR with the Arduino programming
-It is used to connect the Arduino to the PC
-It is completely OPEN-SOURCE like the Arduino
http://processing.org/learning/gettingstarted/
http://wiki.processing.org/w/Main_Page
http://www.ecole-art-aix.fr/rubrique.php?id_rubrique=81
Processing sketches are very similar to the Arduino
• setup() – sketch establishment
• draw() - like loop() in Arduino (called permanently)
• other features are based on libraries

## Slide 275: PROCESSING
Download and Install PROCESSING:
1 – Load TOPICS/MOTION/BOUNCE example
2 – Press RUN
=> you just created a JAVA applet
http://processing.org/download/
/** Bounce.
* When the shape hits the edge of the window, it reverses its direction.
*/
int size = 60; // Width of the shape
float xpos, ypos; // Starting position of shape
float xspeed = 2.8; // Speed of the shape
float yspeed = 2.2; // Speed of the shape
int xdirection = 1; // Left or Right
int ydirection = 1; // Top to Bottom
void setup()
{
size(640, 200);
noStroke();
frameRate(30);
smooth();
// Set the starting position of the shape
xpos = width/2;
ypos = height/2;
}
void draw()
{
background(102);
// Update the position of the shape
xpos = xpos + ( xspeed * xdirection );
ypos = ypos + ( yspeed * ydirection );
// Test to see if the shape exceeds the boundaries of the screen
// If it does, reverse its direction by multiplying by -1
if (xpos > width-size || xpos < 0) {
xdirection *= -1;
}
if (ypos > height-size || ypos < 0) {
ydirection *= -1;
}
// Draw the shape
ellipse(xpos+size/2, ypos+size/2, size, size);
}

## Slide 276: PROCESSING & ARDUINO: SERIAL COMMUNICATION
• Processing and Arduino talking both the "series"
• but, one program possible by serial port:
thus, close the Arduino monitor series when you connect via Processing, and vice versa.
• Processing has a library "Series" to talk to Arduino:
port = new Serial(this,“mon_nom_port”,19200)
port.read(), port.write(), port.available(), etc.
serialEvent() { }
Make sure you put the good name of serial port!
4 steps:
1 - load the library
2. Set the name of the port: portname
3. Open port: port = new Serial (...); 4. read/write on port

## Slide 277: ARDUINO SPEAKS PROCESSING
/* PotSend
* Send analog values from pots or similar over the serial port
* Also see: http://www.arduino.cc/en/Tutorial/Graph
*/
int potPin = 2;
void setup() {
Serial.begin(19200);
}
void loop() {
int val = analogRead(potPin);
val = val/4;
Serial.print(val,BYTE);
delay(100);
}
Arduino Sketch:
Create an Arduino program that reads the value of a potentiometer and sends it to Processing in the form of a number between 0 and 255:
Note: do not send the value as ASCII text, but rather as a binary number (the BYTE are easier to handle in Processing)
<= RETOUR

## Slide 278: I - LES MICROCONTROLEURS
TP5-B

## Slide 279: ARDUINO & PROCESSING: PONG
/** Collision (Pong).
* Move the mouse up and down to move the paddle.
* Modified to use Serial port by Tod E. Kurt, 2007
* Updated 13 January 2003 by K Pfeiffer
*/
import processing.serial.*;
String portname = "/dev/tty.usbserial-A4001qa8"; // or "COM8"
Serial port; // Create object from Serial class
// Global variables for the ball
float ball_x;
float ball_y;
float ball_dir = 1;
float ball_size = 5; // Radius
float dy = 0; // Direction
// Global variables for the paddle
int paddle_width = 5;
int paddle_height = 20;
int paddle_pos; // new position
int paddle_ppos; // last position
int dist_wall = 15;
void setup()
{
size(255, 255);
rectMode(CENTER_RADIUS);
ellipseMode(CENTER_RADIUS);
noStroke();
smooth();
ball_y = height/2;
ball_x = 1;
// Open the port that the board is connected to and use the same speed (19200 bps)
port = new Serial(this, portname, 19200);
}
void draw()
{
background(51);
ball_x += ball_dir * 1.0;
ball_y += dy;
if(ball_x > width+ball_size) {
ball_x = -width/2 - ball_size;
ball_y = random(0, height);
dy = 0;
}
if (port.available() > 0) { // If data is available,
paddle_ppos = paddle_pos; // save old position
paddle_pos = port.read(); // read it and store it as the new pos
paddle_pos = paddle_pos *2; //pour avoir les valeurs de 0 à 255
println(paddle_pos);
}
// Constrain paddle to screen
float paddle_y = constrain(paddle_pos, paddle_height, height-paddle_height);
// Test to see if the ball is touching the paddle
float py = width-dist_wall-paddle_width-ball_size;
if(ball_x == py
&& ball_y > paddle_y - paddle_height - ball_size
&& ball_y < paddle_y + paddle_height + ball_size) {
ball_dir *= -1;
if(paddle_pos != paddle_ppos) {
dy = (paddle_pos - paddle_ppos)/2.0;
if(dy > 5) { dy = 5; }
if(dy < -5) { dy = -5; }
}
}
// If ball hits paddle or back wall, reverse direction
if(ball_x < ball_size && ball_dir == -1) {
ball_dir *= -1;
}
// If the ball is touching top or bottom edge, reverse direction
if(ball_y > height-ball_size) {
dy = dy * -1;
}
if(ball_y < ball_size) {
dy = dy * -1;
}
// Draw ball
fill(255);
ellipse(ball_x, ball_y, ball_size, ball_size);
// Draw the paddle
fill(153);
rect(width-dist_wall, paddle_y, paddle_width, paddle_height);
}
The basic game of pong
the potentiometer controls the position of the racket
=> add a potentiometer and a few lines of code and you will have a two-player game
<= RETOUR
http://moodle.insa-toulouse.fr/course/view.php?id=494

## Slide 280: ARDUINO & PROCESSING: Wii Nunchuk & CUBE 3D (EXAMPLE 2)
#include <math.h>
#include "Wire.h"
#include "WiiChuck.h"
//#include "nunchuck_funcs.h"
#define MAXANGLE 90
#define MINANGLE -90
WiiChuck chuck = WiiChuck();
int angleStart, currentAngle;
int tillerStart = 0;
double angle;
void setup() {
//nunchuck_init();
Serial.begin(115200);
chuck.begin();
chuck.update();
//chuck.calibrateJoy();
}
void loop() {
delay(20);
chuck.update();
Serial.print(chuck.readRoll());
Serial.print(", ");
Serial.print(chuck.readPitch());
Serial.print(", ");
Serial.print((int)chuck.readAccelX());
Serial.print(", ");
Serial.print((int)chuck.readAccelY());
Serial.print(", ");
Serial.print((int)chuck.readAccelZ());
Serial.println();
}
Sketch ARDUINO:
http://arduino.cc/playground/Main/WiiChuckClass

## Slide 281: ARDUINO & PROCESSING: Wii Nunchuk & CUBE 3D (EXAMPLE 2)
Call WiiChuck.h:
void begin()
{
Wire.begin();
cnt = 0;
averageCounter = 0;
// instead of the common 0x40 -> 0x00 initialization, we
// use 0xF0 -> 0x55 followed by 0xFB -> 0x00.
// this lets us use 3rd party nunchucks (like cheap $4 ebay ones)
// while still letting us use official oness.
// only side effect is that we no longer need to decode bytes in _nunchuk_decode_byte
// see http://www.arduino.cc/cgi-bin/yabb2/YaBB.pl?num=1264805255
//
Wire.beginTransmission(0x52); // device address
Wire.send(0xF0);
Wire.send(0x55);
Wire.endTransmission();
delay(1);
Wire.beginTransmission(0x52);
Wire.send(0xFB);
Wire.send(0x00);
Wire.endTransmission();
update();
for (i = 0; i<3;i++) {
angles[i] = 0;
}
zeroJoyX = DEFAULT_ZERO_JOY_X;
zeroJoyY = DEFAULT_ZERO_JOY_Y;
}
void calibrateJoy() {
zeroJoyX = joyX;
zeroJoyY = joyY;
}
void update() {
Wire.requestFrom (0x52, 6); // request data from nunchuck
while (Wire.available ()) {
// receive byte as an integer
status[cnt] = _nunchuk_decode_byte (Wire.receive()); //
cnt++;
}
if (cnt > 5) {
lastZ = buttonZ;
lastC = buttonC;
lastJoyX = readJoyX();
lastJoyY = readJoyY();
//averageCounter ++;
//if (averageCounter >= AVERAGE_N)
// averageCounter = 0;
cnt = 0;
joyX = (status[0]);
joyY = (status[1]);
for (i = 0; i < 3; i++)
//accelArray[i][averageCounter] = ((int)status[i+2] << 2) + ((status[5] & (B00000011 << ((i+1)*2) ) >> ((i+1)*2)));
angles[i] = (status[i+2] << 2) + ((status[5] & (B00000011 << ((i+1)*2) ) >> ((i+1)*2)));
//accelYArray[averageCounter] = ((int)status[3] << 2) + ((status[5] & B00110000) >> 4);
//accelZArray[averageCounter] = ((int)status[4] << 2) + ((status[5] & B11000000) >> 6);
buttonZ = !( status[5] & B00000001);
buttonC = !((status[5] & B00000010) >> 1);
_send_zero(); // send the request for next bytes
}
}
/* Nunchuck -- Use a Wii Nunchuck * Tim Hirzel http://www.growdown.com *
notes on Wii Nunchuck Behavior.
This library provides an improved derivation of rotation angles from the nunchuck accelerometer data. The biggest different over existing libraries (that I know of ) is the full 360 degrees of Roll data
from the combination of the x and z axis accelerometer data using the math library atan2.
It is accurate with 360 degrees of roll (rotation around axis coming out of the c button, the front of the wii), and about 180 degrees of pitch (rotation about the axis coming out of the side of the wii). (read more below)
In terms of mapping the wii position to angles, its important to note that while the Nunchuck
sense Pitch, and Roll, it does not sense Yaw, or the compass direction. This creates an important
disparity where the nunchuck only works within one hemisphere. At a result, when the pitch values are less than about 10, and greater than about 170, the Roll data gets very unstable. essentially, the roll data flips over 180 degrees very quickly. To understand this property better, rotate the wii around the axis of the joystick. You see the sensor data stays constant (with noise). Because of this, it cant know the difference between arriving upside via 180 degree Roll, or 180 degree pitch. It just assumes its always 180 roll. *
* This file is an adaptation of the code by these authors:
* Tod E. Kurt, http://todbot.com/blog/
* The Wii Nunchuck reading code is taken from Windmeadow Labs
* http://www.windmeadow.com/node/42
*/
#ifndef WiiChuck_h
#define WiiChuck_h
#include "WProgram.h"
#include <Wire.h>
#include <math.h>
// these may need to be adjusted for each nunchuck for calibration
#define ZEROX 510
#define ZEROY 490
#define ZEROZ 460
#define RADIUS 210 // probably pretty universal
#define DEFAULT_ZERO_JOY_X 124
#define DEFAULT_ZERO_JOY_Y 132
class WiiChuck {
private:
byte cnt;
uint8_t status[6]; // array to store wiichuck output
byte averageCounter;
//int accelArray[3][AVERAGE_N]; // X,Y,Z
int i;
int total;
uint8_t zeroJoyX; // these are about where mine are
uint8_t zeroJoyY; // use calibrateJoy when the stick is at zero to correct
int lastJoyX;
int lastJoyY;
int angles[3];
boolean lastZ, lastC;
public:
byte joyX;
byte joyY;
boolean buttonZ;
boolean buttonC;
// UNCOMMENT FOR DEBUGGING
//byte * getStatus() {
// return status; //}
float readAccelX() {
// total = 0; // accelArray[xyz][averageCounter] * FAST_WEIGHT;
return (float)angles[0] – ZEROX; }
float readAccelY() {
// total = 0; // accelArray[xyz][averageCounter] * FAST_WEIGHT;
return (float)angles[1] - ZEROY; }
float readAccelZ() {
// total = 0; // accelArray[xyz][averageCounter] * FAST_WEIGHT;
return (float)angles[2] - ZEROZ; }
boolean zPressed() {
return (buttonZ && ! lastZ); }
boolean cPressed() {
return (buttonC && ! lastC); }
// for using the joystick like a directional button
boolean rightJoy(int thresh=60) {
return (readJoyX() > thresh and lastJoyX <= thresh); }
// for using the joystick like a directional button
boolean leftJoy(int thresh=60) {
return (readJoyX() < -thresh and lastJoyX >= -thresh); }
int readJoyX() {
return (int) joyX - zeroJoyX; }
int readJoyY() {
return (int)joyY - zeroJoyY; }
// R, the radius, generally hovers around 210 (at least it does with mine)
// int R() {
// return sqrt(readAccelX() * readAccelX() +readAccelY() * readAccelY() + readAccelZ() * readAccelZ());
// }
// returns roll degrees
int readRoll() {
return (int)(atan2(readAccelX(),readAccelZ())/ M_PI * 180.0); }
// returns pitch in degrees
int readPitch() {
return (int) (acos(readAccelY()/RADIUS)/ M_PI * 180.0); // optionally swap 'RADIUS' for 'R()'
}
private:
byte _nunchuk_decode_byte (byte x)
{
//decode is only necessary with certain initializations
//x = (x ^ 0x17) + 0x17;
return x; }
void _send_zero()
{
Wire.beginTransmission (0x52); // transmit to device 0x52
Wire.send (0x00); // sends one byte
Wire.endTransmission (); // stop transmitting
}
};
#endif

## Slide 282: ARDUINO & PROCESSING: Wii Nunchuk & CUBE 3D (EXAMPLE 2)
/**
* Wii controlled
* RGB Cube.
* The three primary colors of the additive color model are red, green, and blue.
* This RGB color cube displays smooth transitions between these colors.
*/
float xmag, ymag = 0;
float newXmag, newYmag = 0;
int sensorCount = 5; // number of values to expect
import processing.serial.*;
Serial myPort; // The serial port
int BAUDRATE = 115200;
char DELIM = ','; // the delimeter for parsing incoming data
void setup()
{
size(200, 200, P3D);
noStroke();
colorMode(RGB, 1);
// Affiche la liste des ports série
println(Serial.list());
//myPort = new Serial(this, Serial.list()[0], BAUDRATE);
//affecte la bonne valeur au tableau Serial.list
myPort = new Serial(this, Serial.list()[1], BAUDRATE);
// clear the serial buffer:
myPort.clear();
}
float x, z;
void draw()
{
background(0.5, 0.5, 0.45);
pushMatrix();
translate(width/2, height/2, -30);
newXmag = mouseX/float(width) * TWO_PI;
newYmag = mouseY/float(height) * TWO_PI;
float diff = xmag-newXmag;
if (abs(diff) > 0.01) {
xmag -= diff/4.0;
}
diff = ymag-newYmag;
if (abs(diff) > 0.01) {
ymag -= diff/4.0;
}
// if ((sensorValues[1] > 15) && (sensorValues[1] < 165)) {
z = sensorValues[0] / 180 * PI ;
x = sensorValues[1] / 180 * PI;
// }
rotateZ(z);
rotateX(x);
scale(50);
beginShape(QUADS);
fill(0, 1, 1);
vertex(-1, 1, 1);
fill(1, 1, 1);
vertex( 1, 1, 1);
fill(1, 0, 1);
vertex( 1, -1, 1);
fill(0, 0, 1);
vertex(-1, -1, 1);
fill(1, 1, 1);
vertex( 1, 1, 1);
fill(1, 1, 0);
vertex( 1, 1, -1);
fill(1, 0, 0);
vertex( 1, -1, -1);
fill(1, 0, 1);
vertex( 1, -1, 1);
fill(1, 1, 0);
vertex( 1, 1, -1);
fill(0, 1, 0);
vertex(-1, 1, -1);
fill(0, 0, 0);
vertex(-1, -1, -1);
fill(1, 0, 0);
vertex( 1, -1, -1);
fill(0, 1, 0);
vertex(-1, 1, -1);
fill(0, 1, 1);
vertex(-1, 1, 1);
fill(0, 0, 1);
vertex(-1, -1, 1);
fill(0, 0, 0);
vertex(-1, -1, -1);
fill(0, 1, 0);
vertex(-1, 1, -1);
fill(1, 1, 0);
vertex( 1, 1, -1);
fill(1, 1, 1);
vertex( 1, 1, 1);
fill(0, 1, 1);
vertex(-1, 1, 1);
fill(0, 0, 0);
vertex(-1, -1, -1);
fill(1, 0, 0);
vertex( 1, -1, -1);
fill(1, 0, 1);
vertex( 1, -1, 1);
fill(0, 0, 1);
vertex(-1, -1, 1);
endShape();
popMatrix();
}
float[] sensorValues = new float[sensorCount]; // array to hold the incoming values
void serialEvent(Serial myPort) {
// read incoming data until you get a newline:
String serialString = myPort.readStringUntil('\n');
// if the read data is a real string, parse it:
if (serialString != null) {
//println(serialString);
//println(serialString.charAt(serialString.length()-3));
// println(serialString.charAt(serialString.length()-2));
// split it into substrings on the DELIM character:
String[] numbers = split(serialString, DELIM);
// convert each subastring into an int
if (numbers.length == sensorCount) {
for (int i = 0; i < numbers.length; i++) {
// make sure you're only reading as many numbers as
// you can fit in the array:
if (i <= sensorCount) {
// trim off any whitespace from the substring:
numbers[i] = trim(numbers[i]);
sensorValues[i] = float(numbers[i]);
}
// Things we don't handle in particular can get output to the text window
print(serialString);
}
}
}
}
http://arduino.cc/playground/Main/WiiChuckClass
Sketch PROCESSING:

## Slide 283
IV-2 ANDROID

## Slide 284: PROCESSING FOR ANDROID
http://processing.org/tutorials/android/
You can now use PROCESSING > V2.0 to quickly create applications for mobile devices that use the Android operating system.
Note: you don't need to have an Android device to make these applications, using the software emulator.

## Slide 285: PROCESSING FOR ANDROID: « HELLO WORLD »

## Slide 286: PROCESSING FOR ANDROID: A BIT OF INTERACTIVITY
/* World's simplest Android App!
blprnt@blprnt.com Sept 25, 2010 */
//Build a container to hold the current rotation of the box
float boxRotation = 0;
void setup() {
//Set the size of the screen (this is not really necessary in Android mode, but we'll do it anyway)
size(480,800);
//Turn on smoothing to make everything pretty.
smooth();
//Set the fill and stroke colour for the box and circle
fill(255);
stroke(255);
//Tell the rectangles to draw from the center point (the default is the TL corner)
rectMode(CENTER);
};
void draw() {
//Set the background colour, which gets more red
as we move our finger down the screen.
background(mouseY * (255.0/800), 100, 0);
//Chane our box rotation depending on how our finger has moved right-to-left
boxRotation += (float) (pmouseX - mouseX)/100;
//Draw the ball-and-stick
line(width/2, height/2, mouseX, mouseY);
ellipse(mouseX, mouseY, 40, 40);
//Draw the box
pushMatrix();
translate(width/2, height/2);
rotate(boxRotation);
rect(0,0, 150, 150);
popMatrix();
};

## Slide 287: I - LES MICROCONTROLEURS
TP5-C

## Slide 288: OTHER WAY : MIT APP INVENTOR
http://appinventor.mit.edu/
http://ai2.appinventor.mit.edu/#5399440480272384
<= RETOUR
http://beta.appinventor.mit.edu/

## Slide 289: OTHER WAY : ANDROID STUDIO
https://developer.android.com/studio/index.html

## Slide 290
IV-3 LABVIEW INTERFACE :
LIFA

## Slide 291: LIFA - LabVIEW Interface for Arduino
https://decibel.ni.com/content/groups/labview-interface-for-arduino
LabVIEW for Arduino (LIFA) Toolkit interface allows developers to acquire data from the Arduino microcontroller and treat in the LabVIEW graphical programming environment and it's free! ;-)
http://innovelectronique.fr/2012/05/04/arduino-et-lifa-labview-interface-for-arduino/
http://innovelectronique.fr/2012/05/23/aduino-et-lifa-episode-2/
http://vishots.com/getting-started-with-the-labview-interface-for-arduino/
Top 5 reasons that makes you more productive with LabVIEW when using Arduino:?
1 - Interact with your system via a graphical user interface. 2 - Optimize your design with intuitive graphical programming process.
3 - Improve your experience of debugging with interactive tools.
4 - Functions of simple implementation for complex tasks. 5 - Open API allows complete customization - customize your programs according to your application.

## Slide 292: LabVIEW Interface for Arduino - LIFA
https://decibel.ni.com/content/groups/labview-interface-for-arduino?view=overview#/?tagSet=undefined

## Slide 293: ARDUINO ET C# CRÉER UNE APPLICATION

## Slide 294
TP6

## Slide 295: TP6 - Connexion Arduino - C#

## Slide 296: TP6 - Connexion Arduino - C#
Avec Microsoft VISUAL STUDIO:
Créer une application qui envoie par port série 3 entiers entre 0 et 255
à 3 trackbars et pilote, côté Arduino, une LED RGB
PISTE VERTE:
1 – Créer une application Windows Form
2 – Créer: - 1 bouton (nommé “CONNEXION PORT SERIE”) +
- 3 trackbars (à mettre en vertical, valeur min 0 max 255,
ENABLE FALSE, couleur de fond R, G, B)
3 – A l’ouverture du formulaire Form1 les 3 trackbars doivent être
Désactivés et leurs valeurs à 0
4 – Ajouter un serialPort (double clic)
=> serialPort1 (configurer sur COMxxx :
le port com de l’arduino, 9600…
5 – Quand on clique sur le bouton CONNEXION PORT SERIE
=> il ouvre le port défini précédemment si il était fermé ou le ferme si il était ouvert - Si on est connecté => le bouton doit indiquer “SE DÉCONNECTER”
- Si on est déconnecté => le bouton doit indiquer “SE CONNECTER”
– Les trackbars s’activent
6 – Dès qu’un trackbar change de valeur, on envoie la valeur de TOUS les trackbars sur le port Série:
objet serialPort1 et méthode WriteLine(…).
7 – Quand on clique sur “SE DÉCONNECTER”, remettre tous les trackbar à 0
PISTE BLEU:
8 – Mettre une liste déroulante pour choisir le port Série:
=> COMBO BOX, double cliquer sur FORM => FORM_LOAD)
Charger la classe série IO.Ports (using System.IO.Ports),
puis créer un tableau de Strings ports récupérant les PortNames
des ports Série avec la méthode GetPortNames()
Puis ajouter tous les éléments du tableau dans la comboBox1
String[] ports = SerialPort.GetPortNames();
foreach (var port in ports) {
comboBox1.Items.Add(port);
}
serialPort1.PortName = comboBox1.SelectedItem.ToString();

## Slide 297: SOLUTION PISTE VERTE : C#
using System;
using System.Collections.Generic;
using System.ComponentModel;
using System.Data;
using System.Drawing;
using System.Linq;
using System.Text;
using System.Threading.Tasks;
using System.Windows.Forms;
//using System.IO.Ports; //Pour récupérer les ports séries
namespace Test_Forms_02022020
{
public partial class Form1 : Form
{
public Form1()
{
InitializeComponent();
}
private void button1_Click(object sender, EventArgs e)
{
if (serialPort1.IsOpen) {
serialPort1.Close();
button1.Text = "Se CONNECTER";
trackBar1.Enabled = false;
trackBar2.Enabled = false;
trackBar3.Enabled = false;
trackBar1.Value = 0;
trackBar2.Value = 0;
trackBar3.Value = 0;
}
else {
button1.Text = "Se DECONNECTER";
serialPort1.PortName = "COM2";
serialPort1.Open();
trackBar1.Enabled = true;
trackBar2.Enabled = true;
trackBar3.Enabled = true;
}
}
private void trackBar1_Scroll(object sender, EventArgs e)
{
serialPort1.WriteLine(trackBar1.Value + "/" + trackBar2.Value + "/" + trackBar3.Value) ;
}
private void trackBar2_Scroll(object sender, EventArgs e)
{
serialPort1.WriteLine(trackBar1.Value + "/" + trackBar2.Value + "/" + trackBar3.Value);
}
private void trackBar3_Scroll(object sender, EventArgs e)
{
serialPort1.WriteLine(trackBar1.Value + "/" + trackBar2.Value + "/" + trackBar3.Value);
}
private void Form1_Load(object sender, EventArgs e)
{ //Initialisation des trackballs
trackBar1.Enabled = false;
trackBar2.Enabled = false;
trackBar3.Enabled = false;
trackBar1.Value = 0; trackBar2.Value = 0; trackBar3.Value = 0;
}
}
}

## Slide 298: SOLUTION PISTE BLEUE: C#
https://docs.microsoft.com/fr-fr/visualstudio/ide/walkthrough-building-an-application?view=vs-2019
Générer un exécutable:

## Slide 299: TO GO FURTHER
VISUAL STUDIO CODE
+ PLATFORM IO

## Slide 300: VISUAL STUDIO CODE + PLATFORM IO + ARDUINO
Vous allez installer:
VsCode - + PlatformIO (écosystème de développement pour les microcontrôleurs - Open source, multiplate-forme, gratuit, facile à prendre en main)
Documentations sur PlatformIO
https://platformio.org/
https://docs.platformio.org/en/latest/
https://fr.wikipedia.org/wiki/GitHub

## Slide 301: INSTALLATION PLATFORM IO
Installation de PlatformIO sur VsCode
Cliquer sur l'icône "Extensions" Rechercher "PlatformIO" Cliquer sur [Install]

## Slide 302: INTEFACE DE BIENVENUE PLATFORM IO
Lorsque PlatformIO est installé, l'interface de "Bienvenue" s'affiche
Si vous avez fermé l'interface de PlatformIO, vous pouvez la ré-ouvrir
Cliquer sur l'icône de PlatformIO dans la barre latérale
Puis PIO Home / Open

## Slide 303: BARRE D’ETAT : PLATFORM IO
BARRE D’ETAT : de gauche à droite ....
Le "X dans un rond - x erreur(s)" indique le nombre d'erreur dans l'écriture du code
Le "! dans un triangle - x erreur(s)" indique le nombre d'erreur
Les "Deux outils en croix avec le chiffre - x" indique le nombre de tache en fonctionnement
La "Maison - PlatformIO: Home" affiche l'interface de "Bienvenue"
Le "V - PlatformIO: Build" execute la vérification et la construction du code
La "Flêche vers la droite - PlatformIO: Upload" téléverse le code dans la carte
Le "Nuage avec la flêche vers le haut - PlatformIO: Upload to remote device" téléverse le code vers un emplacement remote
La "Poubelle - PlatformIO: Clean" efface le terminal
La "Fiole - PlatformIO: Test" teste le code
Les "Dossiers - PlatformIO: Run Task" affiche des commandes disponibles
La "Prise de courant - PlatformIO: Serial Monitor" affiche le moniteur série
Le "Prompt - PlatformIO: New Terminal" ouvre un nouveau terminal

## Slide 304: PAGES PLATFORM IO

## Slide 305: PAGES PLATFORM IO

## Slide 306: PAGES PLATFORM IO

## Slide 307: PAGES PLATFORM IO

## Slide 308: ARBORESCENCE PlatformIO
Vous avez créé un projet
L'explorateur affiche l'arborescence PlatformIO
Nom_du_projet # PlatformIO-Test .pio .vscode # Dossier contenant les fichiers de configuration du projet
{} c_cpp_properties.json # Fichier configuration c_cpp_properties {} extensions.json # fichier de configuration des extensions {} launch.json # Fichier de configuration de xxxxx
include lib src # Dossier contenant le fichier code
main.cpp # Fichier code cpp
test .gitignore .travis.yml platformio.ini # Fichier ini de platformio

## Slide 309: EXPLICATION DE L’ARBORESCENCE
Explication barre d’état....
c_cpp_properties.json
Dossier .vscode
Ce fichier contient les chemins nécessaires pour que VsCode puisse retrouver les lib, le compilateur etc...
Documentation officielle https://code.visualstudio.com/docs/cpp/c-cpp-properties-schema-reference
extensions.json
Dossier .vscode Ce fichier contient les extensions utilisées
launch.json
Dossier .vscode Ce fichier contient les extensions utilisées
Documentation officielle https://code.visualstudio.com/docs/cpp/launch-json-reference
main.cpp
Dossier src Ce fichier contient le fichier code du projet - main.cpp # nom_du_fichier.cpp
(Sous IDE Arduino le fichier code se nomme nom_du_fichier.ino)
platformio.ini
A la racine du projet
Ce fichier contient les références de la carte utilisée

## Slide 310: TO GO FURTHER
TP VISUAL STUDIO CODE
+ PLATFORM IO

## Slide 311: PLATFORM IO – CREATION D’UN PROJET
Cliquer sur [+ New Project]
La fenêtre "Project Wizard" s'ouvre
Renseigner les champs:
Name: NOM_DE_VOTRE_PROJET e.g. Test_PPT Board: SELECTIONNER_VOTRE_CARTE # Arduino Uno
Framework: # Le champ se renseigne automatiquement
Sur les postes INSA : (problème d’accès réseau pour le compilateur)
décocher « Use Default Location » et choisir un répertoire sur disque C:
Ne surtout pas choisir le disque U:
Puis cliquer sur Finish … puis Patience ...
L’arborescence de votre projet devrait apparaître sur la gauche !

## Slide 312: PLATFORM IO - PROGRAMME BLINK
Création d'un fichier Blink – PlatformIO
Dans le main.cpp

## Slide 313: Moniteur série - PlatformIO
Modifier le code Blink, afin que le moniteur série affiche
led allumée led éteinte etc ...
Dans void setup()
Serial.begin(9600);
Dans void loop()
Serial.println("led allumée"); Serial.println("led éteinte");
Ouvrir le moniteur série
Ctrl + Maj + P puis saisir "Serial Monitor"
ou
Cliquer sur l'icône "Serial Monitor" dans la barre d'état

## Slide 314: IV-3 TO GO FURTHER
IV-4 TO GO FURTHER:
PYTHON

## Slide 315: INTERFACE ARDUINO – PYTHON – AJAX - BDD
https://www.python.org/

## Slide 316: INTERFACE ARDUINO – PYTHON – AJAX - BDD
CODE: MANAGEMENT OF THE ROTARY ENCODER AND SENDING THE STRING BY ARDUINO VIA ITS SERIAL PORT:

## Slide 317: INTERFACE ARDUINO – PYTHON – AJAX - BDD
PYTHON CODE TO READ FROM THE SERIAL PORT ON PC:
PYTHON CODE:
LAUNCHING THE WEB SERVER
- WEB CLIENT
- TKINTER INTERFACE GRAPH

## Slide 318: INTERFACE ARDUINO – PYTHON – AJAX - BDD
CODE AJAX data recovery sent to JSON from PYHTON SCRIPT: Technical AJAX - XMLHttpRequest send data in JSON format
WEB PAGE to display data with dynamic update (~ 100ms)
BDD DE STOCKAGE DES DONNEES
DISPLAY DYNAMICS OF VOTING DATA WEB PAGE:

## Slide 319
ARDUINO ET INTELLIGENCE ARTIFICIELLE

## Slide 320: APPLICATION INTELLIGENCE ARTIFICIELLE
Entrainer un réseau de neurone sur la base d’une correspondance entre jeu de valeurs R, G, B et le caractère chaud ou froid de la couleur issue du mélange

## Slide 321: APPLICATION INTELLIGENCE ARTIFICIELLE
Réseau de neurones: perceptron multicouche
organisés en couches interconnectées
L’information circule au travers du réseau !

## Slide 322: LE CAPTEUR R, G ,B : TCS34725
Matrice de photodiodes
Description
The TCS34725 RGB Color Sensor Module incorporates high precision RGB and ambient light sensors, white LED light source and I2C interface.

## Slide 323
TP11

## Slide 324: TP11 - LE SKETCH D’APPRENTISSAGE

## Slide 325: LE RESULTAT DU TEST D’APPRENTISSAGE: 1er test
Connexion des 3 premiers neurones
à la première couche de 12
Connexion des 12 neurones de la couche 2
Aux 12 neurones de la couche 3
Connexion des 12 neurones de la couche 3
Au seul neurones de sortie
0: 0.9972061
1: 0.0058303
2: 0.0066308
3: 0.9937487
4: 0.0009738
5: 0.9930828
0: 0.9766245
1: 0.1751021
2: 0.0299375
3: 0.7535102
4: 0.2796261
5: 0.9583353
----------------------
3 12| bias:1.00
1 W:-3.2345151 W:0.1309597 W:0.5248704
2 W:1.7743554 W:-1.1128615 W:-1.0229023
3 W:1.0439237 W:-0.9548942 W:-0.7500634
4 W:-0.2013842 W:-0.2736966 W:0.6675353
5 W:1.3244508 W:-0.5756721 W:0.0717406
6 W:1.2812261 W:-1.0434827 W:0.1039599
7 W:0.0799494 W:-0.1168651 W:0.4985597
8 W:-0.0033359 W:0.4396488 W:0.0837857
9 W:-1.7958540 W:0.0385646 W:-0.3189595
10 W:-0.7197753 W:-0.6555705 W:0.1462377
11 W:1.8314944 W:-0.9454978 W:-1.2856529
12 W:-2.2472562 W:0.3385596 W:0.6582292
----------------------
12 12| bias:1.00
1 W:0.2504118 W:-0.0748784 W:0.1988482 W:0.3846305 W:-0.1931987 W:-0.2184220 W:0.4247591 W:0.8196946 W:0.7680702 W:-0.4695768 W:0.5541190 W:0.8695870
2 W:0.5016391 W:-0.3038916 W:0.0342278 W:0.0589705 W:0.1627688 W:0.1904305 W:-0.6407276 W:-0.1182652 W:-0.0600728 W:-0.1725170 W:-0.8090185 W:0.2743827
3 W:2.0405766 W:-1.4764641 W:-0.1413182 W:-0.3740782 W:-1.1956558 W:-0.6935209 W:-0.4548573 W:-0.0658056 W:0.2264159 W:0.6869005 W:-0.4933598 W:1.5914235
4 W:1.1155270 W:-0.8572950 W:-0.8008734 W:-0.6697721 W:-0.5013657 W:-0.1460065 W:-0.4328084 W:0.7530125 W:-0.0634269 W:0.3862528 W:-0.7250428 W:0.6111167
5 W:0.2705692 W:0.1760945 W:-0.1719677 W:-0.1129410 W:0.6726030 W:-0.9636604 W:-0.8179512 W:-0.0434211 W:0.4941928 W:0.0682246 W:-0.6848159 W:0.8007918
6 W:0.9544466 W:-0.6757089 W:-1.0301469 W:0.8338283 W:-0.7996262 W:-0.4537288 W:0.2324169 W:0.0687901 W:1.4843548 W:-0.6338199 W:-1.5104135 W:0.4744215
7 W:-1.7229041 W:-0.1798249 W:0.8212229 W:-0.3724416 W:0.0407116 W:0.9176830 W:0.1829736 W:0.5380781 W:-1.4646476 W:-0.7382750 W:1.0299470 W:-1.6410176
8 W:-1.0853009 W:1.3814204 W:0.6354837 W:0.0697226 W:0.4225459 W:0.1417617 W:-0.1362197 W:-0.6431421 W:-1.2836674 W:-0.4104369 W:-0.0603579 W:-1.0465948
9 W:1.0762183 W:-0.1442365 W:0.6064275 W:0.5933339 W:-0.9387536 W:-0.9469555 W:-0.0846194 W:-0.6753968 W:0.0977126 W:0.0045570 W:-1.2911614 W:0.6011035
10 W:-0.9536161 W:0.6358527 W:0.8789533 W:-0.1719329 W:0.8641534 W:-0.5096537 W:-0.8671501 W:-0.4959279 W:-0.1789059 W:-0.7331338 W:0.6689547 W:-0.4755179
11 W:0.6226391 W:0.1799965 W:-0.3603446 W:-0.9016899 W:0.4566050 W:-0.9944236 W:0.2678848 W:0.5542941 W:0.1134568 W:-0.2819874 W:-0.5971943 W:-0.1648310
12 W:1.5341858 W:-0.9963873 W:-0.8347433 W:-0.4640187 W:0.0578763 W:-0.9646052 W:0.5995245 W:0.2797670 W:-0.3659082 W:0.7878527 W:-0.6523962 W:-0.4423539
----------------------
12 1| bias:1.07
1 W:0.8991649 W:-0.6896954 W:-3.0657675 W:-1.5418012 W:-0.5206811 W:-2.5220344 W:3.0342688 W:2.4633121 W:-1.7153653 W:1.5582633 W:-0.4350041 W:-1.4809799
----------------------

## Slide 326: 2ème test d’entraînement
Connexion des 3 premiers neurones
à la première couche de 12
Connexion des 12 neurones de la couche 2
Aux 12 neurones de la couche 3
Connexion des 12 neurones de la couche 3
Au seul neurones de sortie
0: 0.9972061
1: 0.0058303
2: 0.0066308
3: 0.9937487
4: 0.0009738
5: 0.9930828
0: 1 //ROUGE
1: 0 //VERT
2: 0 //BLEU
3: 1 // JAUNE
4: 0 // CYAN
5: 1 //MAGENTA
RESULTAT
SORTIE
INTRODUITE
LE RESULTAT DU TEST D’APPRENTISSAGE: 2ème test
0: 0.9972061
1: 0.0058303
2: 0.0066308
3: 0.9937487
4: 0.0009738
5: 0.9930828
----------------------
3 12| bias:1.00
1 W:-3.2345151 W:0.1309597 W:0.5248704
2 W:1.7743554 W:-1.1128615 W:-1.0229023
3 W:1.0439237 W:-0.9548942 W:-0.7500634
4 W:-0.2013842 W:-0.2736966 W:0.6675353
5 W:1.3244508 W:-0.5756721 W:0.0717406
6 W:1.2812261 W:-1.0434827 W:0.1039599
7 W:0.0799494 W:-0.1168651 W:0.4985597
8 W:-0.0033359 W:0.4396488 W:0.0837857
9 W:-1.7958540 W:0.0385646 W:-0.3189595
10 W:-0.7197753 W:-0.6555705 W:0.1462377
11 W:1.8314944 W:-0.9454978 W:-1.2856529
12 W:-2.2472562 W:0.3385596 W:0.6582292
----------------------
12 12| bias:1.00
1 W:0.2504118 W:-0.0748784 W:0.1988482 W:0.3846305 W:-0.1931987 W:-0.2184220 W:0.4247591 W:0.8196946 W:0.7680702 W:-0.4695768 W:0.5541190 W:0.8695870
2 W:0.5016391 W:-0.3038916 W:0.0342278 W:0.0589705 W:0.1627688 W:0.1904305 W:-0.6407276 W:-0.1182652 W:-0.0600728 W:-0.1725170 W:-0.8090185 W:0.2743827
3 W:2.0405766 W:-1.4764641 W:-0.1413182 W:-0.3740782 W:-1.1956558 W:-0.6935209 W:-0.4548573 W:-0.0658056 W:0.2264159 W:0.6869005 W:-0.4933598 W:1.5914235
4 W:1.1155270 W:-0.8572950 W:-0.8008734 W:-0.6697721 W:-0.5013657 W:-0.1460065 W:-0.4328084 W:0.7530125 W:-0.0634269 W:0.3862528 W:-0.7250428 W:0.6111167
5 W:0.2705692 W:0.1760945 W:-0.1719677 W:-0.1129410 W:0.6726030 W:-0.9636604 W:-0.8179512 W:-0.0434211 W:0.4941928 W:0.0682246 W:-0.6848159 W:0.8007918
6 W:0.9544466 W:-0.6757089 W:-1.0301469 W:0.8338283 W:-0.7996262 W:-0.4537288 W:0.2324169 W:0.0687901 W:1.4843548 W:-0.6338199 W:-1.5104135 W:0.4744215
7 W:-1.7229041 W:-0.1798249 W:0.8212229 W:-0.3724416 W:0.0407116 W:0.9176830 W:0.1829736 W:0.5380781 W:-1.4646476 W:-0.7382750 W:1.0299470 W:-1.6410176
8 W:-1.0853009 W:1.3814204 W:0.6354837 W:0.0697226 W:0.4225459 W:0.1417617 W:-0.1362197 W:-0.6431421 W:-1.2836674 W:-0.4104369 W:-0.0603579 W:-1.0465948
9 W:1.0762183 W:-0.1442365 W:0.6064275 W:0.5933339 W:-0.9387536 W:-0.9469555 W:-0.0846194 W:-0.6753968 W:0.0977126 W:0.0045570 W:-1.2911614 W:0.6011035
10 W:-0.9536161 W:0.6358527 W:0.8789533 W:-0.1719329 W:0.8641534 W:-0.5096537 W:-0.8671501 W:-0.4959279 W:-0.1789059 W:-0.7331338 W:0.6689547 W:-0.4755179
11 W:0.6226391 W:0.1799965 W:-0.3603446 W:-0.9016899 W:0.4566050 W:-0.9944236 W:0.2678848 W:0.5542941 W:0.1134568 W:-0.2819874 W:-0.5971943 W:-0.1648310
12 W:1.5341858 W:-0.9963873 W:-0.8347433 W:-0.4640187 W:0.0578763 W:-0.9646052 W:0.5995245 W:0.2797670 W:-0.3659082 W:0.7878527 W:-0.6523962 W:-0.4423539
----------------------
12 1| bias:1.07
1 W:0.8991649 W:-0.6896954 W:-3.0657675 W:-1.5418012 W:-0.5206811 W:-2.5220344 W:3.0342688 W:2.4633121 W:-1.7153653 W:1.5582633 W:-0.4350041 W:-1.4809799
----------------------

## Slide 327: LE SKETCH DE DETECTION

## Slide 328: Simple MLP - NeuralNetwork Library For Microcontrollers
https://github.com/GiorgosXou/NeuralNetworks
Simple MLP - NeuralNetwork Library For Microcontrollers
Nothing "Import ant", just a simple library for implementing Neural-Networks(NNs) easily and effectively on any Arduino board and other microcontrollers.

## Slide 329: Autres fonctions d’activation
LES FONCTIONS DE L’IA

## Slide 330: La courbe sigmoïde
Elle représente la fonction de répartition de la loi logistique.
Elle est souvent utilisée dans les réseaux de neurones parce qu'elle est dérivable, ce qui est une contrainte pour l'algorithme de rétropropagation de Werbos.
La forme de la dérivée de sa fonction inverse est extrêmement simple et facile à calculer, ce qui améliore les performances des algorithmes.
La courbe sigmoïde génère par transformation affine une partie des courbes logistiques et en est donc un représentant privilégié.
Fait activer le neurone rapidement dès qu’elle est supérieure à 0.5 ou inversement le désactiver rapidement si elle est inférieure à 0.5
pour tout x réel
En mathématiques, la fonction sigmoïde (dite aussi courbe en S) est définie par :
Ne trouvez-vous pas une similitude avec la fonction de Fermi-Dirac utilisée en physique du solide ;-) ?
https://fr.wikipedia.org/wiki/Sigmo%C3%AFde_(math%C3%A9matiques)
The main reason why we use sigmoid function is because it exists between (0 to 1). Therefore, it is especially used for models where we have to predict the probability as an output. Since probability of anything exists only between the range of 0 and 1, sigmoid is the right choice.
LES FONCTIONS DE L’IA

## Slide 331
ROUGE
VERT
BLEU
JAUNE
CYAN
MAGENTA
COULEURS DE TEST

## Slide 333: ARDUINO ET NODE-RED

## Slide 334: What’s Node-RED?
Node-RED is a powerful open source visual wiring tool for building Internet of
Things (IoT) applications.
Node-RED uses visual programming that allows you to connect code blocks,
known as nodes, together to perform a task.
The nodes when wired together are called flows.
On the left-side, you can see a list with a bunch of blocks.
These blocks are called nodes and they are grouped by their functionality.
If you select a node, you can see how it works in the info tab.
In the center, you have the Flow.
The Flow is where you place the nodes.

## Slide 335: Why Node-RED is a great solution?
Why Node-RED is a great solution?
 Node-RED is open source and developed by IBM and runs perfectly with the Raspberry Pi.
Node-RED allows you to prototype a complex home automation system quickly, giving you more time to spend on designing and making cool stuff.
What can you do with Node-RED?
Node-RED makes it easy to:
 Access your Raspberry Pi GPIOs;
 Establish an MQTT connection with other boards (ESP32, ESP8266, Arduino,
etc.);
 Create a responsive graphical user interface for your projects with Node-RED Dashboard;
 Communicate with third-party services (IFTTT.com, Adafruit.io, Thing Speak, and others);
 Retrieve data from the web (weather forecast, stock prices, emails, etc…);
 Create time triggered events;
 Store and retrieve data from a database;
 And much more…
Here’s a resource with some flow examples and nodes for Node-RED.

## Slide 336: Installing Node-RED
Installing Node-RED in your Raspberry Pi is quick and easy. It just takes a few commands. Having a Terminal window of your Raspberry Pi open, enter the next command to install Node-RED:
The installation should be completed after a couple of minutes.
Autostart Node-RED on boot
To run Node-RED automatically when the Pi boots up, you need to enter the following command:
Now, restart your Raspberry Pi, so the auto-start takes effect:
Raspberry Pi IP Address
Retrieving your Raspberry Pi IP address, type next command in the terminal window:
pi@raspberry:~ $ hostname –I
pi@raspberry:~ $
bash <(curl -sL https://raw.githubusercontent.com/nodered/
raspbian-deb-package/master/resources/update-nodejs-andnodered)
pi@raspberry:~ $ sudo systemctl enable nodered.service
pi@raspberry:~ $ sudo reboot
In this case, the Raspberry Pi
IP address is 192.168.1.144
(save yours, because
you’ll need it in the next Unit).

## Slide 337: TESTING THE INSTALLATION
When your Pi is back on, you can test the installation by entering the IP address of your Pi in a web browser followed by the 1880 port number:
http://YOUR_RPi_IP_ADDRESS:1880
In my case is:
http://192.168.1.144:1880
A page as shown in the next figure should load:

## Slide 338: Installing Node-RED Dashboard
Node-RED Dashboard is a set of nodes that provides tools to create a user interface with buttons, charts, text, and other widgets.
To learn more about Node-RED Dashboard you can check the following links:
 Node-RED site: http://flows.nodered.org/node/node-red-dashboard
 GitHub: https://github.com/node-red/node-red-dashboard
A new window opens with the User Settings. Open the “Install” tab, search for “node-red-dashboard“, and press the “install” button:
Installing Node-RED Dashboard
To install the Node-RED Dashboard, go to the “Settings” menu in the top-right corner and open the “Manage palette” menu:
Close the menu and a new set of nodes should appear in your left window with the dashboard nodes:

## Slide 339
TP7:
ARDUINO AND NODE-RED

## Slide 340: TP7 - ARDUINO & NODE-RED
Installer le Node Serial
Depuis la version 0.20, il est nécessaire d’installer le node Serial qui permet de communiquer via le port série. Comme précédemment, faites une recherche sur le mot clé Serial et installez le package officiel node-red-node-serialport.
On va simplement lire à intervalle régulier (ici toutes les 5s, 5000ms), la valeur du signal analogique (de 0 à 1023) pour chaque sonde d’humidité du sol. Ensuite on envoi la sortie sur le moniteur série de l’IDE Arduino.
Ce qui donne maintenant sur le moniteur série
{"Capteur1":250, " Capteur2":301}
=> FORMAT JSON (clé = valeur)

## Slide 341: FORMAT JSON
Formater les données en JSON
On pourrait envoyer directement les mesures sur le port série de l’Arduino avec un séparateur, par exemple un caractère spécial (|, -, #…) mais cette stratégie implique que l’on sache précisément la position de chaque données.
- Aucun problème avec une ou deux données, ça devient plus compliqué lorsqu’il y en à une dizaine.
- Autre problème, la conversion de chaine de caractères qui est un éternel problème en informatique.
Pour éviter tous ce problème, nous allons mettre en forme les données et indiquer à chaque fois à quoi elle correspond.
Pour cela, nous allons utiliser le format JSON.
L’avantage, c’est qu’il est supporté par tous les langages modernes.
C’est même la structure de données par défaut du javascript, langage sur lequel repose Node-RED.
Le JSON est une mise en forme structurée des données de type clé = valeur.
Chaque ligne de données est séparée par une virgule (sans la dernière ligne).
Une valeur peut être:
une chaine de caractères (une image sera une chaine),
un nombre (entier ou décimal),
un tableau (chaine, nombre),
une structure (qui contiendra elle même des données sous la forme clé = valeur).
Voici un exemple. Tout d’abord en ligne, c’est ce que le code Arduino va généré
{"sonde1":22.1,"sonde2":64.1,"unites":{"sonde1":"°C","sonde2":"%"}}

## Slide 342: FORMAT JSON
Pour vérifier votre code, je vous conseille d’utiliser le site jsonlint.com qui est gratuit.
{
"sonde1":22.1,
"sonde2":64.1,
"unites": {
"sonde1": "°C« ,
"sonde2": "%"
}
}
Pour de gros projet, je vous conseille d’utiliser la librairie ArduinoJSON.
Elle permet de stocker les données au format JSON dans la mémoire de l’Arduino.
C’est très pratique pour :
extraire des données,
des réglages,
enregistrer un historique dans la mémoire SPIFFS ou une carte SD.
Ici, on va faire plus simple et directement construire une chaine de caractères et l’envoyer sur le port série ce qui donne le code suivant

## Slide 343: NODE-RED
Se connecter à l’Arduino à l’aide du Node Serial (dans la palette Input, puisqu’on veut lire les mesures).
Glissez-déposer le node sur la page blanche et faites un double clic sur le Node Serial pour ouvrir le panneau de configuration.
Cliquez sur le crayon pour ajouter une nouvelle connexion. Utilisez la loupe pour lister les ports COM. Ici l’Arduino est connecté sur un Raspberry Pi 3, donc le chemin vers l’Arduino est au format Linux. Sur Windows, ce sera un port COMx.
Dans le code Arduino, la ligne de code Serial.begin(115200) permet d’initialiser la vitesse à 115200 bauds, indiquez la vitesse sous Baud Rate. Enregistrez, c’est tout ce qu’il y à faire
Cherchez le Node Debug
Reliez le Node Serial au Node debug. Pour cela, placez la souris sur le carré qui symbolise la sortie de Node Serial, un fil orange apparaît. Allez l’accrocher à l’entrée du node debug. Vous venez de créer votre premier flow.
Déployez le flow et cliquant sur Deploy et ouvrez l’onglet debug pour visualiser les données qui arrivent de l’Arduino. Attendez quelques secondes en fonction de la temporisation programmée dans le code Arduino.

## Slide 344: EXTRAIRE LES DONNÉES DU JSON VENANT DE L’ARDUINO
Pour le moment, on récupère une chaine de caractère sur le port série de l’Arduino, on va la convertir en un objet JSON exploitable par Node-RED à l’aide du node JSON. Placez le sur le flow et reliez-le au port série.
On va maintenant extraire chaque mesure avec un peu de code javascript. Placez un node Function et reliez le à la sortie de node JSON
Ouvrez la fonction et collez ce code javascript.
msg.topic = "Capteur 1";
msg.payload = msg.payload.Capteur1;
return msg;
Node-RED transfère des messages (msg) au format JSON entre chaque Node (noeud du programme).
Les données se trouvent dans la clé payload.
La première ligne extrait la mesure du capteur 1 (ou Capteur 2) et écrase le payload actuel.
La fonction retourne le message (msg)actualisé. Il ne renvoit plus que la mesure du premier capteur
Faites la même chose pour le second capteur en ajoutant un second flow

## Slide 345: VISUALISER LES MESURES SUR UN GRAPHIQUE
Cherchez le node chart et placer le sur le flow
Reliez les des fonctions au node chart. Ouvrez le panneau de configuration du graphique. Cliquez d’abord sur le crayon pour créer un groupe.
Ensuite vous pouvez modifier certains paramètres :
Group : sélectionnez le groupe que vous venez de créer
Size : taille
Label : libellé
X-axis : nombre de points ou période de temps
Name : le nom qui apparait sur le flow

## Slide 346: VISUALISER LES MESURES SUR UN GRAPHIQUE
Enregistrez, déployez et allez l’adresse localhost:1880/ui (ou IP:1880/ui) pour visualiser les mesures de vos capteurs connectés à l’Arduino

## Slide 347: ENREGISTRER LES MESURES DANS UN FICHIER CSV
Exploiter vos données sur un tableur en les enregistrant au format csv (fichier texte dont le séparateur de données est un point-virgule).
=> On ajoute une nouvelle fonction qui renvoie une ligne dont chaque données est séparée par un point virgule. Voici l’ordre des colonnes :
date au format année/mois/jour (supporté par tous les tableurs)
heure au format hh:mm:ss
valeur de la sonde Capteur1
valeur de la sonde Capteur2
var date = new Date().toLocaleDateString();
var time = new Date().toLocaleTimeString();
var output = date + ";" + time + ";" + msg.payload.Capteur1 + ";" + msg.payload.Capteur2;
msg.payload = output;
return msg;
Cherchez le node file et placez un node input sur le flow
Sur le panneau de configuration, indiquez le chemin de destination. Par défaut le fichier est enregistré dans le répertoire de Node-RED. Cochez Add newline to each payload pour ajouter une nouvelle ligne au fichier à chaque nouvel enregistrement
Déployez, après quelques minutes, voici à quoi va ressembler le fichier CSV

## Slide 348: RESULTAT FINAL
[{"id":"62e97db.8731284","type":"tab","label":"Flow 2","disabled":false,"info":""},{"id":"54ab6674.d42c38","type":"serial in","z":"62e97db.8731284","name":"","serial":"aa3b554b.8d2e5","x":270,"y":180,"wires":[["8fb47c21.deaf78","3839e942.ff2806"]]},{"id":"8fb47c21.deaf78","type":"debug","z":"62e97db.8731284","name":"","active":true,"tosidebar":true,"console":false,"tostatus":false,"complete":"false","x":470,"y":160,"wires":[]},{"id":"3839e942.ff2806","type":"json","z":"62e97db.8731284","name":"","property":"payload","action":"","pretty":false,"x":450,"y":240,"wires":[["6f21aec7.17f468","599ec37e.beae6c","dd2233da.8b38b8"]]},{"id":"6f21aec7.17f468","type":"function","z":"62e97db.8731284","name":"Capteur 2","func":"msg.topic = \"Capteur 2\";\nmsg.payload = msg.payload.Capteur2;\nreturn msg;","outputs":1,"noerr":0,"x":640,"y":280,"wires":[["26b897fb.2568e8"]]},{"id":"599ec37e.beae6c","type":"function","z":"62e97db.8731284","name":"Capteur 1","func":"msg.topic = \"Capteur 1\";\nmsg.payload = msg.payload.Capteur1;\nreturn msg;","outputs":1,"noerr":0,"x":640,"y":200,"wires":[["26b897fb.2568e8"]]},{"id":"26b897fb.2568e8","type":"ui_chart","z":"62e97db.8731284","name":"","group":"3de6bd76.a0e5ba","order":2,"width":"8","height":"6","label":"Capteurs d'humitidés","chartType":"line","legend":"true","xformat":"HH:mm:ss","interpolate":"bezier","nodata":"","dot":true,"ymin":"0","ymax":"1023","removeOlder":"60","removeOlderPoints":"","removeOlderUnit":"60","cutout":0,"useOneColor":false,"colors":["#1f77b4","#aec7e8","#ff7f0e","#2ca02c","#98df8a","#d62728","#ff9896","#9467bd","#c5b0d5"],"useOldStyle":false,"outputs":1,"x":860,"y":240,"wires":[[]]},{"id":"1457badc.cfef6d","type":"file","z":"62e97db.8731284","name":"","filename":"/home/pi/capteurs.csv","appendNewline":true,"createDir":false,"overwriteFile":"false","encoding":"none","x":860,"y":340,"wires":[[]]},{"id":"dd2233da.8b38b8","type":"function","z":"62e97db.8731284","name":"Formatage vers CSV","func":"var date = new Date().toLocaleDateString(); \nvar time = new Date().toLocaleTimeString(); \n\nvar output = date + \";\" + time + \";\" + msg.payload.Capteur1 + \";\" + msg.payload.Capteur2;\nmsg.payload = output; \nreturn msg; \n","outputs":1,"noerr":0,"x":620,"y":340,"wires":[["1457badc.cfef6d"]]},{"id":"aa3b554b.8d2e5","type":"serial-port","z":"","serialport":"/dev/ttyUSB0","serialbaud":"115200","databits":"8","parity":"none","stopbits":"1","waitfor":"","dtr":"none","rts":"none","cts":"none","dsr":"none","newline":"\\n","bin":"false","out":"char","addchar":"","responsetimeout":"10000"},{"id":"3de6bd76.a0e5ba","type":"ui_group","z":"","name":"Main","tab":"a15fdf1b.c86f1","disp":true,"width":"8","collapse":false},{"id":"a15fdf1b.c86f1","type":"ui_tab","z":"","name":"Home","icon":"dashboard","disabled":false,"hidden":false}]

## Slide 349: IMPORTER/EXPORTER UN FLOW
Copiez le code précédent. Ouvrez le menu de NodeRED puis Import -> Clipboard
Collez le code et choisissez ou vous voulez le coller puis Import

## Slide 350: MicroPython on ESP32

## Slide 351: MicroPython on ESP32
What is MicroPython?
MicroPython is a re-implementation of Python 3 targeted for microcontrollers and embedded systems. MicroPython is very similar with regular Python.
So, if you already know how to program in Python, you also know how to program in MicroPython.
Python vs MicroPython
Apart from a few exceptions, the language features of Python are also available in MicroPython. The biggest difference, is that MicroPython was designed to work under constrained conditions.
Because of that, MicroPython does not come with the full standard library.
It only includes a small subset of the Python standard library.
However, it does include modules to access low-level hardware
– this means that there are libraries to easily access and interact with the GPIOs.
Additionally, devices with Wi-Fi capabilities like the ESP8266 and ESP32 include modules to support network connections.

## Slide 352: MicroPython on ESP32
Why MicroPython?
Python is one of the most widely used, simple and easy-to-learn programming languages around. So, the emergence of MicroPython makes it extremely easy and simple to program digital electronics.
MicroPython’s goal is to make programming digital electronics as simple as possible, so it can be used by anyone.
Currently, MicroPython is used by hobbyists, researchers, teachers, educators, and even in commercial products.
The code for blinking a LED on a ESP32 or ESP8266 is as simple as follows:
One great feature of MicroPython is that it comes with an interactive REPL (Read-Evaluate-Print Loop). The REPL allows you to connect to a board and execute code quickly without the need to compile or upload code

## Slide 353: MicroPython on ESP32
MicroPython – Boards support
MicroPython runs on many different devices and boards, such as:
ESP32
ESP8266
PyBoard
Micro:Bit
Teensy 3.X
WiPy – Pycom
Adafruit Circuit Playground Express
Other ESP32/ESP8266 based boards
REM: ESP32 is the successor of the ESP8266, and at the moment, not all features are available in MicroPython to take the most out of the ESP32 – it’s still an ongoing project.
However, it’s very usable and you can make a lot of projects with it.
ESP32 and ESP8266 boards are similar, and you won’t feel almost any difference programming them using MicroPython. This means that anything you write for the ESP8266 should also run with no changes or minimal changes on the ESP32 (mainly changing the pin assignment).

## Slide 354: ESP32 - Pinouts
https://randomnerdtutorials.com/esp32-pinout-reference-gpios/
Note: not all GPIOs are accessible in all development boards, but each specific GPIO works in the same way regardless of the development board you’re using.
If you’re just getting started with the ESP32, we recommend reading our guide: Getting Started with the ESP32 Development Board.

## Slide 355: ESP32 DEV KIT V1 - Pinouts

## Slide 356: FLASHING MICROPYTHON TO ESP32 and ESP8266

## Slide 357: MicroPython on ESP32
[ESP32] Downloading and Flashing the MicroPython Firmware on ESP32:
To download the latest version of MicroPython firmware for the ESP32, go to the MicroPython Downloads page and scroll all the way down to the ESP32 section.
You should see a similar web page (see figure below) with the latest link to download the ESP32 .bin file –
for example: esp32-20181007-v1.9.4-631-g338635ccc.bin.

## Slide 358: MicroPython on ESP32
Selecting Serial Port
Go to Tools > Serial and select your ESP32 COM port (in our case it’s COM5).
The ESP32 DEVKIT V1 DOIT board uses the CP2102 chip.
You can download the CP2102 drivers on the Silicon Labs website.

## Slide 359: MicroPython on ESP32
After they are installed, restart the uPyCraft IDE and you should see the COM port in the Tools menu.
2. If you have the drivers installed, but you can’t see your device, double-check that you’re using a USB cable with data wires.
USB cables from powerbanks often don’t have data wires (they are charge only). So, your computer will never establish a serial communication with your ESP32. Using a a proper USB cable should solve your problem.
Selecting the Board
Go to Tools > Board. For this tutorial, we assume that you’re using the ESP32, so make sure you select the “esp32” option:
Flashing/Uploading MicroPython Firmware
Finally, go to Tools > BurnFirmware menu to flash your ESP32 with MicroPython.
Select all these options to flash the ESP32 board:
board: esp32
burn_addr: 0x1000
erase_flash: yes
com: COMX (in our case it’s COM5)
Firmware: Select “Users” and choose the ESP32xxx.bin file downloaded earlier

## Slide 360: MicroPython on ESP32
After pressing the “Choose” button, navigate to your Downloads folder and select the ESP32 .bin file:
Having all the settings selected,
hold-down the “BOOT/FLASH” button in your ESP32 board:
While holding down the “BOOT/FLASH“, click the “ok” button in the burn firmware window:

## Slide 361: MicroPython on ESP32
When the “EraseFlash” process begins, you can release the “BOOT/FLASH” button.
After a few seconds, the firmware will be flashed into your ESP32 board.
Note: if the “EraseFlash” bar doesn’t move and you see an error message saying “erase false.“, it means that your ESP32 wasn’t in flashing mode:
=> You need to repeat all the steps described earlier and hold the “BOOT/FLASH” button again to ensure that your ESP32 goes into flashing mode.

## Slide 362: GETTING STARTED WITH uPyCraft IDE

## Slide 363: uPyCraft IDE
uPyCraft IDE software, so that you can start programming the ESP32/ESP8266 with MicroPython.
There are many ways to program your ESP board with MicroPython.
We’ve chosen uPyCraft IDE because it is simple and intuitive to use and works great with the ESP boards.
Folder and files
Editor
MicroPython Shell/Terminal
Tools
2
3
4
1

## Slide 364: uPyCraft sections
Several folders and files:
1 - The device folder shows the files that are currently stored on your ESP board.
If you have your ESP32 or ESP8266 connected via serial to uPyCraft IDE, when you expand the device folder, all files stored should load.
By default, you should only have a boot.py file.
To run your main code, it is recommended to create a main.py file.
  boot.py: runs when the device starts and sets up several configuration options;
  main.py: this is the main script that contains your code. It is executed immediately after the boot.py.
2 - The sd folder is meant to access files stored on SD cards
– this is only works with boards like the PyBoard that come with an SD card slot.
3 - The uPy_lib shows the built-in IDE library files.
4 - Finally, the workspace is a directory to save your files.
These files are saved in your computer in a directory defined by you.
This is a specially useful to keep all your files organized at hand.
When using uPyCraft for the first time, to select your working directory, click the workspace folder. A new window pops up for you to chose your workspace path.
Create a new folder or select an existing folder to be your working directory.

## Slide 365: uPyCraft sections
2. Editor
The Editor section is where you write your code and edit your .py files.
You can open more than one file, and the Editor will open a new tab for each file.
New file: creates a new file on the Editor;
Open file: open a file from your computer;
Save file: saves a file;
Download and run: upload the code to your board and execute the code;
Stop: stop the execution of the code – it’s the same as entering CRTL+C on the Shell to stop all scripts from running;
Connect/Disconnect: connect or disconnect to your board via Serial. You must select the serial port first in Tools > Serial;
Undo: undo last change in the code Editor;
Redo: redo last change in the code Editor;
Syntax check: checks the syntax of your code;
Clear: clear the Shell/terminal window messages.
4. Tools
The icons placed at the rightmost side allow you to quickly perform tasks.
Each button is labeled in the figure below:
3. MicroPython Shell/terminal
On the MicroPython Shell, you can type commands to be executed immediately by your ESP board without the need to upload new files.
The terminal also provides information about the state of an executing program, shows errors related with upload, syntax errors, prints messages, etc…
2
3
4

## Slide 366: RUNNING YOUR FIRST SCRIPT
Establishing a communication with the board
After :
1 - having the MicroPython firmware installed on your board and
2 - having the board connected to your computer through an USB cable,
follow the next steps:
1. Go to Tools > Board and select the board you’re using.
2. Go to Tools > Port and select the com port your ESP is connected to.
3. Press the Connect button to establish a serial communication with your board.
4. The >>> should appear in the Shell window after a successful connection with your board.
You can type the print command to test if it’s working:
>>> print('Hello')
Hello
>>>

## Slide 367: CREATING THE main.py FILE ON YOUR BOARD
1. Press the “New file” button to create a new file.
2. Press the “Save file” button to save the file in your computer.
6. The device directory should now load the main.py file.
Your ESP has the file main.py stored.
3. A new window opens, name your file main.py and save it in your PC:
4. After that, you should see the following in your uPyCraft IDE
(the boot.py file in your device and a new tab with the main.py file):
5. Click the “Download and run” button to upload the file to your ESP board:

## Slide 368: UPLOADING THE BLINK LED SCRIPT
Copy the following code to the Editor on the main.py file:
2. Press the “Stop” button to stop any script from running in your board:
3. Click the “Download and Run button” to upload the script to the ESP32 or ESP8266:
4. You should see a message saying “download ok” in the Shell window:

## Slide 369: TESTING THE SCRIPT
To run the script that was just uploaded to your board,
you need to follow these steps:
1. Press the “Stop” button:
2. Press the on-board ESP32/ESP8266 EN (ENABLE) or RST (RESET) button to restart your board and run the script from the start:
Your ESP32 or ESP8266 on-board LED should be blinking every 500 milliseconds. Here’s where the ESP32’s on-board LED is located:
If you’re using an ESP32, your Terminal messages should look something as shown in the following figure after a EN/RST button press:

## Slide 370: TROUBLESHOOTING TIPS
>>> Select Serial Port could not open port 'COM4': FileNotFoundError(2, 'The system cannot find the file specified.', None, 2)
Some common problems and error messages occur with uPyCraft IDE.
Usually restarting your ESP with the on-board EN/RST button fixes your problem.
Or pressing the uPyCraft IDE “Stop” button and repeating your desired action.
In case it doesn’t work for you, see the common errors and discover how to solve them.
Error #1: You get the following message:
Unplug, and plug back your ESP board. Then, double-check that you’ve selected the right serial port in the Tools > Serial menu.
Then, click the “Connect/disconnect” button to establish a serial communication.
You should now be able to upload a new script or re-run new code.
This error might also mean that you have your serial port being used in another program (like a serial terminal or in the Arduino IDE).
Finally, restart the uPyCraft IDE – try to select the serial port in the Tools > Serial menu.
already in download model, please wait.
Error #2: Trouble uploading a new script.
Press the “STOP” button in uPyCraft IDE (1 or 2 times) to make sure any code that was running stops. After that,
press the “Download and run” button to upload the new script to your ESP board.

## Slide 371: TROUBLESHOOTING TIPS
Error #3: After uploading a new script, if you see the following messages:
>>> Ready to download this file, please wait!
...
download ok
os.listdir('.')
Traceback (most recent call last):
File "<stdin>", line 1, in <module>
NameError: name 'os' isn't defined
>>> Ready to download this file, please wait!
...
download ok
os.listdir('.')
OSError: [Errno 98]
It means the new file was uploaded to your board successfully. You can notice that it printed the “download ok” message. Press the ESP on-board “EN/RST” button to restart your board and re-run the new uploaded script from the beginning
Error #4: Problem restarting your ESP board, running a new script or opening the serial port:
>>> Brownout detector was triggered
The “Brownout detector was triggered” error message means that there’s some sort of hardware problem.
It’s often related to one of the following issues: Poor quality USB cable; USB cable is too long; Board with some defect (bad solder joints); Bad computer USB port; Or not enough power provided by the computer USB port.
Solution: try a different shorter USB cable (with data wires), try a different computer USB port or use a USB hub with an external power supply.
Important: if you keep having constant problems or weird error messages, we recommend re-flashing your ESP board with the latest version of MicroPython firmware.
Error #5: When I try to open a serial communication with the ESP32/ESP8266 in uPyCraft IDE, sometimes it prompts the “Burn Firmware” window asking to re-flash the MicroPython firmware.
Basically, it’s happening when you’re running a script in your board, sometimes it’s busy running that script and performing the tasks. So, you need to try opening the COM port multiple times or restart the ESP to catch it available to establish the serial communication with uPyCraft IDE.
If you’re running a script that uses Wi-Fi, deep sleep, or it’s doing multiple tasks, I recommend trying 3 or 4 times to establish the communication. If you can’t, I recommend re-flash the ESP with MicroPython firmware.

## Slide 372: MICROPYTHON PROGRAMMING BASICS

## Slide 373: MICROPYTHON PROGRAMMING BASICS
Programming in MicroPython is the same as Python. Just keep in mind that MicroPython is used for constrained devices. So, you must keep your code as simple as possible.
Operator | Mathematical Operation
+ | Addition
– | Subtraction
* | Multiplication
/ | Division
// | Division, discarding the decimal point
% | Remainder after division
>>> 2+2*9-3
17
>>> 28594/2312
12.36765
>>> 214522236/7.5 2.860297e+07
>>> 23//2
11
>>> 25%3
1
Mathematical Operators
Operator | Description
== | Equal to
!= | Not equal to
> | Greater than
< | Less than
>= | Greater than or equal to
<= | Less than or equal to
Relational Operators
You can make comparisons using relational operators, these compare the values on either sides and show the relation between them.
>>> 2 == 3
False
>>> 4 == 4
True
>>> 3 > 2
True
>>> 489808234 != 2223
True
>>> 4.5 >= 4.5
True

## Slide 374: MICROPYTHON - VARIABLES
Assigning Values to Variables :
In Python you don’t need to declare what type each variable is.
If you’re used to program your boards using Arduino IDE, you know that you need to declare the type of a variable when creating a new variable.
There isn’t such thing in Python.
Variables are simply a storage placeholder for values: number or text.
To assign a value to a variable you use the equal sign (=), with the variable name on the left and the value on the right.
For example, to create a variable to hold the GPIO number where an LED is connected to, you can simply type the following:
led_pin = 23
const int led_pin =23;
In the Arduino IDE, you would have something like:
As you can see, Python is much simpler than programming in C (in Arduino IDE).
Note: the names you give variables can’t have spaces and are case sensitive, so led_pin is different from LED_PIN or Led_Pin.

## Slide 375: MICROPYTHON – DATA TYPES
Data Types: Variables can store several types of values, not just whole numbers. That’s where data types come in. A data type is a classification of a value that tells what operations can be done with the value and how it should be stored.
The following table shows the data types we’ll use most often in our projects.
Data type | Description
int (Int) | Integer (whole number)
float (Float) | Number with a decimal point
str (String) | Set of characters between quotation marks
bool (Boolean) | True or False
Let’s create variables with different data types:
>>> a = 6
>>> b = 95.32
>>> c = 'Hello World!’
>>> d = True
The first value assigned to a, is an integer, which is a whole number.
The b variable contains a float value, which is a number with a decimal.
The third value, ‘Hello World!’, is a string, which is a series of characters.
    Rem: a string must be put inside single (‘Hello World!’) or double quotation (“Hello World!”) marks.
Finally, d is a Boolean, which is a type that can only take either True or False.
There is a function to check the data type of a variable: the type() function. This function accepts as argument the variable you want to check the data type.
type(variable)
This tells that a is an int (integer). Experiment with the other variables and you should get
>>> type(a)
<class 'int'>
>>> type(b)
<class 'float’>
>>> type(c)
<class 'str’>
>>> type(d)
<class 'bool'>

## Slide 376: MicroPython – Print() function
print() Function
The print() function prints the message between parentheses into the Shell. This is specially useful in our projects to debug the code and keep track of what’s going on.
For example:
Comments
Comments in Python start with the hash character (#) and continue to the end of the line. A comment is useful to add “notes” in your program or to tell anyone who reads the program what the script does. This doesn’t add any functionality to your program.
For example:
Because in MicroPython we are working under constrained conditions, there are occasions in which you should avoid adding comments to save space on the ESP memory.
# This is just a comment
>>> print('LED is on') LED is on

## Slide 377: MicroPython – Conditional Statements
Important: Python’s standard indentation is 4 spaces. In MicroPython indentation should be only 2 spaces to fit more code into the microcontroller memory.
Conditional Statements
To write useful programs, you’ll probably need to perform different actions depending on whether a certain condition is True or False.
We’re talking about conditional statements.
They have the following structure:
if <expr1>:
<statement1>
elif <expr2>:
<statement2>
elif <expr3>:
<statement3>
(...)
else:
<statementn>
<expr> is a Boolean expression and it can be either True or False.
If it is True, the <statement> right after it is executed.
The <statement> should be indented so that Python knows what statement belongs to each expression.
The elif statement stands for else if and runs only if the first if condition is not True.
The else statement only runs if none of the other expressions are True.
There’s no limit to the number of elif statements in a program. It’s also not necessary to include an else clause, but if there is one, it must come at the end.
In the Arduino IDE, we use {} curly brackets to define code blocks.
With MicroPython, we use indentation.
Additionally, you need to use a colon : after each expression. Contrary to the Arduino IDE, the expression doesn’t need to be inside parentheses.

## Slide 378: MicroPython – While and For loops
Loops allow you to execute a block of code multiple times for as long as a condition is met. There are two kinds of loops: while and for loops.
For example, you can print all numbers from 1 to 10 with a while loop:
number = 1
while number <= 10:
print(number)
number = number + 1
The code that belongs to the while loop, indicated by the indentation, is executed as long as the value in the number variable is less than or equal to (<=) 10. In every loop, the current number is printed and then 1 is added to it.
You can also print numbers from 1 to 10 using a for loop, like this:
number = 1
for number in range(1, 11):
print(number)
The for loop is executed as long as the value in the number variable is within the range of 1 and 11.
The range() function automatically assigns the next value to the number variable, until 1 below the final number you specify.
Note: - you should use a for loop when you want to repeat a block of code a certain number of times.
- you use a while loop when you want to repeat code until a certain condition is no longer met. In some situations, you can use either one, oftentimes one is more suitable than the others.
Similar to the conditional statements, the for and while Boolean expressions should have a colon : right after them, and the expressions to be executed should be indented.

## Slide 379: MicroPython – User-defined Functions
To define a new function, you use the word def followed by the name you want to give the function and a set of parentheses (and arguments inside, if necessary).
After the parentheses you add a colon : and then tell the function what instructions to perform.
The statements should be indented with 2 spaces (in MicroPython), for example:
def my_function(<arg1>, <arg2>, ...):
<statement>
(...)
return
For example, a function that converts the temperature in Celsius to Fahrenheit could be the following:
def celsius_to_fahrenheit(temp_celsius):
temp_fahrenheit = temp_celsius * (9/5) + 32
return temp_fahrenheit
The celsius_to_fahrenheit() function accepts as argument a temperature in Celsius (temp_celsius). Then, it does the calculation to convert the temperature.
Finally, it returns the temperature in Fahrenheit (temp_fahrenheit).
Note: functions don’t necessarily need to return something. They could just perform some work without the need to return anything.

## Slide 380: MicroPython – Class
Classes and Objects
Python is an Object-Oriented Programming (OOP) language.
There are two important concepts you need to understand about OOP:
- classes and objects.
A class is a blueprint for objects. It defines a set of attributes (data and functions) that characterize an object.
The functions inside of a class are called methods.
Classes are defined by the keyword class followed by the name of the class.
For example:
class MyClass:
(...)
Note:
by convention, classes’ names in Python should be CapWords. However, you can give whatever name you want.
An object is an instance of a class. It’s simply a collection of data and methods into a single entity. Through the object, you can use all functionalities of its class.
Confused? Let’s take a look at a simple example.
If we would like to define several persons in a Python program using the same attributes, we can think of the term person as a class.
We may want to define a person using attributes like name, age, country, etc.

## Slide 381: MicroPython – Class
So, we can create a class called Person.
Our class will have the following attributes: name, age, and country.
You can add as many attributes as you want. We’ll also create a function (method) that prints a description of the person based on its attributes:
class Person:
name = ""
age = 0
country = ""
def description(self):
print("%s is %d years old and from %s." %(self.name, self.age, self.country))
As you can see, we define a new class by using the keyword class, followed by the name we want to give to the class.
Inside the Person class, we define several variables to hold values.
By default the name and country are empty strings, and the age is 0.
Then, we also define a function (method) that prints all the variables values into the Shell.
All functions inside a class should have the self parameter as argument and other arguments, if needed.
The self parameter refers to the object itself.
It is used to access variables that belong to the class.
For example, to access the name variable inside the class, we should use self.name.
Now that we’ve create a class, we can create as many Person objects as we want by using that class. The Person object will have a name, age, and country.
We’ll also be able to print its description using the description() method.
For example, to create a new Person object called person1:
>>> person1 = Person()

## Slide 382: MicroPython – Class
Set the object’s properties
To set the name, age, and country of the person1 object. You can do it as follows:
>>> person1.name = "Rui"
>>> person1.age = 25
>>> person1.country = "Portugal"
Calling methods
Later in your code you can use the created description() method on any Person object. To call the description() method on the person1 object:
>>> person1.description()
Rui is 25 years old and he is from Portugal.
You should now understand that you can create as many objects as you want using the same class and you are able to use the available methods with all the objects of that class.

## Slide 383: MicroPython – Class – Constructor methods
Instead of having to define a class, and then set the object’s properties, which can be time consuming, you can use the constructor method inside your class.
The constructor method is used to initiate data as soon as an object of a class is instantiated.
The constructor method is also known as __init__ method.
Using the __init__ method, the Person() class looks as follows:
class Person():
def __init__(self, name, age, country):
self.name = name
self.age = age
self.country = country
def description(self):
print("%s is %d years old and he is from %s." %(self.name, self.age, self.country))
Then, to instantiate a Person object with the same attributes we’ve defined earlier, we just need to do the following:
>>> person1 = Person("Rui", 25, "Portugal")
>>> person1.description()
Rui is 25 years old and he is from Portugal.
If you call the description() on the person1 object, you’ll get the same result:

## Slide 384: MicroPython – Modules
A module is a file that contains a set of classes and functions you can use in your code – you can also call it library.
To access the classes and functions inside that code, you just need to import that module into your code. You can create your own modules, or use already created modules from the standard Python library.
When it comes to MicroPython, it only comes with a small subset of the standard Python library, but it does come with a set of modules to control GPIOs, make networks connections and much more.
Importing modules/libraries is as simple as using:
For example, to import the machine library that contains classes to control GPIOs, type the following:
import module_name
import machine
In most programs you won’t need all the classes from one module.
You may just want to import a single class.
For example, to import only the Pin class from the machine module:
from machine import pins

## Slide 385: MicroPython – Wrapping Up
We’ve just scratched the surface of Python basics that also apply to MicroPython.
If you are used to program electronics using the Arduino IDE, you’ll find that MicroPython has a much simpler and user-friendly syntax.
Let’s just summarize some of the main differences between your Arduino sketches and programs in MicroPython:
You don’t use semicolon ; at the end of a statement
After Boolean expressions in conditional statements and loops, you use a colon:
To define code blocks use indentation instead of curly brackets {}
When creating a variable, you don’t need to define which data type it is – you don’t need to declare a variable
Indentation in MicroPython is 2 spaces (instead of 4 in Python)

## Slide 386: MICROPYTHON MODULES

## Slide 387: MICROPYTHON MODULES
Python standard libraries and micro-libraries
MicroPython-specific libraries
http://docs.micropython.org/en/latest/library/machine.html
http://docs.micropython.org/en/latest/library/index.html#micropython-specific-libraries

## Slide 388: MICROPYTHON MODULES: machine
Classes
class Pin – control I/O pins
class Signal – control and sense external I/O devices
class ADC – analog to digital conversion
class UART – duplex serial communication bus
class SPI – a Serial Peripheral Interface bus protocol (master side)
class I2C – a two-wire serial protocol
class RTC – real time clock
class Timer – control hardware timers
class WDT – watchdog timer
class SD – secure digital memory card (cc3200 port only)
class SDCard – secure digital memory card
http://docs.micropython.org/en/latest/library/machine.Pin.html
http://docs.micropython.org/en/latest/esp32/quickref.html

## Slide 389: TP8 - 1 – ANALOG READ ON ESP32

## Slide 390: AnalogRead with MicroPython
The ESP8266 supports analog reading only on the pin.
https://randomnerdtutorials.com/esp32-esp8266-analog-readings-micropython/
https://randomnerdtutorials.com/esp32-pinout-reference-gpios/
Pinout Reference:
The following script for the ESP32 reads analog values from
GPIO 34
A0

## Slide 391: AnalogRead with MicroPython
Analog Readings – ESP32
There are several pins on the ESP32 that can act as analog pins – these are called ADC pins. All the following GPIOs can act as ADC pins: 0, 2, 4, 12, 13, 14, 15, 25, 26, 27, 32, 33, 34, 35, 36, and 39.
ESP32 ADC pins have 12-bit resolution by default. These pins read voltage between 0 and 3.3V and then return a value between 0 and 4095. The resolution can be changed on the code. For example, you may want to have just 10-bit resolution to get a value between 0 and 1023.
The following table shows some differences between analog reading on the ESP8266 and the ESP32:
 | ESP8266 | ESP32
Analog pins | A0 (ADC 0) | GPIOs: 0, 2, 4, 12, 13, 14, 15, 25, 26, 27, 32, 33, 34, 35, 36, and 39.
Resolution | 10-bit (0-1023) | 12-bit (0-4095)
Change resolution | No | Yes

## Slide 392: AnalogRead with MicroPython
How the code works
To read analog inputs, import the ADC class in addition to the Pin class from the machine module. We also import the sleep method.
from machine import Pin, ADC
from time import sleep
Then, create an ADC object called pot on
GPIO 34
pot = ADC(Pin(34))
pot.atten(ADC.ATTN_11DB)
The following line defines that we want to be able to read voltage in full range.
This means we want to read voltage from 0 to 3.3V.
This corresponds to setting the attenuation ratio of 11db.
For that, we use the atten() method and pass as argument: ADC.ATTN_11DB.
The atten() method can take the following arguments:
ADC.ATTN_0DB — the full range voltage: 1.2V
ADC.ATTN_2_5DB — the full range voltage: 1.5V
ADC.ATTN_6DB — the full range voltage: 2.0V
ADC.ATTN_11DB — the full range voltage: 3.3V

## Slide 393: AnalogRead with MicroPython
In the while loop, read the pot value and save it in the pot_value variable.
To read the value from the pot, simply use the read() method on the pot object.
Then, print the pot value
At the end, add a delay of 100 ms.
pot_value = pot.read()
print(pot_value)
sleep(0.1)
When you rotate the potentiometer, you get values from 0 to 4095 – that’s because the ADC pins have a 12-bit resolution by default. You may want to get values in other ranges. You can change the resolution using the width() method as follows:
ADC.width(bit)
The bit argument can be one of the following parameters:
ADC.WIDTH_9BIT : range 0 to 511
ADC.WIDTH_10BIT: range 0 to 1023
ADC.WIDTH_11BIT: range 0 to 2047
ADC.WIDTH_12BIT: range 0 to 4095
ADC.width(ADC.WIDTH_12BIT)
In summary:
. To read an analog value you need to import the ADC class;
To create an ADC object simply use ADC(Pin(GPIO)), in which GPIO is the number of the GPIO you want to read the analog values;
To read the analog value, simply use the read() method on the ADC object.

## Slide 394: TIPS
https://randomnerdtutorials.com/esp32-adc-analog-read-arduino-ide/
Note: ADC2 pins cannot be used when Wi-Fi is used. So, if you’re using Wi-Fi and you’re having trouble getting the value from an ADC2 GPIO, you may consider using an ADC1 GPIO instead, that should solve your problem.
ADC is Non-linear
Ideally, you would expect a linear behavior when using the ESP32 ADC pins. However, that doesn’t happen. What you’ll get is a behavior as shown in the following chart:

## Slide 395: TP8 - 2 – OLED ON ESP32

## Slide 396: MicroPython: OLED Display with ESP32 and ESP8266
https://randomnerdtutorials.com/micropython-oled-display-esp32-esp8266/
https://randomnerdtutorials.com/esp32-i2c-communication-arduino-ide/
In this guide we’ll use the 0.96 inch SSD1306 OLED display that is 128×64 pixels and uses I2C communication protocol.

## Slide 397: SSD1306 OLED Library – Part 1
#MicroPython SSD1306 OLED driver, I2C and SPI interfaces created by Adafruit
import time
import framebuf
# register definitions
SET_CONTRAST = const(0x81)
SET_ENTIRE_ON = const(0xa4)
SET_NORM_INV = const(0xa6)
SET_DISP = const(0xae)
SET_MEM_ADDR = const(0x20)
SET_COL_ADDR = const(0x21)
SET_PAGE_ADDR = const(0x22)
SET_DISP_START_LINE = const(0x40)
SET_SEG_REMAP = const(0xa0)
SET_MUX_RATIO = const(0xa8)
SET_COM_OUT_DIR = const(0xc0)
SET_DISP_OFFSET = const(0xd3)
SET_COM_PIN_CFG = const(0xda)
SET_DISP_CLK_DIV = const(0xd5)
SET_PRECHARGE = const(0xd9)
SET_VCOM_DESEL = const(0xdb)
SET_CHARGE_PUMP = const(0x8d)
class SSD1306:
def __init__(self, width, height, external_vcc):
self.width = width
self.height = height
self.external_vcc = external_vcc
self.pages = self.height // 8
# Note the subclass must initialize self.framebuf to a framebuffer.
# This is necessary because the underlying data buffer is different
# between I2C and SPI implementations (I2C needs an extra byte).
self.poweron()
self.init_display()
def show(self):
x0 = 0
x1 = self.width - 1
if self.width == 64:
# displays with width of 64 pixels are shifted by 32
x0 += 32
x1 += 32
self.write_cmd(SET_COL_ADDR)
self.write_cmd(x0)
self.write_cmd(x1)
self.write_cmd(SET_PAGE_ADDR)
self.write_cmd(0)
self.write_cmd(self.pages - 1)
self.write_framebuf()
def init_display(self):
for cmd in (
SET_DISP | 0x00, # off
# address setting
SET_MEM_ADDR, 0x00, # horizontal
# resolution and layout
SET_DISP_START_LINE | 0x00,
SET_SEG_REMAP | 0x01, # column addr 127 mapped to SEG0
SET_MUX_RATIO, self.height - 1,
SET_COM_OUT_DIR | 0x08, # scan from COM[N] to COM0
SET_DISP_OFFSET, 0x00,
SET_COM_PIN_CFG, 0x02 if self.height == 32 else 0x12,
# timing and driving scheme
SET_DISP_CLK_DIV, 0x80,
SET_PRECHARGE, 0x22 if self.external_vcc else 0xf1,
SET_VCOM_DESEL, 0x30, # 0.83*Vcc
# display
SET_CONTRAST, 0xff, # maximum
SET_ENTIRE_ON, # output follows RAM contents
SET_NORM_INV, # not inverted
# charge pump
SET_CHARGE_PUMP, 0x10 if self.external_vcc else 0x14,
SET_DISP | 0x01): # on
self.write_cmd(cmd)
self.fill(0)
self.show()
def poweroff(self):
self.write_cmd(SET_DISP | 0x00)
def contrast(self, contrast):
self.write_cmd(SET_CONTRAST)
self.write_cmd(contrast)
def invert(self, invert):
self.write_cmd(SET_NORM_INV | (invert & 1))

## Slide 398: SSD1306 OLED Library – Part 2
def fill(self, col):
self.framebuf.fill(col)
def pixel(self, x, y, col):
self.framebuf.pixel(x, y, col)
def scroll(self, dx, dy):
self.framebuf.scroll(dx, dy)
def text(self, string, x, y, col=1):
self.framebuf.text(string, x, y, col)
class SSD1306_I2C(SSD1306):
def __init__(self, width, height, i2c, addr=0x3c, external_vcc=False):
self.i2c = i2c
self.addr = addr
self.temp = bytearray(2)
# Add an extra byte to the data buffer to hold an I2C data/command byte
# to use hardware-compatible I2C transactions. A memoryview of the
# buffer is used to mask this byte from the framebuffer operations
# (without a major memory hit as memoryview doesn't copy to a separate
# buffer).
self.buffer = bytearray(((height // 8) * width) + 1)
self.buffer[0] = 0x40 # Set first byte of data buffer to Co=0, D/C=1
self.framebuf = framebuf.FrameBuffer1(memoryview(self.buffer)[1:], width, height)
super().__init__(width, height, external_vcc)
def write_cmd(self, cmd):
self.temp[0] = 0x80 # Co=1, D/C#=0
self.temp[1] = cmd
self.i2c.writeto(self.addr, self.temp)
def write_framebuf(self):
# Blast out the frame buffer using a single I2C transaction to support
# hardware I2C interfaces.
self.i2c.writeto(self.addr, self.buffer)
def poweron(self):
pass
class SSD1306_SPI(SSD1306):
def __init__(self, width, height, spi, dc, res, cs, external_vcc=False):
self.rate = 10 * 1024 * 1024
dc.init(dc.OUT, value=0)
res.init(res.OUT, value=0)
cs.init(cs.OUT, value=1)
self.spi = spi
self.dc = dc
self.res = res
self.cs = cs
self.buffer = bytearray((height // 8) * width)
self.framebuf = framebuf.FrameBuffer1(self.buffer, width, height)
super().__init__(width, height, external_vcc)
def write_cmd(self, cmd):
self.spi.init(baudrate=self.rate, polarity=0, phase=0)
self.cs.high()
self.dc.low()
self.cs.low()
self.spi.write(bytearray([cmd]))
self.cs.high()
def write_framebuf(self):
self.spi.init(baudrate=self.rate, polarity=0, phase=0)
self.cs.high()
self.dc.high()
self.cs.low()
self.spi.write(self.buffer)
self.cs.high()
def poweron(self):
self.res.high()
time.sleep_ms(1)
self.res.low()
time.sleep_ms(10)
self.res.high()

## Slide 399: A. Upload OLED library with uPyCraft IDE
How to upload a library using uPyCraft IDE ?
1. Create a new file by pressing the New File button.
2. Copy the OLED library code into that file.
The OLED library code can be found here.
Note: the SSD1306 OLED display library was built by Adafruit and will no longer be updated. At the moment, it works fine.
3. After copying the code, save the file by pressing the Save button.
4. Call this new file “ssd1306.py” and press ok.
5. Click the Download and Run button.
The file should be saved on the device folder with the name “ssd1306.py” as highlighted in the following figure.
Now, you can use the library functionalities in your code by importing the library.

## Slide 400: How the OLED code works
Start by importing the necessary modules to interact with the GPIOs and send data to the OLED via I2C communication.
You need to import the Pin and I2C classes from the machine module AND also the OLED library that you previously uploaded to the board as ssd1306.py file.
The ESP32 default I2C pins are GPIO 22 (SCL) and GPIO 21 (SDA).
The ESP8266 default I2C pins are GPIO 5 (SCL) and GPIO 4 (SDA).
Define the OLED width and height on the following variables:
After that, create an SSD1306_I2C object called oled.
This object accepts the OLED width, height, and the I2C pins you’ve defined earlier.
After initializing the OLED display, you just need to use the text() function on the oled object to write text. After the text() function, you need to call the show() method to update the OLED.
The text() method accepts the following arguments:
Message: must be of type String
X position: where the text starts
Y position: where the text is displayed vertically
Text color: it can be either black or white. The default color is white and this parameter is optional:
  0 = black / 1 = white
For example, the following line writes the ‘Hello, World 1!’ message in white color. The text starts on x = 0 and y = 0.
The next line of code writes the text on the next line (y =10).
Finally, for the changes to take effect, use the show() method on the oled object.

## Slide 401: Other OLED functions
Fill the screen
To fill the entire screen with white, use the fill() function as follows:
To clear the screen use the fill() method as pass 0 as argument. (Sets all pixels to black):
oled.fill(1)
oled.show()
oled.fill(0)
oled.show()
Draw a pixel
To draw a pixel, use the pixel() method, followed by the show() method. The pixel() method accepts the following arguments:
X coordinate: pixel location horizontally
Y coordinate: pixel location vertically
Pixel color: can be black or white
  0 = black
  1 = white
For example, to draw a white pixel on the top left corner:
oled.pixel(0,0,1)
oled.show()
Invert colors
You can also invert the OLED colors: white with black and vice versa, using the invert() method:
To get back to the original colors, use:
oled.invert(False)
oled.show()

## Slide 402: DISPLAYING DATA FROM SENSORS
The text() function only accepts variables of type String as a message. Sensor readings are usually stored in int or float variables.
If you want to display sensor readings and they are stored in int or float variables, they should be converted to a String. To convert the data to a string you can use the str() function:
temperature = 12.34
temperature_string = str(temperature)
oled.text(temperature_string)
oled.show()
Then, you can display the temperature_string variable on the OLED using the text() and show() methods:
from machine import Pin, I2C, ADC
import ssd1306
from time import sleep
# ESP32 Pin assignment
i2c = I2C(-1, scl=Pin(22), sda=Pin(21))
# ESP8266 Pin assignment
#i2c = I2C(-1, scl=Pin(5), sda=Pin(4))
pot= ADC(Pin(34))
pot.atten(ADC.ATTN_11DB) #Full range 3.3V
oled_width = 128
oled_height = 64
oled = ssd1306.SSD1306_I2C(oled_width, oled_height, i2c)
oled.text('Hello, World 1!', 0, 0)
oled.text('Hello, World 2!', 0, 10)
oled.text('Hello, World 3!', 0, 20)
while True:
#led.value(not led.value())
pot_value = pot.read()
print(pot_value)
#Efface l'écran
oled.fill(0)
sleep(0.1)
#Passe la valeur du potard à l'écran
#oled.text('Hello, World 4!', 0, 30)
oled.text(str(pot_value), 50, 30)
oled.show()

## Slide 403: TP8 - 4 – CAPACITIVE TOUCH

## Slide 404: Introducing the ESP32 Touch Sensor
The ESP32 has 10 capacitive sensing GPIOs.
These GPIOs can sense variations in anything that holds an electrical charge, like the human skin. So, they can detect variations induced when touching the GPIOs with a finger. Here are the capacitive touch GPIOs:
 T0 (GPIO 4)
 T1 (GPIO 0)
 T2 (GPIO 2)
 T3 (GPIO 15)
 T4 (GPIO 13)
 T5 (GPIO 12)
 T6 (GPIO 14)
 T7 (GPIO 27)
 T8 (GPIO 33)
 T9 (GPIO 32)
Pink PIN are touch sensitive
Note: Touch sensor 1 is GPIO 0. However, it’s not available as a pin in the ESP32 model with 30 GPIOs. GPIO 0 is available on the board with 36 pins.
https://docs.espressif.com/projects/esp-idf/en/latest/api-reference/peripherals/touch_pad.html

## Slide 405: MICRO-PYTHON SCRIPT
Pin 0 that corresponds to GPIO 4. Wire a cable to GPIO 4, in a way that you can touch the metal part:
from machine import TouchPad, Pin
from time import sleep
touch_pin = TouchPad(Pin(4))
while True:
touch_value = touch_pin.read()
print(touch_value)
sleep(0.5)
To read from the ESP32 touch pins, you need:
1 - to import the TouchPad class from the machine module.
2 - the Pin class to setup the GPIOs, and
3 - the sleep() method to add delays.
Then, create a TouchPad object called touch_pin on GPIO 4:
Finally, to read the value from the touch pin, use the read() method on the TouchPad object as follows:
Then, the touch pin reading is printed on the Shell:

## Slide 406: DEMONSTRATION
Note: the values you get depend on the board, on your surroundings, on the wires you’re using and other external factors.

## Slide 407: OTHER CAPACITIVE TOUCH EXAMPLE
Use the TouchPad class in the machine module:
from machine import TouchPad, Pin
t = TouchPad(Pin(14))
t.read() # Returns a smaller number when touched
TouchPad.read returns a value relative to the capacitive variation. Small numbers (typically in the tens) are common when a pin is touched, larger numbers (above one thousand) when no touch is present. However the values are relative and can vary depending on the board and surrounding composition so some calibration may be required.
There are ten capacitive touch-enabled pins that can be used on the ESP32: 0, 2, 4, 12, 13 14, 15, 27, 32, 33. Trying to assign to any other pins will result in a ValueError.
Note that TouchPads can be used to wake an ESP32 from sleep:
import machine
from machine import TouchPad, Pin
import esp32
t = TouchPad(Pin(14))
t.config(500) # configure the threshold at which the pin is considered touched
esp32.wake_on_touch(True)
machine.lightsleep() # put the MCU to sleep until a touchpad is touched
For more details on touchpads refer to Espressif Touch Sensor

## Slide 408: ARDUINO LIKE SCRIPT
touchRead()
Reading the touch sensor is straightforward. In the Arduino IDE, you use
the touchRead() function, that accepts as argument, the GPIO you want to read.
// ESP32 Touch Test
// Just test touch pin - Touch0 is T0 which is on GPIO 4.
void setup()
{
Serial.begin(115200);
delay(1000); // give me time to bring up serial monitor
Serial.println("ESP32 Touch Test");
}
void loop()
{
Serial.println(touchRead(4)); // get value of Touch 0 pin = GPIO 4
delay(1000);
}
This example reads the touch pin 0 and displays the results in the serial monitor.
The T0 pin (touch pin 0), corresponds to GPIO 4, as we’ve seen previously in the pinout.

## Slide 409: TOUCH SENSITIVE LED
// set pin numbers
const int touchPin = 4;
const int ledPin = 16;
// change with your threshold value
const int threshold = 20;
// variable for storing the touch pin value
int touchValue;
void setup(){
Serial.begin(115200);
delay(1000);
pinMode (ledPin, OUTPUT);
}
void loop(){
// read the state of the pushbutton value:
touchValue = touchRead(touchPin);
Serial.print(touchValue);
// check if the touchValue is below the threshold
// if it is, set ledPin to HIGH
if(touchValue < threshold){
// turn LED on
digitalWrite(ledPin, HIGH);
Serial.println(" - LED on");
}
else{
// turn LED off
digitalWrite(ledPin, LOW);
Serial.println(" - LED off");
}
delay(500);
}
In our case, when we aren’t touching the pin, the normal value is above 70 and when we touch the aluminum foil it drops to some value below 10.
So, we can set a threshold value, and when the reading goes below that value, an LED lights up.
A good threshold value in this case is 20, for example.

## Slide 410: TP8 - 5 – HALL EFFECT SENSOR

## Slide 411: READ HALL EFFECT SENSOR
The ESP32 features a built-in hall effect sensor which is located as shown in the figure
below (behind that metal cap):
A hall effect sensor can detect variations in the magnetic field in its surroundings.
The greater the magnetic field, the greater the output voltage.
A hall effect sensor can be combined with a threshold detection to act as a switch. Hall effect sensors are mainly used to:
 Detect proximity;
 Calculate positioning;
 Count the number of revolutions of a wheel;
 Detect a door closing;
 And much more.

## Slide 412: READ HALL EFFECT SENSOR
// Access the internal hall effect detector on the esp32 values can be quite low.
int val = 0;
void setup() {
Serial.begin(9600);
}
void loop() {
// read hall effect sensor value
val = hallRead();
Serial.println(val);
delay(1000);
}
Reading the hall effect sensor measurements with the ESP32 using the Arduino IDE is as simple as using the hallRead() function.
Or decreasing depending on the magnet pole that is facing the sensor:
NOTE: The closer the magnet is to the sensor, the greater the absolute values are.
Approaching a magnet to the ESP32 hall sensor and see the values increasing…

## Slide 413: MICROPYTHON SCRIPT: main.py
https://docs.micropython.org/en/latest/library/esp32.html?highlight=hall%20sensor#esp32.hall_sensor
from machine import TouchPad, Pin
import esp32
from time import sleep
touch_pin = TouchPad(Pin(4))
while True:
touch_value = touch_pin.read()
#print(touch_value)
hall_value = esp32.hall_sensor()
print("C=" + str(touch_value) + "|
B=" + str(hall_value))
sleep(0.5)

## Slide 414: TP9 – 1 MQTT ON ESP32/ESP8266

## Slide 415: MicroPython – Getting Started with MQTT on ESP32/ESP8266
As an example, we’ll exchange simple text messages between two ESP boards. The idea is to use the concepts learned here to exchange sensor readings, or commands.
MQTT Broker
To use MQTT, you need a broker. We’ll be using Mosquitto broker installed on a Raspberry Pi.
Read How to Install Mosquitto Broker on Raspberry Pi.
If you’re not familiar with MQTT make sure you read our introductory tutorial: What is MQTT and How It Works
https://randomnerdtutorials.com/how-to-install-mosquitto-broker-on-raspberry-pi/
https://randomnerdtutorials.com/what-is-mqtt-and-how-it-works/

## Slide 416: HOW MQTT WORKS

## Slide 417: What is MQTT and How It Works
MQTT stands for
Message Queuing Telemetry Transport.
It is a lightweight publish and subscribe system where you can publish and receive messages as a client.
MQTT is a simple messaging protocol, designed for constrained devices with low-bandwidth. So, it’s the perfect solution for Internet of Things applications. MQTT allows you to send commands to control outputs, read and publish data from sensor nodes and much more.
Therefore, it makes it really easy to establish a communication between multiple devices.
If you like home automation and you want to build a complete home automation system, I recommend downloading my home automation course.

## Slide 418: HIGH LEVEL OVERVIEW
You can send a command with a client (like Node-RED) to control an output:
Or you can read data from a sensor and publish it to a client (like Node-RED):
MQTT Basic Concepts
In MQTT there are a few basic concepts that you need to understand:
    Publish/Subscribe
    Messages
    Topics
    Broker

## Slide 419: HIGH LEVEL OVERVIEW
MQTT – Publish/Subscribe:
The first concept is the publish and subscribe system. In a publish and subscribe system, a device can publish a message on a topic, or it can be subscribed to a particular topic to receive messages
For example Device 1 publishes on a topic.
Device 2 is subscribed to the same topic as device 1 is publishing in.
So, device 2 receives the message.
MQTT – Messages:
Messages are the information that you want to exchange between your devices. Whether it’s a command or data.
MQTT – Topics:
Another important concept are the topics.
Topics are the way you register interest for incoming messages or how you specify where you want to publish the message.
Topics are represented with strings separated by a forward slash. Each forward slash indicates a topic level. Here’s an example on how you would create a topic for a lamp in your home office:
Note: topics are case-sensitive, which makes these two topics different:

## Slide 420: HIGH LEVEL OVERVIEW
If you would like to turn on a lamp in your home office using MQTT you can imagine the following scenario:
You have a device that publishes “on” and “off” messages on the home/office/lamp topic.
You have a device that controls a lamp (it can be an ESP32, ESP8266, or any other board). The ESP32 that controls your lamp, is subscribed to that topic: home/office/lamp.
So, when a new message is published on that topic, the ESP32 receives the “on” or “off” message and turns the lamp on or off.
This first device, can be an ESP32, an ESP8266, or an Home Automation controller platform like Node-RED, Home Assistant, Domoticz, or OpenHAB, for example.

## Slide 421: MQTT – Broker
At last, you also need to be aware of the term broker.
The broker is primarily responsible for receiving all messages, filtering the messages, decide who is interested in them and then publishing the message to all subscribed clients.
There are several brokers you can use. In our home automation projects we use the Mosquitto broker which can be installed in the Raspberry Pi. Alternatively, you can use a cloud MQTT broker.

## Slide 422: How to Use MQTT in Home Automation and IoT Projects
As we’ve seen previously, MQTT is great for home automation and internet of things projects. If you want to start making your own projects using MQTT here’s an example of what you can do.
Here’s the steps you should follow:
1) Set up your Raspberry Pi. Follow our Getting Started Guide with Raspberry Pi.
2) Enable and Connect your Raspberry Pi with SSH.
3) You need Node-RED installed on your Pi and Node-RED Dashboard.
4) Install the Mosquitto broker on the Raspberry Pi.
5) Add the ESP8266 or the ESP32 to this system. You can follow the next MQTT tutorials:
ESP32 and Node-RED with MQTT – Publish and Subscribe
ESP8266 and Node-RED with MQTT – Publish and Subscribe

## Slide 423: Installing Mosquitto Broker on Raspbian OS
Installing Mosquitto Broker on Raspbian OS
Open a new Raspberry Pi terminal window:
To install the Mosquitto Broker enter these next commands:
pi@raspberry:~ $ sudo apt update
pi@raspberry:~ $ sudo apt install -y mosquitto mosquitto-clients
You’ll have to type Y and press Enter to confirm the installation.
To make Mosquitto auto start on boot up enter:
pi@raspberry:~ $ sudo systemctl enable mosquitto.service
Testing Installation
Send the command:
pi@raspberry:~ $ mosquitto -v
This returns the Mosquitto version that is currently running in your Raspberry Pi.
It should be 1.4.X or above.
Raspberry Pi IP Address
To use Mosquitto broker later on your projects, you’ll need your Raspberry Pi IP address. To retrieve your Raspberry Pi IP address, type the next command in your Terminal window:
pi@raspberry:~ $ hostname -I

## Slide 424: Testing Mosquitto Broker on Raspbian OS
After installing MQTT Broker, I recommend installing an MQTT Client to test the Broker installation and publish sample messages.
The next command shows how to install MQTT Mosquitto Client:
pi@raspberry:~ $ sudo apt-get install mosquitto-clients
You’ll have to type Y and press Enter to confirm the installation.
Run Mosquitto on background as a daemon: pi@raspberry:~ $ mosquitto -d
Subscribing to testTopic Topic
To subscribe to an MQTT topic with Mosquitto Client open a terminal Window #1 and enter the command:
pi@raspberry:~ $ mosquitto_sub -d -t testTopic
You’re now subscribed to a topic called testTopic.
Publishing “Hello World!” Message to testTopic Topic
To publish a sample message to testTopic, open a terminal Window #2
and run this command:
pi@raspberry:~ $ mosquitto_pub -d -t testTopic -m "Hello world!"
The message “Hello World!” is received in Window #1 as illustrated in the figure above.

## Slide 425: PUBLISHING A MESSAGE TO MULTIPLE CLIENTS
Having Window #1 still subscribed to topic testTopic,
open a new terminal Window #3
and run this command to subscribe to testTopic topic:
pi@raspberry:~ $ mosquitto_sub -d -t testTopic
On Window #2 publish the “Hello World!” message:
pi@raspberry:~ $ mosquitto_pub -d -t testTopic -m "Hello world!"
Since two clients are subscribed to testTopic topic, they will both receive “Hello world!” message.
This simple example shows how MQTT works and how your devices (for example: ESP8266) could be subscribed to the same topic to receive messages or a device could publish messages to multiple devices.
https://randomnerdtutorials.com/testing-mosquitto-broker-and-client-on-raspbbery-pi/

## Slide 426: PROJECT OVERVIEW
Here’s a high-level overview of the project we’ll build:
ESP#1 publishes messages on the hello topic. It publishes a “Hello” message followed by a counter (Hello 1, Hello 2, Hello 3, …). It publishes a new message every 5 seconds.
ESP#1 is subscribed to the notification topic to receive notifications from the ESP#2 board.
ESP#2 is subscribed to the hello topic. ESP #1 is publishing in this topic. Therefore, ESP#2 receives ESP#1 messages.
When ESP#2 receives the messages, it sends a message saying ‘received’. This message is published on the notification topic. ESP#1 is subscribed to that topic, so it receives the message.

## Slide 427: PREPARING ESP#1
Let’s start by preparing ESP#1: .It is subscribed to the notification topic
                It publishes on the hello topic
Importing umqtttsimple library:
To use MQTT with the ESP32/ESP8266 and MicroPython, you need to install the umqttsimple library.
1. Create a new file by pressing the New File button.
2. Copy the umqttsimple library code into it. You can access the umqttsimple library code in the following link:
https://raw.githubusercontent.com/RuiSantosdotme/ESP-MicroPython/master/code/MQTT/umqttsimple.py
4. Call this new file “umqttsimple.py” and press ok.
5. Click the Download and Run button.
Now, you can use the library functionalities in your code by importing the library.
3. Save the file by pressing the Save button.
6. The file should be saved on the device folder with the name “umqttsimple.py” as highlighted in the figure below.

## Slide 428: PREPARING ESP#1: How the Code Works - boot.py
How the Code Works
You need to import all the following libraries:
Set the debug to None and activate the garbage collector.
In the following variables, you need to enter your network credentials and your broker IP address.
To create an MQTT client, we need to get the ESP unique ID. That’s what we do in the following line (it is saved on the client_id variable).
Next, write the topic the ESP#1 is subscribed to, and the topic it will be publishing messages:
Then, create the following variables:
The last_message variable will hold the last time a message was sent.
The message_interval is the time between each message sent. Here, we’re setting it to 5 seconds (this means a new message will be sent every 5 seconds).
The counter variable is simply a counter to be added to the message.
After that, we make the procedures to connect to the network.

## Slide 429: PREPARING ESP#1: How the Code Works - main.py
In the main.py file is where we’ll write the code to publish and receive the messages:
topic_sub))
The first thing you should do is creating a callback function (cb) that accept as parameters the topic and the message and WILL run whenever a message is published on a topic the ESP is subscribed to.
- Start by printing the topic and the message.
Then, check if the message was published on the notification topic, and if the content of the message is ‘received’.
If this if statement is True, it means that ESP#2 received the ‘hello’ message sent by ESP#1. Basically, this callback function handles what happens when a certain message is received on a certain topic.
Connect and subscribe : connect_and_subscribe() function responsible for connecting to the broker as well as to subscribe to a topic.
Start by declaring the client_id, mqtt_server and topic_sub variables as global variables.
This way, we can access these variables throughout the code.
Then, create a MQTTClient object called client and need to pass as parameters the cliend_id, and the IP address of the MQTT broker (mqtt_server).
These variables were set on the boot.py file.
After that, set the callback function to the client (sub_cb).
Next, connect the client to the broker using the connect() method on the MQTTClient object.
After connecting, we subscribe to the topic_sub topic. Set the topic_sub on the boot.py file (notification).
Finally, print a message and return the client:

## Slide 430: PREPARING ESP#1: How the Code Works - main.py
topic_sub))
Restart and reconnect: a function called restart_and_reconnect() will be called in case the ESP32 or ESP8266 fails to connect to the broker. It prints a message to inform that the connection was not successful. We wait 10 seconds. Then, we reset the ESP using the reset() method.
Receive and publish messages
Until now, we’ve created functions to handle tasks related with the MQTT communication. From now on, the code will call those functions to make things happen.
The first thing we need to do is to connect to the MQTT broker and subscribe to a topic. So, we create a client by calling the connect_and_subscribe() function.
In case we’re not able to connect to the MQTTT broker, we’ll restart the ESP by calling the restart_and_reconnect() function
In the while loop is where we’ll be receiving and publishing the messages. We use try and except statements to prevent the ESP from crashing in case something goes wrong.
Inside the try block, we start by applying the check_msg() method on the client.
The check_msg() method checks whether a pending message from the server is available. It waits for a single incoming MQTT message and process it. The subscribed messages are delivered to the callback function we’ve defined earlier (the sub_cb() function). If there isn’t a pending message, it returns with None.
Then, we add an if statement to checker whether 5 seconds (message_interval) have passed since the last message was sent.
If it is time to send a new message, we create a msg variable with the “Hello” text followed by a counter.
To publish a message on a certain topic, you just need to apply the publish() method on the client and pass as arguments, the topic and the message. The topic_pub variable was set to hello in the boot.py file.
After sending the message, we update the last time a message was received by setting the last_message variable to the current time.
Finally, we increase the counter variable in every loop.
If something unexpected happens, we call the restart_and_reconnect() function.

## Slide 431: UPLOADING SCRIPTS
That’s it for ESP#1. Remember that you need to upload all the next files to make the project work (you should upload the files in order):
    umqttsimple.py;
    boot.py;
    main.py.
After uploading all files, you should get success messages on: establishing a network connection; connecting to the broker; and subscribing to the topic.
AND see all the files under device folder

## Slide 432: PREPARING ESP#2: umqttsimple.py and boot.py
Let’s now prepare ESP#2:
It is subscribed to the hello topic
It publishes on the notification topic
Like the ESP#1, you also need to upload the umqttsimple.py, boot.py, and main.py files.
Importing umqttsimple
To use MQTT with the ESP32/ESP8266 and MicroPython, you need to install the umqttsimple library. Follow the steps described earlier to install the umqttsimple library in ESP#2.
You can access the umqttsimple library code in the following link:
https://raw.githubusercontent.com/RuiSantosdotme/ESP-MicroPython/master/code/MQTT/umqttsimple.py
This code is very similar with the previous boot.py file. You need to replace the following variables with your network credentials and the broker IP address.
The only difference here is that we subscribe to the hello topic and publish on the notification topic.
ssid = 'REPLACE_WITH_YOUR_SSID'
password = 'REPLACE_WITH_YOUR_PASSWORD'
mqtt_server = 'REPLACE_WITH_YOUR_MQTT_BROKER_IP'
topic_sub = b'hello'
topic_pub = b'notification'

## Slide 433: PREPARING ESP#2: main.py
This code is very similar with the main.py from ESP#1.
We create the sub_cb(), the connect_and_subscribe() and the restart_and_reconnect() functions.
This time, the sub_cb() function just prints information about the topic and received message.
In the while loop, we check if we got a new message and save it in the new_message variable.
If we receive a new message, we publish a message saying ‘received’ on the topic_sub topic
(in this case we set it to notification in the boot.py file).
That’s it for ESP#2.
Remember that you need to upload all the next files to make the project work (you should upload the files in order):
        umqttsimple.py;
        boot.py;
        main.py.
The ESP32/ESP8266 should establish a network connection and connect to the broker successfully.
def sub_cb(topic, msg):
print((topic, msg))
new_message = client.check_msg()
if new_message != 'None':
client.publish(topic_pub, b'received')

## Slide 434: DEMONSTRATION
After uploading all the necessary scripts to both ESP boards and having both boards and the Raspberry Pi with the Mosquitto broker running, you are ready to test the setup.
The ESP#2 should be receiving the “Hello” messages from ESP#1, as shown in the figure below
On the other side, ESP#1 board should receive the “received” message. The “received” message is published by ESP#2 on the notification topic. ESP#1 is subscribed to that topic, so it receives the message.

## Slide 435: TP9 – 2 MQTT - Connect ESP32/ESP8266 to Node-RED

## Slide 436: PROJECT OVERVIEW
In the Node-RED Dashboard, a slider switch allows you to control an output of the ESP32/ESP8266.
To simplify the project, we’ll control the on-board LED (GPIO 2).
 When you turn the slider switch on, Node-RED publishes a “on” message on the output topic. When the slider switch changes its state to off, it publishes a “off” message on the output topic.
The ESP32/ESP8266 is subscribed to the output topic.
When it receives a message, it turns the LED on or off accordingly - instead of an LED you can control any other output on a different GPIO;
The ESP32 takes temperature readings with the DS18B20 temperature sensor.
  =>The readings are published on the temp topic every 5 seconds;
Node-RED is subscribed to the temp topic.
=> So, it receives the DS18B20 temperature readings and publishes the readings in a chart.

## Slide 437: Introducing the DS18B20 Temperature Sensor
The DS18B20 temperature sensor is a one-wire digital temperature sensor.
This means that you can read the temperature with a very simple circuit setup.
It communicates on common bus, which means that you can connect several devices and read their values using just one digital pin.
Features
Here’s some main features of the DS18B20 temperature sensor:
 Communicates over 1-Wire bus communication
 Operating range temperature: -55ºC to 125ºC
 Accuracy +/-0.5 ºC (between the range -10ºC to 85ºC)
Copy:
https://github.com/RuiSantosdotme/ESPMicroPython/blob/master/code/MQTT/umqttsimple.py
Save to device (download and run)
Copy:
https://github.com/RuiSantosdotme/ESP-MicroPython/blob/master/code/MQTT/Node_RED_Client/boot.py
Save to device (download and run)
Resistance to DS18B20 = 4,7kOhm

## Slide 438: MICRO-PYTHON SCRIPT: BOOT.PY
import time
import onewire
import ds18x20
from umqttsimple import MQTTClient
import ubinascii
import machine
import micropython
import network
import esp
esp.osdebug(None)
import gc
gc.collect()
ssid = 'REPLACE_WITH_YOUR_SSID'
password = 'REPLACE_WITH_YOUR_PASSWORD'
mqtt_server = 'REPLACE_WITH_YOUR_MQTT_BROKER_IP'
#EXAMPLE IP ADDRESS
#mqtt_server = '192.168.1.144'
client_id = ubinascii.hexlify(machine.unique_id())
topic_sub = b'output'
topic_pub = b'temp'
last_sensor_reading = 0
readings_interval = 5
station = network.WLAN(network.STA_IF)
station.active(True)
station.connect(ssid, password)
while station.isconnected() == False:
pass
print('Connection successful')
print(station.ifconfig())
ds_pin = machine.Pin(14)
ds_sensor = ds18x20.DS18X20(onewire.OneWire(ds_pin))
led = machine.Pin(2, machine.Pin.OUT, value=0)

## Slide 439: MICRO-PYTHON SCRIPT: BOOT.PY
Among other libraries, you need to import the onewire and the ds18x20 library to read from the DS18B20 temperature sensor.
import onewire
import ds18x20
You also need to import the MQTTClient class from the umqttsimple library to set the ESP32/ESP8266 as an MQTT client.
from umqttsimple import MQTTClient
You need to include your network credentials as well as the broker IP address on the following variables:
ssid = 'REPLACE_WITH_YOUR_SSID'
password = 'REPLACE_WITH_YOUR_PASSWORD'
mqtt_server = 'REPLACE_WITH_YOUR_MQTT_BROKER_IP’
The ESP32/ESP8266 is subscribed to the output topic and publishes on the temp topic.
topic_sub = b'output'
topic_pub = b'temp’
Create auxiliary variables to save the last time a sensor reading was taken (last_sensor_reading) and
to save the interval between readings (readings_interval), here, we’re setting the interval to 5 seconds.
last_sensor_reading = 0
readings_interval = 5
Create a variable called ds_pin that refers to GPIO 14, data wire pin of DS18B20 sensor is connected to.
ds_pin = machine.Pin(14)
Then, create a ds18x20 object called ds_sensor on the ds_pin defined earlier.
If you want to read the sensor using a different pin, you need to modify the previous line.
ds_sensor = ds18x20.DS18X20(onewire.OneWire(ds_pin))
Finally, create a Pin object on GPIO 2 called led that is off when the ESP32 first boots.
led = machine.Pin(2, machine.Pin.OUT, value=0)
That’s it for the boot.py file. Proceed to the main.py file.
ssid = 'Livebox-BBB6'
password = ‘xxxxxxxxxxxxxx'
mqtt_server = '192.168.1.31'

## Slide 440: MICRO-PYTHON SCRIPT: MAIN.PY
def read_ds_sensor():
roms = ds_sensor.scan()
print('Found DS devices: ', roms)
print('Temperatures: ')
ds_sensor.convert_temp()
time.sleep(1)
for rom in roms:
temp = ds_sensor.read_temp(rom)
if isinstance(temp, float):
# uncomment for Fahrenheit
#temp = temp * (9/5) + 32.0
msg = (b'{0:3.1f}'.format(temp))
print(temp, end=' ')
print('Valid temperature')
return msg
return b'0.0'
def sub_cb(topic, msg):
print((topic, msg))
if msg == b'on':
led.value(1)
elif msg == b'off':
led.value(0)
def connect_and_subscribe():
global client_id, mqtt_server, topic_sub
client = MQTTClient(client_id, mqtt_server)
client.set_callback(sub_cb)
client.connect()
client.subscribe(topic_sub)
print('Connected to %s MQTT broker, subscribed to %s topic' %
(mqtt_server, topic_sub))
return client
def restart_and_reconnect():
print('Failed to connect to MQTT broker. Reconnecting...')
time.sleep(10)
machine.reset()
try:
client = connect_and_subscribe()
except OSError as e:
restart_and_reconnect()
while True:
try:
client.check_msg()
if (time.time() - last_sensor_reading) > readings_interval:
msg = read_ds_sensor()
client.publish(topic_pub, msg)
last_sensor_reading = time.time()
except onewire.OneWireError:
print('Failed to read/publish sensor readings.')
time.sleep(1)
except OSError as e:
restart_and_reconnect()

## Slide 441: MICRO-PYTHON SCRIPT: MAIN.PY
This script reads the temperature from the DS18B20 temperature sensor and publishes the sensor readings on the temp topic.
It also subscribes the ESP32/ESP8266 to the output topic and turns the on-board LED on or off accordingly.
DS18B20 temperature readings
We start by creating a function called read_ds_sensor(). You can use this function in other projects that use the DS18B20 sensor.
def read_ds_sensor():
The DS18B20 communicates via 1-Wire communication protocol.
This means you can read several temperature sensors wired on the same GPIO.
The function starts by scanning for DS18B20 sensors and saves the found addresses on the roms variable.
roms = ds_sensor.scan()
Then, you need to execute the convert_temp() function to initiate a temperature reading and wait a second.
ds_sensor.convert_temp()
After that, we can read the temperature on the addresses found earlier by using the read_temp()
method and passing the address as argument.
temp = ds_sensor.read_temp(rom)
Then, check if it has have valid temperature reading and create a msg variable with the sensor readings.
if isinstance(temp, float):
# uncomment for Fahrenheit
# temp = temp * (9/5) + 32.0
msg = (b'{0:3.1f}'.format(temp))
By default, we’re getting the temperature readings in Celsius degrees. If you want to get the temperature readings in Fahrenheit degrees,
you need to uncomment the following line of code.
# temp = temp * (9/5) + 32.0

## Slide 442: MICRO-PYTHON SCRIPT: MAIN.PY
MQTT functions
Then, we create functions to handle MQTT tasks: sub_cb,
connect_and_subscribe, and restart_and_reconnect. The connect_and_subscribe, and
restart_and_reconnect functions were already explained in detail in previous Units.
The sub_cb function handles what happens when a new message is received on the topic we are subscribed to.
In this case, the ESP32/ESP8266 is subscribed to the output topic.
When it receives a new message, we check if the content is either “on” or “off” and set the LED state accordingly.
print((topic, msg))
if msg == b'on’:
led.value(1)
elif msg == b'off’:
led.value(0)
In the following try and except statement, we create a new client by calling the connect_and_subscribe() function.
In case we’re not able to create a new client, call the restart_and_reconnect() function.
try:
client = connect_and_subscribe()
except OSError as e:
restart_and_reconnect()

## Slide 443: Getting and publishing messages
Getting and publishing messages
In the while loop, we check if we have a new message. New messages are then handled by the sub_cb function.
client.check_msg()
Then, check if 5 seconds (readings_interval) have passed since the last sensor reading.
if (time.time() - last_sensor_reading) > readings_interval:
If yes, call the read_ds_sensor() function to save a new temperature reading in the msg variable.
msg = read_ds_sensor()
After getting the temperature, publish it on the temp topic (topic_sub).
client.publish(topic_pub, msg)
Finally, update the last time the ESP32/ESP8266 published the temperature.
last_sensor_reading = time.time()
In case there’s an error getting the temperature from the sensor, we print an error message, and wait for one second before trying again.
except onewire.OneWireError:
print('Failed to read/publish sensor readings.’)
time.sleep(1)

## Slide 444: Importing the Node-RED flow
We won’t show you how to create the Node-RED flow from scratch.
We provide the code to import the complete flow, and then we’ll take a closer look at each node and see what they do.
To import the Node-RED flow, go to the GitHub repository and copy the code provided:
Node-RED flow: https://raw.githubusercontent.com/RuiSantosdotme/ESPMicroPython/master/code/MQTT/Node_RED_Client/Node_RED_Flow.txt
Next, in the Node-RED window, at the top right corner, select the menu, and go
to ImportClipboard.
Then, paste the code provided and click Import.
After a successful import, you should see the following nodes on your flow.
DEPLOY

## Slide 445: Understanding the flow - 1
Let’s look at each node and understand what they do.
LED Switch Node
The LED Switch node creates a switch in the UI (User Interface).
The switch is connected to an MQTT node called “output”.
The switch sends different messages to the output accordingly to its state.
If you double-click on the LED Switch node, you should get something as follows:
The “Group” field indicates in which part of the UI the switch appears.
For this example, we’ll leave the default settings.
When the switch is turned on (“On Payload”), we send a String message with “on” to the output (the MQTT output node).
When the switch is off, we send a “off” message to the output.

## Slide 446: Understanding the flow - 2
MQTT output node
When the switch changes its state, it sends an “on” or “off” message to an output node (in this case an MQTTT output node).
This node receives the messages and publishes them on a specific topic.
Double-click the MQTT output node.
The important fields are the “Server” and the “Topic”.
The “Server” field refers to the MQTT broker.
Because we’re using the Raspberry Pi to run both Node-RED and Mosquitto broker, we can set the “Server” to “localhost”.
The “topic” field refers to the topic where the messages will be published. As we’ve seen previously in this Unit, the switch publishes messages on the output topic.

## Slide 447: Understanding the flow - 3
MQTT temp node
The MQTT temp node listens for messages on a specific topic.
In this case, Node-RED wants to receive messages on the temp topic.
This is the topic the ESP32/ESP8266 is publishing the temperature readings.
Double-click the MQTT temp node.
As with the previous node, we set the “Server” field to the “localhost”.
Set the topic to temp and the QoS to 2.
QoS means quality of service. A QoS of 2 ensures that the message is always delivered exactly once.
You can learn more about MQTT QoS here.
In summary, the MQTT temp node receives the messages published on the temp topic and sends them to a chart.

## Slide 448: Understanding the flow - 4
Temperature chart node
The temperature chart node receives the temperature readings from the MQTT temp node and publishes them on a chart.
Double-click the temperature chart node.
You can select the type of chart, the X-axis and the Y-axis label, color and others.
In this example, the chart is set to display the sensor readings from the last hour.

## Slide 449: Node-RED
Click the Deploy button to save all the changes.
Now, your Node-RED application is ready. To access Node-RED Dashboard and see how your application looks, access any browser in your local network and type:
http://Your_RPi_IP_address:1880/ui
Your application should look as in the following figure.
You should have an LED switch, and a Temperature chart.
You can check the data at a specific data point by sliding the cursor over a point in
the chart.

## Slide 450: Wrapping Up
Now, you should be able to control the ESP32/ESP8266 on-board LED from the
Node-RED Dashboard and check the latest sensor readings on the chart.
Wrapping Up
In this project, you’ve learned the basic concepts to publish and subscribe messages using Node-RED and how to establish a communication between Node-RED and your ESP32/ESP8266 board.
You can modify the project presented here to control any other outputs and display readings from other sensors or other pieces of information you may find useful in your home automation system.

## Slide 451: ROUTEUR MQTT: NODE-RED
https://projetsdiy.fr/routeur-mqtt-node-red-sonoff-tasmota-cloudmqtt/
La première chose à faire et d’ajouter un Node MQTT au flow courant
Faites un double clic pour éditer les paramètres du Node. Cliquez sur le crayon à coté du sélecteur Add new mqtt-broker.
Configurer la connexion à Mosquitto
Server : indiquez l’adresse IP ou localhost si Mosquitto est installé sur le même Raspberry Pi que NodeRED
Port : 1883 par défaut
User et password à l’onglet Security (conseillé)

## Slide 452: ROUTEUR MQTT: NODE-RED
Il est possible de publier des messages automatiquement pour connaître l’état du routeur en allant sur l’onglet Messages pour
Le démarrage du routeur (birth message)
L’arrêt du routeur (close message)
Une erreur (will message) droit.
Je vous conseille de fixer le QoS à 2.
Terminer la configuration en cliquant sur Done dans le coin supérieur

## Slide 453: Déployer le routeur MQTT sur Node-RED
Il ne reste plus qu’à relier les deux Nodes et déployer le flow en cliquant sur Deploy dans le coin supérieur droit.
Ouvrez sur le Websocket UI sur cloudMQTT pour vérifier que le routeur est bien démarré.
Ici, j’ai également allumé une prise connectée Sonoff S26 hackée avec le firmware Tasmota. Le message avec l’état stopped a été envoyé au moment du déploiement du flow, c’est parfaitement normal.

## Slide 454: Déployer le routeur MQTT sur Node-RED
Routeur bi-directionnel pour les accessoires Tasmota
Cette configuration ne fonctionne malheureusement que dans un sens. Avec le flow précédent, On va pouvoir récupérer tous les états et les valeurs (sur Homy par exemple), mais on ne pourra pas renvoyer des commandes pour allumer / éteindre un module Sonoff. Pour faire cela, il va falloir renvoyer les messages entrant sur cloudMQTT et les renvoyer vers le broker local.
Pour que ça fonctionne, on va filtrer les messages suivants le type de topic. Tasmota publie des messages sur 3 topics différents :
cmnd : commande à exécuter sur le module (on, off, toggle)
stat : retour d’état d’une commande sur le module
tele : information sur l’état du module.
Le premier bloc transfert tous les messages publiés sur le topic stat/# vers cloudMQTT. Le # permet de renvoyer de tous les accessoires Tasmota
Le second flow transfert les commandes envoyés sur cloudMQTT sur le broker local (sur lequel sont connectés les accessoires Sonoff – Tasmota sont connectés). Cette fois on filtre uniquement les messages publiés sur le topic cmnd et qui se termine par POWER. Pour cela on utilise le + (wildcard un seul niveau*)
N’oubliez pas d’adapter le topic si vous avez configuré un préfix sur Tasmota
(*) le wildcard multi-niveau # ne fonctionne pas sur Node-RED.

## Slide 455: Déployer le routeur MQTT sur Node-RED
Connecter le routeur à cloudMQTT
Ajouter un nouveau Node MQTT de type Output sur le flow. Faites un double clic pour le configurer.
https://projetsdiy.fr/routeur-mqtt-node-red-sonoff-tasmota-cloudmqtt/
Configurer la connexion avec les paramètres récupérés sur l’instance cloudMQTT :
Server : l’instance cloudMQTT
Port : indiquez le port SSL pour que la connexion soit sécurisée
Cocher Enable secure SSL/TLS connection
Saisissez le user et password de l’instance dans l’onglet Security
Vous pouvez également configurer des messages qui permettront de connaître l’état du routeur. Voici un exemple de configuration.

## Slide 456: Déployer le routeur MQTT sur Node-RED
Code source du routeur MQTT Node-RED
Coller ce code de ce flow sur votre Node-RED puis modifiez les paramètres de connexion avant de le déployer.
[{"id":"4de21b42.3cb0d4","type":"mqtt in","z":"1c02b62a.c1ff4a","name":"","topic":"stat/#","qos":"0","datatype":"auto","broker":"80ccacd4.35a24","x":90,"y":100,"wires":[["ddff4f0.0c79fb"]]},{"id":"ddff4f0.0c79fb","type":"mqtt out","z":"1c02b62a.c1ff4a","name":"cloudMQTT","topic":"","qos":"","retain":"","broker":"6c628311.0486ac","x":330,"y":100,"wires":[]},{"id":"e6695679.c6a678","type":"mqtt in","z":"1c02b62a.c1ff4a","name":"","topic":"cmnd/+/POWER","qos":"0","datatype":"auto","broker":"6c628311.0486ac","x":120,"y":180,"wires":[["d756894a.745608","80b760e.ba703a"]]},{"id":"d756894a.745608","type":"mqtt out","z":"1c02b62a.c1ff4a","name":"Mosquitto local","topic":"","qos":"","retain":"","broker":"80ccacd4.35a24","x":340,"y":180,"wires":[]},{"id":"80b760e.ba703a","type":"debug","z":"1c02b62a.c1ff4a","name":"","active":true,"tosidebar":true,"console":false,"tostatus":false,"complete":"false","x":330,"y":240,"wires":[]},{"id":"80ccacd4.35a24","type":"mqtt-broker","z":"","name":"mosquitto","broker":"192.168.1.90","port":"1883","clientid":"","usetls":false,"compatmode":true,"keepalive":"60","cleansession":true,"birthTopic":"node-red-router","birthQos":"2","birthRetain":"false","birthPayload":"started","closeTopic":"node-red-router","closeQos":"2","closePayload":"stopped","willTopic":"node-red-router","willQos":"2","willPayload":"stopped"},{"id":"6c628311.0486ac","type":"mqtt-broker","z":"","name":"cloudMQTT","broker":"m24.cloudmqtt.com","port":"26307","tls":"","clientid":"","usetls":true,"compatmode":true,"keepalive":"60","cleansession":true,"birthTopic":"node-red-router/status","birthQos":"2","birthRetain":"false","birthPayload":"online","closeTopic":"node-red-router/status","closeQos":"2","closePayload":"stopped","willTopic":"node-red-router/status","willQos":"2","willPayload":"stopped"}]
Voilà, vous pouvez maintenant connecter autant d’accessoires domotiques et objets connectés MQTT et les piloter hors de chez vous depuis Homy ou une appli.
Rien ne vous empêche d’adapter le principe pour l’adapter à d’autres firmware (Espurna, ESPEasy, code Arduino ou Python…)

## Slide 457: TP10 – LoRa ON ESP32

## Slide 458: LoRa
What is LoRa?
LoRa is a wireless data communication technology that uses a radio modulation technique that can be generated by Semtech LoRa transceiver chips.
This modulation technique allows long range communication of small amounts of data (which means a low bandwidth), high immunity to interference, while minimizing power consumption. So, it allows long distance communication with low power requirements.

## Slide 459: LoRa
LoRa Frequencies :
LoRa uses unlicensed frequencies that are available worldwide. These are the most widely used frequencies:
868 MHz for Europe
915 MHz for North America
433 MHz band for Asia
Because these bands are unlicensed, anyone can freely use them without paying or having to get a license. Check the frequencies used in your country.
LoRa Applications :
LoRa long range and low power features, makes it perfect for battery-operated sensors and low-power applications in:
Internet of Things (IoT)
Smart home
Machine-to-machine communication
And much more…
So, LoRa is a good choice for sensor nodes running on a coil cell or solar powered, that transmit small amounts of data.
Keep in mind that LoRa is not suitable for projects that:
Require high data-rate transmission;
Need very frequent transmissions;
Or are in highly populated networks.

## Slide 460: LoRa Topologies
You can use LoRa in:
Point to point communication
Or build a LoRa network (using LoRaWAN for example)
Point to Point Communication
In point to point communication, two LoRa enabled devices talk with each other using RF signals.
For example, this is useful to exchange data between two ESP32 boards equipped with LoRa transceiver chips that are relatively far from each other or in environments without Wi-Fi coverage.
Unlike Wi-Fi or Bluetooth that only support short distance communication, two LoRa devices with a proper antenna can exchange data over a long distance.
You can easily configure your ESP32 with a LoRa chip to transmit and receive data reliably at more than 200 meters distance (you can get better results depending on your enviroment and LoRa settings). There are also other LoRa solutions that easily have a range of more than 30Km.
LoRaWAN
You can also build a LoRa network using LoRaWAN.
The LoRaWAN protocol is a Low Power Wide Area Network (LPWAN) specification derived from LoRa technology standardized by the LoRa Alliance. We won’t explore LoRaWAN in this tutorial, but for more information you can check the LoRa Alliance and The Things Network websites.

## Slide 461: LoRa
How can LoRa be useful in your home automation projects?
Let’s take a look at a practical application.
Imagine that you want to measure the moisture in your field. Although, it is not far from your house, it probably doesn’t have Wi-Fi coverage. So, you can build a sensor node with an ESP32 and a moisture sensor, that sends the moisture readings once or twice a day to another ESP32 using LoRa.
The later ESP32 has access to Wi-Fi, and it can run a web server that displays the moisture readings.

## Slide 462: LoRa module – RFM95/96/97/98
https://www.aliexpress.com/snapshot/0.html?spm=a2g0s.buyer_leave_review.0.0.3a846c1bhgQUif&orderId=3001775197871894&productId=32831799362

## Slide 463: LoRa module – RFM95/96/97/98

## Slide 464: LoRa - Schematics
In this section we’ll show you how to get started with LoRa with your ESP32 using Arduino IDE. As an example, we’ll build a simple LoRa Sender and a LoRa Receiver.
The LoRa Sender will be sending a “hello” message followed by a counter for testing purposes. This message can be easily replaced with useful data like sensor readings or notifications
To follow this part you need the following components:
2x ESP32 DOIT DEVKIT V1 Board
2x LoRa Transceiver modules (RFM95)
RFM95 LoRa breakout board (optional)
Jumper wires
Breadboard or stripboard

## Slide 465: LoRa - Alternative
2x TTGO LoRa32 SX1276 OLED
Instead of using an ESP32 and a separated LoRa transceiver module, there are ESP32 development boards with a LoRa chip and an OLED built-in, which makes wiring much simpler. If you have one of those boards, you can follow: TTGO LoRa32 SX1276 OLED Board: Getting Started with Arduino IDE.

## Slide 466: Preparing the project: Arduino IDE and RFM modules
Installing the LoRa Library
There are several libraries available to easily send and receive LoRa packets with the ESP32. In this example we’ll be using the arduino-LoRa library by sandeep mistry.
Getting LoRa Tranceiver Modules
To send and receive LoRa messages with the ESP32 we’ll be using the RFM95 transceiver module. All LoRa modules are transceivers, which means they can send and receive information. You’ll need 2 of them.
You can also use other compatible modules like Semtech SX1276/77/78/79 based boards including: RFM96W, RFM98W, etc…

## Slide 467: WIRING
Antenna
The RFM95 transceiver chip requires an external antenna connected to the ANA pin.
You can connect a “real” antenna, or you can make one yourself by using a conductive wire as shown in the figure below. Some breakout boards come with a special connector to add a proper antenna.
There are a few options that you can use to access the transceiver pins.
You may solder some wires directly to the transceiver;
Break header pins and solder each one separately;
Or you can buy a breakout board that makes the pins breadboard friendly.
We’ve soldered a header to the module as shown in the figure below.
The wire length depends on the frequency:
868 MHz: 86,3 mm (3.4 inch) (Remainder: l=/4=c/4f => l=3x108/(4*868x106)=86,4mm)
915 MHz: 81,9 mm (3.22 inch)
433 MHz: 173,1 mm (6.8 inch)
For our module we need to use a 86,3 mm wire soldered directly to the transceiver’s ANA pin. Note that using a proper antenna will extend the communication range.
Important: you MUST attach an antenna to the module.

## Slide 468: Wiring the RFM95 LoRa Transceiver Module
The RFM95 LoRa transceiver module communicates with the ESP32 using SPI communication protocol. So, we’ll use the ESP32 default SPI pins. Wire both ESP32 boards to the corresponding transceiver modules as shown in the next schematic diagram:
Here’s the connections between the RFM95 LoRa transceiver module and the ESP32:
ANA: Antenna
GND: GND
DIO3: don’t connect
DIO4: don’t connect
3.3V: 3.3V
DIO0: GPIO 2
DIO1: don’t connect
DIO2: don’t connect
GND: don’t connect
DIO5: don’t connect
RESET: GPIO 14
NSS: GPIO 5
SCK: GPIO 18
MOSI: GPIO 23
MISO: GPIO 19
GND: don’t connect
Note: the RFM95 transceiver module has 3 GND pins. It doesn’t matter which one you use, but you need to connect at least one.

## Slide 469: The LoRa Sender Sketch
This sketch transmits messages every 10 seconds using LoRa. It sends a “hello” followed by a number that is incremented in every message
Then, define the pins used by your LoRa module. If you’ve followed the previous schematic, you can use the pin definition used in the code.
If you’re using an ESP32 board with LoRa built-in, check the pins used by the LoRa module in your board and make the right pin assignment.
It starts by including the needed libraries.
Set the pins for the LoRa module.
LoRa transceiver modules listen to packets within its range. It doesn’t matter where the packets come from. To ensure you only receive packets from your sender, you can set a sync word (ranges from 0 to 0xFF).
And initialize the transceiver module with a specified frequency.
In the setup(), you initialize a serial communication.
Both the receiver and the sender need to use the same sync word. This way, the receiver ignores any LoRa packets that don’t contain that sync word.
Next, in the loop() you send the LoRa packets. You initialize a packet with the beginPacket() method.
You write data into the packet using the print() method. As you can see in the following two lines, we’re sending a hello message followed by the counter
Then, close the packet with the endPacket() method.
After this, the counter message is incremented by one in every loop, which happens every 10 seconds.

## Slide 470: Testing the Sender Sketch
Upload the code to your ESP32 board.
Make sure you have the right board and COM port selected.
After that, open the Serial Monitor, and press the ESP32 enable button. You should see a success message as shown in the figure below. The counter should be incremented every 10 seconds.

## Slide 471: The LoRa Receiver Sketch
Now, grab another ESP32 and upload the LoRa receiver sketch.
This sketch listens for LoRa packets with the sync word you’ve defined and prints the content of the packets on the Serial Monitor, as well as the RSSI.
The RSSI measures the relative received signal strength.
This sketch is very similar to the previous one. Only the loop() is different!:
You might need to change the frequency and the sycnword to match the one used in the sender sketch.
If there’s a new packet,
we’ll read its content while it is available.
To read the incoming data you use the readString() method.
In the loop() the code checks if a new packet has been received using the parsePacket() method.
The incoming data is saved on the LoRaData variable and printed in the Serial Monitor.
Finally, the code print the RSSI of the received packet in dB.

## Slide 472: Testing the LoRa Receiver Sketch
Upload this code to your ESP32.
At this point you should have two ESP32 boards with different sketches:
- the sender and
- the receiver.
Open the Serial Monitor for the LoRa Receiver, and press the LoRa Sender enable button. You should start getting the LoRa packets on the receiver.

## Slide 473: Wrapping Up
In summary, in this tutorial we’ve shown you the basics of LoRa technology:
LoRa is a radio modulation technique;
LoRa allows long-distance communication of small amounts of data and requires low power;
You can use LoRa in point to point communication or in a network;
LoRa can be especially useful if you want to monitor sensors that are not covered by your Wi-Fi network and that are several meters apart.
Taking It Further
Now, you should test the communication range between the Sender and the Receiver on your area.
The communication range greatly varies depending on your environment (if you live in a rural or urban area with a lot of tall buildings).
To test the communication range you can add an OLED display to the LoRa receiver and go for a walk to see how far you can get a communication.

## Slide 474: Taking It Further – OLED version

## Slide 476: TESTING THE DISTANCE
Additionally, note that we’re using the library’s default definitions for LoRa, you may get a wider communication range by changing some settings. We’ll not explore this topic in this Unit,
but there’s a discussion on github on to to configure the LoRa library for better range.
Feel free to take a look.

## Slide 477: TESTING THE DISTANCE AND ENERGY
The following table is based on midband frequency of 915MHz (North America - you'll get better results when using 868MHz) and sender and receiver isotropic antenna gains of 1 (e.g. a whip antenna without any gain)
Distance - SF/BW
10km - 7/500
20km - 8/500
30km - 9/500
40km - 10/500
60km - 11/500
80km - 12/500
100km - 11/250
125km - 12/250
https://www.loratools.nl/#/airtime
https://sx1272-lora-calculator.software.informer.com/download/
https://dramco.be/tools/lora-calculator/

## Slide 478: I - LES MICROCONTROLEURS
TP12 –
The Things Network (TTN) +
Node-Red

## Slide 479: OTAA vs ABP ?

## Slide 480: « LoRaWAN In a nutshell » : principes de jonction au réseau
Deux modes de jonction existent qui se distinguent par leur sécurité et leur facilité de mise en œuvre :
ABP : Activation By Personnalization
OTAA : Over The Air Activation
L’ABP:
Avantage : Raccordement au réseau simplifié ; l’objet est rapidement opérationnel.
Inconvénient : Les clés de chiffrement permettant la communication avec le réseau, sont préconfigurées dans l’objet : sécurité affaiblie.
ATTENTION : Cette stratégie de simplicité dans la procédure de jonction se fait au détriment de la sécurité. S’il y a intrusion physique dans l’objet, le vol des clés est possible et peut conduire à l’usurpation de l’identité de l’objet, entrainant une corruption des données collectées
Exemple : Un compteur d’eau pourrait envoyer une indication de consommation d’eau erronée pouvant entrainer des nuisances (inondation, surfacturation…).
Afin d’établir la jonction au réseau et d’identifier l’objet, il est nécessaire de connaitre plusieurs informations :
AppEUI : C’est un identifiant unique d’application qui permet de regrouper les objets. Cette adresse, sur 64 bits, permet de classer les périphériques par application. Ce paramètre est modifiable.
DevEUI : c’est un identifiant qui rend unique chaque objet, programmé en usine. Ce paramètre n’est théoriquement pas modifiable.
AppKey : Il s’agit d’un secret partagé entre le périphérique et le réseau, utilisé pour dériver les clefs de session. Ce paramètre peut être modifié.
Les clefs de chiffrements sont préprogrammées dans le périphérique :
DevAddr : il s’agit d’une adresse logique pour identifier l’objet dans le réseau.
NetSKey (Network Session Key) : Clé de chiffrement entre l’objet et l’opérateur utilisée pour les transmissions et valider l’intégrité des messages.
AppSKey (Application Session Key) : Clé de chiffrement entre l’objet et l’utilisateur (via l’application) utilisée pour les transmissions et valider l’intégrité des messages.
L’OTAA:
Avantage : Le réseau génère et envoie les clés de chiffrement ; la sécurité est renforcée.
C’est la méthode la plus utilisée dans le monde de l’IoT/LoRaWAN, car la plus sécurisée.
Inconvénient : L’objet doit implémenter ce mécanisme de jonction ce qui introduit une complexité supplémentaire.
Afin d’établir la jonction au réseau et d’identifier l’objet, il est nécessaire de connaitre plusieurs informations.
AppEUI : C’est un identifiant unique d’application qui permet de regrouper les objets. Cette adresse, sur 64 bits, permet de classer les périphériques par application. Ce paramètre est modifiable.
DevEUI : c’est un identifiant qui rend unique chaque objet, programmé en usine. Ce paramètre n’est théoriquement pas modifiable.
AppKey : Il s’agit d’un secret partagé entre le périphérique et le réseau, utilisé pour dériver les clefs de session. Ce paramètre peut être modifié.
Zoom sur l’OTAA
Le composant logiciel en charge d’établir le raccordement avec les objets et d’animer le cœur de réseau, est le “Network Server“. Lors d’une jonction de type OTAA, si l’objet est autorisé à rejoindre le réseau, celui-ci va échanger des clés de chiffrement propres à cette session avec le cœur de réseau.
Le Network Server va alors attribuer des informations propres à la session et les communiquer au périphérique :
DevAddr : adresse logique (équivalent d’une adresse IP) qui sera utilisé pour toutes les communications ultérieures.
NetSKey (Network Session Key) : Clé de chiffrement entre l’objet et l’opérateur utilisée pour les transmissions et valider l’intégrité des messages.
AppSKey (Application Session Key) : Clé de chiffrement entre l’objet et l’utilisateur (via l’application) utilisée pour les transmissions et valider l’intégrité des messages.

## Slide 481: The THINGS UNO
https://www.thethingsnetwork.org/docs/devices/uno/
https://www.microchip.com/design-centers/wireless-connectivity/low-power-wide-area-networks/lora-technology/sam-r34-r35
Troubles: https://sighmon.com/says/connecting-to-the-things-network/

## Slide 482: TUTORIEL THE THINGS UNO
1 – Dans l’IDE Arduino: installer la librairie TTN
2 – Charger le sketch DeviceInfo pour récupérer les identifiants EUI du RN2483 (Arduino Leonardo + PORT COM):
(remplacer freqPlan REPLACE_ME par la freqPlan de notre lieu (eg EU ou US)
3 – Ouvrir le port Série (9600 baud): => Device Information
        EUI: 0004A30B001BE16C
        Battery: 3283
        AppEUI: 0000000000000000
        DevEUI: 0004A30B001BE16C
        Data Rate: 5
        RX Delay 1: 1000
        RX Delay 2: 2000
        Use the EUI to register the device for OTAA
        ------------------------------------------
        4 – Recopier les DevEUI: (eg DevEUI: 0004A30B001BE16C)
        5 – Sur The Things Networks:
          Device registration https://www.thethingsnetwork.org/docs/devices/registration.html
          Console https://console.thethingsnetwork.org/
        Créer une application: eg thingsuno_test
        => Génére l’APPEUI: 70B3D57ED0036E7D
        Dans l’application, cliquer sur DEVICE: https://console.thethingsnetwork.org/applications/thingsuno_test/devices
        Activer le device sur TheThingsNetwork: soit par la méthode OTA soit par la méthode ABP
        Attention, pour OTA, il faut au moins le firmware V1.4 sur le RN2483 pour ne pas avoir l’erreur “No Channel“ (lié au duty cycle)
        – Choisir le sketch en function d’ABP ou OTAP
          6.1 rendre l’exemple SendABP.ino:
          Depuis la console TTN, récupérer les constantes du device en ABP :
            const char *devAddr = "26013946";
                const char *nwkSKey = "E400FBFA5C76C7836C2380F27ADB77FF";
                const char *appSKey = "7B0218AE8B0ACBCBE1414FE19F5ABD61";
                Et le coller dans l’exemple de l’IDE Arduino:
                Vérifier que l’on reçoit les données: 1 – sur TTN ou 2 – sur le port série
        6.2 Prendre l’exemple SendOTAA.ino:
              Depuis la console TTN, recopier
                const char *appEui = "70B3D57ED0036E7D";
                const char *appKey = "35ED785B4848E6F1A8F55C697F029706";
              Et le coller dans l’exemple de l’IDE Arduino et uploader le sketch:
              Vérifier que l’on reçoit les données: 1 – sur TTN ou 2 – sur le port série

## Slide 483: TUTORIEL SENDING DATA
        6, Test de data sensor: SendABp_DataSensor.ino, ajouter:
            uint32_t humidity = 7625;//à diviser par 100
            uint32_t temperature = 3215;//à diviser par 100
            byte payload[4];
            payload[0]=highByte(humidity);
            payload[1]=lowByte(humidity);
            payload[2]=highByte(temperature);
            payload[3]=lowByte(temperature);
            // Send it off
            ttn.sendBytes(payload, sizeof(payload));
        7. Sur TTN: Payload functions
        Dans Application/Payload Formats
        Decoder function => turn bytes into json objects !
        Initial decoder:
        function Decoder(bytes, port) {
        // Here can decode the payload into json.
        // bytes is of type Buffer.
        var length = bytes.length;
        var my_payload = ‘’;
        for (i = 0; i < length; i++) {
        //my_payload += String.fromCharCode(bytes[i]);
        my_payload += parseInt(bytes[i]); }
        Custom decoder:
        function Decoder(bytes, port) {
        // Decoder
        // bytes is of type Buffer.
        var humidity = (bytes[0] << 8) | bytes[1];
        var temperature = (bytes[2] << 8) | bytes[3];
        return{
        humidity: humidity,
        temperature: temperature}
        }
        A tester, dans le champ Payload:
        Eg 1D C9 0C 8F + SAVE Payload Format
https://www.thethingsnetwork.org/docs/devices/bytes.html

## Slide 484: I - LES MICROCONTROLEURS
TEST WITH RN2483

## Slide 485: TEST AVEC ARDUINO UNO + RN2483
1 – Dans l’IDE Arduino:
Installer la librairie TTN
Installer la librairie RN2483
Charger Demo_Arduino_Uno_RN2483
Configurer les pins du RN2483
        #define TX 10
        #define RX 11
        #define RST 12
        SoftwareSerial mySerial(TX, RX);
Dans le port Série: récupérer le DEV EUI: 0004A30B00201396
        2 – Recopier les DevEUI: (eg DevEUI: 0004A30B001BE16C)
        3 – Sur The Things Networks:
          Device registration https://www.thethingsnetwork.org/docs/devices/registration.html
          Console https://console.thethingsnetwork.org/
        Créer ou choisir une application: eg thingsuno_test
        Dans l’application, cliquer sur DEVICE: https://console.thethingsnetwork.org/applications/thingsuno_test/devices
        Activer le device sur TheThingsNetwork: soit par la méthode OTA soit par la méthode ABP
        Attention, pour OTAA, il faut avoir au moins le firmware V1.4 sur le RN2483
        pour ne pas avoir l’erreur “No Channel“ (lié au duty cycle)
        3.1 Depuis la console TTN, récupérer les constantes du device en ABP :
            const char *devAddr = "26013946";
                const char *nwkSKey = "E400FBFA5C76C7836C2380F27ADB77FF";
                const char *appSKey = "7B0218AE8B0ACBCBE1414FE19F5ABD61";
                Et le coller dans l’exemple de l’IDE Arduino + Vérifier que l’on reçoit les données: 1 – sur TTN ou 2 – sur le port série
                4. Insérer les lignes suivantes dans le sketch:

## Slide 486: COMMANDE RN2483

## Slide 487: TEST AVEC ARDUINO UNO + RN2483

## Slide 488: TUTORIEL DOWNLINK
        Test de Downlink + data sensor: SendABp_DataSensor_Downlink, ajouter:
#define LED_PIN 13
void led_on() { digitalWrite(LED_PIN, HIGH); }
void led_off() { digitalWrite(LED_PIN, LOW); }
void message(const uint8_t *payload, size_t size, port_t port)
{
  debugSerial.println("-- MESSAGE");
  debugSerial.print("Received " + String(size) + " bytes on port " + String(port) + ":");
  for (int i = 0; i < size; i++)
  {
  debugSerial.print(" " + String(payload[i]));
  }
  debugSerial.println();
if (payload[0] == 1){led_on();} else {led_off();}
}
Dans le void Setup():
ttn.onMessage(message); //For downlink

## Slide 489: I - LES MICROCONTROLEURS
TEST WITH RFM95

## Slide 490: TEST AVEC ARDUINO UNO + RFM95
1 – Dans l’IDE Arduino:
Installer la librairie TTN
Installer la librairie LMIC
Installer la librairie Low Power Master
Configurer les pins du RFM95 par exemple comme ci-dessous
2 – Recopier les DevEUI: (eg DevEUI: 0004A30B001BE16C)
3 – Sur The Things Networks:
          Dans l’application, créer un DEVICE: https://console.thethingsnetwork.org/applications/thingsuno_test/devices
        Activer le device sur TheThingsNetwork: méthode ABP
        3.1 Depuis la console TTN, récupérer les constantes du device en ABP :
            const char *devAddr = "26013946";
                const char *nwkSKey = "E400FBFA5C76C7836C2380F27ADB77FF";
                const char *appSKey = "7B0218AE8B0ACBCBE1414FE19F5ABD61";
                Et le coller dans l’exemple de l’IDE Arduino + Vérifier que l’on reçoit les données: 1 – sur TTN ou 2 – sur le port série
                4. Charger le sketch Arduino_LMIC.ino
                Ou faire un autre exemple
https://www.thethingsnetwork.org/labs/story/build-the-cheapest-possible-node-yourself
https://github.com/matthijskooijman/arduino-lmic
https://wiki.dragino.com/index.php?title=Connect_to_TTN
https://github.com/dragino/Arduino-Profile-Examples

## Slide 491: DRAGINO LoRa + GPS SHIELD
https://wiki.dragino.com/index.php?title=Lora_Shield

## Slide 492: I - LES MICROCONTROLEURS
TEST GPS + RFM95

## Slide 493: DRAGINO LoRa + GPS SHIELD
https://wiki.dragino.com/index.php?title=Lora/GPS_Shield
Tester avec le sketch TinyGPS.ino pour vérifier que le GPS fonctionne
Tester avec le sketch LoRa_GPS_Shield_TTN.ino
https://github.com/dragino/Arduino-Profile-Examples/tree/master/libraries/Dragino/examples/GPS

## Slide 494: LoRaWAN End Device Example
http://wiki.dragino.com/index.php?title=Connect_to_TTN#Use_LoRa_GPS_Shield_and_Arduino_as_LoRa_End_Device
1 – Dans l’IDE Arduino:
Installer la librairie TTN
Installer la librairie LMIC
Installer la librairie Low Power Master
Installer la librairie TinyGPS
Configurer les pins du RFM95 Shield comme ci-contre
2 – Sur The Things Networks:
          Dans l’application, créer un DEVICE:
          https://console.thethingsnetwork.org/applications/thingsuno_test/devices
        Mettre un DevEUI:
        Activer le device sur TheThingsNetwork: méthode ABP
        3.1 Depuis la console TTN, récupérer les constantes du device en ABP :
            const char *devAddr = "26013946";
                const char *nwkSKey = "E400FBFA5C76C7836C2380F27ADB77FF";
                const char *appSKey = "7B0218AE8B0ACBCBE1414FE19F5ABD61";
                Et le coller dans l’exemple de l’IDE Arduino + Vérifier que l’on reçoit les données: 1 – sur TTN ou 2 – sur le port série
                3 - Charger le sketch LoRa_GPS_Shield_TTN.ino
                4 – Dans le port série:
                Receive data:
                3914227: 10
                EV_TXCOMPLETE (includes waiting for RX windows)
                Packet queued
                LMIC.freq:868100000
                Receive data:
                5614245: 10
                EV_TXCOMPLETE (includes waiting for RX windows)
                ########### NO.1 ###########
                The longtitude and latitude and altitude are:
                [1.320810,43.678528,1000000/00]

## Slide 495: PAYLOAD FUNCTIONS
The payload: function Decoder(b, port) {
var lat = (b[0] | b[1]<<8 | b[2]<<16 | (b[2] & 0x80 ? 0xFF<<24 : 0)) / 10000;
var lng = (b[3] | b[4]<<8 | b[5]<<16 | (b[5] & 0x80 ? 0xFF<<24 : 0)) / 10000;
return {
  location: {
    latitude: lat,
    longitude: lng
    },
  love: "TTN payload functions"
  };
}

## Slide 496: I - LES MICROCONTROLEURS
GATEWAY LoRa

## Slide 497: GATEWAY LoRa: e.g. DRAGINO
Dragino:
https://wiki.dragino.com/index.php?title=Connect_to_TTN
https://medium.com/@marcozecchini.2594/connect-dragino-lg01-p-gateway-and-a-dragino-lora-shield-arduino-uno-to-the-things-network-301d27184e05
Dans le navigateur:
http://192.168.1.10/cgi-bin/luci/admin
User will see the login interface of LG01.
The account for Web Login is:
User Name: root
Password: dragino
https://medium.com/@marcozecchini.2594/connect-dragino-lg01-p-gateway-and-a-dragino-lora-shield-arduino-uno-to-the-things-network-301d27184e05
http://wiki.dragino.com/index.php?title=Connect_to_TTN#Use_LoRa_GPS_Shield_and_Arduino_as_LoRa_End_Device_2

## Slide 498: I - LES MICROCONTROLEURS
TTN to Node-Red

## Slide 499: TTN to NODE-RED
https://www.thethingsnetwork.org/docs/applications/nodered/
https://www.thethingsnetwork.org/docs/applications/nodered/quick-start.html
https://www.thethingsnetwork.org/docs/devices/uno/quick-start.html
http://silanus.fr/sin/?p=1163
On peut installer ces nodes :
1 - directement à partir du gestionnaire de palette de Node Red
2 - à partir d'un terminal :
  $ cd $HOME/.node-red $
  npm install node-red-contrib-ttn
L'installation terminée, on dispose de 3 nouveaux nodes dans la palette :

## Slide 500: RECEPTION DES DONNEES DE TTN DANS NODE-RED
Double cliquer sur le node ttn uplink pour le configurer :
Déployer le flow et observer les trace Debug :

## Slide 501: CONSTRUCTION DU FRONT END NODE-RED
Les fonctions getTemperature() et getHumidity() ont pour rôle de fournir un payload adapté au nodes du dashboard :
[{"id":"2c0d3796.eef9e8","type":"tab","label":"Flow 3","disabled":false,"info":""},{"id":"ead5f2fa.e891c8","type":"debug","z":"2c0d3796.eef9e8","name":"","active":true,"tosidebar":true,"console":false,"complete":"false","statusVal":"","statusType":"auto","x":610,"y":140,"wires":[]},{"id":"19503597.e16fa2","type":"ttn uplink","z":"2c0d3796.eef9e8","name":"","app":"d89401f7.eba358","dev_id":"myunodemo","field":"","x":280,"y":140,"wires":[["ead5f2fa.e891c8","99bf72ce.614e28","6539180a.36143"]]},{"id":"99bf72ce.614e28","type":"function","z":"2c0d3796.eef9e8","name":"getTemperature","func":"var temp = {}\ntemp.payload = msg.payload.temperature/100; // /100 pour remettre le bon format\nreturn temp;\n","outputs":1,"noerr":0,"initialize":"","finalize":"","x":620,"y":200,"wires":[["3375a2db.276366","b9214035.335d58"]]},{"id":"6539180a.36143","type":"function","z":"2c0d3796.eef9e8","name":"getHumidity","func":"var humidity = {}\nhumidity.payload = msg.payload.humidity/100; // /100 pour remettre le bon format;\nreturn humidity;\n","outputs":1,"noerr":0,"initialize":"","finalize":"","x":600,"y":260,"wires":[["17080723.4a0889","3778c092.f7a348"]]},{"id":"3375a2db.276366","type":"ui_chart","z":"2c0d3796.eef9e8","name":"temperature","group":"cea21180.eca388","order":0,"width":"12","height":"8","label":"Evolution de la temperature (°C)","chartType":"line","legend":"false","xformat":"HH:mm:ss","interpolate":"linear","nodata":"","dot":false,"ymin":"","ymax":"","removeOlder":1,"removeOlderPoints":"","removeOlderUnit":"3600","cutout":0,"useOneColor":false,"useUTC":false,"colors":["#1f77b4","#aec7e8","#ff7f0e","#2ca02c","#98df8a","#d62728","#ff9896","#9467bd","#c5b0d5"],"useOldStyle":false,"outputs":1,"x":870,"y":180,"wires":[[]]},{"id":"b9214035.335d58","type":"ui_gauge","z":"2c0d3796.eef9e8","name":"temperature","group":"cea21180.eca388","order":4,"width":"12","height":"6","gtype":"gage","title":"Température","label":"°C","format":"{{value}}","min":0,"max":"1000","colors":["#00b500","#e6e600","#ca3838"],"seg1":"","seg2":"","x":860,"y":220,"wires":[]},{"id":"17080723.4a0889","type":"ui_chart","z":"2c0d3796.eef9e8","name":"humidite","group":"cea21180.eca388","order":0,"width":"12","height":"8","label":"Evolution de l'humidité (%)","chartType":"line","legend":"true","xformat":"HH:mm:ss","interpolate":"linear","nodata":"","dot":false,"ymin":"0","ymax":"10000","removeOlder":1,"removeOlderPoints":"","removeOlderUnit":"3600","cutout":0,"useOneColor":false,"useUTC":false,"colors":["#1f77b4","#aec7e8","#ff7f0e","#2ca02c","#98df8a","#d62728","#ff9896","#9467bd","#c5b0d5"],"useOldStyle":false,"outputs":1,"x":860,"y":280,"wires":[[]]},{"id":"3778c092.f7a348","type":"ui_gauge","z":"2c0d3796.eef9e8","name":"humidite","group":"cea21180.eca388","order":4,"width":"12","height":"6","gtype":"gage","title":"Humidité Relative","label":"%HR","format":"{{value}}","min":0,"max":"100","colors":["#00b500","#e6e600","#ca3838"],"seg1":"","seg2":"","x":860,"y":320,"wires":[]},{"id":"d89401f7.eba358","type":"ttn app","appId":"dragino_test_application3","accessKey":"ttn-account-v2.NZWVxiBngSwuBVmiIPcmT3Vh3jJTehfyjLGK-MrPNw4","discovery":"discovery.thethingsnetwork.org:1900"},{"id":"cea21180.eca388","type":"ui_group","name":"TTN","tab":"5a0a53f3.c08c3c","order":1,"disp":true,"width":"24","collapse":false},{"id":"5a0a53f3.c08c3c","type":"ui_tab","name":"TTN","icon":"dashboard"}]
var temp = {}
temp.payload = msg.payload.temperature/100; // /100 pour remettre le bon format
return temp;
var humidity = {}
humidity.payload = msg.payload.humidity/100; // 100 pour remettre le bon format;
return humidity;

## Slide 502: PROPRIETES DES NODES ET CHARTS NODE-RED

## Slide 503: VISUALISATION DES DONNEES SUR LE FRONT-END NODE-RED

## Slide 504: I - LES MICROCONTROLEURS
MQTT from TTN

## Slide 505: MQTT FROM TTN to NODE-RED
Saisir le flow suivant :
Configurer le node mqtt in :
La consultation de la documentation de l'API de The Things Network permet de trouver les éléments suivants nécessaires à la configuration du node :
  Host: <Region>.thethings.network, where <Region> is last part of the handler you registered your application to, e.g. eu.
  Port: 1883
  Username: Application ID
  Password: Application Access Key
Topic: <AppID>/devices/<DevID>/up
Double-cliquer sur le node mqtt in pour faire apparaitre la boite de dialogue de configuration.

## Slide 506: MQTT FROM TTN to NODE-RED

## Slide 509: II – 3 ADRESSABLE DEVICES ?
II – 3 ADRESSABLE
DEVICES ?

## Slide 510: WHAT COMPONENTS TO USE WITH THE ARDUINO?

## Slide 511: QUELS COMPOSANTS UTILISER AVEC L’ARDUINO ?

## Slide 512: QUELS COMPOSANTS UTILISER AVEC L’ARDUINO ?
Capteur Flamme
Capteur Son
GPS
OptoCoupleur
Flex Sensor
Digital Strip
Capteur Température/Humidité
Matrice de LED
Capteur InfraRouge
Capteur Inclinaison
Capteur Force
Capteur Effet Hall
Capteur de mouvement PIR
Capteur de Gaz
Ecran LCD 16*2
Modules Sonar
Gyroscope 2 axes

## Slide 513: QUELS COMPOSANTS UTILISER AVEC L’ARDUINO ?
Kinect
Mini-capteur Manche
Capteur Couleur
Capteur Rotation
Capteur de chaleur
Camera JPEG
Capteur Vibration
Capteur Pression-Barométrique
Capteur Lumière
Dalle Tactile
Nunchuk
et bien d’autres que nous ne pourrions citer par manque de place…

## Slide 514: SENSORS Vs ACTUATORS
http://wiki.t-o-f.info/index.php?n=Arduino.Capteur
=> PAY US ON THE COMPONENTS OF THE ARDUINO KIT!
Actuators:
Sensors :

## Slide 515: I - MICROCONTROLLERS
I - MICROCONTROLLERS

## Slide 516: BUT BY THE WAY: A MICROCONTROLLER IS NEEDED FOR WHAT?
1 - A microcontroller takes something as input
2 - he takes a decision in relation to a program you entered in his memory, he calculates, he communicates...
3 - It produces an output result
Current platforms based on microcontrollers (such as the Arduino, Teensy, ESP32...) are real small computers taking lots of entries, dialogue between them by WIFI, showing items on OLED screens, pressing the engines etc.
Programs can be quite complex. But this isn't the goal in reality! Even if microcontrollers are powerful and can misrepresent them in computer,
GOAL: be normally independent interfaces, aggregating the sensors and actuators and which delegate to more complex computer calculations tasks.
There is so much to say... here's an explanation simple, reductive, but gives you an overview of its features:
Remember that:
a software implementation is always slower than a hard-wired logic implementation: the microprocessor executes a statement at the time (see also language VHDL-AMS=> FPGA programming)
Applications:
-microcontrollers are often used in embedded systems development, requiring specialized treatment (car stereos, mobile phones, mp3 player, GPS, etc.)
-but also to achieve rapid prototyping applications.

## Slide 517: MICROCONTROLLERS: PRO & CONS
The μcontroleurs = benefit of the μprocesseurs but limited to applications that do not require too much computing power, number of components very reduced, but often oversizing before the needs of the application
Benefits of microcontrollers:
- Simplification of the layout of the circuit board (no need to draw bus!)
- Reduced costs of Labor (design and Assembly)
reduction of congestion of the material and the circuit board
increase in the reliability of the system the
  number of components ↓
  connections components/materials and component PCB ↓.
Integration in technology MOS, CMOS, or HCMOS (High Speed CMOS) decrease in consumption - programming and advanced simulation environments
The defects of microcontrollers:
often oversized before the application needs
investment in development tools (except for the Arduino...)
write programs, test and test their implementation on the material that surrounds the µcontroleur possible
incompatibility of the development tools for microcontrollers same brand

## Slide 518: DEFINITION
A microcontroller is an integrated circuit gathering in one case all the electronic functions of a system:
a microprocessor (C.P.U.),
memory (RAM and EEPROM) data,
program memory (ROM,...),
parallel interfaces for the connection of inputs/outputs,
- interfaces (synchronous or asynchronous) series for dialogue with other units.
timers for generating or measuring signals with a high temporal precision,
analog-to-digital converters for processing analog signals.
a structure receiving the oscillator to pace the µproc
And the communications bus: address, data and controls that connect these various devices !

## Slide 519: INSIDE OF THE MICROCONTROLLER
1- C.P.U. (MICROPROCESSOR): usually consists of the following elements:
a counter program pointing the address of the next instruction to execute
an arithmetic and logical unit (ALU) to perform operations between the accumulator and an operand: loaded with calculations +, -, *, /, AND, OR, NOT
different registers containing the operands, the results of the operations, the addressing mode...
Typical operation:
1 - it sequentially executes the instructions stored in the program memory.
2 - it is capable of operating on binary words whose size, in bits, is that of the data bus
the microprocessor needs some elements to work:
so-called read only memory ROM: mainly to store the program
Free memory RAM : mainly to store the variables,
- devices (mainly to interact with the outside world)
a clock to pace it (mainly in quartz).
It may be noted that there are 2 categories of microprocessors: the CISC and the RISC.
- CISC (Complex Instruction Set Computer): the microprocessor has a significant number of instructions. Each of them runs in several periods of clocks.
- RISC (Reduced Instruction Set Computer): the microprocessor has a small number of instructions. Each of them runs in a clock period.

## Slide 520: CISC ou RISC
-In addition, with fewer transistors RISC heater less => can more easily increase in frequency.
Saved transistors are used to create memory or registers (the PowerPC RISC has 2 or 3 x more than a PC (CISC)), which avoids too often access to memory (slowing the processor).
In 1975, David Patterson (University of California, Berkeley):
80% of the instructions of a program use only 20% of the instructions of the CPU
idea: remove instructions that are not and thanks to space-saving add useful elements (such as the) memory, records...)
=> strategic choice to shorten the time CPU:
In the end: the ICSC decrease processing speed, but instructions are more complex, more powerful, and more numerous
on the contrary, the RISC is to move the major complexities of the hardware to the software,
=> a CISC to make a small complex,
=> a RISC program to make a big complicated program.
1 - The ICSC shorten the execution time by reducing the number of instructions per program a expensive processor (CISC) as complex and much heat
2 - the RISC shorten the execution time by reducing the number of clock cycles per statement (i.e., simple instructions take less time to interpret)
=> An economic processor (RISC) as simple and which consumes few... but that the program requires more standard and so more memory.
RISC VS CISC

## Slide 521: RISC VS CISC
The number of total cycle for the CISC: (2 movs + 1 cycle) + (1 mul × 30 cycles) = 32 cycles
the number of total cycle for the RISC: (3 movs × 1 cycle) + (5 × adds 1 cycle) + (5 × loops 1 cycle) = 13 cycles
ASM x 86 program fragment (multiplication of two integers):
10*5 = 50
10 + 10 + 10 + 10 + 10 = 50
Unfortunately, the RISC technology also has flaws:
indeed, fewer instructions is that the resulting software, to functions to accomplish equal, occupies more memory than a machine ICSC, as well statically that dynamically.
All RISC machines use the technique of "pipelining" to increase their benefits in terms of statements executed in the unit of time.
Sequencing of instructions in a processor without pipeline. It takes 15 cycles to run 3 instructions.
Sequencing of instructions in a processor equipped with a pipeline to 5 floors. It takes 9 cycles to run 5 instructions. At t = 5, all the floors of the pipeline are solicited, and 5 operations take place at the same time.
RISC 1 / CISC 0
What happens to a multiplication of 10 * 500000?
not so simple !
RISC 1 / CISC 1

## Slide 522: RISC VS CISC: POUR ALLER PLUS LOIN…
In summary:
There is no winner!
It depends on the context:
-In the CISC architecture, used especially in the range of the x 86 AMD, and INTEL, Cyrix..., designers rely on the reduction of the number of instructions required to run the program, designing very powerful instructions, which has the inconvenience of increase in average number of cycles machine needed to complete an instruction.
In this case, the frequency of the system is reduced because we have to introduce a phase of interpretation of the machine through the firmware code.
In the RISC architecture, we put a lot on the minimization of the number of cycles machine and it makes most executable instructions in a single clock cycle, allowing to increase the frequency of the system.
This is possible by eliminating the phase of interpretation through the simplicity of instructions that can be decoded and executed directly by a simple cable control unit. The simplification of the type RISC machines control units is particularly advantageous for the realization of the CPU on a single VLSI chip.
Obtained space allows, equal area of silica, to substantially increase the number of internal registers and embed directly on the chip's cache to exploit to the maximum speed of the microprocessor.
RISC VS CISC

## Slide 523
Do INTEL and AMD have any concerns to worry about?
RISC VS CISC

## Slide 524: THE MICROCONTROLLER INSIDE: MEMORY...
2.2 memory programs:
it contains instructions of the program to be run by the CPU.
This type of memory, called ROM, is only read.
Its programming requires a special procedure and equipment.
There are different types according to their programming mode: ROM content is programmed during its manufacture:
- The PROM programmable electrically only once by the developer (also called OTPROM)
the EPROM programmable electrically and erasable by UV light (also called UVPROM).
the programmable and erasable EEPROM electrically,
The Flash, much faster than the others.
2.3 data memory:
allows you to temporarily store the data generated by the CPU during the different phases of the digital processing (results of operations, States of sensors...).
These briefs are available in writing and reading.
There are 2 types:
of the memory (RAM) volatile (lost data in case of power failure) with a time of reading and writing short (a few ns),
Read only memory (EEPROM) (permanently data even if power supply failure) with a writing time high enough (a few ms) compared to the time of reading which is quite low (a few ns).

## Slide 525: THE MICROCONTROLLER INSIDE: MEMORY...
For example: the ATMEGA32 is equipped with 3 types of main memory:
1 - the FLASH: memory that keeps its content when it is no longer under tension. Capacity is 32 KB ($00 to $7FFF).
At the end of this memory-online space preset to the BOOTLOADER: small piece of program that runs before your own program in order to perform various operations.
2 - RAM: memory that loses its content when it is no longer supplied. Capacity of 2 k ($00 to $85F).
Allows to:
- store temporary information when running a program,
- contains the return address during a call to a sub program or an interrupt routine.
3 - In the EEPROM: memory that retains data when power failure. Capacity of 1 KB ($00 to $3FF).
It allows to memorize information that must be recharged to power.

## Slide 526
TO GO FURTHER

## Slide 527: THE MICROCONTROLLER INSIDE: PARALLEL INTERFACE
2.4 the parallel INTERFACE :
this type of interface, distributed on several ports (maximum 8-bit), allows to take into account:
logical States applied input (State of sensors) or
generate binary output (control of actuators) signals.
-The pins of these ports can be configured as input or output, with different options (open reminder resistance, output collector, interruption...).
-The configuration as well as the logical state of these pins is achieved by reading or writing operations in different registers associated with each port.
There are usually:
A registry of direction for a configuration input or output,
a data register copying logical States of each pin of ports,
a registry of option allowing several configurations as input or output.

## Slide 528: INSIDE OF THE MICROCONTROLLER
2.5 the INTERFACE series:
it allows the µcontroleur to communicate with other systems microprocessor based.
The data sent or received arise in the form of a temporal (on a single bit) succession of values binary images of a Word. There are 2 types of serial link: asynchronous and SYNCHRONOUS
Ø asynchronous serial communication :
this device does not provide synchronization clock signal.
Liaison units each have an internal clock clocked at the same frequency.
When one wants to make a binary Word, it generates a front descending on its issuing line.
At the end of the show of this word, the line returns to the high level.
The data to be transmitted may contain an additional bit called "parity" and used for error correction.
Ø SYNCHRONOUS serial :
in this device the transmission is synchronized by a clock signal from the master unit, jointly to the signal carrying data.
Examples:
SPI (Serial Peripheral Interface Bus) by Motorola => 3 wires
I2C (Inter Integrated Circuit) by Philips ~ 1980 => 2 wires
One Wire (Protocol of MAXIM DALLAS) => 1 wire
Example: your favorite serial RS232 managed by a UART or USART (Universal Asynchronous Receiver Transmitter) which is a universal asynchronous transceiver, (which has a buffer of 128 characters in the Arduino 7bits + 1 parity bit), and who does too, through a converter USB-serial, the connection to the PC.

## Slide 529: INSIDE OF THE MICROCONTROLLER
2.6 the CAN: analog-to-digital converter:
the built-in microcontrollers CAN is usually the type of "Successive Approximations".
It has several accessible multiplexed inputs via the pins of the parallel interface ports.
The CAN has normally 2 registers:
- a register of data containing the result of the conversion,
- a registry of control to launch and monitor conversion.
2.7. the TIMER: the Timers allow you to perform the following functions:
Generation of a periodic signal modulated (PWM) pulse width or not,
Generation of a calibrated pulse
timing,
counting of events.
Several registers associated with Timers allow to configure the modes described here.
2.8. the WATCHDOG (Watch Dog): is a system anti-plantage of the microcontroller, which ensures that there is no prolonged executions of a same sequence of instruction.
Example: If the program is waiting for the result of an external system (e.g. CAN) or if the program runs in an endless loop => no response-online block.
In practice: it resets periodically (at a definable interval) internal record thanks to the instruction clrwdt (clear watchdog).
If the program is blocked, more happening in the branch of reset and counting goes to the end (e.g. 16-bit counter that causes a Reset when it reaches its maximum (0xFFFF)), triggers the watchdog that restarts the program.
The watchdog of the AVR microcontrollers is timed by an internal clock at 1 MHz, so it can work also in the absence of the system clock because it is independent of it.

## Slide 530: Inside of the microcontroller: The ATMEGA328
The registers of devices allow to access
the configuration of embedded devices (USART, CAN, SPI,...) and timers, EEPROM...
and get the States on their functioning.
For example: the table below lists the name of the registers of the ATMEGA32
http://www.atmicroprog.com/cours/atmega/regsystem.php
Parallel I/O interfaces
Analog/Device converter
Serie port
Memory
Timers 8 and 16 bits

## Slide 531: INSIDE OF THE MICROCONTROLLER: THE BUS...
The various blocks are connected by 3 bus:
the address bus: allows the µprocessor to select the memory box or device to which it wants access to read or write information (instruction or given);
the data bus: allows the transfer of information between different blocks. This information will be: - either instructions,
    the data source or destination memory or devices;
the control bus: indicates if the current operation is a read or a write, if a device requires an interruption etc.

## Slide 532: FUSES
Fuses have always existed only for protection against the downloading of program in order to prevent duplication or disassembly:
In short of what lock all industrial curiosity program!
For example: the ATMEGA class has 21 fuses allowing multiple settings: source and clock speed, detector of undervoltage (brown-out)...
A programmed fuse as for value '0’ An unprogrammed fuse as for value "1"
Jargon used by Atmel:
so we can retain the intellectual logic is reversed.
Screenshot of the fuses on an ATMEGA32 with Pony Prog software

## Slide 533: FUSES
CKOPT | CKSEL3 | CKSEL2 | CKSEL1 | CKSEL0 | Frequency (MHz)
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0 | 2
1 | 0 | 0 | 1 | 1 | 4
1 | 0 | 1 | 0 | 0 | 8
CALIBRATED internal RC OSCILLATOR MODE: Uses the internal oscillator of RC type at speeds pre-set 1, 2, 4, 8 MHz. These frequencies are given for a supply voltage of 5V and 25 ° C.
CKOPT | CKSEL3 | CKSEL2 | CKSEL1 | Frequency range (MHZ) | oscillation capacitor Recommended
1 | 1 | 0 | 1 | 0.4 -0.9 * | -
1 | 1 | 1 | 0 | 0.9 - 3.0 | 12 - 22 pF
1 | 1 | 1 | 1 | 3.0 - 8.0 | 12 - 22 pF
0 | 101,110,111 |  |  | 1.0 <= | 12 - 22 pF
EXTERNAL quartz OSCILLATOR MODE:
The most used Mode.
CKOPT allows you to select 2 different modes: 1 - if programmed (0): rail to rail, either the maximum capacity.
2. If not programmed (1): the oscillation circuit will consume less energy but will have a limited operating frequency.
ATMEL calls to program this fuse for f=16 MHz
Bootlock2 | Bootlock1 | Protection type
1 | 1 | No restrictions of access to the memory.
1 | 0 | Programming the FLASH or EEPROM by programming series and parallel. The programming of the fuses is disabled
0 | 0 | No programming and checking the FLASH or EEPROM by programming series and parallel. The programming of the fuses is disabled
THE PROTECTION fuses:
Bootlock2, Bootlock1: pair of fuses for control rights of access to FLASH and EEPROM memories.

## Slide 534: INSIDE OF THE MICROCONTROLLER
INSTRUCTION set: we class the instructions that a µcontroleur is able to perform in groups:
1 - transfer Instructions: the µcontroller spends much of his time to move bytes from one place to another in the system:
-a device to a registry internal or vice versa,
- a registry internal to the RAM memory or vice versa.
Attention: a direct transfer from one memory to another or to a device, or an entry in ROM memory, generally cannot be done, the structure of the microcontroller makes mandatory the passage of information by one of its internal registers. Note that, with some exceptions, it is rather a copy that a transfer since the memory of origin box keeps its information (as long as there is no written something else instead).
2 - Arithmetic instructions: A µcontroller, especially 8-bit, isn't a great mathematician. It is only able to make additions, subtractions, multiplications and divisions. All complex mathematical operations (treatment of large numbers, fractional, square roots, trigonometric functions,...) must be reduced to a succession of simple operations only on bytes.
3 - Logical instructions: the µcontroleurs perform logical operations: and, or, XOR, not (inverter), rotations, shifts... Operations are operated simultaneously on the bits corresponding to the two registers.
Example: compare two bytes A and B according to a logical operation, is to realize a subtraction which overlooked the result;
We just want to know if it is null (=> A = B), positive (A > B) or negative (A < B). These indications are registered in States indicators (small stores 1 bit located in the processor)

## Slide 535: A L’INTERIEUR DU MICRO-CONTRÔLEUR
4 instructions of E/S, used to:
- read the status of a port of entry (allowing interfacing to switches, switches, optocouplers, analog/digital converters, keyboards, etc.);
- write information to the registry to an output port, which keeps the information at the disposal of the external circuits (leds, motors, relays, digital/analog converters, etc.)
- write or read information in the registers of a serial port.
5 - Connection instructions: instructions that alter the normal conduct of the program.
Jumps and subroutines are distinguished:
the jumps cause a branch of the program to a memory address that is not contiguous to the place where you are.
The subroutine or subprogram is a program part that is needed in several places in the execution of the main program.
The big difference compared to the jump, this is when connecting to memorize the address where we come from, in order to come back once the subprogram completed. This is done by memorizing the start address in a special register (stack) of the microcontroller.
Both jumps that subroutines can be:
- inconditional
- conditional, which is achieved if a certain condition is met
6 - Instructions:
- instructions of the battery management (area of memory RAM to store data during the execution of the program);
the processor control instructions: e.g. switching mode low consumption, control of devices shipped (i.e. on the same chip as the processor);
instructions to position the processor internal indicators.
These instructions vary highly according to families of microcontrollers.

## Slide 536: ALL ABOUT THE MICROCONTROLLER
In view of the integration of all these elements in a single integrated circuit case, it takes very few external electronic components around the µcontroller to make it work:
1 - The power:
all current µcontrollers work under a voltage of 1.8 to 6V with a predilection for the 5V (as a result the abundance of the so-called family TTL logic circuits that use this tension).
Soon however => 3.3V.
Very important: the voltage must be stabilized so that it works correctly.
2 - The clock: A µcontroller is a sequential logic circuit, i.e. that works at the pace of a rectangular signal, called clock that cadence all his internal circuitry.
Range: a few kHz to several MHz (compared to a PC we're over the GHz.)
Note: most f↑, it is quick but more it consumes, and more it heats up!
Attention: it is recommended to have a stable clock-online controlled by a quartz or a ceramic resonator, only electronic components capable of generating stable and precise frequency signals.
3 - Reset circuit: just like a PC, it runs a program permanently, and if the program crashes, there must be out of this situation
=> reset restart the program without disconnecting the power supply.

## Slide 537
II WHAT FAMILY OF MICROCONTROLLERS?

## Slide 538: BRIEF HISTORY AND DEVELOPMENT OF MICROCONTROLLERS
3 major steps:
1 - first microcontrollers date back to the 1970s: (Texas TMS1000 and Intel 4048, with a mask-ROM
Mask - ROM: hidden memory, written directly in Silicon memory.)
Needed:
1 - write a program,
2 - pass it on to the manufacturer and a few months later:
3 - receive a number of copies of our integrated circuit
4 - hope that our program is fair and it works!
2 - EPROM: Erasable Programmable Read Only Memory (with erasure by ultraviolet rays): Intel 8748, Motorola 68705, etc...
3 - EEPROM: since PIC 16c84 (1993)

## Slide 539: A FEW FAMILIES OF MICROCONTROLLERS
8 bits:
  PIC Microchip
  AVR Atmel
  Derivatives 80C51, 80C52
16 bits:
  dsPIC
  MSP430 Texas Instruments
32 bits:
  AVR32, PIC 32, MIPS, Power PC, STM32
  ARM produced by various companies: NxP, STMicro, Texas, Samsung, Infineon, Toshiba, Analog Device, Qualcomm, Freescale…

## Slide 540: FAMILLES DE MICRO-CONTRÔLEUR
Atmel AT91 family;
Atmel AVR family;
C167 Siemens/Infineon ;
Hitachi H8 family;
Intel 8051 family (some recent processors using a 8051 core, which is supplemented by various devices (IO ports, counters/timers, A/D and D/A, watch dog, voltage supervisor, etc.);)
Intel 8085, originally designed to be a microprocessor, often practice as a microcontroller.
Motorola/Freescale 68HC08 , 68HC12 et 68HC11 family : barcode readers, hotel card programmers, robots of amateurs, and other systems onboard.
PIC Microchip family;
ST6 STMicroelectronics family;
ADuC d'Analog Devices ;
PICBASIC Comfile Technology;
MSP430 Texas Instruments.
8080, z80, Rabbit: the 8080 is one of the great ancestors, but z80 and Rabbit are still very much alive
PSoC Cypress
LPC21xx ARM7-TDMI Philips
NEC: V800, K0…
Microcontrôleur ST6 équipé d'une mémoire EPROM effaçable aux UV.
Le MC68HC11A8 est disponible en version DIP à 48 broches, ainsi que PLCC à 52 broches, comme ici.
This processor was released for the first time in July 1976. In the early 1980s he was very popular in the design of 8 - bit computers like the Radio Shack TRS-80, the Sinclair ZX80, ZX81, ZX Spectrum, MSX, the Amstrad CPC standard and later in embedded systems.
Quatre microcontrôleurs PIC de familles différentes : 18F, 16F, 12F et 10F.

## Slide 541
AUTOPSY OF AN ARDUINO UNO PLATFORM

## Slide 542: THE ATMEL AVR microcontrollers
AVR is the term used by Atmel for the heart of the processor and the family of microcontrollers RISC implementing them (developed in 1996 by ATMEL corporation).
The architecture was designed by two students of the Institute of technology of Norway (NTH : Norges Tekniske Høgskole): Alf-Egil Bogen and Vegard Wollan
=> Alf-Egil Bogen and Vegard Wollan RISC microcontroller that gives also Advanced Virtual RISC.
Historically: the AT90S8515 was the first microcontroller based on the AVR architecture, but it's the AT90S1200 who was the 1st microcontroller to meet commercial success in 1997.
The Arduino platform is based on the architecture of the Atmel ATMEGA microcontrollers that use a heart AVR (Advanced Virtual RISC):
Attention: the language machine of AVR is incompatible with the Microchip PIC family.

## Slide 543: ATMEL AVR ARCHITECTURE
SOURCE: http://www.atmel.com/dyn/resources/prod_documents/8271S.pdf

## Slide 544: LES MICROCONTROLEURS AVR d’ATMEL – ATMEGA328
The heart of the kernel is based on 131 instructions RISC architecture. This number of instructions is quite high for such an architecture => Advanced RISC Architecture
Up to 20 million instructions per second (MIPS) for a 20 MHz Quartz (the majority of the instructions being conducted in 1 or 2 cycles)
microcontrollers AVR are so very fast!
The internal architecture of the ATMEGA328 allows us to point out the following devices:
2 Timer/Counter 8 bit with independent pre-division factor
1 Timer/Counter 16-bit with independent pre-division
1 clock time real factor with external quartz
6 channels PWM Converter
1 Analog/digital 8 channels (10 bit resolution)
1 Communication interface asynchronous USART
1 interface series synchronous I2C (Philips I2C Compatible)
1 communication Interface synchronous SPI (also used to programming In-situ)
2 interrupts on the changes of States of pins
1 timer Watchdog programmable...
The above list is the list of devices that have a major role in communication with the outside world to the microcontroller. It takes also on other typical internal functions, such as different types of Flash memory...

## Slide 545: AVR instructions
https://www.microchip.com/webdoc/avrassembler/avrassembler.wb_instructions.html

## Slide 546: AVR Assembler : I/O Registers

## Slide 547: AVR Assembler : Instructions & Directives

## Slide 548: AVR instructions

## Slide 549: LA CARTE ARDUINO « UNO »
The Arduino "Uno" is a microcontroller based on the ATmega328 which features:
of 14 digital pins of I/o (of which 6 output PWM (pulse modulated width)),
of 6 analog inputs (which can also be used in pins entrees/sorties digital),
of a 16 MHz quartz
a USB connection,
of a power jack connector,
a connector CPSI (programming "in-circuit"), cf. http://arduino.cc/en/Hacking/Programmer
and a reset button (reset).
It contains all that is necessary for the operation of the microcontroller; To use it, simply connect it to a PC by USB (or with a power adapter or a battery).

## Slide 550: ARDUINO « UNO » BOARD
Microcontroller | ATmega328
Working voltage | 5V
Power supply voltage (recommended) | 7-12V
Power supply voltage (limits) | 6-20V
I/O digital pins | 14 (among 6 with PWM output)
Broches d'entrées analogiques | 6 (used as I/O digital)
Maximum current avalaible per I/O pin (5V) | 40 mA (ATTENTION : 200mA cumulé pour l'ensemble des broches E/S)
Maximum current availaible per I/O pin (3,3V) | 50 mA
Maximum current avalaible for 5V output | Depending on power supply - 500 mA max if USB port is used alone
Flash programmable memory | 32 KB (ATmega328) with 0.5 KB used for bootloader
SRAM memory (volatile) | 2 KB (ATmega328)
EEPROM memory (non volatile) | 1 KB (ATmega328)
Clock frequency | 16 MHz
Analog Inputs/Outputs :
Arduino cards have 6 analog inputs (A0 to A5), each of which can provide a measure of resolution 10-bit (i.e. on 1024 levels) using the function analogRead() of the Arduino language.
By default, these pins measure between the (value 0) 0V and 5V (value 1023), but it is possible to change the upper measuring range reference using the AREF pin and the analogReference() Arduino language instruction.
Specific analog pins: A4 (SDA) and A5 (SCL). Support protocol I2C communications (or interface TWI (Two Wire Interface - Interface "2-wire"), available by using the Wire/I2C library.)
Note: the analog pins can also be used as digital pins: in this case, they are numbered as digital pin 14 to 19.

## Slide 551: ARDUINO « UNO » BOARD
Digital INPUTS and Outputs :
The 14 digital pins of the UNO (D0 to D13) card are used in 5V either as a digital input, digital output,
using pinMode(), digitalWrite(), and digitalRead() of the Arduino language instructions.
Each pin can provide or receive up to 40mA intensity and has a "reminder at most" internal resistance (pull up) (disconnected by default) of 20-50 KOhms. This internal resistance is activated on a PIN entry using the statement digitalWrite (PIN, HIGH).
In addition, some pins have specialized functions:
Communication series: pins D0 (RX) and D1 (TX). Used for receive (RX) and transmit (TX) data series of TTL level.
External interrupts: Pin D2 and D3. These pins can be configured to trigger an interrupt to a low value, a front rising or falling, or a change in value, see attachInterrupt()...
Pulse PWM (pulse modulated width): pins 3, 5, 6, 9, 10, and 11. Provide a 8 - bit PWM pulse using the analogWrite() statement.
SPI (serial device Interface): Pin D10 (SS), D11 (MOSI), D12 D13 (SCK) (MISO). Support communication SPI (Interface Series device) available with the library for communication SPI. The SPI pins are also connected on the ICSP connector.
LED: Pin D13. A LED is included in the map is connected to pin 13. When PIN is at the top level, the LED is lit, when the PIN is at the bottom level, the LED is off.
Other pins:
AREF: reference to (if different from the 5V) analog input voltage. Used with analogReference() instruction.
RESET: Put this PIN to the bottom level causes the reset of the microcontroller. Typically, this PIN is used to add a reset button on the circuit which blocks one present on the map.

## Slide 552: IV-4 ET DANS LE FUTUR ?
IV-4 ARDUINO FAMILY

## Slide 553: ARDUINO FAMILY …
LORA

## Slide 554: ARDUINO FAMILY !

## Slide 555: ARDUINO FAMILY !

## Slide 556: IV-4 ET DANS LE FUTUR ?
IV-4 OTHER INTERESTING
TRACKS ?

## Slide 557: IV-2 OTHER INTERESTING TRACKS!: LES MICROCHIP
Quand Microchip se réveille? Il fait des 32bits compatibles avec l’Arduino (8bits) et au même prix !!!!

## Slide 558: IV-2 OTHER INTERESTING TRACKS! : LE RASPBERRY PI
An ARM GNU/Linux box for $25. Take a byte!
Mais attention à l’arrivée de l’ARDUINO YUN:

## Slide 559: INTEL GALILEO

## Slide 560: GENUINO 101

## Slide 561: ESP32 – ESP8266
ESP32
ESP8266
PyBoard
Micro:Bit
Teensy 3.X
WiPy – Pycom
Adafruit Circuit Playground Express
Other ESP32/ESP8266 based boards

## Slide 562: TEENSY FAMILY
https://www.pjrc.com/store/teensy40.html
Technical Specifications
ARM Cortex-M7 at 600 MHz
1024K RAM (512K is tightly coupled)
2048K Flash (64K reserved for recovery & EEPROM emulation)
2 USB ports, both 480 MBit/sec
3 CAN Bus (1 with CAN FD)
2 I2S Digital Audio
1 S/PDIF Digital Audio
1 SDIO (4 bit) native SD
3 SPI, all with 16 word FIFO
3 I2C, all with 4 byte FIFO
7 Serial, all with 4 byte FIFO
32 general purpose DMA channels
31 PWM pins
40 digital pins, all interrrupt capable
14 analog pins, 2 ADCs on chip
Cryptographic Acceleration
Random Number Generator
RTC for date/time
Programmable FlexIO
Pixel Processing Pipeline
Peripheral cross triggering
Power On/Off management
 | Teensy 4.0 Development Board

## Slide 563: TEENSY FAMILY

## Slide 564: TEENSY FAMILY
Feature | Teensy 2.0 | Teensy++ 2.0 | Teensy LC | Teensy 3.2 | Teensy 3.5 | Teensy 3.6 | Units
Price | $16.00 | $24.00 | $11.65 | $19.80 | $24.25 | $29.25 | US Dollars
Processor Core Rated Speed Overclockable | ATMEGA32U4 AVR 16 - | AT90USB1286 AVR 16 - | MKL26Z64VFT4 Cortex-M0+ 48 - | MK20DX256VLH7 Cortex-M4 72 96 | MK64FX512VMD12 Cortex-M4F 120 - | MK66FX1M0VMD18 Cortex-M4F 180 240 | MHz MHz
Flash Memory Bandwidth Cache | 31.5 32 - | 127 32 - | 62 96 64 | 256 192 256 | 512 192 256 | 1024 411 8192 | kbytes Mbytes/sec Bytes
RAM | 2.5 | 8 | 8 | 64 | 256 | 256 | kbytes
EEPROM | 1024 | 4096 | 128 (emu) | 2048 | 4096 | 4096 | bytes
Direct Memory Access | - | - | 4 | 16 | 16 | 32 | Channels
Digital I/O Breadboard I/O Voltage Output Current Output Voltage Input Interrupts | 25 22 5V 20mA 5V 4 | 46 36 5V 20mA 5V 8 | 27 24 3.3V / 5V 5mA / 20mA 3.3V Only 18 | 34 24 3.3V 10mA 5V Tolerant 34 | 58 40+2 3.3V 10mA 5V Tolerant 58 | 58 40+2 3.3V 10mA 3.3V Only 58 | Pins Pins Volts milliAmps Volts Pins
Analog Input Converters Usable Resolution Prog Gain Amp Touch Sensing Comparators | 12 1 10 1 - 1 | 8 1 10 1 - 1 | 13 1 12 - 11 1 | 21 2 13 2 12 3 | 27 2 13 - - 3 | 25 2 13 - 11 4 | Pins Bits Pins
Analog Output DAC Resolution | - - | - - | 1 12 | 1 12 | 2 12 | 2 12 | Pins Bits
Timers PWM, 16 bit PWM, 8-10 bit Total PWM Outputs PDB Type CMT Type LPTMR Type PIT/Interval IEEE1588 Systick RTC | 4 Total 2 2 7 - - - - - - - | 4 Total 2 2 9 - - - - - - - | 7 Total 3 - 10 - - 1 2 - 1 0 ** | 12 Total 3 - 12 1 1 1 4 - 1 1 ** | 17 Total 4 - 20 1 1 1 4 4 1 1 | 19 Total 6 - 22 1 1 1 4 4 1 1 | Pins
Communication USB Serial With FIFOs High Res Baud SPI With FIFOs I2C CAN Bus Digital Audio SD Card Ethernet | 1 1 - - 1 - 1 - - - - | 1 1 - - 1 - 1 - - - - | 1 3 - - 2 1 2 - 1 - - | 1 3 2 3 1 1 2 1 2 - - | 1 6 2 6 3 1 3 1 2 1 1 | 2 6 2 5 3 1 4 2 2 1 1 | 

## Slide 565: COMPARATIFS

## Slide 566: QUEL MCU, MINI-PC CHOISIR EN FONCTION DE L’APPLICATION ?
 | Atmel AVR (Arduino et compatibles) | ATTiny | ESP8266 | ESP32 | STM32 | Mini-PC ARM* | Mini-PC x86**
Initiation à la programmation | ***** | **** | ***** | *** | *** | ***** | *****
Initiation à la mesure avec des capteurs | ***** | ** | ***** | **** | **** | **** | ****
Initiation au pilotage d’actionneur : moteur, servo-moteur, LED, pompe… | ***** | ** | ***** | **** | **** | **** | ***
Communiquer avec un serveur domotique en WiFi | ** | * | ***** | **** | ** | ***** | *****
Publier des mesures sur un serveur distant | ** | * | ***** | **** | ** | ***** | *****
Projets électronique vestimentaire (cosplay, wearable…) | ** | ***** | *** | *** | *** | – | –
Projets |  |  |  |  |  |  | 
RC, drone | *** | * | **** | ***** | *** | *** | *
Robotique | **** | * | ***** | ***** | ***** | ***** | *****
Environnemental | **** | ** | ***** | ***** | ***** | ***** | *****
CNC, impression 3D | ***** | * | ** | **** | ***** | ***** | *****
Accessoires domotiques | *** | * | ***** | ***** | *** | ** | *
Mobile, embarqué | * | ** | **** | ***** | *** | ***** | **
Vision | – | – | – | * | ** | ***** | ****
Traitement du signal | ** | * | ** | *** | **** | **** | *****
IA, réseau de neurones | – | – | – | – | – | **** | *****
(*) Ordinateur carte à processeur ARM
(**) Mini-PC à architecture x86 Intel ou AMD
https://projetsdiy.fr/guide-projet-objet-connecte-diy-choix-micro-controleur-bus-donnees-format/

## Slide 567: COMPARAISON DES MCU
Spécification | ATMega328P | ESP8266EX | ESP32 (2019) | SAMD21 | STM32F103C8T6 | STM32F407VET6
Core |  | Tensilica L106 32-bit RISC | Xtensa 32-bit LX6 (1 ou 2 Cores) | ARM M0 | ARM M3 | ARM M4
Puissance DMIPS | 20 | ? | 600 | ? | 90 | 225
Fréquence | 20 MHz | 160 MHz | 80 ou 240 MHz | 48 MHz | 72 MHz | 180 MHz
Mémoire Flash | 4/8/16/32 KB | 2 MB | 4 MB | 32/64/128/256 KB | 64 ou 128 Kbytes | 1 Mbytes
SRAM | 512/1K/1K/2KB | Partagée < 36KB | 520 KB | 4/8/16/32 KB | 20 KB | 192+4 Kbytes
Timers | x2 (8 bits) x1 (16 bits) |  |  | x5 (16-bits) x3 (24-bits) | x3 (16-bits) x2 watchdog x1 SysTick | x12 (16-bits) x2 (32-bits)
Cryptage (accélération matériel) |  |  | AES (FIPS PUB 197), SHA (FIPS PUB 180-4), RSA, et ECC |  |  | AES 128, 192, 256, DES, MD5, SHA-1
Debug | USB (série) | USB (série) | USB (série) + JTAG | USB (série) | Série (SWD) + JTAG | Série (SWD) + JTAG
Economie énergie | Idle, ADC Noise Reduction, Power-save, Power-down, Standby, Extended Standby | Active, modem-sleep, light-sleep, deep-sleep | Active, modem-sleep, light-sleep, deep-sleep | Idle, Standly | Sleep, Stop, Standby | Sleep, Stop, Standby
Interface et connectivité |  |  |  |  |  | 
UART | x1 | x2 | x3 | x6** | x3 | x6 (11.25 Mbit/s max.)
SPI | x1 | x2 | x3 | x6** | x2 (18 Mbit/s) | x3 (45 Mbit/s max.)
I2C | x2 | x1 | x2 | x1 | x2 | x3
I2S |  | x1 | x2 | x6** |  | x2
PWM | x6 | x4 | x16 |  | x1 (16-bits) | 
ADC | x8 (10-bits) | x1 (10-bits) | x2 (12-bits) | x1 (12-bits) | x2 (12-bits) | x3 (12-bits)
DAC |  |  | x8 (8-bits) | x1 (10-bits) |  | x2 (12-bits)
CAN 2.0 |  |  | x1 |  | x1 | x2
E/S (GPIO) | x23 | x17 | x34 | x52 | 26/37/51/80 | x140 (dont 138 tolérantes 5V)
SDIO |  | x2 (slave) | x1 |  |  | x1
Interface tactile |  |  | x10 (capacitif) | x256 (capacitif, proximité) |  | 
Infrarouge |  | x1 | x8 |  |  | 
Caméra |  |  |  |  |  | x1
Ethernet |  |  | x1 |  |  | x1 IEEE 1588v2
USB 2.0 micro-OTG |  |  | x1 | x1 | x1 | x2
WiFi |  | 802.11 b/g/n | 802.11 b/g/n |  |  | 
Bluetooth LE 4.x |  |  | Oui |  |  | 
Documentation technique | Lire | Lire | Lire | Lire | Lire | Lire
https://projetsdiy.fr/guide-projet-objet-connecte-diy-choix-micro-controleur-bus-donnees-format/

## Slide 568: QUELLE SOLUTION WIRELESS CHOISIR ?

## Slide 569: QUELLE SOLUTIONS POUR L’IOT?
http://www.linuxembedded.fr/2016/03/protocoles-de-communication-frameworks-et-systemes-dexploitation-pour-les-objets-connectes/#lora-lorawan

## Slide 570
IV-5 AND SECURITY ?

## Slide 571: AND issues of security in the Internet of things!
We’ve been waiting for this one. A worm was written for the Internet-connected Arduino Yun that gets in through a memory corruption exploit in the ATmega32u4 that’s used as the serial bridge.
The paper (as PDF) is a bit technical, but if you’re interested, it’s a great read. (Edit: The link went dead. Here is our local copy.)
The crux of the hack is getting the AVR to run out of RAM, which more than a few of us have done accidentally from time to time. Here, the hackers write more and more data into memory until they end up writing into the heap, where data that’s used to control the program lives. Writing a worm for the AVR isn’t as easy as it was in the 1990’s on PCs, because a lot of the code that you’d like to run is in flash, and thus immutable. However, if you know where enough functions are located in flash, you can just use what’s there. These kind of return-oriented programming (ROP) tricks were enough for the researchers to write a worm.
In the end, the worm is persistent, can spread from Yun to Yun, and can do most everything that you’d love/hate a worm to do. In security, we all know that a chain is only as strong as its weakest link, and here the attack isn’t against the OpenWRT Linux system running on the big chip, but rather against the small AVR chip playing a support role. Because the AVR is completely trusted by the Linux system, once you’ve got that, you’ve won.
Will this amount to anything in practice? Probably not. There are tons of systems out there with much more easily accessed vulnerabilities: hard-coded passwords and poor encryption protocols. Attacking all the Yuns in the world wouldn’t be worth one’s time. It’s a very cool proof of concept, and in our opinion, that’s even better.

## Slide 572: REFERENCES

## Slide 573: REFERENCE BOOKS

## Slide 574: REFERENCE BOOKS
ISBN13: 978-1-4302-3183-7
628 Pages
User Level: Intermediate to Advanced
Publication Date: July 18, 2011

## Slide 575: MicroPython on ESP32 - REFERENCES
https://randomnerdtutorials.com/install-upycraft-ide-windows-pc-instructions/
Installing Python 3.7.X – Windows PC
Installing uPyCraft IDE – Windows PC
https://randomnerdtutorials.com/uPyCraftWindows.
https://github.com/adobe-fonts/source-code-pro
adobe-fonts/source-code-pro
https://randomnerdtutorials.com/flash-upload-micropython-firmware-esp32-esp8266/
Flash/Upload MicroPython Firmware to ESP32 and ESP8266
https://docs.micropython.org/en/latest/esp32/tutorial/intro.html
https://randomnerdtutorials.com/esp32-esp8266-analog-readings-micropython/
https://randomnerdtutorials.com/micropython-programming-basics-esp32-esp8266/
https://randomnerdtutorials.com/esp32-lora-rfm95-transceiver-arduino-ide/
ESP32 + LoRa :
https://randomnerdtutorials.com/esp32-pinout-reference-gpios/
Pinout Reference
https://lecluseo.scenari-community.org/CircuitPython/co/AA_MQTT_1.html
My_Scenari:
https://randomnerdtutorials.com/esp32-dual-core-arduino-ide/
How to use ESP32 Dual Core with Arduino IDE

## Slide 576: MAIN RESSOURCES
MAIN RESSOURCES (ARDUINO/PROCESSING/FRITZING) & OPEN SOURCE HARDWARE: Site principal : http://arduino.cc/ Téléchargement : http://arduino.cc/en/Main/Software Guide de référence du langage : http://arduino.cc/en/Reference/HomePage Forum de discussion : http://arduino.cc/forum/ Le forum français : http://www.arduino.cc/cgi-bin/yabb2/YaBB.pl?board=francais
Blog : http://arduino.cc/blog/ Wiki / playground (incontournable) : http://arduino.cc/playground/ wikipedia (fr) http://fr.wikipedia.org/wiki/Arduino
Liste des Shields: http://shieldlist.org/
Education: http://scuola.arduino.cc/
Processing: http://processing.org/
Fritzing : http://fritzing.org/ (Prototypage Dessin des cartes , circuit graphique, schématique ou électronique)
Open Source Hardware: http://dangerousprototypes.com/2011/06/30/tutorial-arduino-and-the-spi-bus/
Et quand cela ne marche PAS !!! : http://arduino.cc/en/Guide/Troubleshooting
SUR LE WEB:
Référence arduino en français : http://www.mon-club-elec.fr/pmwiki_refe … n.HomePage
Référence en français: http://www.mon-club-elec.fr/ : site perso amateur sur lequel je mets en ligne mes développements en électronique numérique programmée, dans une optique ludique et expérimentale, “just for fun” ! Initiation à Arduino (2006) : http://www.craslab.org/arduino/livretht … oCRAS.html (ou en version pdf) The World Famous Index of Arduino & Freeduino Knowledge : http://www.freeduino.org/ Tutoriels de Tronixstuff http://tronixstuff.wordpress.com/tutorials/
Tutoriels d’Adafruit: http://www.adafruit.com/tutorials
Ressources / tutoriaux pour arduino sur le site du labomedia : http://wiki.labomedia.org/index.php/Lie … ux_Arduino Scratch pour Arduino : http://seaside.citilab.eu/scratch/arduino Liste de discussion des développeurs d'arduino : http://arduino.cc/mailman/listinfo/deve … arduino.cc Documentaire sur Arduino: http://vimeo.com/18539129

## Slide 577: WEB LINKS
GENERALISTES:
http://www.bricoelec.com/[fr] Portail francophone de l’arduino : Robotique, Bidouillage et hacking matériel (DIY)! http://arts-numeriques.codedrops.net/-Microcontrolleur-arduino-[fr] http://www.ladyada.net/learn/arduino/index.html http://itp.nyu.edu/physcomp/Tutorials/ArduinoBreadboard http://todbot.com/blog/bionicarduino/[en] It is an introduction to microcontroller programming and interfacing with the real world using the Arduino physical computing platform. It focuses on building new physical senses and making motion with the building blocks of robotics, using Arduino as a platform.
•Très bon tutoriels progressifs : http://todbot.com/blog/spookyarduino/
•le site de Tom Igoe http://tigoe.net/pcomp/
•les sites Make, Hackaday, Sensorwiki, We make money not art, et bien d’autres encore pour avoir des conseils, des schémas, des idées....
•les sites de service de liens, de vidéos et d’images ( google, delicious, youtube, flickr,)
http://luckylarry.co.uk/arduino-projects/arduino-weblinks-projects/
http://hacknmod.com/hack/top-40-arduino-projects-of-the-web/
http://santy.wikidot.com/arduino
http://zedomax.com/blog/2010/02/16/top-10-diy-arduino-projects-and-how-to-tutorials/
Liens divers: http://www.uni-weimar.de/medien/wiki/Arduino/Links
http://barzilouik.free.fr/wiki/doku.php?id=arduino:tutorial
REVENDEURS:
http://shop.snootlab.com/ (Toulouse !!!)
http://www.lextronic.fr/
http://www.robotshop.com/eu/arduino-en.html
http://boutique.semageek.com/fr/2-arduino
http://adafruit.com/
http://www.sparkfun.com/

## Slide 578: TO GO FURTHER : BUS I2C
I2C: http://www.byteparadigm.com/kb/article/AA-00255/22/Introduction-to-SPI-and-IC-protocols.html
http://www.atmicroprog.com/cours/I2C/i2c.php
http://www.esacademy.com/en/library/technical-articles-and-documents/miscellaneous/i2c-bus.html
http://www.robot-electronics.co.uk/acatalog/I2C_Tutorial.html
http://www.neufeld.newton.ks.us/electronics/?p=241
Librairie Wii-Nunchuk: https://github.com/lgeek/Arduino-Wii-Nunchuk
TOP 30 utilisation du Nunchuk: http://hacknmod.com/hack/top-30-wiimote-hacks-of-the-web/
http://johnnylee.net/projects/wii/
http://www.planete-sciences.org/robot/ressources/electronique/protocoleI2C/index.html
http://www.pobot.org/Controle-avec-un-Wii-Nunchuck.html
Wii Motion Plus + Nunchuck: http://voidbot.net/nunchchuk-and-wii-motion-plus-6-DOF.html
http://randomhacksofboredom.blogspot.com/2009/06/wii-motion-plus-arduino-love.html
http://www.freelug.org/spip.php?article917
http://www.aurel32.net/elec/i2c.php
http://todbot.com/blog/bionicarduino/
http://todbot.com/blog/2010/09/25/softi2cmaster-add-i2c-to-any-arduino-pins/
http://tronixstuff.wordpress.com/2010/10/20/tutorial-arduino-and-the-i2c-bus/
http://tronixstuff.wordpress.com/2010/10/29/tutorial-arduino-and-the-i2c-bus-part-two/
http://tronixstuff.wordpress.com/2010/05/20/getting-started-with-arduino-%E2%80%93-chapter-seven/
http://www.nearfuturelaboratory.com/2009/07/17/lis302dl-a-3-axis-accelerometer/
http://wiire.org/Main_Page
http://wiire.org/Wii/protocols/wiimote_bus#Wiimote_Bus_Pins_.286-pin_proprietary_connector_on_Wiimote.29
Note:
There are both 7- and 8-bit versions of I2C addresses. 7 bits identify the device, and the eighth bit determines if it's being written to or read from. The Wire library uses 7 bit addresses throughout. If you have a datasheet or sample code that uses 8 bit address, you'll want to drop the low bit (i.e. shift the value one bit to the right), yielding an address between 0 and 127.
COMMUNICATION EN GENERAL: http://arduino.cc/playground/Main/InterfacingWithHardware#Communication

## Slide 579: WEB LINKS
TAPIS SENSITIF, ÉCRANS MULTI-TOUCH…: http://numuscus.pascsaq.org/?p=551
http://www.interface-z.com/
http://codelab.fr/2552, partie table Multi-Touch et reactive: http://codelab.fr/1076
ROBOT: http://arduino103.blogspot.com/2011/06/comment-dimensionner-un-moteur.html
http://www.pobot.org/[fr] L’association POBOT a été créée en 2003, par un groupe de passionnés de robotique, dans le but : d’apprendre ensemble, de se perfectionner, d’échanger, de s’entre-aider.
http://www.robot-maker.com/index.php?/topic/3380-divers-robots-a-a-base-darduino-et-de-wifi/
http://robot.aspi.free.fr/
POUR LES ARTISTES:
http://softwear.cc/book/2011/open-softwear-2nd-edition/page/2/
http://web.media.mit.edu/~leah/LilyPad/
ANDROID ADK MEETS ARDUINO: http://www.amarino-toolkit.net/index.php/my-apps.html
http://www.mobot.es/MobotBTCar.html
Vélo pour Geek: http://www.michaelfretz.com/2011/01/03/punkt-fizen-android-and-arduino-powered-bike-navigation/
http://www.labradoc.com/i/follower/p/android-arduino-accessory
http://www.labradoc.com/i/follower
http://www.semageek.com/handbag-une-application-android-pour-piloter-ladk-arduino-sans-programmation/
CAPTEURS: http://itp.nyu.edu/physcomp/sensors/Reports/Reports
vers l’interface MIDI avec une arduino: http://itp.nyu.edu/physcomp/Labs/MIDIOutput
RFID: http://www.sparkfun.com/products/8419
http://jadiema.blogspot.com/2011/03/arduino-rfid-reader-piezo-sounder.html
COMPASS: http://lusorobotica.com/index.php/topic,36.0.html, http://wiring.org.co/learning/libraries/hmc6352sparkfun.html
APPROCHE CLIENT-SERVEUR AVEC LIAISON WIFI : http://www.mon-club-elec.fr/pmwiki_mon_club_elec/pmwiki.php?n=MAIN.ArduinoExpertSymbioseArduinoPCPrincipeDeploiement
NUNCHUK MEETS NXT: http://www.mindstormsforum.de/viewtopic.php?t=3828
CELLULES SOLAIRES : http://www.doctormonk.com/2011/09/arduino-solar-radio.html
RASPBERRY-Pi : http://www.doctormonk.com/2012/04/raspberry-pi-and-arduino.html

## Slide 580: LINKS
Introduction au système Arduino :
http://www.mon-club-elec.fr/pmwiki_reference_arduino/pmwiki.php?n=Main.DebuterIntroduction
Vue d’ensemble des cartes :
http://www.mon-club-elec.fr/pmwiki_reference_arduino/pmwiki.php?n=Main.Materiel
FAQ : => http://www.mon-club-elec.fr/pmwiki_reference_arduino/pmwiki.php?n=Main.FAQ
Définition de l’open source ! et plein d’autres bricoles => Lien avec les shields…
Le Logiciel :
http://www.mon-club-elec.fr/pmwiki_reference_arduino/pmwiki.php?n=Main.DebuterPresentationLogiciel
La carte Duemilanove :
http://www.mon-club-elec.fr/pmwiki_reference_arduino/pmwiki.php?n=Main.MaterielDuemilanove
Le brochage :
http://www.mon-club-elec.fr/pmwiki_mon_club_elec/pmwiki.php?n=MAIN.REFERENCESBrochageDuemilanove
Compilation :
http://www.mon-club-elec.fr/pmwiki_reference_arduino/pmwiki.php?n=Main.ApprendreProcedureCompilation
Premier programme :
http://www.mon-club-elec.fr/pmwiki_reference_arduino/pmwiki.php?n=Main.ApprendreProgrammeTypeMinimum
Références :
http://www.mon-club-elec.fr/pmwiki_reference_arduino/pmwiki.php?n=Main.Reference
Références Etendues:
http://www.mon-club-elec.fr/pmwiki_reference_arduino/pmwiki.php?n=Main.ReferenceEtendue
Les librairies de références :
http://www.mon-club-elec.fr/pmwiki_reference_arduino/pmwiki.php?n=Main.ReferenceLibrairies
http://www.mon-club-elec.fr/pmwiki_reference_arduino/pmwiki.php?n=Main.Librairies
Serial : http://www.mon-club-elec.fr/pmwiki_reference_arduino/pmwiki.php?n=Main.Serial
Stepper: http://www.mon-club-elec.fr/pmwiki_reference_arduino/pmwiki.php?n=Main.LibrairieStepper
Servo: http://www.mon-club-elec.fr/pmwiki_reference_arduino/pmwiki.php?n=Main.LibrairieServo
LCD: http://www.mon-club-elec.fr/pmwiki_reference_arduino/pmwiki.php?n=Main.LibrairieLCD
http://www.aurel32.net/elec/lcd.php , http://fabrice.sincere.pagesperso-orange.fr/cm_electronique/projet_pic/LCDalpha/LCDalpha.htm

## Slide 581: LINKS
Comment écrire une librairie: http://www.robotix.fr/tutoriel-1-59-creer-une-bibliotheque-arduino.html
http://www.robot-maker.com/index.php?/user/4963-Philippe-RX/page__tab__tutorials
Fiche sur LCD => Communication avec LCD : http://www.mon-club-elec.fr/pmwiki_mon_club_elec/pmwiki.php?n=MAIN.TechniquePreparationLCD
Fiche Touch Shield Nintendo DS (Entrée analogique et Sortie Digitale)
Fiche sur Nunchuck (accelerometer) => Bus I2C
Bus SPI http://www.arduino.cc/playground/Code/Spi
Pourquoi ne pas écrire dans une carte SD ? => il faut le shield Ethernet officiel:
http://www.ladyada.net/learn/arduino/ethfiles.html
Fiche sur l’ethernet Shield : http://www.ladyada.net/learn/arduino/ethfiles.html
Tester les interruptions externes => Optocoupleur à fourche : http://www.mon-club-elec.fr/pmwiki_mon_club_elec/pmwiki.php?n=MAIN.ArduinoInitiationEntreesOnOffOptoFourcheTestSimple
http://www.mon-club-elec.fr/pmwiki_mon_club_elec/pmwiki.php?n=MAIN.MaterielCapteurIRoptofourcheLTH301-07
http://www.gotronic.fr/catalog/opto/interrupteurs.htm
http://www.mon-club-elec.fr/pmwiki_mon_club_elec/pmwiki.php?n=MAIN.ArduinoExpertServoPanSuiviBalle
Focus sur les Shields
http://www.mon-club-elec.fr/pmwiki_mon_club_elec/pmwiki.php?n=MAIN.MATERIEL
Alimentation de PC:
http://www.mon-club-elec.fr/pmwiki_mon_club_elec/pmwiki.php?n=MAIN.TECHNIQUETrucsUtiliserAlimPC
LIENS PROCESSING :
http://www.mon-club-elec.fr/pmwiki_mon_club_elec/pmwiki.php?n=MAIN.OUTILSProcessing
http://www.scoop.it/t/arduino-processing
ARDUINO MEETS PROCESSING:
http://webzone.k3.mah.se/projects/arduino-workshop/projects/arduino_meets_processing/instructions/index.html
ARDUINO MEETS FLASH:
http://www.fabiobiondi.com/blog/2009/11/arduino-and-flash-modify-your-existent-flash-games-to-work-with-a-joystick/
http://www.fabiobiondi.com/blog/2009/10/arduino-and-flex-connect-a-joystick-to-your-application/
Divers :
Générateur de code: http://www.mon-club-elec.fr/pmwiki_generateur_code/pmwiki.php?n=Main.HomePage
R2D2 Translator: http://www.r2d2translator.com/
ARDUINO MEETS LABVIEW: http://sine.ni.com/nips/cds/view/p/lang/en/nid/209835
http://vishots.com/getting-started-with-the-labview-interface-for-arduino/
Et un article pour réfléchir: http://www.framablog.org/index.php/post/2010/06/02/arduino-materiel-libre

## Slide 582: LINKS
OPEN SOURCE HARDWARE ET LICENCE LIBRE
http://en.wikipedia.org/wiki/Open_source_hardware
http://fr.wikipedia.org/wiki/Copyleft
http://fr.wikipedia.org/wiki/Licence_Creative_Commons
http://freedomdefined.org/Definition/Fr
http://creativecommons.org/licenses/by-nc-sa/2.0/fr/
http://opensource.org/osd
http://www.siteduzero.com/sciences/tutoriels/arduino-pour-bien-commencer-en-electronique-et-en-programmation/transformation-pwm-signal-analogique
http://arduino-info.wikispaces.com/Arduino-PWM-Frequency
PWM
https://fr.wikiversity.org/wiki/Micro_contr%C3%B4leurs_AVR
http://blog.cicatrice.eu/electronique/avr

## Slide 583: LINKS ON TOULOUSE
http://linuxedu.ac-toulouse.fr/doku.php?id=materiel:arduino:ressources:pedagogiques
http://www.planete-sciences.org/robot/boiteabots/index.php?option=com_content&task=view&id=44
http://planet.madeinfr.org/tag/arduino
TETALAB: http://tetalab.org/
The Tetalab is a hackerspace Toulouse created in June 2009, with a framework for software/hardware projects.

## Slide 584: GITHUB

## Slide 585: GitHUB
- Vous écrivez un peu de code et souhaitez collaborer avec d'autres développeurs ?
Vous voulez toujours savoir pourquoi une modification a été faite et ne plus risquer de perdre des jours de travail ?
Vous avez clairement besoin de versionner votre code !
Un logiciel de gestion de versions est un outil incontournable pour tout développeur. Il en existe de nombreux, et dans ce cours vous découvrirez Git, le logiciel créé par Linus Torvald, auteur du Kernel Linux.
Vous découvrirez ce qu'est la gestion de version et les avantages que cela apporte.
Puis, vous plongerez dans l'univers de Git : commit, branches, merge... tous ces termes n'auront plus de secrets pour vous !
Enfin vous apprendrez à utiliser GitHub pour héberger votre code et collaborer facilement sur des projets open-source.

## Slide 586: COMMANDES LINUX LES PLUS UTILES

## Slide 587: COMMANDES LES PLUS UTILES SUR LINUX - RASPBIAN
Les 42 commandes les plus utiles sur Raspberry PI
Si vous souhaitez connaitre les commandes, il vous suffira de rentre les commande suivie de –help.
Commandes générales
apt-get update : Met à jour votre version de Raspbian.
apt-get upgrade : Met à niveau tous les logiciels que vous avez installés.
clear : Efface l’écran du terminal des commandes et du texte précédemment exécutés.
date : Affiche la date actuelle.
find / -name exemple.txt : Recherche dans le système entier le fichier exemple.txt et génère une liste de tous les répertoires qui contiennent le fichier.
nano example.txt : Ouvre le fichier example.txt dans “Nano”, l’éditeur de texte de linux.
poweroff : Arrêt immédiat du raspberry PI.
raspi-config : Ouvre le menu des paramètres de configuration.
reboot : Pour rebooter immédiatement le Raspberry PI.
shutdown -h now : Pour éteindre immédiatement le Raspberry PI.
shutdown -h 01:22 : Pour éteindre le Raspberry PI à 1:22 AM.
startx : Ouvrir l’interface graphique GUI (Graphical User Interface).
Commandes sur les fichiers et répertoires
cat exemple.txt : Affiche le contenu du fichier exemple.txt.
cd /abc/xyz : Change de répertoire courant pour le répertoire /abc/xyz.
cp XXX : Copie le fichier ou le répertoire XXX et le colle à un emplacement spécifique. Par exemple: cp exemplefile.txt /home/pi/office/ copie exemplefile.txt du répertoire courant et le colle dans le répertoire /home/pi/ directory. Si le fichier n’est pas présent dans le répertoire courant, vous pouvez ajouter son chemin en préfixe (par exemple : cp /home/pi/documents/examplefile.txt /home/pi/office/ copie le fichier du répertoire documents dans le répertoire office).
ls -l : Liste tous les fichiers du répertoire en cours, ainsi que la taille du fichier, la date de modification et les autorisations.
mkdir exemple_directory : Créer dans le répertoire courant un nouveau répertoire exemple_directory.
mv XXX : Déplace un fichier ou un répertoire nomé XXX à un emplacement spécifique.Par exemple, mv exemplefile.txt /home/pi/office/ déplace exemplefile.txt dans le répertoire /home/pi/office. Si le fichier n’est pas présent dans le répertoire courant, vous pouvez ajouter son chemin en préfixe (par exemple :. cp /home/pi/documents/exemplefile.txt /home/pi/office/ déplace le fichier du répertoire documents dans le répertoire office). Cette commande peut aussi être utilisé pour renommer des fichier (mais seulement dans le même répertoire). par exemple, mv examplefile.txt newfile.txt renomme examplefile.txt en newfile.txt, et conserve le fichier dans le même répertoire.
rm example.txt : Effacer le fichier example.txt.
rmdir example_directory : Effacer le répertoire example_directory (seulement si il est vide).
scp user@10.0.0.32 :/some/path/file.txt : Copier un fichier à travers SSH. Peut être utilisé pour télécharger un fichier à partir d’un ordinateur de bureau / ordinateur portable sur le Raspberry Pi. user@10.0.0.32 est le nom d’ utilisateur et l’adresse IP locale du bureau / ordinateur portable et /some/path/file.txt est le chemin d’accès et le nom du fichier sur le bureau / ordinateur portable.
touch :Crée un nouveau fichier vide dans le répertoire courant.

## Slide 588: COMMANDES LES PLUS UTILES SUR LINUX - RASPBIAN
Commandes Réseau et Internet:
ifconfig :Pour vérifier l’état de la connexion réseau que vous utilisez (pour voir si wlan0 dispose d’ une adresse IP par exemple).
iwconfig : Pour vérifier quel réseau l’adaptateur sans fil utilise par exemple.
iwlist wlan0 scan : Affiche une liste des réseaux sans fil actuellement disponibles sur wlan0.
iwlist wlan0 scan | grep ESSID : Utilisez grep avec le nom d’un champ pour répertorier uniquement les champs dont vous avez besoin (par exemple, pour lister les ESSID uniquement).
nmap : Analyse votre réseau et répertorie les périphériques connectés, le numéro de port, le protocole, le système d’exploitation, l’état (ouvert ou fermé), les adresses MAC et d’autres informations.
ping : Teste la connectivité entre deux périphériques connectés sur un réseau. Par exemple, ping 10.0.0.32 envoie un paquet à l’appareil à IP 10.0.0.32 et attend une réponse. Il fonctionne également avec les adresses de sites Web.
wget http://www.website.com/example.txt : Télécharge le fichier example.txt depuis le Web et l’enregistre dans le répertoire courant.
Commandes d’informations systèmes:
cat /proc/meminfo : Affiche des détails sur votre mémoire.
cat /proc/partitions :Affiche la taille et le nombre de partitions sur votre carte SD ou votre disque dur.
cat /proc/version : Affiche la version de la Rasperry Pi que vous utilisez.
df -h : Affiche des informations sur l’espace disque disponible.
df / :Indique la quantité d’espace disque disponible.
dpkg –get-selections | grep XXX : Affiche tous les packages installés qui sont liés à XXX.
dpkg –get-selections : Affiche tous les paquets installés.
free : Indique la quantité de mémoire libre disponible.
hostname -I : Affiche l’adresse IP de votre Raspberry Pi.
lsusb : Liste tous les périphériques USB connectés à votre Raspberry Pi.
Touche HAUT : En appuyant sur la touche HAUT, vous entrez la dernière commande entrée dans l’invite de commande. C’est un moyen rapide de corriger les commandes qui ont été faites par erreur.
vcgencmd measure_temp :Affiche la température de la CPU.
vcgencmd get_mem arm && vcgencmd get_mem gpu : Affiche la mémoire divisée entre le processeur et le GPU.

## Slide 589: RASPBERRY PI 4
from gpiozero import LED
from time import sleep
led = LED(17)
while True:
led.on()
sleep(1)
led.off()
sleep(1)
https://gpiozero.readthedocs.io/en/stable/installing.html
import RPi.GPIO as GPIO
import time
GPIO.setmode(GPIO.BCM)
GPIO.setup(23, GPIO.IN, pull_up_down=GPIO.PUD_UP) #Button to GPIO23
GPIO.setup(24, GPIO.OUT) #LED to GPIO24
try:
while True:
button_state = GPIO.input(23)
if button_state == False:
GPIO.output(24, True)
print('Button Pressed...')
time.sleep(0.2)
else:
GPIO.output(24, False)
except:
GPIO.cleanup()
GPIO.PUD_UP , the pull-up resistor is enabled;

## Slide 590: CHEAT SHEET

## Slide 591: GLOSSARY & VOCABULARY OF THE ARDUINO
ANALOG : Analogique (0 à 1023 sur l’arduino) .
AREF : Abréviation pour Analog REFérence, référence analogique.
AVAILABLE : Disponible.
BEGIN : Début.
BIT : bit, unité d'information informatique pouvant prendre soit la valeur 0 soit la valeur 1.
BUFFER : Tampon, dans le sens de "zone tampon". Mémoire temporaire
BYTE : Octet, soit un groupe de 8 bits.
BPS : Abréviation pour Bits Per Second, Bits Par Seconde. Attention, abréviation toujours en minuscules.
BREADBOARD: plaque d’expérimentation
CAPACITOR: condensateur
CHAR : Pour CHARacter, caractère (typographique). Type de variable d'une taille d'un octet. C'est un synonyme de "byte" utilisé pour déclarer des variables stockant un caractère ou des chaines de caractères.
DEFINE : Définit.
DIGITAL : Numérique (0 (LOW) ou 1 (HIGH))
DO : Faire.
FALSE : Faux.
FOR : Pour. Jusqu'à ce que.
GND : Abréviation pour GrouND, la terre. C'est la masse, 0 Volt.
HIGH : Haut.
ICSP: Abréviation pour In Cicuit Serial Programming, programmation série sur circuit.
IF / THEN/ ELSE : Si / Alors / Sinon.
IN : Souvent l'abréviation pour INput, Entrée. Est toujours en rapport avec le sens extérieur vers carte Arduino.
INCLUDE : Inclut.
INPUT : Entrée.
IS : Est (souvent dans le sens d'une question : Est ?).
INT : Abréviation pour INTeger, entier. Groupe de 16 bits, 2 octets groupés, considérés comme représentant un nombre entier négatif ou positif.
LONG : Abréviation pour "entier long". Groupe de 32 bits, 4 octets groupés, considérés comme représentant un nombre entier négatif ou positif.
LOOP : Boucle.
LOW : Bas.
OUT : Souvent l'abréviation pour OUTput, Sortie. Est toujours en rapport avec le sens carte Arduino vers extérieur.
OUTPUT : Sortie.
PIN : Broche d’E/S connectée à quelque chose (e.g. une LED).
POWER : Puissance, alimentation.
PWM : Abréviation de (Pulse Width Modulation), soit Modulation en Largeur d'Impulsion.
PWR : Abréviation pour PoWeR, puissance, alimentation.
READ: Lire.
RESISTOR: résistance.
RELAY: relais.
RX : Abréviation pour Receive, réception.
SERIAL : Série.
SETUP : Initialisation.
SENSOR: capteur
SKETCH: programme qui tourne sur le micro-contrôleur
SWITCH : basculer, interrupteur
TRUE : Vrai.
TX: Abréviation pour Transmit, transmission.
WIRING: câble, fils montrant les interconnections physiques des composants.
WHILE : Tant que.
WORD : mot, soit dans le sens de langage ; soit dans le sens d'un groupe de 16 bits, 2 octets groupés considérés comme représentant un nombre entier positif (>= 0).
WRITE: Ecrire.

## Slide 592: A QUIZ FOR YOUR TRAINING...
http://moodle.insa-toulouse.fr/mod/quiz/view.php?id=18029
After taking this course, here's a quiz to test your knowledge:
Quiz section of the course on MOODLE :

## Slide 593: BONUS

## Slide 594
MICROCONTROLERS & OPEN SOURCE HARDWARE
http://moodle.insa-toulouse.fr/course/view.php?id=494
INTRODUCTION TO THE MEASUREMENT CHAIN AND SMART DEVICES
GITHUB
PTP INNOVATIVE SMART SYSTEM - ISS
SENSORS
AND DATASHEET
SENSOR FABRICATION (CLEAN ROOM AIME)
PCB ELABORATION (KICAD) + ANALOG CIRCUIT

## Slide 595: PRATICAL WORK: PTP ISS
TP n°1A: My first program : Blink
TP n°1C: Serial Monitor (Arduino => PC)
[ TP n°1G: Buzzer melody ]
TP n°1H: temperature sensor
TP n°2A: Touch Pad DS
TP n°2B: LCD (autonomus)
TP n°2D: LCD & Temperature (1/2 Group)
TP n°2C: Touch Pad & LCD (1/2 Group)
TP n°3A: Continus Current Motor
TP n°3B: Photorésistance
[ TP n°3C: Servo-motor ]
[ TP n°3D: Software debouncing ]
[ TP n°3E: Hardware debouncing ]
TP n°3F: Interruptions
TP n°4A: Nunchuk Wii
[ TP n°4B: Nunchuk Wii & Servo-motor ]
[ TP n°4C: My first library]
TP n°4D: Processing & Arduino: my first program
TP n°1
TP n°2
TP n°3
TP n°4
TP n°1D: Serial Monitor (PC => Arduino)
TP PCB DESIGN
KiCAD + Design de shield Arduino®
Android and Arduino application creation :
bi-direction communication
TP n°5
Files for TP n°1 to 12 are avalaible on MOODLE: http://moodle.insa-toulouse.fr/course/view.php?id=494
TP GiTHub
GitHub
Piste Verte
Piste Bleue
Piste Rouge
TP n°8
  TP8 - 1 - TP ANALOG READ ON ESP32
  TP8 - 2 - TP OLED ON ESP32
  TP8 - 3 - TP ANALOG + OLED ON ESP32
  TP8 - 4 - TP CAPACITIVE TOUCH
  TP8 - 5 - TP HALL EFFECT SENSOR
TP n°7
TP 7 - ARDUINO ET NODE-RED
TP INTRO
MICROPYTHON PROGRAMMING BASICS
GETTING STARTED WITH uPiCraft
TP n°10
  TP10 - TP LoRa ON ESP32
TP n°9
  TP9 - 1 – TWO WAY COM via MQTT ON ESP32
  TP9 - 2 – CONNECT ESP32 AND NODERE AND DALLAS TEMP
TP n°12
TP12 THE THING NETWORK
TP n°1B: Blink without delay
TP n°1E: Module HC-05 Bluetooth
TP n°1F: Encodeur rotatoire
TP n°4E: SPI Digital Potentiometer
TP INTRO
TP VISUAL STUDIO CODE + PLATFORM IO

## Slide 596: PRATICAL WORK – PTP ISS
Construction of an Open Hardware solution:
Creating a shield to send data from a gas by LoRa sensor to The Thing Networks:
Link : https://moodle.insa-toulouse.fr/course/view.php?id=494#section-19
GREEN track :
I) Communication even LoRa pair
1 - communicate with the chip RN2483
2 - setting in place of a chip in rec mode reconstructed
3 - bet place a chip in transmit mode
BLUE track :
II) creating a LoRaWAN application: 'Gas sensor connected' to accomplish this application we will use several components: Arduino Uno, RN2483, Buzzer, MQ, button gas sensor tappet, Resistance, Led
1) a quick prototype: purpose: network connection TTN, management of a disruption on the gas sensor indicating the presence of danger, sends the data over the network.
2) realize the shield: the realization of the shield will be done through the KiCAD software.
RED track :
III) manage the power consumption of the entire system 1) find a way to measure consumption
2) manage consumption
BLACK track :
Goal: achieve a dashboard with NodeRed to visualize the data of TTN!
TP
Mini-Lab